## Slide 1
IEEE 802.11 TGbp Motion Dock
Date: 2024-07-18
Author:

## Slide 2
This document records TGbp motions planned and conducted during TGbp meetings.
TGbp motions during teleconferences should be announced at least 10 days before the teleconference running those motions.
TGbp motions on leadership confirmation and approval of meeting minutes are not included in this dock.
Note 1 - 802.11 WG Operation Manual requests “Teleconferences are a means to prepare input for sessions provided that the teleconference date, time, agenda, and arrangements are announced on the TG email reflector at least 10 calendar days prior to the teleconference date"
Note 2 - Teleconferences are bound by the conditions stipulated by the documentation below. Please review them and bring up any questions/concerns you may have before proceeding with the teleconference:
Abstract

## Slide 3
Motion #1 (May 16, PM1, 2024)
Approve the TGbp initial timeline plan as illustrated in slide 33 as in 11-24/0666r5.
Note, the timeline plan is subject to change according to the 11bp developing progress.
Result: Approved with unanimous consent

## Slide 4
Motion #2 (Jul 18, PM1, 2024)
Move to approve the TGbp selection procedure as defined in 11-24/0897r1
Moved: Bo Sun
Seconded: Vytas Kezys
Result: Approved with unanimous consent

## Slide 5
Motion #3 (Jul 18, PM1, 2024)
Move to approve the baseline of TGbp Function Requirements doc as included in 11-24/1307r1, for future development based on consensus
Moved: Bin Qian
Seconded: Bin Tian
Result: Approved with unanimous consent

## Slide 6
Motion #4 (Sep 9, PM1, 2024)
Move to approve the baseline of TGbp Specification Framework Document (SFD) as included in 11-24/1613r0, for future development based on consensus
Moved: Yinan Qi
Seconded: Sebastian Max
Result: Approved with unanimous consent

## Slide 7
Motion #5 (FRD; Sep 12, PM2, 2024)
Move to include following content to sub-clause 2.1 of TGbp FRD:
“11bp defines at least one mode of MAC/PHY that supports close-range mono-static backscattering communication in 2.4 GHz.”
[DCN# 11-24/0798r1] SP: 37Y/6N/23A
Moved: Rui Cao
Seconded: Lei Huang
Result: Approved with unanimous consent

## Slide 8
Motion #6 (FRD; Sep 12, PM2, 2024)
Move to include following content to sub-clause 2.1 of TGbp FRD:
“11bp defines at least one mode of MAC/PHY that supports bi-static backscattering communication in 2.4 GHz.”
[DCN# 11-24/1215r1] SP:No objection
Moved: Bin Qian
Seconded: Hongyuan Zhang
Result: Approved with unanimous consent

## Slide 9
Motion #7 (SFD; Sep 12, PM2, 2024)
Move to include following content to TGbp SFD:
“11bp supports a mode to enable AMP devices to operate in legacy WLAN network by defining AMP DL and required control/signaling.”
[DCN# 11-24/1263r0] SP: 33Y/2N/6A
Moved: Pooria Pakrooh
Seconded: Bin Tian
Result: Approved with unanimous consent

## Slide 10
Motion #8 (SFD; Sep 12, PM2, 2024)
Move to include following content to sub-clause 4 of TGbp SFD:
  “IEEE 802.11bp will specify, in 2.4 GHz, an AMP Downlink PPDU containing at least an 802.11 preamble field, an AMP-Sync field and an AMP-Data field. Inclusion of an AMP-SIG field is TBD.
    The details of the 802.11 preamble field are TBD.
    Additionally, for transmission to backscatter STAs there will be one or more Excitation fields
    Additionally, for transmission to backscatter STAs there may be more than one AMP-Data field
      Additionally, AMP-Sync and AMP-SIG field may precede each AMP-Data field
    Name of this Downlink PPDU is TBD.
[DCN# 11-24/1345r2] SP: No objection
Moved: Steve Shellhammer
Seconded: Christian Berger
Result: Approved with unanimous consent

## Slide 11
Motion #9 (SFD; Sep 12, PM2, 2024)
Move to include following content to sub-clause 4 of TGbp SFD:
“The AMP Downlink PPDU AMP-Sync field and the AMP-Data field will use On-Off Keying (OOK) modulation.”
[DCN# 11-24/1345r2] SP: no objection
Moved: Steve Shellhammer
Seconded: Weijie Xu
Result: Approve with unanimous consent

## Slide 12
Motion #10 (SFD; Sep 12, PM2, 2024)
Move to include following content to sub-clause 4 of TGbp SFD:
“The AMP Downlink PPDU AMP-Data field will use Manchester encoding for non-backscatter operation.
  For the Backscatter case, the AMP-Data field encoding scheme is TBD.
”
[DCN# 11-24/1345r2] SP: No objection
Moved: Steve Shellhammer
Seconded: Bin Qian
Result: Approved with unanimous consent

## Slide 13
Motion #11 (SFD; Sep 12, PM2, 2024)
Move to include following content to sub-clause 4 of TGbp SFD:
“IEEE 802.11bp shall specify, in 2.4 GHz, an AMP uplink PPDU for AMP STA supporting active transmission that contains an AMP-Sync field and AMP-Data field. Inclusion of an AMP-SIG field in the AMP uplink PPDU is TBD.
  The bandwidth of the AMP uplink PPDU is less than 20 MHz”
[DCN# 11-24/1496] SP: no objection
Moved: Bin Qian
Seconded: Weijie Xu
Result: Approved with unanimous consent

## Slide 14
Motion #12 (FRD; Sep 12, PM2, 2024)
Move to include following content to TGbp FRD:
“802.11bp defines AMP Timing Synchronization Function (AMP TSF)”
[DCN# 11-24/1475r3] SP: 31Y/7N/32A
Moved: Weijie Xu
Seconded: Yinan Qi
Result: Approved with unanimous consent

## Slide 15
Motion #13 (SFD; Sep 12, PM2, 2024)
Move to include following content to TGbp SFD:
  “If AMP device is able to support AMP TSF, the maximum timing offset is ± 10^4 ppm”
[DCN# 11-24/1475r3] SP: no objection
Moved: Weijie Xu
Seconded: Lei Huang
Result: Approved with unanimous consent

## Slide 16
Motion #14 (SFD; Sep 12, PM2, 2024)
Move to include following content to TGbp SFD:
“11bp defines at least one mode of MAC/PHY that allows an AMP-only device with active uplink communication in 2.4GHz subject to the following requirements:
  clock accuracy requirement is relaxed compared to legacy 802.11 devices;
  the active uplink communication can only be sent in response to being polled by the AP”
[DCN# 11-24/1535r2] SP: No objection
Moved: Yinan Qi
Seconded: Rui Cao
Result: Approved with unanimous consent

## Slide 17
Motion #15 (SFD; Sep 12, PM2, 2024)
Move to include following content to sub-clause 4 of TGbp SFD: “11bp defines at least one mode of MAC/PHY that supports close-range mono-static backscattering communication in 2.4 GHz. 11bp defines at least one mode of MAC/PHY that supports bi-static backscattering communication in 2.4 GHz.” ” [DCN# 11-24/0798r1, 11-24/1215r1]
Moved: Rui Cao Seconded: Bin Qian
Result: Approved with unanimous consent

## Slide 18
Motion #16 (SFD; Nov 14, AM1, 2024)
Move to include the following content to sub-clause 4 of SFD:
The AMP Downlink PPDU in 2.4 GHz shall support the following data rates:
  1 Mb/s (for non-Backscatter STAs only)
  250 kb/s
[Reference DCN# 11-24/1793r1]
Moved: Steve Shellhammer Seconded: Rui Cao
Result: 31Y/2N/8A, passed

## Slide 19
Motion #17 (FRD; Nov 14, AM1, 2024)
Move to include the following topologies for energizer in FRD?
  Topology 1: Energizer is physically integrated with the AP.
  Topology 2: Energizer is connected to the AP with wired connection.
  Topology 3: Energizer is connected to the AP with wireless connection.
    The details of the wireless connection are TBD
[Reference: 11-24/1781r2]
Moved: Yinan Qi Seconded: Weijie Xu
Result: Approved with unanimous consent

## Slide 20
Motion #18 (SFD; Nov 14, AM1, 2024)
Move to include the following text to the 11bp SFD:
  The AMP-Sync field in AMP Downlink PPDU in 2.4 GHz is defined with chip duration of 2us for backscattering case.
[Reference contribution: 11-24/1797r0]
Moved: Rui Cao Seconded: Bin Qian
Result: Approved with unanimous consent

## Slide 21
Motion #19 (SFD; Nov 14, AM1, 2024)
Move to include the following text to the 11bp SFD:
  11bp defines Manchester encoding for the data portion of UL transmission in 2.4 GHz, including both backscattering and active transmission.
[Reference contribution: 11-24/1798r0]
Moved: Rui Cao Seconded: Weijie Xu
Result: Approve with unanimous consent

## Slide 22
Motion #20 (SFD; Nov 14, AM1, 2024)
Move to add the following content to sub-clause 4 of SFD:
  When performing transmission, the maximum clock offset is ± 10^3 ppm for AMP Non-AP STA supporting active transmission.
[Reference: 11-24/1475r3, 11-24/1799r0]
Moved: Weijie Xu Seconded: Amichai Sanderovich
Result: Approved with unanimous consent

## Slide 23
Motion #21 (SFD; Nov 14, AM1, 2024)
Move to add the following content to sub-clause 4 of SFD:
  11bp will define On-Off Keying (OOK) modulation for AMP-Sync field and the AMP-Data field in an AMP Uplink PPDU for Active Transmission
[Reference: 11-24/1780r1, 11-24/1237r0]
Moved: Weijie Xu Seconded: Yaron BenArie
Result: Approved with unanimous consent

## Slide 24
Motion #22 (SFD; Jan 16, PM1, 2025)
Move to add the following content to the SFD:
  11bp defines an “AMP AP STA”
    AMP non AP STAs may or may not communicate with AMP AP STA without association
    The AMP AP STA may or may not provide access to the DS for the AMP non AP STA
  Note: the AMP AP STA may be part of an access point
[Reference contribution: 11-25/0055r1, 11-24/1537r2]
Moved: Solomon Trainin; Seconded: Weijie Xu
Result: Approved with unanimous consent

## Slide 25
Motion #23 (SFD; Jan 16, PM1, 2025)
Move to add the following content to the SFD:
  11bp defines communication between AMP non AP STA and AMP AP STA through 11bp frames
[Reference contribution: 11-25/0055r1, 11-24/1537r2]
Moved: Solomon Trainin; Seconded: Weijie Xu
Result: Approved with unanimous consent

## Slide 26
Motion #24 (SFD; Jan 16, PM1, 2025)
Move to add the following content to the SFD:
  11bp defines a mechanism to allow an AP to solicit AMP uplink PPDU(s) from one or more 802.11bp clients.
[Reference contribution: 11-24/2113r0]
Moved: Sanket Kalamkar; Seconded: Rojan Chitrakar
Result: Approved with unanimous consent

## Slide 27
Motion #25 (SFD; Jan 16, PM1, 2025)
Move to add the following content to the SFD:
  11bp defines a Time Division Multiple Access (TDMA) mechanism for multiple 802.11bp clients to transmit AMP uplink PPDU(s).
[Reference contribution: 11-24/2113r0]
Moved: Sanket Kalamkar; Seconded:
Result: [deferred]

## Slide 28
Motion #26 (SFD; Jan 16, PM1, 2025)
Move to add the following content to the SFD:
  11bp defines a mechanism to support secure communications for 802.11bp clients.
[Reference contribution: 11-24/2112r0]
Moved: Sanket Kalamkar; Seconded: Solomon Trainin
Result: Approved with unanimous consent

## Slide 29
Motion #27 (SFD; Jan 16, PM1, 2025)
Move to add the following content to the SFD:
  11bp defines one mode of backscattering without carrier center frequency shift.
[Reference contribution: 11-25/0058r1]
Moved: Rui Cao; Seconded: Bin Qian
Result: Approved with unanimous consent

## Slide 30
Motion #28 (SFD; Jan 16, PM1, 2025)
Move to add the following content to the SFD:
  The preamble of an AMP DL PPDU includes L-STF, L-LTF, L-SIG, RL-SIG, and U-SIGs for AMP enabled non-AP STA and active TX non-AP AMP STA in 2.4 GHz.
[Reference contribution: 11-24/1859r0]
Moved: Youwei Chen; Seconded: Sebastian Max
Result: Approved with unanimous consent

## Slide 31
Motion #29 (SFD; Jan 16, PM1, 2025)
Move to add the following content to the SFD:
  Backscatter non-AP AMP STA: A non-AP AMP STA that is capable of receiving only AMP Downlink PPDUs and supports uplink backscatter transmission.
  Active Tx non-AP AMP STA: A non-AP AMP STA that is capable of receiving only AMP Downlink PPDUs and supports active transmission of AMP Uplink PPDUs.
  AMP Enabled non-AP STA: A non-AP STA (e.g. non-HT, HT or HE STA) that is also capable of receiving AMP Downlink PPDUs
[Reference contribution: 11-24/1846r2]
Moved: Rojan Chitrakar; Seconded: Sebastian Max
Result: Approved with unanimous consent

## Slide 32
Motion #30 (SFD; Jan 16, PM1, 2025)
Move to add the following content to the SFD:
  The (3dB) bandwidth of the AMP DL PPDU in 2.4 GHz is at least 10 MHz for backscattering communication. The transmit spectrum mask is TBD.
[Reference contribution: 11-25/0050r1, 11-25/0051r1]
Moved: Panpan Li; Seconded: Sebastian Max
Result: Approved with unanimous consent

## Slide 33
Motion #31 (SFD; Jan 16, PM1, 2025)
Move to add the following content to the SFD:
  11bp defines the following data rates for AMP uplink transmissions at 2.4GHz
    250kbps and 1Mbps for both backscatter and non-backscatter uplink transmission;
    4Mbps for non-backscatter uplink transmission only.
      Mandatory or optional is TBD
[Reference contribution: 11-25/0033r0, 11-25/0027r0]
Moved: Yinan Qi; Seconded: Sebastian Max
Result: Approved with unanimous consent

## Slide 34
Motion #32 (SFD; Jan 16, PM1, 2025)
Move to add the following content to the SFD:
  If an AMP device is able to support TSF, it can monitor AMP DL Frame in a duty-cycle manner..
[Reference contribution: 11-25/0032r0, 11-25/0039r0]
Moved: Yinan Qi; Seconded: Amichai Sanderovich
Result: Approved with unanimous consent

## Slide 35
Motion #33 (SFD; Jan 16, PM1, 2025)
Move to add the following content to the SFD:
  IEEE 802.11bp defines at least one AMP-Sync in the AMP Downlink PPDU in 2.4 GHz for backscatter communication, and at least one AMP-Sync in the AMP Downlink PPDU in 2.4 GHz for non-backscatter communication. The AMP-Sync is independent of the integrated and non-integrated deployment.
[Reference contribution: 11-25/0047r0]
Moved: Bin Qian; Seconded: Yinan Qi
Result: Approved with unanimous consent

## Slide 36
Motion #34 (SFD; Jan 16, PM1, 2025)
Move to add the following content to the SFD:
  IEEE 802.11bp defines an AMP Energizer that contains an Energizing Function, which is capable of transmitting WPT waveform and/or excitation waveform for backscattering operation. Additionally, the AMP Energizer may contain or be co-located (which one is TBD) with an IEEE 802.11 non-AMP non-AP STA.
  Note: WPT waveform is transmitted over sub1-GHz. Depending on whether the backscattering operation happens in sub1-GHz or 2.4GHz, accordingly the excitation waveform will be transmitted in the same band.
[Reference contribution: 11-24/1767r0, 11-25/0037r0]
Moved: Ian Bajaj; Seconded: Weijie Xu
Result: Approved with unanimous consent

## Slide 37
Motion #35 (SFD; Jan 16, PM1, 2025)
Move to add the following content to the SFD:
  IEEE 802.11bp defines a mechanism that allows control information to be sent by AMP AP STA to the AMP Energizer. The control information is TBD.
[Reference contribution: 11-24/1208r1, 11-24/1769r0, 11-25/0037r0]
Moved: Ian Bajaj; Seconded: Yinan Qi
Result: Approved with unanimous consent

## Slide 38
Motion #36 (SFD; Jan 16, PM1, 2025)
Move to add the following content to the SFD:
  IEEE 802.11bp defines a mechanism that allows an AMP non-AP STA to report its energy harvesting and power related information to AMP AP STA. The parameters that are included in the report and how to report such information is TBD.
[Reference contribution: 11-24/1208r1, 11-24/1381r0, 11-24/1524r2, 11-24/1539r0, 11-24/1561r2, 11-24/1769r0, 11-24/1781r2, 11-24/1939r0]
Moved: Ian Bajaj; Seconded: Sebastian Max
Result: Approved with unanimous consent

## Slide 39
Motion #37 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
  The AMP-Data field of AMP DL PPDU for backscatter communication uses Manchester encoding.
[Reference contribution: 11-25/0339r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 40
Motion #38 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
  The AMP-Sync field and the AMP-Data field of AMP UL PPDU for backscatter communication use OOK modulation.
[Reference contribution: 11-25/0339r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 41
Motion #39 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
  The carrier waveform for AMP Downlink PPDU is constructed by repeating one predefined base waveform of TBD micro-second, and additional pseudo-random phase is applied to each base waveform
  The base waveform definition is TBD
  Note:
    The SYNC and Data fields are OOK modulated on the carrier waveform
    The Excitation field is not OOK modulated.
[Reference contribution: 11-25/0305, 11-25/0325, 11-25/0339, 11-25/0369]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 42
Motion #40 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
  For DL PPDU and UL PPDU for backscattering:
    For AMP Manchester encoded OOK of rate 250kbps, each data bit is encoded based on the chip duration of 2us.
    For AMP Manchester encoded OOK of rate 1Mbps, each data bit is encoded based on the chip duration of 0.5us.
[Reference contribution: 11-25/0305, 11-25/0325, 11-25/0339, 11-25/0369]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 43
Motion #41 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
  For DL PPDU and UL PPDU for backscattering:
    For AMP Manchester encoded OOK, data bit 1 is encoded as chip bits “01” and data bit 0 is encoded as chip bits“10”
    Note: same definition as WUR HDR definition.
[Reference contribution: 11-25/0305, 11-25/0325, 11-25/0339, 11-25/0369]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 44
Motion #42 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
  11bp shall specify, in 2.4 GHz, an AMP UL PPDU for backscatter non-AP AMP STAs that contains an AMP-Sync field and an AMP-Data field.
  Note: This AMP UL PPDU is within one excitation field of an AMP DL PPDU.
[Reference contribution: 11-25/0316r0, 11-25/0027r1, 11-24/1780r2]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 45
Motion #43 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
  The PHY parameters (at least data rate) for AMP UL transmission are indicated by the AMP AP.
  Other PHY parameters TBD.
[Reference contribution: 11-25/0316r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 46
Motion #44 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD security sub-clause:
  IEEE 802.11bp will specify secure data communication methods that do not require maintaining security associations.
  Note:
    The methods are based on existing 802.11 security protocols.
    The security for backscattering AMP devices are TBD.
    The details are TBD.
[Reference contribution: 11-24/0178, 11-24/0526, 11-24/0871, 11-24/1998, 11-24/1242]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 47
Motion #45 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
  802.11bp to define a slot-based procedure to enable one or more clients to access the medium to send uplink AMP PPDU(s).
[Reference contribution: 11-24/2113]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 48
Motion #46 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
802.11bp defines an AMP Trigger frame that an AP transmits to solicit UL AMP PPDU(s) from one or more 802.11bp clients and may carry the following content?
  Transmitter ID
  Receiver ID(s)
  FCS
  Other parameters TBD.
[Reference contribution: 11-24/2112, 11-25/398]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 49
Motion #47 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
  An 802.11bp client may use the receive time of the AMP Trigger frame, which solicits UL AMP PPDUs from the client, to determine the timing for transmitting UL AMP PPDUs in the same TXOP?
  The definition of receive time is TBD.
[Reference contribution: 11-25/0353]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 50
Motion #48 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
when the AP solicits UL AMP PPDUs from 802.11bp clients using a slot-based procedure, the AMP Trigger frame shall carry the following parameters?
  Number of slots for UL PPDU transmissions in that TXOP
  Other parameters TBD.
[Reference contribution: 11-24/2113, 11-25/0353]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 51
Motion #49 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
802.11bp defines an AMP Ack frame that an AMP AP transmits to acknowledge the received UL AMP frame(s).
[Reference contribution: 11-25/0398]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 52
Motion #50 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
802.11bp supports a time-slot based random access mechanism for Active Tx non-AP AMP STAs:
  AMP AP transmits an AMP frame that indicates one or more time-slots.
  Further details (e.g., frame formats, how a STA chooses a random access time-slot etc.) are TBD
[Reference contribution: 25/334r1, 25/0046r0, 11-24/1549r0, 11-24/1212r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 53
Motion #51 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
802.11bp supports a time-slot based scheduled access mechanism for Active Tx non-AP AMP STAs:
  AMP AP transmits an AMP frame to assign one or more transmission time-slots.
  Further details (e.g., frame formats, how the time-slots are assigned etc.) are TBD
[Reference contribution: 25/334r1, 25/0046r0, 11-24/1549r0, 11-24/1212r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 54
Motion #52 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
11bp supports a mode of operation in which a sub-set of the logical interface of the UHF RFID Standard is used for backscattering communication.
  Applicable UHF commands are carried in 802.11bp frames.
  Applicable to both mono-static & bi-static backscattering.
  The sub-set of the logical interface to be reused is TBD.
  NOTE – The logical interface of the UHF RFID Standard is defined by the EPC® Radio-Frequency Identity Generation-2 UHF RFID Standard
[Reference contribution: 25/334r1, 25/0046r0, 11-24/1549r0, 11-24/1212r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 55
Motion #53 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
Control information that is sent from the AMP AP to the AMP Energizer relating to the WPT waveform may include at least one or more of the following: Start Time, Duration, Interval, Transmit Power, and frequency related parameters.
The frequency related parameters may include central frequency information, bandwidth information, etc.
Note: Interval refers to a repetition of the WPT waveform
[Reference contribution: 25/334r1, 25/0046r0, 11-24/1549r0, 11-24/12 11-24/1208r1, 11-24/1524r2, 11-24/1769r0, 11-25/0037r0, 11-25/0318r0, 11-25/0336r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 56
Motion #54 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
WPT signals from two or more transmitters in S1GHz are allowed to occupy the same channel simultaneously
[Reference contribution: 11-25/0320r1, 11-25/0029r1]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 57
Motion #55 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
Energizer should report its WPT and excitation related capability to the AMP AP. The parameters to be reported are TBD.
[Reference contribution: 11-25/0318r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 58
Motion #56 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
AMP trigger frame may indicate parameters for a slot-based procedure of time slots to AMP non-AP STA(s).
  The exact parameters are TBD.
[Reference contribution: 11-25/0340r0, 11-24/1774r1]
Moved: Weijie Xu Second: Rui Cao
Result: Approved with unanimous consent
Note: this is the approved motion #2 in 11-25/0228r7