## Slide 1
IEEE 802.11 TGbp Motion Deck
Date: 2024-07-18
Author:

## Slide 2
This document records TGbp motions planned and conducted during TGbp meetings.
TGbp motions during teleconferences should be announced at least 10 days before the teleconference running those motions.
TGbp motions on leadership confirmation and approval of meeting minutes are not included in this deck.
Note 1 - 802.11 WG Operation Manual requests “Teleconferences are a means to prepare input for sessions provided that the teleconference date, time, agenda, and arrangements are announced on the TG email reflector at least 10 calendar days prior to the teleconference date"
Note 2 - Teleconferences are bound by the conditions stipulated by the documentation below. Please review them and bring up any questions/concerns you may have before proceeding with the teleconference:
Abstract

## Slide 3
Motion #1 (May 16, PM1, 2024)
Approve the TGbp initial timeline plan as illustrated in slide 33 as in 11-24/0666r5.
Note, the timeline plan is subject to change according to the 11bp developing progress.
Result: Approved with unanimous consent

## Slide 4
Motion #2 (Jul 18, PM1, 2024)
Move to approve the TGbp selection procedure as defined in 11-24/0897r1
Moved: Bo Sun
Seconded: Vytas Kezys
Result: Approved with unanimous consent

## Slide 5
Motion #3 (Jul 18, PM1, 2024)
Move to approve the baseline of TGbp Function Requirements doc as included in 11-24/1307r1, for future development based on consensus
Moved: Bin Qian
Seconded: Bin Tian
Result: Approved with unanimous consent

## Slide 6
Motion #4 (Sep 9, PM1, 2024)
Move to approve the baseline of TGbp Specification Framework Document (SFD) as included in 11-24/1613r0, for future development based on consensus
Moved: Yinan Qi
Seconded: Sebastian Max
Result: Approved with unanimous consent

## Slide 7
Motion #5 (FRD; Sep 12, PM2, 2024)
Move to include following content to sub-clause 2.1 of TGbp FRD:
“11bp defines at least one mode of MAC/PHY that supports close-range mono-static backscattering communication in 2.4 GHz.”
[DCN# 11-24/0798r1] SP: 37Y/6N/23A
Moved: Rui Cao
Seconded: Lei Huang
Result: Approved with unanimous consent

## Slide 8
Motion #6 (FRD; Sep 12, PM2, 2024)
Move to include following content to sub-clause 2.1 of TGbp FRD:
“11bp defines at least one mode of MAC/PHY that supports bi-static backscattering communication in 2.4 GHz.”
[DCN# 11-24/1215r1] SP:No objection
Moved: Bin Qian
Seconded: Hongyuan Zhang
Result: Approved with unanimous consent

## Slide 9
Motion #7 (SFD; Sep 12, PM2, 2024)
Move to include following content to TGbp SFD:
“11bp supports a mode to enable AMP devices to operate in legacy WLAN network by defining AMP DL and required control/signaling.”
[DCN# 11-24/1263r0] SP: 33Y/2N/6A
Moved: Pooria Pakrooh
Seconded: Bin Tian
Result: Approved with unanimous consent

## Slide 10
Motion #8 (SFD; Sep 12, PM2, 2024)
Move to include following content to sub-clause 4 of TGbp SFD:
  “IEEE 802.11bp will specify, in 2.4 GHz, an AMP Downlink PPDU containing at least an 802.11 preamble field, an AMP-Sync field and an AMP-Data field. Inclusion of an AMP-SIG field is TBD.
    The details of the 802.11 preamble field are TBD.
    Additionally, for transmission to backscatter STAs there will be one or more Excitation fields
    Additionally, for transmission to backscatter STAs there may be more than one AMP-Data field
      Additionally, AMP-Sync and AMP-SIG field may precede each AMP-Data field
    Name of this Downlink PPDU is TBD.
[DCN# 11-24/1345r2] SP: No objection
Moved: Steve Shellhammer
Seconded: Christian Berger
Result: Approved with unanimous consent

## Slide 11
Motion #9 (SFD; Sep 12, PM2, 2024)
Move to include following content to sub-clause 4 of TGbp SFD:
“The AMP Downlink PPDU AMP-Sync field and the AMP-Data field will use On-Off Keying (OOK) modulation.”
[DCN# 11-24/1345r2] SP: no objection
Moved: Steve Shellhammer
Seconded: Weijie Xu
Result: Approve with unanimous consent

## Slide 12
Motion #10 (SFD; Sep 12, PM2, 2024)
Move to include following content to sub-clause 4 of TGbp SFD:
“The AMP Downlink PPDU AMP-Data field will use Manchester encoding for non-backscatter operation.
  For the Backscatter case, the AMP-Data field encoding scheme is TBD.
”
[DCN# 11-24/1345r2] SP: No objection
Moved: Steve Shellhammer
Seconded: Bin Qian
Result: Approved with unanimous consent

## Slide 13
Motion #11 (SFD; Sep 12, PM2, 2024)
Move to include following content to sub-clause 4 of TGbp SFD:
“IEEE 802.11bp shall specify, in 2.4 GHz, an AMP uplink PPDU for AMP STA supporting active transmission that contains an AMP-Sync field and AMP-Data field. Inclusion of an AMP-SIG field in the AMP uplink PPDU is TBD.
  The bandwidth of the AMP uplink PPDU is less than 20 MHz”
[DCN# 11-24/1496] SP: no objection
Moved: Bin Qian
Seconded: Weijie Xu
Result: Approved with unanimous consent

## Slide 14
Motion #12 (FRD; Sep 12, PM2, 2024)
Move to include following content to TGbp FRD:
“802.11bp defines AMP Timing Synchronization Function (AMP TSF)”
[DCN# 11-24/1475r3] SP: 31Y/7N/32A
Moved: Weijie Xu
Seconded: Yinan Qi
Result: Approved with unanimous consent

## Slide 15
Motion #13 (SFD; Sep 12, PM2, 2024)
Move to include following content to TGbp SFD:
  “If AMP device is able to support AMP TSF, the maximum timing offset is ± 10^4 ppm”
[DCN# 11-24/1475r3] SP: no objection
Moved: Weijie Xu
Seconded: Lei Huang
Result: Approved with unanimous consent

## Slide 16
Motion #14 (SFD; Sep 12, PM2, 2024)
Move to include following content to TGbp SFD:
“11bp defines at least one mode of MAC/PHY that allows an AMP-only device with active uplink communication in 2.4GHz subject to the following requirements:
  clock accuracy requirement is relaxed compared to legacy 802.11 devices;
  the active uplink communication can only be sent in response to being polled by the AP”
[DCN# 11-24/1535r2] SP: No objection
Moved: Yinan Qi
Seconded: Rui Cao
Result: Approved with unanimous consent

## Slide 17
Motion #15 (SFD; Sep 12, PM2, 2024)
Move to include following content to sub-clause 4 of TGbp SFD: “11bp defines at least one mode of MAC/PHY that supports close-range mono-static backscattering communication in 2.4 GHz. 11bp defines at least one mode of MAC/PHY that supports bi-static backscattering communication in 2.4 GHz.” ” [DCN# 11-24/0798r1, 11-24/1215r1]
Moved: Rui Cao Seconded: Bin Qian
Result: Approved with unanimous consent

## Slide 18
Motion #16 (SFD; Nov 14, AM1, 2024)
Move to include the following content to sub-clause 4 of SFD:
The AMP Downlink PPDU in 2.4 GHz shall support the following data rates:
  1 Mb/s (for non-Backscatter STAs only)
  250 kb/s
[Reference DCN# 11-24/1793r1]
Moved: Steve Shellhammer Seconded: Rui Cao
Result: 31Y/2N/8A, passed

## Slide 19
Motion #17 (FRD; Nov 14, AM1, 2024)
Move to include the following topologies for energizer in FRD?
  Topology 1: Energizer is physically integrated with the AP.
  Topology 2: Energizer is connected to the AP with wired connection.
  Topology 3: Energizer is connected to the AP with wireless connection.
    The details of the wireless connection are TBD
[Reference: 11-24/1781r2]
Moved: Yinan Qi Seconded: Weijie Xu
Result: Approved with unanimous consent

## Slide 20
Motion #18 (SFD; Nov 14, AM1, 2024)
Move to include the following text to the 11bp SFD:
  The AMP-Sync field in AMP Downlink PPDU in 2.4 GHz is defined with chip duration of 2us for backscattering case.
[Reference contribution: 11-24/1797r0]
Moved: Rui Cao Seconded: Bin Qian
Result: Approved with unanimous consent

## Slide 21
Motion #19 (SFD; Nov 14, AM1, 2024)
Move to include the following text to the 11bp SFD:
  11bp defines Manchester encoding for the data portion of UL transmission in 2.4 GHz, including both backscattering and active transmission.
[Reference contribution: 11-24/1798r0]
Moved: Rui Cao Seconded: Weijie Xu
Result: Approve with unanimous consent

## Slide 22
Motion #20 (SFD; Nov 14, AM1, 2024)
Move to add the following content to sub-clause 4 of SFD:
  When performing transmission, the maximum clock offset is ± 10^3 ppm for AMP Non-AP STA supporting active transmission.
[Reference: 11-24/1475r3, 11-24/1799r0]
Moved: Weijie Xu Seconded: Amichai Sanderovich
Result: Approved with unanimous consent

## Slide 23
Motion #21 (SFD; Nov 14, AM1, 2024)
Move to add the following content to sub-clause 4 of SFD:
  11bp will define On-Off Keying (OOK) modulation for AMP-Sync field and the AMP-Data field in an AMP Uplink PPDU for Active Transmission
[Reference: 11-24/1780r1, 11-24/1237r0]
Moved: Weijie Xu Seconded: Yaron BenArie
Result: Approved with unanimous consent

## Slide 24
Motion #22 (SFD; Jan 16, PM1, 2025)
Move to add the following content to the SFD:
  11bp defines an “AMP AP STA”
    AMP non AP STAs may or may not communicate with AMP AP STA without association
    The AMP AP STA may or may not provide access to the DS for the AMP non AP STA
  Note: the AMP AP STA may be part of an access point
[Reference contribution: 11-25/0055r1, 11-24/1537r2]
Moved: Solomon Trainin; Seconded: Weijie Xu
Result: Approved with unanimous consent

## Slide 25
Motion #23 (SFD; Jan 16, PM1, 2025)
Move to add the following content to the SFD:
  11bp defines communication between AMP non AP STA and AMP AP STA through 11bp frames
[Reference contribution: 11-25/0055r1, 11-24/1537r2]
Moved: Solomon Trainin; Seconded: Weijie Xu
Result: Approved with unanimous consent

## Slide 26
Motion #24 (SFD; Jan 16, PM1, 2025)
Move to add the following content to the SFD:
  11bp defines a mechanism to allow an AP to solicit AMP uplink PPDU(s) from one or more 802.11bp clients.
[Reference contribution: 11-24/2113r0]
Moved: Sanket Kalamkar; Seconded: Rojan Chitrakar
Result: Approved with unanimous consent

## Slide 27
Motion #25 (SFD; Jan 16, PM1, 2025; deferred)
Move to add the following content to the SFD:
  11bp defines a Time Division Multiple Access (TDMA) mechanism for multiple 802.11bp clients to transmit AMP uplink PPDU(s).
[Reference contribution: 11-24/2113r0]
Moved: Sanket Kalamkar; Seconded:
Result:

## Slide 28
Motion #26 (SFD; Jan 16, PM1, 2025)
Move to add the following content to the SFD:
  11bp defines a mechanism to support secure communications for 802.11bp clients.
[Reference contribution: 11-24/2112r0]
Moved: Sanket Kalamkar; Seconded: Solomon Trainin
Result: Approved with unanimous consent

## Slide 29
Motion #27 (SFD; Jan 16, PM1, 2025)
Move to add the following content to the SFD:
  11bp defines one mode of backscattering without carrier center frequency shift.
[Reference contribution: 11-25/0058r1]
Moved: Rui Cao; Seconded: Bin Qian
Result: Approved with unanimous consent

## Slide 30
Motion #28 (SFD; Jan 16, PM1, 2025)
Move to add the following content to the SFD:
  The preamble of an AMP DL PPDU includes L-STF, L-LTF, L-SIG, RL-SIG, and U-SIGs for AMP enabled non-AP STA and active TX non-AP AMP STA in 2.4 GHz.
[Reference contribution: 11-24/1859r0]
Moved: Youwei Chen; Seconded: Sebastian Max
Result: Approved with unanimous consent

## Slide 31
Motion #29 (SFD; Jan 16, PM1, 2025)
Move to add the following content to the SFD:
  Backscatter non-AP AMP STA: A non-AP AMP STA that is capable of receiving only AMP Downlink PPDUs and supports uplink backscatter transmission.
  Active Tx non-AP AMP STA: A non-AP AMP STA that is capable of receiving only AMP Downlink PPDUs and supports active transmission of AMP Uplink PPDUs.
  AMP Enabled non-AP STA: A non-AP STA (e.g. non-HT, HT or HE STA) that is also capable of receiving AMP Downlink PPDUs
[Reference contribution: 11-24/1846r2]
Moved: Rojan Chitrakar; Seconded: Sebastian Max
Result: Approved with unanimous consent

## Slide 32
Motion #30 (SFD; Jan 16, PM1, 2025)
Move to add the following content to the SFD:
  The (3dB) bandwidth of the AMP DL PPDU in 2.4 GHz is at least 10 MHz for backscattering communication. The transmit spectrum mask is TBD.
[Reference contribution: 11-25/0050r1, 11-25/0051r1]
Moved: Panpan Li; Seconded: Sebastian Max
Result: Approved with unanimous consent

## Slide 33
Motion #31 (SFD; Jan 16, PM1, 2025)
Move to add the following content to the SFD:
  11bp defines the following data rates for AMP uplink transmissions at 2.4GHz
    250kbps and 1Mbps for both backscatter and non-backscatter uplink transmission;
    4Mbps for non-backscatter uplink transmission only.
      Mandatory or optional is TBD
[Reference contribution: 11-25/0033r0, 11-25/0027r0]
Moved: Yinan Qi; Seconded: Sebastian Max
Result: Approved with unanimous consent

## Slide 34
Motion #32 (SFD; Jan 16, PM1, 2025)
Move to add the following content to the SFD:
  If an AMP device is able to support TSF, it can monitor AMP DL Frame in a duty-cycle manner..
[Reference contribution: 11-25/0032r0, 11-25/0039r0]
Moved: Yinan Qi; Seconded: Amichai Sanderovich
Result: Approved with unanimous consent

## Slide 35
Motion #33 (SFD; Jan 16, PM1, 2025)
Move to add the following content to the SFD:
  IEEE 802.11bp defines at least one AMP-Sync in the AMP Downlink PPDU in 2.4 GHz for backscatter communication, and at least one AMP-Sync in the AMP Downlink PPDU in 2.4 GHz for non-backscatter communication. The AMP-Sync is independent of the integrated and non-integrated deployment.
[Reference contribution: 11-25/0047r0]
Moved: Bin Qian; Seconded: Yinan Qi
Result: Approved with unanimous consent

## Slide 36
Motion #34 (SFD; Jan 16, PM1, 2025)
Move to add the following content to the SFD:
  IEEE 802.11bp defines an AMP Energizer that contains an Energizing Function, which is capable of transmitting WPT waveform and/or excitation waveform for backscattering operation. Additionally, the AMP Energizer may contain or be co-located (which one is TBD) with an IEEE 802.11 non-AMP non-AP STA.
  Note: WPT waveform is transmitted over sub1-GHz. Depending on whether the backscattering operation happens in sub1-GHz or 2.4GHz, accordingly the excitation waveform will be transmitted in the same band.
[Reference contribution: 11-24/1767r0, 11-25/0037r0]
Moved: Ian Bajaj; Seconded: Weijie Xu
Result: Approved with unanimous consent

## Slide 37
Motion #35 (SFD; Jan 16, PM1, 2025)
Move to add the following content to the SFD:
  IEEE 802.11bp defines a mechanism that allows control information to be sent by AMP AP STA to the AMP Energizer. The control information is TBD.
[Reference contribution: 11-24/1208r1, 11-24/1769r0, 11-25/0037r0]
Moved: Ian Bajaj; Seconded: Yinan Qi
Result: Approved with unanimous consent

## Slide 38
Motion #36 (SFD; Jan 16, PM1, 2025)
Move to add the following content to the SFD:
  IEEE 802.11bp defines a mechanism that allows an AMP non-AP STA to report its energy harvesting and power related information to AMP AP STA. The parameters that are included in the report and how to report such information is TBD.
[Reference contribution: 11-24/1208r1, 11-24/1381r0, 11-24/1524r2, 11-24/1539r0, 11-24/1561r2, 11-24/1769r0, 11-24/1781r2, 11-24/1939r0]
Moved: Ian Bajaj; Seconded: Sebastian Max
Result: Approved with unanimous consent

## Slide 39
Motion #37 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
  The AMP-Data field of AMP DL PPDU for backscatter communication uses Manchester encoding.
[Reference contribution: 11-25/0339r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 40
Motion #38 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
  The AMP-Sync field and the AMP-Data field of AMP UL PPDU for backscatter communication use OOK modulation.
[Reference contribution: 11-25/0339r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 41
Motion #39 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
  The carrier waveform for AMP Downlink PPDU is constructed by repeating one predefined base waveform of TBD micro-second, and additional pseudo-random phase is applied to each base waveform
  The base waveform definition is TBD
  Note:
    The SYNC and Data fields are OOK modulated on the carrier waveform
    The Excitation field is not OOK modulated.
[Reference contribution: 11-25/0305, 11-25/0325, 11-25/0339, 11-25/0369]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 42
Motion #40 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
  For DL PPDU and UL PPDU for backscattering:
    For AMP Manchester encoded OOK of rate 250kbps, each data bit is encoded based on the chip duration of 2us.
    For AMP Manchester encoded OOK of rate 1Mbps, each data bit is encoded based on the chip duration of 0.5us.
[Reference contribution: 11-25/0305, 11-25/0325, 11-25/0339, 11-25/0369]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 43
Motion #41 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
  For DL PPDU and UL PPDU for backscattering:
    For AMP Manchester encoded OOK, data bit 1 is encoded as chip bits “01” and data bit 0 is encoded as chip bits“10”
    Note: same definition as WUR HDR definition.
[Reference contribution: 11-25/0305, 11-25/0325, 11-25/0339, 11-25/0369]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 44
Motion #42 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
  11bp shall specify, in 2.4 GHz, an AMP UL PPDU for backscatter non-AP AMP STAs that contains an AMP-Sync field and an AMP-Data field.
  Note: This AMP UL PPDU is within one excitation field of an AMP DL PPDU.
[Reference contribution: 11-25/0316r0, 11-25/0027r1, 11-24/1780r2]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 45
Motion #43 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
  The PHY parameters (at least data rate) for AMP UL transmission are indicated by the AMP AP.
  Other PHY parameters TBD.
[Reference contribution: 11-25/0316r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 46
Motion #44 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD security sub-clause:
  IEEE 802.11bp will specify secure data communication methods that do not require maintaining security associations.
  Note:
    The methods are based on existing 802.11 security protocols.
    The security for backscattering AMP devices are TBD.
    The details are TBD.
[Reference contribution: 11-24/0178, 11-24/0526, 11-24/0871, 11-24/1998, 11-24/1242]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 47
Motion #45 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
  802.11bp to define a slot-based procedure to enable one or more clients to access the medium to send uplink AMP PPDU(s).
[Reference contribution: 11-24/2113]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 48
Motion #46 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
802.11bp defines an AMP Trigger frame that an AP transmits to solicit UL AMP PPDU(s) from one or more 802.11bp clients and may carry the following content?
  Transmitter ID
  Receiver ID(s)
  FCS
  Other parameters TBD.
[Reference contribution: 11-24/2112, 11-25/398]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 49
Motion #47 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
  An 802.11bp client may use the receive time of the AMP Trigger frame, which solicits UL AMP PPDUs from the client, to determine the timing for transmitting UL AMP PPDUs in the same TXOP?
  The definition of receive time is TBD.
[Reference contribution: 11-25/0353]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 50
Motion #48 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
when the AP solicits UL AMP PPDUs from 802.11bp clients using a slot-based procedure, the AMP Trigger frame shall carry the following parameters?
  Number of slots for UL PPDU transmissions in that TXOP
  Other parameters TBD.
[Reference contribution: 11-24/2113, 11-25/0353]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 51
Motion #49 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
802.11bp defines an AMP Ack frame that an AMP AP transmits to acknowledge the received UL AMP frame(s).
[Reference contribution: 11-25/0398]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 52
Motion #50 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
802.11bp supports a time-slot based random access mechanism for Active Tx non-AP AMP STAs:
  AMP AP transmits an AMP frame that indicates one or more time-slots.
  Further details (e.g., frame formats, how a STA chooses a random access time-slot etc.) are TBD
[Reference contribution: 25/334r1, 25/0046r0, 11-24/1549r0, 11-24/1212r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 53
Motion #51 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
802.11bp supports a time-slot based scheduled access mechanism for Active Tx non-AP AMP STAs:
  AMP AP transmits an AMP frame to assign one or more transmission time-slots.
  Further details (e.g., frame formats, how the time-slots are assigned etc.) are TBD
[Reference contribution: 25/334r1, 25/0046r0, 11-24/1549r0, 11-24/1212r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 54
Motion #52 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
11bp supports a mode of operation in which a sub-set of the logical interface of the UHF RFID Standard is used for backscattering communication.
  Applicable UHF commands are carried in 802.11bp frames.
  Applicable to both mono-static & bi-static backscattering.
  The sub-set of the logical interface to be reused is TBD.
  NOTE – The logical interface of the UHF RFID Standard is defined by the EPC® Radio-Frequency Identity Generation-2 UHF RFID Standard
[Reference contribution: 25/334r1, 25/0046r0, 11-24/1549r0, 11-24/1212r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 55
Motion #53 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
Control information that is sent from the AMP AP to the AMP Energizer relating to the WPT waveform may include at least one or more of the following: Start Time, Duration, Interval, Transmit Power, and frequency related parameters.
The frequency related parameters may include central frequency information, bandwidth information, etc.
Note: Interval refers to a repetition of the WPT waveform
[Reference contribution: 25/334r1, 25/0046r0, 11-24/1549r0, 11-24/12 11-24/1208r1, 11-24/1524r2, 11-24/1769r0, 11-25/0037r0, 11-25/0318r0, 11-25/0336r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 56
Motion #54 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
WPT signals from two or more transmitters in S1GHz are allowed to occupy the same channel simultaneously
[Reference contribution: 11-25/0320r1, 11-25/0029r1]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 57
Motion #55 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
Energizer should report its WPT and excitation related capability to the AMP AP. The parameters to be reported are TBD.
[Reference contribution: 11-25/0318r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0228r7

## Slide 58
Motion #56 (SFD; Mar 13, PM1, 2025)
Move to add the following content to the SFD:
AMP trigger frame may indicate parameters for a slot-based procedure of time slots to AMP non-AP STA(s).
  The exact parameters are TBD.
[Reference contribution: 11-25/0340r0, 11-24/1774r1]
Moved: Weijie Xu Second: Rui Cao
Result: Approved with unanimous consent
Note: this is the approved motion #2 in 11-25/0228r7

## Slide 59
Motion #57 (SFD; May 15, PM1, 2025)
Move to add the following content to the SFD:
802.11bp defines an AMP Wake-Up frame, which an AMP AP transmits to AMP-enabled non-AP STA(s) to indicate that the AP intends to exchange non-AMP frames with the non-AP STA?
  The expectation is to reuse WUR frame format for the AMP Wake-Up frame and to carry it in an AMP PPDU
[Reference contribution: 11-25/0779r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0611r7

## Slide 60
Motion #58 (SFD; May 15, PM1, 2025)
Move to add the following content to the SFD:
802.11bp defines an AMP duty cycle operation for an AMP-enabled non-AP STA, which follows the state transition diagram shown in the figure?
  AMP duty cycle operation follows the negotiation procedure defined for WUR in the baseline
[Reference contributions: 11-25/0779r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0611r7

## Slide 61
Motion #59 (SFD; May 15, PM1, 2025)
Move to add the following content to the SFD:
if an AMP-enabled non-AP STA successfully receives an AMP Wake-Up frame from the associated AMP AP, the non-AP STA should transition to the Awake State and transmit a PS-Poll/UL frame to the AP to indicate that it is in the Awake State (PS/Active mode).
[Reference contributions: 11-25/0779r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0611r7

## Slide 62
Motion #60 (SFD; May 15, PM1, 2025)
Move to add the following content to the SFD:
if the non-AP STA transmits a frame with PM = 1 to the associated AP, then the non-AP may transition to the Doze state, and the AMP-enabled non-AP STA shall enter the AMP mode
[Reference contributions: 11-25/0779r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0611r7

## Slide 63
Motion #61 (SFD; May 15, PM1, 2025)
Move to add the following content to the SFD:
802.11bp defines for AMP-enabled non-AP STA:
  AMP temporal key (ATK) to protect individually addressed AMP frames
  AMP integrity group temporal key (AIGTK) to protect group addressed AMP frames
[Reference contributions: 11-25/0779r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0611r7

## Slide 64
Motion #62 (SFD; May 15, PM1, 2025)
Move to add the following content to the SFD:
802.11bp uses the baseline authentication procedure for AMP-enabled non-AP STA to generate AMP temporal key(s) to protect individually and group addressed AMP frames?
[Reference contributions: 11-25/0779r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0611r7

## Slide 65
Motion #63 (SFD; May 15, PM1, 2025)
Move to add the following content to the SFD:
an AMP-enabled non-AP STA and the associated AMP AP use AMP mode setup to exchange AMP capabilities
  AMP mode setup may occur during the association procedure or post-association
[Reference contributions: 11-25/0779r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0611r7

## Slide 66
Motion #64 (SFD; May 15, PM1, 2025)
Move to add the following content to the SFD:
802.11bp defines a mechanism to generate a transient key for an AMP non-AP STA that supports secure communication, where:
  An AMP AP transmits a downlink frame containing an ANonce.
  After receiving the downlink AMP frame from the AMP AP that contains an ANonce, an AMP non-AP STA generates an SNonce.
  The AMP non-AP STA generates a transient key using the ANonce, the SNonce, the Authenticator Address (AA), the Supplicant Address (SA), and a Pairwise Master Key (PMK) between the AP and the client.
  Note—Whether to include backscatter non-AP STAs in this procedure is TBD.
[Reference contributions: 11-24/1998, 11-24/2112, 11-25/0860r0, 11-24/1203r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0611r7

## Slide 67
Motion #65 (SFD; May 15, PM1, 2025)
Move to add the following content to the SFD:
802.11bp defines a mechanism to generate a transient key for an AMP AP that supports secure communication, where:
  In response to the DL AMP frame from the AMP AP that contains an ANonce, the AMP AP receives an UL AMP frame from an AMP non-AP STA that carries the SNonce and a MIC.
    The AMP non-AP STA generates the MIC using the derived transient key at the AMP non-AP STA.
    If the uplink AMP frame is carrying any UL data, the data payload portion of the uplink AMP frame may be encrypted using the transient key generated at the AMP non-AP STA.
  If the MIC is verified:
    The AP uses the ANonce it transmitted in the previous downlink AMP frame, the SNonce, the Authenticator Address (AA), the Supplicant Address (SA), and the PMK to generate the transient key.
    Using the generated transient key, the AMP AP decrypts the UL data payload (if the payload was encrypted).
  Note—Whether to include backscatter non-AP STAs in this procedure is TBD.
[Reference contributions: 11-24/1998, 11-24/2112, 11-25/0860r0, 11-24/1203r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0611r7

## Slide 68
Motion #66 (SFD; May 15, PM1, 2025)
Move to add the following content to the SFD:
the transient key generation at the AP and the AMP client in 802.11bp may occur concurrently with AMP downlink and uplink data communication:
  The downlink AMP frame from the AP carries ANonce along with downlink data from the AP (e.g., AMP trigger).
  The uplink AMP frame from the AMP client carries SNonce and MIC along with the UL data (e.g., UL response to the AMP trigger).
    The UL data may be encrypted using the transient key generated at the AMP non-AP STA.
  Note—Whether to include backscatter non-AP STAs in this procedure is TBD.
[Reference contributions: 11-24/2112, 11-25/0860r0, 11-24/1203r0, 11-24/1998]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0611r7

## Slide 69
Motion #67 (SFD; May 15, PM1, 2025)
Move to add the following content to the SFD:
the transient key generation at the AP and the AMP client in 802.11bp may be performed immediately before AMP downlink and uplink data communication:
  Once the transient key is derived at both the AP and the AMP client, subsequent AMP data communication between the AP and the client can be secured using MIC and/or encryption based on the generated transient key.
  Note—Whether to include backscatter non-AP STAs in this procedure is TBD.
[Reference contributions: 11-25/2112]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0611r7

## Slide 70
Motion #68 (SFD; May 15, PM1, 2025)
Move to add the following content to the SFD:
2.11bp uses short local addresses for AMP non-AP STAs in secure AMP communications.
Note—Whether to include backscatter non-AP STAs in this procedure is TBD
[Reference contributions: 11-25/0263, 11-25/0831]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0611r7

## Slide 71
Motion #69 (SFD; May 15, PM1, 2025)
Move to add the following content to the SFD:
IEEE 802.11bp defines 4 base sequences used for AMP DL/UL SYNC field in 2.4GHz frequency band.
  1 base sequences, S1, for DL non-backscatter SYNC field. S1 and a function of S1, are used for different DL data rate.
  1 sequence, S2, for DL backscatter SYNC field.
  1 base sequence, S3, for UL active transmission SYNC field.
  1 sequence, S4, for UL backscatter SYNC field.
  Detailed SYNC sequence designs are TBD
Besides the above 4 base sequences, the need of additional sequence S5 is TBD if mono-static and bi-static backscattering UL SYNC field design is different
[Reference contributions: 11-25/0795r1]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0611r7

## Slide 72
Motion #70 (SFD; May 15, PM1, 2025)
Move to add the following content to the SFD:
The SYNC, Data field and Excitation field of 11bp DL PPDU use OFDM symbol as base carrier waveform for OOK modulated AMP communication?
[Reference contributions: 11-25/0797, 11-25/0305, 11-25/0325]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0611r7

## Slide 73
Motion #71 (SFD; May 15, PM1, 2025)
Move to add the following content to the SFD:
The base OFDM symbol is defined as 4us OFDM symbol, and generated by performing 64-point IFFT of the predefined sequence and pre-append the last 0.8us waveform as the cyclic prefix?
[Reference contributions: 11-25/0797, 11-25/0305, 11-25/0325]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0611r7

## Slide 74
Motion #72 (SFD; May 15, PM1, 2025)
Move to add the following content to the SFD:
The maximum allowed clock inaccuracy for the backscattering tag using OOK modulation is 100,000 ppm for both receive mode and backscattering transmit mode?
[Reference contributions: 11-25/0798, 11-24/1237]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0611r7

## Slide 75
Motion #73 (SFD; May 15, PM1, 2025)
Move to add the following content to the SFD:
11bp defines at least one mode of MAC/PHY that supports mono-static backscattering communication in sub-1 GHz
[Reference contributions: 11-25/0816]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0611r7

## Slide 76
Motion #74 (SFD; May 15, PM1, 2025)
Move to add the following content to the SFD:
Control information that may be sent from the AMP AP to the AMP Energizer relating to the excitation signal includes one or more of the following: Start Time, Duration, Transmit Power and frequency related parameters.
The frequency related parameters may include central frequency information, etc.
[Reference contributions: 11-25/0037r0, 11-25/0786r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0611r7

## Slide 77
Motion #75 (SFD; May 15, PM1, 2025)
Move to add the following content to the SFD:
IEEE 802.11bp defines an AMP Service Period, that allows an Active Tx non-AP AMP STA to enter doze state after a minimum wake up time since the start of the AMP Service Period, if the Active Tx non-AP AMP STA does not receive any AMP DL PPDU from the AMP AP.
[Reference contributions: 11-25/0039r0, 11-25/0285r1, 11-25/0787r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0611r7

## Slide 78
Motion #76 (SFD; May 15, PM1, 2025)
Move to add the following content to the SFD:
IEEE 802.11bp will specify, in 2.4 GHz, DL synchronization sequence with the same chip duration for all data rates for non-backscatter case.
[Reference contributions: 11-25/0790r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0611r7

## Slide 79
Motion #77 (SFD; May 15, PM1, 2025)
Move to add the following content to the SFD:
For DL PPDU for non backscattering case:
  For AMP Manchester encoded OOK of rate 250kbps, each data bit is encoded based on the chip duration of 2us.
  For AMP Manchester encoded OOK of rate 1Mbps, each data bit is encoded based on the chip duration of 0.5us.
[Reference contributions: 11-25/0790r0, 11-25/0316r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0611r7

## Slide 80
Motion #78 (SFD; May 15, PM1, 2025)
Move to add the following content to the SFD:
For UL PPDU for non backscattering case, for AMP Manchester encoded OOK the chip duration of data portion is different for different data rates. The exact chip duration is TBD.
  4Mbps is TBD.
[Reference contributions: 11-25/0790r0, 11-25/0316r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0611r7

## Slide 81
Motion #79 (SFD; May 15, PM1, 2025)
Move to make the following amendment to the 11bp SFD:
For DL PPDU and UL PPDU for backscattering:
  For AMP Manchester encoded OOK, data bit 1 is encoded as chip bits “01” and data bit 0 is encoded as chip bits“10”
  Note: same definition as WUR HDR definition.
[Reference contributions: None]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0611r7

## Slide 82
Motion #80 (SFD; May 15, PM1, 2025)
Move to make the following amendment to the 11bp SFD:
Energizer may perform LBT before transmitting WPT signals in S1G. The details of LBT are TBD.
[Reference contributions: 11-25/0791r0, 11-25/0320r1, 11-25/0029r1]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0611r7

## Slide 83
Motion #81 (SFD; May 15, PM1, 2025)
Move to make the following amendment to the 11bp SFD:
IEEE 802.11bp defines at least the following capability parameters to be reported by the energizer to the AMP AP.
  Whether or not support S1G WPT transmission
    If supported, frequency related parameters for WPT. The frequency related parameters may include central frequency information, bandwidth information, etc.
  Whether or not support 2.4G excitation waveform transmission.
  Maximum Tx power.
  Note: The energizer should at least support one of the following transmissions: S1G WPT transmission or 2.4G excitation waveform transmission
[Reference contributions: 11-25/0791r0, 11-25/0318r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0611r7

## Slide 84
Motion #82 (SFD; May 15, PM1, 2025)
Move to make the following amendment to the 11bp SFD:
802.11bp defines short timestamp to enable AMP NON-AP STA to monitor DL frames in duty-cycle operation.
  The length of short timestamp is TBD.
[Reference contributions: 11-25/0814r0, 11-25/0342r0, 11-24/1774r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0611r7

## Slide 85
Motion #83 (SFD; Jul 31, PM1, 2025)
Move to add the following text to the 11bp SFD:
11bp defines at least one mode of bistatic backscatter that can use frequency shifting within a 40 MHz channel in 2.4 GHz band.
Existing 40 MHz medium protection mechanisms will be leveraged
[References: 11-25/1228, 11-25/1229, 11-24/2128, 11-24/2002]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0990r5

## Slide 86
Motion #84 (SFD; Jul 31, PM1, 2025)
Move to add the following text to the 11bp SFD:
The maximum clock offset for a non-backscatter STA is ±10,000 PPM when receiving
[References: 11-24/0853]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0990r5

## Slide 87
Motion #85 (SFD; Jul 31, PM1, 2025)
Move to add the following text to the 11bp SFD:
IEEE 802.11bp will specify that the same chip duration is used for AMP sync field and AMP data field of a single AMP UL PPDU in 2.4 GHz
  For both UL backscattering transmission and UL non-backscattering transmission
[References: 11-25/1262, 11-25/0790, 11-25/1231, 11-25/1217, 11-25/1216]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0990r5

## Slide 88
Motion #86 (SFD; Jul 31, PM1, 2025)
Move to add the following text to the 11bp SFD:
The RATE field in L-SIG of an AMP DL PPDU in 2.4 GHz shall be set to the value representing 6 Mb/s in the 20 MHz channel spacing.
The LENGTH field in L-SIG of an AMP DL PPDU in 2.4 GHz is set to a value satisfying the condition that the remainder is zero when LENGTH is divided by 3.
[References: 11-25/1219, 11-25/1262]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0990r5

## Slide 89
Motion #87 (SFD; Jul 31, PM1, 2025)
Move to add the following text to the 11bp SFD:
An DL AMP PPDU in 2.4 GHz is identified in its U-SIG with the following setting:
  PHY version value sets to 0
  One or multiple Validate bit subfields sets to 0 or subfield(s) set to a validate state.
[References: 11-25/1219 , 11-25/1262]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0990r5

## Slide 90
Motion #88 (SFD; Jul 31, PM1, 2025)
Move to add the following text to the 11bp SFD:
11bp defines two PPDU variants of the AMP DL PPDU for backscattering operation in 2.4GHz
  PPDU subtype 1 consists of the 802.11bp preamble, an Excitation field, an AMP SYNC field, and an AMP Data field and an Excitation field
  PPDU subtype 2 consists of the 802.11bp preamble, an AMP SYNC field, and an AMP Data field and an Excitation field
[References: 11-25/1232]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0990r5

## Slide 91
Motion #89 (SFD; Jul 31, PM1, 2025)
Move to add the following text to the 11bp SFD:
The AMP DL SYNC for backscattering without frequency shift shall differentiate the operating band of sub-1GHz or 2.4GHz
[References: 11-25/1230]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0990r5

## Slide 92
Motion #90 (SFD; Jul 31, PM1, 2025)
Move to add the following text to the 11bp SFD:
The Chip Duration of the Downlink Sync Field Transmitted in 2.4 GHz to a non-Backscatter STA shall be 2 µs
[References: 11-25/1222r1]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0990r5

## Slide 93
Motion #91 (SFD; Jul 31, PM1, 2025)
Move to add the following text to the 11bp SFD:
The Downlink Sync Field Transmitted in 2.4 GHz to a non-Backscatter STA shall use a Sequence of Chips to indicate a data rate of 250 kb/s and a Sequence of Chips to indicate a data rate of 1 Mb/s
Note, is the Logical Complement of
[References: 11-25/1222r1]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0990r5

## Slide 94
Motion #92 (SFD; Jul 31, PM1, 2025)
Move to add the following text to the 11bp SFD:
The Downlink Sync Field transmitted in 2.4 GHz to a non-Backscatter STA consists of two Segments
  The first Segment is a Chip Sequence designed to support Sync Field Detection and Timing alignment
  The second Segment is a “Special Segment” which is designed to reduce the False Alarm rate
[References: 11-25/1220r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0990r5

## Slide 95
Motion #93 (SFD; Jul 31, PM1, 2025)
Move to add the following text to the 11bp SFD:
The AMP-Sync field of the AMP DL PPDU for non-backscatter STAs in 2.4 GHz, shall support both the correlation-based Sync field detector and the differential decoder Sync field detector.
[References: 11-25/1249r1, 11-25/1221r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0990r5

## Slide 96
Motion #94 (SFD; Jul 31, PM1, 2025)
Move to add the following text to the 11bp SFD:
11bp recommend single carrier wave as WPT waveform in Sub-1GHz.
[References: 11-25/1227r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0990r5

## Slide 97
Motion #95 (SFD; Jul 31, PM1, 2025)
Move to add the following text to the 11bp SFD:
11bp shall adopt the following channelization scheme for China:
  Operating bands: 920-925MHz
  Bandwidth 250kHz
  There are 20 channels, with center frequency (MHz): (920.125+N*0.25) MHz, N=0,…,19
[References: 11/25-1224r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0990r5

## Slide 98
Motion #96 (SFD; Jul 31, PM1, 2025)
Move to add the following text to the 11bp SFD:
For mono-static backscattering communication in sub-1 GHz, the maximum allowed clock inaccuracy for the backscattering tag is 100,000 ppm for both receive mode and backscattering transmit mode.
11bp shall specify an AMP-S1G Downlink PPDU supporting downlink transmission for backscattering AMP STA in sub-1 GHz. AMP-S1G Downlink PPDU contains at least an Excitation field, an AMP-Sync field and an AMP-Data field.
Inclusion of an AMP-SIG field is TBD.
Inclusion of an 802.11 preamble is TBD.
Additionally, there will be one or more Excitation fields
Additionally, there may be more than one AMP-Data field
Additionally, AMP-Sync and AMP-SIG field may precede each AMP-Data field
11bp shall specify an AMP-S1G Uplink PPDU supporting uplink transmission for backscattering AMP STA in sub-1 GHz. AMP-S1G Uplink PPDU contains an AMP-Sync field and AMP-Data field.
The AMP-S1G Downlink PPDU and AMP-S1G Uplink PPDU AMP-Data field will use Manchester encoding for backscattering operation.
The AMP-Sync field and the AMP-Data field of AMP-S1G Downlink PPDU and AMP-S1G Uplink PPDU for backscatter communication use OOK modulation
[References: 11/25-1224r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0990r5

## Slide 99
Motion #97 (SFD; Jul 31, PM1, 2025)
Move to add the following text to the 11bp SFD:
The AMP-S1G Downlink PPDU shall support at least one the following data rates:
  62.5 kb/s
  Support of other data rates is TBD
[References: 11-25/1225r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0990r5

## Slide 100
Motion #98 (SFD; Jul 31, PM1, 2025)
Move to add the following text to the 11bp SFD:
The SYNC, Data field and Excitation field of 11bp AMP-S1G Downlink PPDU and AMP-S1G Uplink PPDU use single carrier wave as base carrier waveform for OOK modulated AMP communication
[References: 11-25/1225r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0990r5

## Slide 101
Motion #99 (SFD; Jul 31, PM1, 2025)
Move to add the following text to the 11bp SFD:
802.11bp allows short timestamp to be carried in an AMP trigger Frame.
  Note: The presence of the short timestamp is configurable
[Reference contributions: 11-25/0814r0, 11-25/0342r0, 11-24/1774r0, 11-25/1251r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0990r5

## Slide 102
Motion #100 (SFD; Jul 31, PM1, 2025)
Move to add the following text to the 11bp SFD:
802.11bp allows duty-cycle configuration to be carried in an AMP trigger Frame.
  Details of Duty-cycle configuration (e.g., AMP service period) are TBD.
  Note: The presence of the duty-cycle configuration is configurable
[Reference contributions: 11-25/0813r0, 11-25/0341r0, 11-24/1775r0, 11-25/1252r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0990r5

## Slide 103
Motion #101 (SFD; Jul 31, PM1, 2025)
Move to add the following text to the 11bp SFD:
802.11bp defines one mechanism that a non-AP AMP STA can derive its specific AMP service period in order to monitor AMP DL Frame.
[Reference contributions: 11-25/0813r0, 11-25/0341r0, 11-25/1252r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0990r5

## Slide 104
Motion #102 (SFD; Jul 31, PM1, 2025)
Move to add the following text to the 11bp SFD:
802.11bp supports a time-slot based random access mechanism, which includes:
  Non-AP AMP STA randomly selects a time-slot among time-slots indicated by an AMP Trigger and the non-AP AMP STA transmits an uplink PPDU in the selected slot.
  How to do random selection is TBD
[Reference contributions: 11-25/0858r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0990r5

## Slide 105
Motion #103 (SFD; Jul 31, PM1, 2025)
Move to add the following text to the 11bp SFD:
802.11bp supports a two phases access mechanism for Active Tx non-AP AMP STAs, which includes:
  Based on the uplink frame received in the one or more random access time-slots indicated by an AMP trigger frame from an AMP AP, the AMP AP can transmit another AMP trigger frame to assign one or more transmission time-slots for non-AP AMP STA(s) in a scheduled phase.
[Reference contributions: 11-25/0815r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0990r5

## Slide 106
Motion #104 (SFD; Jul 31, PM1, 2025)
Move to add the following text to the 11bp SFD:
802.11bp specifies, for a short timestamp, coarse timing granularity larger than 1µs.
  The detailed timing granularity are TBD
[Reference contributions: 11-25/1251r0, 11-25/0814r0, 11-25/0342r0, 11-24/1774r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0990r5

## Slide 107
Motion #105 (SFD; Jul 31, PM1, 2025)
Move to add the following text to the 11bp SFD:
An AMP AP transmits an AMP Trigger frame indicating a time-slot based random access session for non-AP AMP STAs. The frame carries:
  Random Access Parameters: Indicates parameters for random access
  Parameters for random access are TBD.
Note (not part of Motion): The AMP Trigger frame is referred to as AMP Poll frame in 25/1240r0.
[Reference: 25/1240r0, 25/0817r0, 25/0818r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0990r5

## Slide 108
Motion #106 (SFD; Jul 31, PM1, 2025)
Move to add the following text to the 11bp SFD:
Upon receiving the AMP Trigger frame indicating a time-slot based random access session, a non-AP AMP STA performs the following actions:
  Based on the Random Access Parameters, the non-AP AMP STA may transmit an uplink AMP PPDU carrying the uplink response in one of the slots allocated by the AMP Trigger frame.
[Reference: 25/1240r0, 25/0817r0, 25/0818r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0990r5

## Slide 109
Motion #107 (SFD; Jul 31, PM1, 2025)
Move to add the following text to the 11bp SFD:
An AMP AP transmits an AMP Trigger frame indicating a time-slot based scheduled access for non-AP AMP STAs. The frame may carry：
  Number of Slots (N) indicating the number of slots immediately after the AMP Trigger frame that are allocated for uplink transmissions, and,
  IDs of one or more non-AP AMP STAs that are scheduled for uplink transmission.
  Other parameters are TBD.
the option of more than one Non-AP AMP STAs in mutiple slots is limited to Active Tx communication.
Note (not part of SP): The AMP Trigger frame is referred to as AMP Request frame in 25/1240r0.
[Reference: 25/1240r0, 25/0817r0, 25/0818r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0990r5

## Slide 110
Motion #108 (SFD; Jul 31, PM1, 2025)
Move to add the following text to the 11bp SFD:
Upon receiving the AMP Trigger frame indicating a time-slot based scheduled access for non-AP AMP STA(s), a non-AP AMP STA performs the following actions:
  If the AMP Trigger frame carries the ID of the non-AP AMP STA, the non-AP AMP STA may transmit an uplink AMP PPDU carrying the requested response in one of the time slots allocated by the AMP trigger frame.
the option of more than one Non-AP AMP STAs in multiple slots is limited to Active Tx communication
[Reference: 25/1240r0, 25/0817r0, 25/0818r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0990r5

## Slide 111
Motion #109 (SFD; Jul 31, PM1, 2025)
Move to add the following text to the 11bp SFD:
If the AMP frame is protected (for security), the FCS field of the AMP frame carries a 16-bits MIC.
[Reference: 25/1102r1,11-25/0817r0, 25/0818r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0990r5

## Slide 112
Motion #110 (SFD; Jul 31, PM1, 2025)
Move to add the following text to the 11bp SFD:
802.11bp defines an AMP frame to carry uplink response from a non-AP AMP STA:
  Names of the AMP Frame is TBD
[Reference: 25/1102r1, 25/0817r0, 25/0818r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0990r5

## Slide 113
Motion #111 (SFD; Jul 31, PM1, 2025)
Move to add the following text to the 11bp SFD:
For backscatter communication, 11bp shall support the following UHF commands as defined by the UHF RFID Standard:
  Select, Read, Write, Authenticate
  Other UHF commands supported by 11bp is TBD
  NOTE – The UHF commands and the tag states are defined by the EPC® Radio-Frequency Identity Generation-2 Version 2 UHF RFID Standard
[Reference: 25/1239r0, 25/0818r0]
Result: Approved with unanimous consent
Note: this is part of approved motion #1 in 11-25/0990r5

## Slide 114
Motion #112 (SFD; Sep 15, AM2, 2025)
Move to add the following text to the 11bp SFD:
For backscatter communication, 11bp shall support the following UHF commands as defined by the UHF RFID Standard:
    Select, Read, Write, Authenticate
    Other UHF commands supported by 11bp is TBD
    NOTE – The UHF commands and the tag states are defined by the EPC® Radio-Frequency Identity Generation-2 Version 2 UHF RFID Standard
[Reference: 25/1239r0, 25/0818r0]
Result: Approved with unanimous consent
Note: this is part of approved Tech Motion #1 in 11-25/1430r8

## Slide 115
Motion #113 (SFD; Sep 15, AM2, 2025)
Move to add the following text to the 11bp SFD:
11bp shall specify a low-complexity secure method to generate and update a PMK for secure AMP communication between an AMP AP and an AMP non-AP STA?
Note:
    The secure AMP communication method is defined in Motion 64, 65, 66.
    Whether to include backscatter non-AP STAs in this method is TBD.
[References: 11-25/1086, 11-25/0831]
Result: Approved with unanimous consent
Note: this is part of approved Tech Motion #1 in 11-25/1430r8

## Slide 116
Motion #114 (SFD; Sep 15, AM2, 2025)
Move to add the following text to the 11bp SFD:
IEEE 802.11bp supports a mechanism in which a non-AP AMP STA may report the transmission time it can sustain.
How the non-AP AMP STA may report this time is TBD
[Reference: 25/0788r0, 25/1243r0]
Result: Approved with unanimous consent
Note: this is part of approved Tech Motion #1 in 11-25/1430r8

## Slide 117
Motion #115 (SFD; Sep 15, AM2, 2025)
Move to add the following text to the 11bp SFD:
An AMP AP may transmit the AMP AP's partial timestamp in a broadcast AMP frame (name TBD). Length of the partial timestamp is TBD.
[Reference: 11-25/0039r0, 11-25/0285r1, 11-25/0787r0, 11-25/1247r0]
Result: Approved with unanimous consent
Note: this is part of approved Tech Motion #1 in 11-25/1430r8

## Slide 118
Motion #116 (SFD; Sep 15, AM2, 2025)
Move to add the following text to the 11bp SFD:
The AMP frame consists of the following basic components:
A MAC header
A variable-length frame body, which if present, contains information specific to the frame type
An FCS, which contains either a TBD-bit CRC or a 16-bit MIC
    Whether FCS is always present or not for backscatter PPDUs is TBD
    Whether to allow both CRC and MIC in the same frame in certain condition is TBD.
With the length of the AMP frame being expressed in octets with the unit TBD.
[Reference contributions: 11-25/0776r2]
Result: Approved with unanimous consent
Note: this is part of approved Tech Motion #1 in 11-25/1430r8
MAC Header | Frame Body | FCS

## Slide 119
Motion #117 (SFD; Sep 15, AM2, 2025)
Move to add the following text to the 11bp SFD:
The MAC Header of the AMP frame comprises Frame Control, ID, and Type Dependent Control fields.
Frame Control contains a Type field that indicates the type of AMP frame, and other fields that are TBD.
ID contains an identifier for the AMP frame
  Whether the ID field is always present or not is TBD
Type Dependent Control contains control information that depends on the type of AMP frame
  Whether Type Dependent Control field is always present or not is TBD
There can be additional identifier(s) of AMP STA(s) in the AMP frame in certain cases and their location, if present, is TBD
Whether there are other fields in the MAC Header is TBD
[Reference contributions: 11-25/0776r2]
Result: Approved with unanimous consent
Note: this is part of approved Tech Motion #1 in 11-25/1430r8
 | Frame Control | ID | Type Dependent Control
Bits | X | Y | Z

## Slide 120
Motion #118 (SFD; Sep 15, AM2, 2025)
Move to add the following text to the 11bp SFD:
The MAC Header of the backscatter AMP frame comprises Frame Control, ID, and Type Dependent Control fields
  Frame Control contains a Type field that indicates the type of backscatter AMP frame, and other fields that are TBD.
  ID contains an identifier for the backscatter AMP frame
    Whether the ID field is always present or not is TBD, and has a length of 16 bits
  Type Dependent Control contains control information that depends on the type of AMP frame
    Whether Type Dependent Control field is always present or not for the backscatter AMP frame is TBD
There can be additional identifier(s) of AMP STA(s) in the AMP frame in certain cases and their location, if present, is TBD
[Reference contributions: 11-25/0776r2]
Result: Approved with unanimous consent
Note: this is part of approved Tech Motion #1 in 11-25/1430r8
 | Frame Control | ID | Type Dependent Control
Bits | tbd | 16 | tbd

## Slide 121
Motion #119 (SFD; Sep 15, AM2, 2025)
Move to add the following text to the 11bp SFD:
  The Frame Control field of the AMP frame is 8 bits
    Type field uses 3 to 4 bits of the Frame Control
    Whether the Type field is the first field of the Frame Control is TBD
[Reference contributions: 11-25/0776r2]
Result: Approved with unanimous consent
Note: this is part of approved Tech Motion #1 in 11-25/1430r8

## Slide 122
Motion #120 (SFD; Sep 18, PM1, 2025)
Move to add the following text to the 11bp SFD:
  The length of the ID field is based on the frame type/use case:
    12 bits for AMP enabled non-AP STAs,
    Either 12 or 16 bits for active TX non-AP AMP STAs,
    16 bits for backscatter non-AP AMP STAs.
[Reference contributions: 11-25/0776r2]
Result: Approved with unanimous consent
Note: this is part of approved SFD Motion in 11-25/1430r8

## Slide 123
Motion #121 (SFD; Sep 18, PM1, 2025)
Move to add the following text to the 11bp SFD:
The Type Dependent Control field is
12 bits for AMP enabled non-AP STAs
If present, either 8, 12 or 16 bits for active TX non-AP AMP STAs
If present, TBD bits (multiple of 8 bits) for backscatter non-AP AMP STAs
[Reference contributions: 11-25/0776r2]
Result: Approved with unanimous consent
Note: this is part of approved SFD Motion in 11-25/1430r8

## Slide 124
Motion #122 (SFD; Sep 18, PM1, 2025)
Move to add the following text to the 11bp SFD:
For Active TX and Backscatter use cases, the length of the Frame Body field (if variable) is indicated in the MAC header of the AMP frame.
Specific location, encoding and size is TBD.
Note – If the length is indicated in the PHY header, there is no need for length indication in the MAC header.
Note – For AMP-enabled use case, the length is already signaled in the Frame Control field.
[Reference contributions: 11-25/0776r2]
Result: Approved with unanimous consent
Note: this is part of approved SFD Motion in 11-25/1430r8

## Slide 125
Motion #123 (SFD; Sep 18, PM1, 2025)
Move to add the following text to the 11bp SFD:
For unprotected Active TX and Backscatter use cases, when the FCS field is carrying the CRC, the length of the FCS field is 16 bits.
It is TBD if the CRC is 8-bit long under certain conditions.
Note – For AMP-enabled use case, we continue to use baseline 16 bits CRCs/MICs.
Note – If the FCS field carries the MIC, the length of the FCS field is 16 bits (already in SFD).
[Reference contributions: 11-25/0776r2]
Result: Approved with unanimous consent
Note: this is part of approved SFD Motion in 11-25/1430r8

## Slide 126
Motion #124 (SFD; Sep 18, PM1, 2025)
Move to add the following text to the 11bp SFD:
The CRC of AMP frames shall use the 16-bit CRC engine from IEEE 802.11ba.
If the group decides to carry 8-bit long CRC in certain AMP frames, it is TBD how to obtain the 8-bit CRC from the 16-bit CRC engine output.
[Reference contributions:11-25/0776r2]
Result: Approved with unanimous consent
Note: this is part of approved SFD Motion in 11-25/1430r8

## Slide 127
Motion #125 (SFD; Sep 18, PM1, 2025)
Move to add the following text to section 4.4.3 of the 11bp SFD:
11bp defines mandatory forward error correcting code (FEC) of coding rate ½ for the data portion of UL active transmission in 2.4 GHz at rates of 0.25,1Mbps and non-coded mode at rate of 4Mbps
[Reference contributions: 11-25/1002r1, 11-25/1215r1]
Result: Approved with unanimous consent
Note: this is part of approved SFD Motion in 11-25/1430r8

## Slide 128
Motion #126 (SFD; Sep 18, PM1, 2025)
Move to add the following text to section 4.4.3 of the 11bp SFD:
11bp defines forward error correcting code (FEC) for the data portion of UL active transmission in 2.4 GHz based on the code as defined in 17.3.5.6 in 802.11-2024
[Reference contributions: 11-25/1002r1, 11-25/1215r1]
Result: Approved with unanimous consent
Note: this is part of approved SFD Motion in 11-25/1430r8

## Slide 129
Motion #127 (SFD; Sep 18, PM1, 2025)
Move to add the following text to the 11bp SFD:
In the data field of AMP UL active transmission in 2.4 GHz,
    250kbps data rate only uses 1us chip duration and rate 1/2 binary convolution code (BCC)
    1Mbps data rate only uses 0.25us chip duration and the same rate 1/2 BCC
    4Mbps doesn’t use BCC
[Reference contributions: 11-25/1215r1, 11-25/1552r0, 11-25/1262r1, 11-25/0790r0]
Result: Approved with unanimous consent
Note: this is part of approved SFD Motion in 11-25/1430r8

## Slide 130
Motion #128 (SFD; Sep 18, PM1, 2025)
Move to add the following text to the 11bp SFD:
The Uplink Sync Field Transmission from a non-Backscatter STA for all data rates shall have a length 48 chips.
[Reference contributions: 11-25/1552r0]
Result: Approved with unanimous consent
Note: this is part of approved SFD Motion in 11-25/1430r8

## Slide 131
Motion #129 (SFD; Sep 18, PM1, 2025)
Move to add the following text to the 11bp SFD:
Length-48 sync sequence for UL non-backscatter transmission is constructed by repeating length-24 base sequence twice, i.e. S48 = [S24 S24]
The length-24 base sequence is given as below:
  S24=[1, 1, 1, 1, 1, 0, 1, 0, 0, 1, 1, 0, 0, 1, 1, 0, 0, 0, 0, 1, 0, 1, 0, 0]
[Reference contributions: 11-25/1552r0]
Result: Approved with unanimous consent
Note: this is part of approved SFD Motion in 11-25/1430r8

## Slide 132
Motion #130 (SFD; Sep 18, PM1, 2025)
Move to add the following text to the 11bp SFD:
The first segment of the Downlink Sync Field transmitted to non-Backscatter STAs, uses the sequence 𝑾 for the 250 kb/s data rate or the sequence for the 1 Mb/s data rate. The sequences are:
  𝑾 = 01011010010111000110001011101100
  = 10100101101000111001110100010011
[Reference contributions: 11-25/1554r0]
Result: Approved with unanimous consent
Note: this is part of approved SFD Motion in 11-25/1430r8

## Slide 133
Motion #131 (SFD; Sep 18, PM1, 2025)
Move to add the following text to the 11bp SFD:
An DL AMP PPDU in 2.4 GHz is identified in its U-SIG with the following setting:
  PHY version value set to 0
  PPDU Type And Compression Mode value set to 3.
[Reference contributions: 11-25/1518r1]
Result: Approved with unanimous consent
Note: this is part of approved SFD Motion in 11-25/1430r8

## Slide 134
Motion #132 (SFD; Sep 18, PM1, 2025)
Move to add the following text to the 11bp SFD:
The AMP DL PPDU for bistatic backscattering operation in 2.4GHz shall be PPDU subtype 2.
  PPDU subtype 2 consists of the 802.11bp preamble, an AMP SYNC field, and an AMP Data field and an Excitation field.
  The AMP SYNC is the same sync design as for active Tx non-AP AMP STA.
  The AMP Data uses the same Manchester encoded OOK with data rates of 250kbps, 1 Mbps.
The AMP Uplink PPDU for bistatic backscattering operation in 2.4GHz shall reuse the following fields from active Tx.
  The AMP SYNC is the same sync design as for active Tx non-AP AMP STA.
  The AMP Data uses the same Manchester encoded OOK with data rates of 250kbps, 1 Mbps as same as Active TX non-AP AMP STA. 4 Mbps is TBD.
[Reference contributions: 11-25/1541r2]
Result: Approved with unanimous consent
Note: this is part of approved SFD Motion in 11-25/1430r8

## Slide 135
Motion #133 (SFD; Sep 18, PM1, 2025)
Move to add the following text to the 11bp SFD:
The receiver requirements for a non-AP AMP STA capable of bistatic backscatter in 2.4 GHz shall be the same as that of an active Tx non-AP AMP STA. This includes,
  Clock accuracy, center frequency accuracy.
[Reference contributions: 11-25/1541r2]
Result: Approved with unanimous consent
Note: this is part of approved SFD Motion in 11-25/1430r8

## Slide 136
Motion #134 (SFD; Sep 18, PM1, 2025)
Move to add the following text to the 11bp SFD:
AMP Sync field for uplink monostatic backscattering transmission has a structure of [S, S, S] for both 2.4GHz and sub-1GHz.
  S = [1 1 0 1 0 1 0 0].
[Reference contributions: 11-25/1556r0]
Result: Approved with unanimous consent
Note: this is part of approved SFD Motion in 11-25/1430r8

## Slide 137
Motion #135 (SFD; Sep 18, PM1, 2025)
Move to add the following text to the 11bp SFD:
The same chip duration shall be used for AMP backscattering uplink Sync field and AMP backscattering uplink data field in sub-1GHz.
[Reference contributions: 11-25/1556r0]
Result: Approved with unanimous consent
Note: this is part of approved SFD Motion in 11-25/1430r8

## Slide 138
Motion #136 (SFD; Sep 18, PM1, 2025)
Move to add the following text to the 11bp SFD:
11bp shall adopt the following channelization scheme for EU:
    Bands: 865-868MHz
    BW: 200kHz
    Channel center frequency: 865.1+N*0.2, N=0,…,14;
Note: support of 400kHz bandwidth in 915-921MHz is TBD.
[Reference contributions: 11-25/1558r0]
Result: Approved with unanimous consent
Note: this is part of approved SFD Motion in 11-25/1430r8