## Slide 1: RLAN Coex with SSTX Radars
Date: 2024-17-07
Authors:

## Slide 2: 5A/93 ITU-R WP5B LS to WP5A (1/3)
ITU AHG is Discussing the LS from WP5B to WP5A and would like to inform Coex SC about the development for possible actions in the future.
Liaison statement to ITU-R Working Party 5A (copy to World Meteorological Organization for information) - Solid-state transmitter radars and wireless access systems and radio local area networks in the 5 GHz frequency band
  In May 2024 Working Party (WP) 5B received contribution 5B/53 provided information on the future deployment of solid-state transmitter (SSTX) weather radars and the technical coexistence with WAS/RLAN in the 5 GHz frequency band.
  Frequency band 5 250-5 725 MHz is allocated on a primary basis to the radiolocation service and Nos. 5.446A and 5.450A of the Radio Regulations (RR). RR No. 5.450A states that in the 5 470-5 725 MHz band, the mobile service shall not claim protection from the radiodetermination services.
  The planned use of SSTX weather radars and current WAS/RLAN operation in the 5 GHz frequency band, in particular in the sub-band 5 600-5 650 MHz, may require further technical coexistence analysis.
  To facilitate this discussion, WP 5B suggests that the following topics be included in a joint meeting during the November 2024 meeting with WP 5A regarding the use of SSTX weather radars and WAS/RLAN:
    the technical and operational characteristics of SSTX weather radars in the 5 GHz band;
    the aspects related to the characteristics and application of DFS in Recommendation ITU R M.1652-1.

## Slide 3: 5A/93 ITU-R WP5B LS to WP5A (2/3)
Future operation of weather radars in the 5 GHz frequency band with solid-state transmitters (SSTX) is covered in Recommendation ITU-R M.1849.
  More than 1 500 weather radars around the world, lifecycle of up to 20 years. Transition will take decades, even if the SSTX technology becomes common very quickly.
  Expected that both tube and SSTX will be used even in new system installations in the near future.
  Differences in the pulse characteristics of SSTX weather radars compared to tube-based weather radar
  Risk that this will reduce the capacity of RLAN DFS to detect radar signal in the 5 GHz band.
    Traditional tube Radars are short pulses with high power levels are transmitted.
    SSTX power is much lower (transmitted peak power, 4-8 kW vs 250-450 kW), leading to poorer detection performance in the RLAN device and possible decreased detection range of SSTX systems.
    Uncertainty on how RLAN devices will behave as the pulses transmitted by SSTX differ from the parameters assumed in RLAN device. Pulse compression can be up to 200 µs (instead of 0.5 to 3.5 µs for tube-based systems) to compensate average power.
    Pulse compression enables the utilization of longer pulses and lower-power transmitters without compromising range resolution.

## Slide 4: Characteristics (1/2)
Pulse compression ratio (PCR): the ratio of uncompressed pulse length to the compressed pulse.
Long transmission pulse (x 60) with low peak power (15-20 dB less) can achieve a better and longer range.
This exceeds the 15 dB margin for DFS detection in RLAN devices.
Pulse compression allows the independent adjustment of range resolution and range sensitivity.
Tube transmitters and SSTX sensitivity depends on transmitted energy (product of the pulse length multiplied by the peak power).
Blind range is the range where the receiver is blocked during the transmission of the compressed pulse. SSTX still requires the transmission of a short uncompressed pulse.
 | Tube based radar | SSTX
Frequency range | 5.4-5.8 GHz | 
Transmitter peak power | ≤ 450 kW in total => 225 kW per polarization | 2-8 kW per polarization
Pulse length | 0.5-3.5 µs | ≤ 200 µs
PRF | ≤ 3 000 Hz | 
Duty cycle | ≤ 0,12 % | ≤ 10%
Technical parameters for tube-based and SSTX radar systems

## Slide 5: Characteristics (2/2)
SSTX are also using short uncompressed pulses (approx. 1 µs) to cover the blind range, caused by the transmission of the compressed pulse. DFS mechanism detects this. There are three ways to implement.
  Dual Pulse Transmission on the same frequency
  Dual pulse transmission on two separate frequencies (frequency separation between 3-6 MHz)
  Long pulse transmission only (future, to detect the short-range targets using a long-compressed pulse)
Dynamic Frequency Selection (DFS) detection
  Compared with tube transmitters the SSTX transmitter power is much lower, leading to a poorer detection performance in the RLAN device and possible decreased detection range of SSTX systems.
  When both pulses are transmitted on the same frequency, the DFS detection algorithm might work better because the uncompressed short pulse is clearly separated and visible.
The Radio Regulations (2020) incorporates the Recommendation ITU-R M.1652-1 (05/2011) “Dynamic frequency selection in wireless access systems including radio local area networks for the purpose of protecting the radiodetermination service in the 5 GHz band” by reference.
The Recommendation ITU-R M.1849-3 (02/2023) “Technical and operational aspects of ground-based meteorological radars” addresses among other things the technical and operational characteristics of meteorological radars.
  The interference impact on weather radar system is more severe than the other way round.

## Slide 6: 5A/93 ITU-R WP5B LS to WP5A (3/3)
Feedback from Nov WP5A-WP5B joint session will be given to 802.11 specifically Coex SC to be considered for possible next steps.
ITU AHG can help with interacting with WP5A; technical discussions/contributions is expected to happen in other 802.11 groups such as Coex SC.
WP5A Contribution to Tuesday 2024-11-19 - Friday 2024-11-29
  IEEE 802 need to participate and contribute to the subject starting November 2024.
  No contribution is required for November session.
  Coex SC may consider submitting a preliminary analysis for discussion with ITU AHG.