## Slide 1: AMP Device Power Status
Date: 2024-08-06
Authors:
Name | Affiliation | Address | Phone | Email
Yinan Qi | OPPO |  |  | v-qiyinan@oppo.com
Weijie Xu |  |  |  | 
Chuanfeng He |  |  |  | 
Doc.: IEEE 802.11-24/1381r0
August 2024

## Slide 2: Abstract
In this contribution, we discuss the definition of power status for AMP devices and propose a scheme for AMP devices to report its own power status to facilitate channel access and WPT.
Doc.: IEEE 802.11-24/1381r0

## Slide 3
Challenges for AMP Devices
  Channel access
    In 802.11 Wi-Fi networks, traffic categories are defined to refer to different classes or priorities assigned to various types of network traffic.
    In general, traffic with high priority can access the channel faster and thus QoS can be guaranteed.
    AMP is set with AC-BK priority, e.g., the lowest priority [1].
    Among AMP devices, we might also need to consider different priority.
      In AMP, power consumption is an essential issue since some devices may not have strong energy harvesting capability or super capacitor for energy storage.
      Such AMP devices should be given higher priority to access channel because long channel access time may drain the power of such devices.
      In some extreme cases, these devices may need to wait for additional long time to store sufficient power for another channel access procedure.
  WPT
    Either periodic or on demand
    On demand should be requested by AMP devices explicitly or implicitly
Yinan Qi (OPPO)
Slide 3
Doc.: IEEE 802.11-24/1381r0
August 2024

## Slide 4
Power Status Definition
  Power status can be defined based on both the long-term or short term power features of the AMP devices and one power status can be assigned with certain channel access priority.
    Long term power feature example
      Low-level: devices with extremely limited energy harvesting and power storage capability;
      Mid-level: devices with limited energy harvesting and power storage capability;
      High-level: devices with reasonable energy harvesting and power storage capability.
    For a single device, short term power feature, e.g., remaining power can also be considered to define power status.
  Channel access: AMP devices with stringent power limit can be configured with higher priority to access the channel to mitigate the latency and fairness issue.
  WPT: can be triggered by power status implicitly, e.g., power status indicating low remaining power
Yinan Qi (OPPO)
Slide 4
Doc.: IEEE 802.11-24/1381r0
August 2024

## Slide 5
Long Term Power Features Considered
  Multiple power features of AMP devices should be taken into account.
    Energy harvesting capability including
      Power source(s)
      Energy harvesting efficiency
    Energy storage capability
      Whether or not energy storage is supported;
      The amount of energy that can be stored;
      Energy storage draining rate;
    Others
      RF energy harvesting operation frequency
Yinan Qi (OPPO)
Slide 5
Doc.: IEEE 802.11-24/1381r0
August 2024

## Slide 6
Power Status Report
  Power status can be reported to the AP so that AP can configure channel access priority and AP/Energizer can conduct WPT.
  For example, AMP devices can report/suggest their own initial power status and AP can determines the actual power status and signals the AMP devices.
  AP can decide whether or not to do WPT based on power status report.
Yinan Qi (OPPO)
Slide 6
Doc.: IEEE 802.11-24/1381r0
August 2024

## Slide 7
Summary
  In this submission, we discuss power status definition and report for AMP:
    Channel access priority and WPT can depend on power status
    AMP devices can report their power status to the AP for the AP to determine channel access priority when activating/scheduling the AMP devices .
Yinan Qi (OPPO)
Slide 7
Doc.: IEEE 802.11-24/1381r0
August 2024

## Slide 8: Reference
[1] “p802.11bp-PAR,” IEEE 802.11-24/0575r1, March 2024
Doc.: IEEE 802.11-24/1381r0
August 2024