## Slide 1
August 2024
Discussion on Channel Switching for NPCA
Date: 2024-08-13
Authors:
Name | Affiliations | Address | Phone | email
Si-Chan Noh | Newracom |  |  | sc.noh@newracom.com
Joonsoo Lee |  |  |  | js.lee@newracom.com

## Slide 2: Motivation
Non-Primary Channel Access(NPCA) STAs may perform NPCA operation when the primary channel is BUSY due to OBSS traffic
Predict/identify how long OBSS traffic will occupy the primary channel can affect NPCA efficiency and performance
The duration for which OBSS traffic occupies the primary channel is beyond the control of NPCA STAs
In this presentation, we discuss how to allow NPCA STAs to predict the NPCA operating duration more clearly for efficient NPCA operation

## Slide 3: Recap[1-3]
The following are the discussions so far on enabling NPCA STAs to perform NPCA operations [1-3]
  After detecting control frame exchange/OBSS PPDU
    Switch back to BSS primary channel before NAV expires/before the end of PPDU
  PPDU-based
    Switch back to the primary channel at the end of the OBSS PPDU
  SP-based
    Switch to a non-primary channel without switching back and forth during an OBSS SPs
When the NPCA STAs detect OBSS traffic, it is required to identify necessary information more clearly for the NPCA operation

## Slide 4: Channel Switching after detecting PHY preamble
When NPCA STAs are enabled to perform NPCA operation after detecting OBSS PPDU, it can perform NPCA through following information
  Based on preamble; or
  Duration/ID field in MAC header
In here, we assume that the NPCA STAs perform NPCA after detecting preamble of the OBSS PPDU where TXOP duration information can be provided
  If NPCA STAs can predict the duration that OBSS traffic occupies the BSS primary channel through TXOP duration, it can perform NPCA during that duration
BSS Primary channel
Preamble
Data payload
TXOP duration
(= may NPCA operating duration)
Channel
switching
BA
Switch back

## Slide 5: Channel Switching after detecting control frame exchange
When NPCA STAs are enabled to perform NPCA after detecting control frame exchange (e.g., (MU)-RTS/CTS), it can perform NPCA through following information
  Based on Duration/ID field
The NPCA STAs can predict the duration that OBSS traffic occupies the BSS primary channel through Duration/ID field and it can perform NPCA during that duration
BSS Primary channel
(MU)-RTS
NAV duration
(= may NPCA operating duration)
Channel
switching
DATA
CTS
NAV set by (MU)-RTS
NAV set by CTS
BA
Switch back

## Slide 6: NPCA operating duration
Through detecting PHY preamble/control frame exchange, the NPCA STAs can obtain NAV duration information that may imply the NPCA operating duration
In some cases, this obtained NAV duration information may not clearly indicate the duration that OBSS traffic occupies the BSS primary channel
  For example, NAV duration can be defined for a fragmented MSDU, which does not indicate the actual/entire/desired TXOP duration
It can be implementation dependent, but also beyond the control of NPCA STAs

## Slide 7: NPCA operating duration
However, from the perspective of NPCA STAs, the following situations may arise
  If the obtained NAV duration information is too short to perform NPCA, even though it may be possible in the long-term manner, channel switching might not be performed; or
  Even though the NPCA operation can be performed continuously in the long-term manner, switching back and forth between BSS and NPCA primary channel can occur
BSS Primary channel
NAV set by (Data 1)
(HE/EHT/UHR) DATA 1
BA 1
Too short to perform NPCA
actual/entire/desired TXOP
* for convenience, assume that NPCA STAs perform NPCA after detecting preamble of the OBSS PPDU
NAV set by (Data 2)
(HE/EHT/UHR) DATA 2
BA 2
Too short to perform NPCA
Switch
back
BSS Primary channel
(MU)-RTS
Channel
switching
DATA 1
CTS
NAV set by (MU)-RTS
NAV set by CTS
BA 1
NAV duration
(= may NPCA operation duration)
actual/entire/desired TXOP
NAV duration
(= may NPCA operation duration)
* for convenience, switching delay is omitted and second (MU)RTS/CTS can be excluded
…
…
…
…
(MU)-RTS
DATA 1
CTS
BA 1
NAV set by (MU)-RTS
NAV set by CTS
Switch
back
Channel
switching
Notes: (MU)RTS/CTS in second

## Slide 8: Proposed approach for NPCA
We can consider ways to convey the TXOP duration information more clearly to NPCA STAs
Indicating the actual/entire/desired TXOP duration explicitly within a UHR PPDU and/or ICF/ICR(e.g., (MU)-RTS/CTS) can be one approach
This means that when allowing NPCA STAs to perform NPCA operation based on UHR PPDU and/or ICF/ICR, the indicated TXOP duration can be used for estimating the NPCA operating duration
This approach can help prevent some scenarios discussed in the previous slide

## Slide 9: Summary
In this presentation, we discuss some approaches for NPCA STAs to predict the NPCA operating duration more clearly
  Including TXOP duration information in UHR PPDU and/or ICF/ICR(e.g., (MU)-RTS/CTS)

## Slide 10: Reference
[1] 24/0495r0, Non-Primary Channel Access (NPCA) - Follow up
[2] 24/0496r1, Secondary Channel Usage Follow Up
[3] 24/1259r0, SP-based non-primary channel access follow-up