## Slide 1: Discussion on aspects in DRU operation – follow up
Date: 2024-07-10
Authors:
Name | Affiliations | Address | Phone | email
Arik Klein | Huawei |  |  | Arik.Klein@huawei.com
Genadiy Tsodik |  |  |  | Genadiy.tsodik@huawei.com
Shimi Shilo |  |  |  | Shimi.Shilo@huawei.com
Oded Redlich |  |  |  | Oded.Redlich@huawei.com

## Slide 2
The Distributed tone RU (DRU) feature is widely discussed in TGbn PHY and has been accepted as a solution for the limit of maximal EIRP PSD regulation in the 6GHz band (TGbn SFD, Motion #1)
  DRU is currently defined for UL transmissions (TB PPDUs)
This results in smaller number of tones within each 1MHz and thus the total transmitted power of the STA may increase while keeping the maximal (regulated) EIRP PSD value
Recap – Distributed RU (DRU)

## Slide 3
In [1], [2] it has been shown that:
  In an uplink MU transmission, the HE STA sets its actual transmit power, as the minimal value between the calculated Tx power and the maximum Tx power defined by the Max EIRP PSD within the allocated BW (we denote it as )
  The transmit power calculations are carried out only at the non-AP STA side whereas the AP has no indication that the STA’s transmit power is uniquely bounded by the Max EIRP PSD
    The UL Power Headroom is 0 in this case.
    Target RSSI setting is bounded and may affect optimal <MCS, NSS> setting.
Recap – DRU allocation Problem Statement

## Slide 4
We propose to add an indication to support the allocation of a DRU type (instead of an RRU type)
Adding the “EIRP PSD limit flag” field (exact name – TBD)
  Set to 1, if the maximal allowed transmit power equals to the value o (maximum Tx power defined by the Max EIRP PSD within the allocated BW ):
  Otherwise, this field should be set to 0.
  If the value of the UPH (as reported by the non-AP STA) is very low, this field indicates the AP that a DRU allocation for that non-AP STA may be considered if Target RSSI needs to be increased
Indication for a DRU allocation

## Slide 5
Suggestion: use 1 bit (B6) of a “reserved” subfield in UPH A-Control
  Note: B7 still remains a reserved subfield for future extensions.
Indication for a DRU allocation

## Slide 6
The DRU feature is accepted in TGbn PHY as a solution for bounded uplink transmit power due to Maximal EIRP PSD regulation in the 6GHz band
Suggest to add an indication to support the AP with a DRU allocation:
  EIRP PSD limit flag
The field may be added in UPH A- control field.
Summary

## Slide 7
Do you support adding the following to the TGbn SFD?
  11bn defines a mechanism to support a UHR AP with a DRU allocation for a UHR non-AP STA.
SP1

## Slide 8
Do you support adding the following to the TGbn SFD?
  11bn defines indication for assisting an UHR AP with DRU allocation for a UHR non-AP STA that is allocated with Regular RU (RRU)
    The indication will be set to 1 if the maximal allowed transmit power equals to the value of the power of max EIRP PSD value within the allocated BW
    The indication field may be added in UPH A-control field.
SP2

## Slide 9
[1] 11-24/1058r0 Discussion on aspects in DRU operation - Arik Klein, Huawei
[2] 11-24/1124r0 Client Experience Reporting – B. Hart et al., Cisco
[3] IEEE 802.11 REVme D6.0, section 27.3.15.2 Power Precorrection
Reference

## Slide 10
Do you support adding the following to the TGbn SFD?
  11bn defines indication for assisting an UHR AP with DRU allocation for a UHR non-AP STA that is allocated with Regular RU (RRU)
    The indication will be set to 1 if the maximal allowed transmit power equals to the value of the power of max EIRP PSD value within the allocated BW
    The indication field - TBD
SP2a