## Slide 1: RSSI Measurement Based on Control Frame Exchange
Date: 2024-07-23
Authors:
July 2024
Notes: September 2012

## Slide 2: Introduction
The off-channel scanning is one of main factors which affects the roaming delay.
In order to reduce the impact of the off-channel scanning, 11bn should allow a non-AP MLD can probe neighboring AP MLDs over the DS via the current AP MLD [1-2].
Then the only thing that shall be done over the air is to periodically monitor RSSI values with one or more candidate AP MLDs in the process of moving
  Thus the non-AP MLD selects a propriate roaming point to initiate the roaming from the current AP MLD to the target AP MLD.

## Slide 3: Motivation
The current link measurements (based on the TPC Request/Response exchange or the Probe Request/Response exchange) are very time consuming.
Hence, a measurement method based on a Control frame exchange had been proposed in several contributions [2-4].
In this contribution, we will discuss the detail on the RSSI measurement based on a Control frame exchange.

## Slide 4: Recap Non-TB Measurement Exchange
A non-TB sensing measurement exchange is defined in 11bf D4.0. [5]
  in which a non-AP STA is the sensing initiator and an AP is the sensing responder.
  Note that the non-AP STA can be a unassociated STA in respective of the AP as the sensing responder.

## Slide 5: RSSI Measurement Procedure
Considering it is the RSSI measurement and no report is required, there is no privacy leakage. Hence, there is no need to establish the sensing measurement session.
So the measurement exchange can be simplified as the below procedure.
  NDPA+NDP
NDPA
NDP
STA
Neighboring
AP
SIFS

## Slide 6: NDPA Frame
The format of the NDPA frame is the same as the HE NDP Announcement frame.
  The RA field of the NDPA frame transmitted by the STA is set to the BSSID of the recipient AP
The NDPA frame contains only one STA Info field with a special AID (e.g. 2043).
  AID11
  Reserved
  NDP Tx Power
    It is set to the transmit power used to transmit the followed NDP frame.
  NSTS
  Repetition Num
  Disambiguation
  Reserved
Note that the NSTS and Repetition Num fields are used to indicate the required HE-LTF configuration of the NDP that follows.

## Slide 7: Conclusions
In this presentation, we propose a new RSSI measurement based on the NDPA+NDP frame exchange.
The proposed RSSI measurement based on the above frame exchange can facility the client to monitor the RSSI values of neighboring APs and significantly reduce the off-channel measurement time.

## Slide 8: References
[1] 11-24-0679-01-00bn-thoughts-on-functionality-and-security-architecture-for-uhr-seamless-roaming
[2]11-23-1897-00-00bn-thoughts-on-improving-roaming-under-existing-architecture
[3] 11-23-0668-02-0uhr-coordinated-measurement
[4] 11-23-2152-01-00bn-uhr-mobility-improvement
[5] Draft P802.11bf_D4.0

## Slide 9: SP
Do you support to define in 11bn a RSSI measurement method based on a Control frame exchange initiated by a STA?
  Details of the Control frame exchange are TBD.

## Slide 10: Annex Sensing NDPA