## Slide 1: Follow-up on Peer-to-peer TWT for handling Coex
Date: 07-01-2024
Authors:

## Slide 2: Abstract
In this contribution, we discuss different modes of P2P TWT operation

## Slide 3: Introduction
Coex/P2P events for a STA can be scheduled or planned ahead of time.
  In such cases, the coex events can occur in a periodic manner with known periodicity parameters such as coex/P2P start time, duration, and interval.
During the coex/P2P events, the STA maybe unavailable for communication with some other STAs.
  For instance, during the coex/P2P window, a non-AP STA may not be available for infrastructure operation with the AP

## Slide 4: Background: Peer-to-Peer TWT
Peer-to-peer TWT was introduced in the baseline to indicate to the AP the periodic unavailability of the STA due to coex/P2P communication.
The baseline channel usage procedure was extended to facilitate peer-to-peer TWT.
  The non-AP STA sends a Channel Usage Request frame and includes a TWT element to request to set up a peer-to-peer TWT schedule with the AP
Once, a peer-to-peer TWT schedule is set up with the non-AP STA, the AP does not send any downlink frame to the non-AP STA and does not solicit uplink frame from the non-AP STA.

## Slide 5: Motivation
The STA that sets up periodic unavailability may also have other competing constraints that need to be accounted for.
There needs to be a mechanism that would allow prioritizing the delivery of certain QoS traffic over certain Coex unavailability SP.

## Slide 6: Modes of P2P TWT
The STA can indicate modes of P2P TWT—
  Complete Unavailability
  QoS-aware Unavailability
In the next few slides, we elaborate on these different modes of unavailability.

## Slide 7: Complete Unavailability
This mode is the legacy behavior
  During the indicated time window, the STA is expected to be unavailable completely.

## Slide 8: QoS-aware Unavailability (1)
Give the options to the STA to decide whether it wants to prioritize a high-priority DL infra traffic.
For example, a TXOP with a certain TID can be prioritized over unavailability SP

## Slide 9: QoS-aware Unavailability (2)
Similar can be done for existing QoS setup (SCS ID or RTWT)

## Slide 10: Summary
A STA negotiating a P2P TWT can indicate complete or QoS-aware unavailability as modes of unavailability during the SPs.
Such enhancements to the current P2P TWT negotiation would provide greater flexibility in handling the STA’s coex operation.

## Slide 11: References
[1] Liwen Chu, et.al., IEEE 802.11-23/1934r0, “In-device interference mitigation follow up”.
[2] Alfred Asterjadhi, et.al., IEEE 802.11-23/1964r0, “Coexistence Protocols for UHR”.
[3] Laurent Cariou, et.al., IEEE 802.11-23/2002r1, “In-device coexistence and interference follow – up”.
[4] Brian Hart, et.al., IEEE 802.11-23/2026r0, “Balanced In-Device Coexistence”.
[5] Rubayet Shafin, et.al., IEEE 802.11-24/509r1, “Thoughts on in-device coexistence and P2P for 11bn”
[6] Rubayet Shafin, et.al., IEEE 802.11-24/676r1, “Peer-to-peer TWT for Handling Co-ex/P2P”