## Slide 1: Signaling for MCS and UEQM in 11bn
Date: 2024-09-xx
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | Ensung.park@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Insik Jung |  |  |  | insik0618.jung@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Sanggook Kim |  | 10680 Treena St San Diego, CA 92131 |  | sanggook.kim@lge.com
September. 2024

## Slide 2: Introduction
In the previous meeting, for the Rate-vs-Range (RvR) enhancement the UEQM (i.e. unequal modulation) and New MCSs have been proposed.[1-8]
To support those features in the UHR transmission, the PHY signaling related to that should defined in the UHR PPDU newly.
In this contribution, we discuss how to indicate those schemes and related information.

## Slide 3: Signaling for MCS (1/2)
For reliable transmission and more accurate link adaptation, new MCSs were proposed in [6-8]
  The proposed new MCSs :
    QPSK-2/3, 16QAM-2/3, 16QAM-5/6, 256QAM-2/3
  Finer granularity of MCS can provide smoother goodput performance by filling out gaps between MCSs.
In 11be, by considering up to 4K QAM the MCS field was defined as 4 bits and this field does not have more room for signaling of additional MCSs.
Therefore, to indicate the MCS set including new MCSs, we should consider expanding the MCS field in the user field of UHR-SIG field.

## Slide 4: Signaling for MCS (2/2)
Assuming 4 new MCSs which seem to compensate enough for large gaps between MCSs are applied, an additional 1 bit may be enough to indicate the expanded MCS set.
  So, the MCS field in the UHR-SIG field can consist of 5 bits and is applied to both a non-MU-MIMO allocation and an MU-MIMO allocation in 11bn.
Herein, we can consider designing the UHR-SIG field that may inherit the structure of the EHT-SIG field.
  Thus, to expand the MCS field to 5 bits, we can take into account the following depending on whether UHR transmission is a non-MU-MIMO allocation or an MU-MIMO allocation.

## Slide 5: Non-MU-MIMO allocation
In the transmission for a non-MU-MIMO allocation, one reserved bit(i.e., B15) after the MCS field can be assigned for expanding the MCS field.
Bit | Subfield
B0–B10 | STA-ID
B11–B14 | MCS
B15 | Reserved
B16–B19 | NSS
B20 | Beamformed
B21 | Coding
User field format for a non-MU-MIMO allocation
Bit | Subfield
B0–B10 | STA-ID
B11–B15 | MCS
B16–B19 | NSS
B20 | Beamformed
B21 | Coding

## Slide 6: MU-MIMO allocation
On the other hand, the user field for an MU-MIMO allocation has no more room for expansion of the MCS field.
  So, we may consider revising some specific fields such as the Spatial Configuration field defined as 6-bit in 11be.
    Although it was designed to accommodate the MAX Nss of 16, Nss more than 8 is not used in the 11be spec.
  Therefore, we can consist of the Spatial Configuration field with 4 bits like 11ax and then, expand the MCS field by using the one bit from remaining bits, and also create one reserved bit which can be potentially used for indication of any new feature in 11bn. .
Bit | Subfield
B0–B10 | STA-ID
B11–B14 | MCS
B15 | Coding
B16–B21 | Spatial Configuration
User field format for a MU-MIMO allocation
Bit | Subfield
B0–B10 | STA-ID
B11–B15 | MCS
B16 | Coding
B17–B20 | Spatial Configuration
B21 | Reserved

## Slide 7: Consideration for UEQM
As described in [1-5], the UEQM is considered in a specific transmission such as Multiple spatial stream transmission(i.e. MIMO) to improve the channel quality difference between spatial streams.
But, UEQM means the adaptation of one encoder and different QAM per spatial stream depending on the SINR of each spatial stream to be required.
Therefore, whether to support UEQM to 11bn transmissions can depend on the STA's capability.
  The UEQM field may be defined by considering the UHR PHY capabilities information and may consist of 1bit information.

## Slide 8: Signaling for UEQM (1/2)
Depending on the capability of UHR STA, it can be applied to 11bn transmissions, which can be defined through user-specific information of the UHR-SIG field.
Since UEQM may not yet be considered in MU-MIMO transmission, we focus on the information that is included in the user field for a non-MU-MIMO allocation.
For indicating UEQM, we can define a new field, for example, UEQM as 1 bit subfield, in the user field for a non-MU-MIMO allocation.

## Slide 9: Signaling for UEQM (2/2)
1 bit is required to indicate the UEQM, but as described in previous slides, there is no available bit in the user field for non-MU-MIMO allocation due to MCS expansion.
  Thus, we can consider revising the NSS subfield, similar to MCS field expansion in the user field for MU-MIMO allocation with same logic to reduce unnecessary field size.
  Considering that the support of Max Nss is equal to 8, the NSS subfield can be reconfigured with 3 bits.
  And then, the remaining 1 bit can be assigned for the UEQM field.
Bit | Subfield
B0–B10 | STA-ID
B11–B15 | MCS
B16–B19 | NSS
B20 | Beamformed
B21 | Coding
Bit | Subfield
B0–B10 | STA-ID
B11–B15 | MCS
B16–B18 | NSS
B19 | UEQM
B20 | Beamformed
B21 | Coding

## Slide 10: Indication of QAM combination(1/3)
In addition, to apply the UEQM on 11bn transmissions, the information of QAM combination for the UEQM as described in[5,6] should be indicated to STA supporting this transmission.
  Although the complete QAM combinations require further discussion, it does not seem necessary to define all combinations.
  And, it is better to keep the same size of the user field as defined in EHT when we design the signaling of this information.
  For the example, we assume the following combination for multiple spatial streams for UEQM in this contribution.
Total Nss | 1st ss | 2nd ss | 3rd ss | 4th ss
2ss | M | M-1 |  | 
 | M | M-2 |  | 
3ss | M | M | M-1 | 
 | M | M | M-2 | 
 | M | M-1 | M-2 | 
4ss | M | M | M | M-1
 | M | M | M | M-2
 | M | M | M-1 | M-2

## Slide 11: Indication of QAM combination(2/3)
Since this information is only used when UEQM is applied, that can be indicated by reusing the conventional field depending on the use of UEQM.
  For that, we can take into account the following methods.
    Option 1: indicated by using the NSS field
      For example, when UEQM is used, the contents of the NSS field are reconfigured as follows.
        M (modulation for the first stream ) is indicated by the MCS field
        Then, the contents of the NSS field can be configured as bellow.
Value of NSS field | Information
0 | 1st ss = M , 2nd ss = M-1
1 | 1st ss = M , 2nd ss = M-2
2 | 1st ss = M , 2nd ss = M, 3rd ss =M-1
…… | ……

## Slide 12: Indication of QAM combination(3/3)
    Option 2 : indicated by using the MCS field
      For example, when UEQM is used, the contents of the MCS field are reconfigured differently according to NSS.
        The number of SS is indicated by the NSS field.
        Depending on the NSS, the contents of the MCS field indicate the different information.
          When NSS = 2, the MCS field can configured below.
We can indicate this information without any signaling overhead in the user field by considering the described options.
  So, we can retain the size of the user field as defined in EHT.
Value of MCS field | Information
0 | 1st ss = MCS1 , 2nd ss = MCS0
1 | 1st ss = MCS3 , 2nd ss = MCS1
2 | 1st ss = MCS3 , 2nd ss = MCS0
…… | ……

## Slide 13: Summary
In this contribution, we show the design way of the user field to indicate the new features (i.e., UEQM and expanded MCS set).
  To support more MCSs, the MCS field in the User field should be expanded to 5 bits.
  For an indication of UEQM, we can add the UEQM field defined 1bit in the user field for non-MU-MIMO allocation.
  Considering that the supported maximum NSS is 8, the NSS field and spatial stream configuration field can be modified.
    After revising this, a remaining bit can be used to indicate UEQM or expand MCS.
  The QAM combination for UEQM can be indicated by reusing the conventional subfield such as the NSS field or the MCS field.

## Slide 14: Straw poll 1
Do you agree to change the assigned bits for NSS field and Spatial configuration field by considering the maximum NSS is 8 in 11bn?
  For non-MU-MIMO allocation of the UHR SIG field
    NSS field consists of 3 bits in the user field
  For MU-MIMO allocation of the UHR SIG field
    Spatial configuration field consists of 4 bits in the user field.

## Slide 15: Straw poll 2
Do you agree to include the following text to the 11bn SFD?
  The MCS field in the user field of UHR-SIG field consists of 5 bits.
    The B11 ~ B15 of the UHR-SIG field is assigned for the MCS field
    The configuration of MCS field is TBD.

## Slide 16: Reference
[1] 11-24-0117-01 Improved Tx Beamforming with UEQM
[2] 11-24-0016-01-00bn-uhr-mimo-rvr-enhancement-with-unequal-modulation
[3] 11-24-0113-01-00bn-unequal-modulation-in-mimo-txbf-in-11bn
[4] 11-24-0176-01-00bn-unequal-modulation-over-spatial-streams
[5] 11-24-0474-00-00bn-UHR unequal modulation pattern and new MCS
[6] 11-24-0498-00-00bn-Unequal Modulation in MIMO TxBF and New MCS for 11bn
[7] 11-24-0469-00-00bn-New MCSs for 11bn
[8] 11-24-0433-00 Analysis on UEQM and UEQ MCS