## Slide 1: Dynamic Power Saving in MLO
Date: 2024-08-30
Authors:

## Slide 2: Introduction
Many contributions related to power saving have been presented
Power saving of (mobile) AP is scope of 11bn
  PAR: “This amendment provides a mechanism to reduce power consumption for Access Points (APs) (including mobile APs) and improved Peer-to-Peer (P2P) operation compared to the Extremely High Throughput MAC/PHY operation.”
In this submission, we would like to discuss PS features that should be considered in 11bn

## Slide 3: Our View on 11bn Power saving
Enhancement of traditional performance (data rate, etc.) of Wi-Fi is slowing down as generations go by, and it seems sufficient to support the use case currently mainly used
  It is time not only to improve traditional performance, but also to improve performance compared to power consumption and user experience performance
As a product/chipset vendor, power saving has higher customer demand than discussed in the standard, so we have implemented various low power technologies as standard/non-standard to satisfy it
  At 11bn, we hope to improve existing 11ax/be technologies in terms of performance compared to power consumption

## Slide 4: Our Observations
- In areas where Wi-Fi infra is not sufficient, demand for mobile APs is still high
- Power consumption will be severe if a smart phone operates Wi-Fi 7 mobile AP due to the requirement to operate as MLMR
- As a result of internal measurement, MLO consumes more than 25% of power compared to single link for 1 bit transmission
- If the payload is small, transmitting in a narrow BW & small Nss
can reduce power consumption per bit, and if the payload is large,
reducing transmission time in a wide BW & large Nss can reduce
power consumption per bit
Wide BW & Large NSS
Narrow BW & Small NSS
Payload
Power Consumption
per bit

## Slide 5: Power saving for MLO/Mobile AP
The power consumption of Multi Link Operation has already been pointed out several times, and various techniques have been introduced [1][2][3]
In this material, we would like to focus on the power saving of MLO from the perspective of mobile AP
  Power consumption reduction technology through switching between LCM and HCM should be developed from a multi-link perspective
  The performance of the associated MLO capable STAs should not be degraded

## Slide 6: Background: Dynamic Power Saving and MLO
AP’s operation in DPS
  Based on what we have discussed so far
    LCM: Lower Capacity Mode (BW = 20 MHz, # of SS = 1)
    HCM: Higher Capacity Mode (BW ≥ 20 MHz, # of SS ≥ 1)
ICF
AP STA
Non-AP STA
HCM
LCM
PPDU
ICR
BA
LCM
Extension to MLO (Assumption)
  Mode per link may be independent
ICF
AP STA @ 2.4 GHz
Non-AP STA @ 2.4 GHz
HCM
LCM
PPDU
ICR
BA
LCM
Doze
AP STA @ 5 GHz
AP MLD
Non-AP STA @ 5 GHz
Non-AP MLD

## Slide 7: Dynamic Power Saving and MLO
Cross-link DPS
  Usually, the mobile AP supports 2.4G/5G dual band
    2.4GHz: It can be used as a coverage link and always maintains the Awake state. Even if it is operated on HCM, the data rate is limited
    5GHz: It can be used as a performance link and is switched to Awake only when high-data rate is required
  Check the resource required for data transmission through ICF/ICR on 2.4 GHz and determine the optimal link
  Complete the data transmission using the minimum power at the specified link
ICF
AP STA @ 2.4 GHz
Non-AP STA @ 2.4 GHz
ICR
BA
LCM
Doze
AP STA @ 5 GHz
AP MLD
Non-AP STA @ 5 GHz
Non-AP MLD
PPDU
HCM
Doze

## Slide 8: Energy Consumption Analysis
Option 1 | Option 2 | Option 3
AP Energy Consumption (Normalized based on option 1) |  | 
RX energy per bit: 1 LCM operating power: 1 | RX energy per bit: 0.38 (for large payload) / 1.12 (for small payload) LCM operating power: 1 | RX energy per bit: 0.40 (for large payload) / 1.58 (for small payload) LCM operating power: 1.48
AP
ICF
LCM
Doze
HCM
ICR
Data
BA
ICF
Doze
LCM
HCM
ICR
Data
BA
ICF
LCM
Doze
HCM
ICR
Data
BA
The transmission method of optimal energy efficiency varies depending on various environments such as payload size, signal strength, etc…
2.4 GHz
STA
5/6 GHz
MLO
2.4 GHz
5/6 GHz
MLO
2.4 GHz
5/6 GHz
MLO
AP
STA
AP
STA
AP
STA
* TX Power analysis is excluded

## Slide 9: Conclusion
In this submission, a technology capable of reducing power consumption of an AP operating as an MLO has been proposed
  Optimizing DPS in MLO can reduce energy consumption per bit while maintaining performance compared to operating DPS in individual links

## Slide 10: Straw poll
Do you agree to add following sentence in 11bn SFD:
- TGbn defines a power save mode for a STA that is a UHR Mobile AP or a UHR non-AP STA wherein the STA may transition from a lower capability mode to a higher capability mode upon reception of an initial control frame
  : Lower capability mode (e.g., 20 MHz BW, one SS, limited data rates, PPDU format)
  : Higher capability mode (e.g., operating BW, NSS and MCSs, with at least one higher capability than that in the lower power capability mode)
  : Initial Control frame is TBD
  : Whether that applies for a non-mobile AP is TBD
  : Link for which ICF is transmitted in the LCM and link for which Data frame is transmitted in the HCM may be different

## Slide 11: Reference
[1] 24/602 Multi link Power Management for MLO
[2] 23/1922 Multi Link SM Power Save Mode
[3] 24/715 Multi-Link SM Power Save Mode Follow Up