## Slide 1: Bluetooth SIG September 2024 Update
Date: 2024-09-10
Authors:
Notes: September 2012

## Slide 2: Abstract
This is an update on Bluetooth SIG actions and plans for sharing the 5 and 6 GHz bands with incumbents and unlicensed/license-exempt devices.
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 2

## Slide 3: Agenda
Bluetooth Sharing Goals
The Overall Bluetooth SIG Plan
Recent Actions
ETSI BRAN #125 (September) outcomes
Recent actions
Bluetooth Next Steps

## Slide 4: Bluetooth Sharing Goals
The Bluetooth SIG recognizes the contribution the Wi-Fi industry has made in opening the 6 GHz band for unlicensed/license-exempt sharing to grow the technology
Today, Bluetooth technology needs to secure its future growth
  The 83.5 MHz of the 2.4 GHz band is not a sufficient hedge against congestion or sufficient to support innovation
Bluetooth and Wi-Fi successfully shared the 2.4 GHz band for many years
  Unfortunately, most of 5 GHz is not viable for Bluetooth, i.e., indoor restrictions and DFS
  5.8 GHz band available in many regulatory domains
  Narrowband technology already deployed in U-NII-3
The 6 GHz band has room for Bluetooth and Wi-Fi, and there is time to develop optimal sharing mechanisms
We will work closely with the Wi-Fi industry in IEEE 802 and ETSI BRAN to enable Bluetooth sharing these band equitably

## Slide 5: The Overall Bluetooth SIG Plan
Leverage the Bluetooth SIG Regulatory Expert Group to drive regulatory and standards changes just as Wi-Fi did
  Including companies with both Wi-Fi and Bluetooth businesses
  Collaborate with Wi-Fi industry to drive needed changes
Work with SDOs to develop optimum spectrum sharing methods and advance regulatory/standards to codify them as required
  ETSI BRAN New Work Item adopted in September 2023 (BRAN #120)
  Draft text for EN 303 687 (Clause 4) to be proposed in September 2024 (BRAN #125)
  FCC Petition for Rulemaking needed to increase PSD limit for all VLP devices
    -5 dBm/MHz was “…a conservative initial approach for permitting VLP devices*”
The detailed plan can best be developed working together
*FCC 23-86 Second Report and Order paragraph 50

## Slide 6: The Overall Bluetooth SIG Plan [2]
Now that the FCC has completed the first round of VLP decisions, we are requesting another for narrowband sharing
  Chairwoman Rosenworcel said there will be a number of additional NPRMs
In August 2024 meeting, OET Deputy Chief suggested we bring a Petition for Rulemaking (PfR)
  Interference analysis, narrowband into incumbents needed
Bluetooth SIG is working to fulfill these requirements
  Wi-Fi also wants better VLP PSD limits
  Should we bring a combined petition?

## Slide 7: ETSI BRAN #125 Outcomes
A group of companies including Bluetooth SIG presented Narrow Band Equipment (NBE) Clause 4 changes for the EN 303 687 draft
Unfortunately, due to the lateness of the revised submission, one member required a 14-day waiting period so the document could not be “Accepted”
  Additionally, there were two TBDs the Chair said could not remain in the submission
  The group will resolve the TBDs and prepare a new submission for two weeks before the October meeting
This appeared to be the final hurdle for channel access
Other topics still in the works, e.g., EDT
Final editing with group consensus (100%) needs to be done before it is ready to begin the formal approval process

## Slide 8: ETSI BRAN New Work Item Provisions
(1) To develop a channel access mechanism for Narrowband Frequency Hopping equipment operation
(2) To develop mechanisms enabling LPI client-to-client operations in accordance with ECC/DEC/(20)01 and EC Decision 2021/1067 on 6 GHz WAS/RLANs
(3) To consider further development of FBE and LBE parameters for channel access mechanism
(4) To consider inclusion of new channelization to support next generation technologies (bandwidths exceeding 160 MHz, e. g. 320 MHz)

## Slide 9: Recent Actions
Bluetooth SIG preparing FCC Petition for Rulemaking
Bluetooth SIG contracting with experienced engineering firm specializing in the type of interference analysis the FCC PfR will require
  Selection process started
Draft text for EN 303 687 submitted to ETSI BRAN #125
  Channel access text delayed by request of one member

## Slide 10: Bluetooth Next Steps
Submitting the PfR to the FCC for narrowband operation inclusion in the 6 GHz rules in Q1 2025
  Interference analysis project will determine the final date of delivery to the FCC
  Can we coordinate with Wi-Fi on this PfR?
Participating in and contributing to the ETSI BRAN development of narrowband rules in 6 GHz (EN 303 687)
Further regulatory action needed on the 2.4 and 5.8 GHz bands globally
  Participation in ETSI ERM TG11 update of EN 300 328 and EN 300 440-1
    EU: EN 300 328 (2.4 GHz band) 5-year update mandated by the EC
    EN 300 440-1 (non-specific SRD for radio communication) must be updated due to lack of recent traction on a WI created Jan-2019, otherwise may be heading towards deprecation
  China: Bluetooth type-approval requirements discussion with MIIT needed