## Slide 1: Roaming with context transfer
Date: 2024-9-2
Authors:

## Slide 2: Background
TGbn defines a mechanism that enables a non-AP MLD to roam from one AP MLD to another AP MLD and the non-AP MLD remains in state 4 (see 11.3) during and after roaming to the other AP MLD
[Motion #2, [1] and [3-9]]
TGbn defines that when a non-AP MLD is in the process of roaming from the current AP MLD to a target AP MLD, the context related to the non-AP MLD is transferred to the target AP MLD such that it preserves the data exchange context for the non-AP MLD or the context can be renegotiated with the target AP MLD.
  Details on what context can be transferred and what context can be renegotiated are TBD.
  How to transfer the context is TBD.
[Motion #26, [1] and [7,8,42-47]]
As part of the seamless roaming procedure, during roaming,
  after the request/response exchange that initiates notification of the DS mapping change from the current AP MLD to the target AP MLD,
    The current AP MLD may deliver buffered DL data frames for a TBD period of time.
    The non-AP MLD may retrieve buffered DL data frames from the current AP MLD
    The non-AP MLD may send UL data to target AP MLD.
    It is assumed that the target AP MLD is able to deliver data frames to non-AP MLD after the DS mapping change
  The current AP MLD may forward DL data to the target AP MLD.
    When and how to initiate the forwarding of DL data is TBD
[Motion #27, [1] and [3, 7, 8, 42-48]]

## Slide 3: Association to both AP MLDs
For the UHR roaming, the group has agreed that after the request/response exchange,
  The current AP MLD may deliver buffered DL data frames for a TBD period of time.
  The non-AP MLD may retrieve buffered DL data frames from the current AP MLD
  The non-AP MLD may send UL data to the target AP MLD.
  It is assumed that the target AP MLD is able to deliver data frames to non-AP MLD after the DS mapping change
To execute data frames transmission with both AP MLDs in the TBD period, the non-AP MLD needs to associate to both the AP MLDs at the same time.
  Reassociation Request/Response exchange with the target AP MLD will happen before the non-AP MLD disconnects the current AP MLD.
  Suggest to set seamless roaming as an optional feature for sake of cost down at low end market.
  It is recommended to use Reassociation Request/Response exchange with the target AP MLD as the request/response exchange.
  After the request/response, the non-AP MLD has associations to both the AP MLDs.
  The STA(s) affiliated with the non-AP MLD that can be reached shall be indicated to the current AP MLD and target AP MLD respectively. The indication can be delivered by FT Request/Response or Reassociation Request/Response.
  The current AP MLD shall be notified when the non-AP MLD disconnects all the links.
  It should be also taken account for the case that the non-AP MLD decides to halt the roaming.

## Slide 4: TID-To-Link Mapping during roaming
  After the request/response exchange and before the roaming complete, some affiliated STA(s) of the non-AP MLD disconnect from the current AP MLD and link to the target AP MLD.
  If the non-default TID-To-Link Mapping is set,
  DL corresponding to the TID(s) mapped the those link(s) only can’t be delivered by the current AP MLD.
  The the others can’t be delivered by the target AP MLD.
  It’s recommended that the default TID-to-Link mapping is used during the period.

## Slide 5
The group has agreed that the current AP MLD may deliver DL data frames for a TBD period after the request/response exchange.
  It is reasonable that the end of the TBD period is the time that the non-AP MLD decides to leave the current AP MLD.
  2 options to start the DL data forwarding:
  Option 1: start the DL data forwarding right after the request/response. More time to forward data but the target AP MLD has to discard those transmitted successfully to the non-AP MLD during the TBD period.
  Option 2: start the DL data forwarding when the non-AP MLD decides to leave the current AP MLD. No extra effort for the network but the time is too limited for the data forwarding.
  Option 1 is better.
  Those to be discarded can be determined after the context is transferred.
When to start DL data forwarding

## Slide 6: How to do with buffered UL data
The group has agreed that the non-AP MLD may send UL data to target AP MLD after the request/response.
May the non-AP MLD send UL data to the current AP MLD after the request/response?
  It should be allowed, to maximize UL data rate so reduce UL transmission latency.
  How to coordinate between UL transmission to the current AP MLD and the UL transmission to the target AP MLD?
  Forwarding the buffered UL data in reordering buffer at the current AP MLD to the target MLD provides gains in terms of latency and wireless resource consumption.
  Similar with DL, it is good to start the buffered UL data forwarding right after the request/response exchange.
  The target AP MLD can pass up the UL data after the context is received.

## Slide 7: When to transfer the context
Context is needed for the target AP MLD to start data transmission
  The context should be delivered as early as possible. It’s recommended to do it right after the request/response.
A delta context is needed when the non-AP MLD decides to fully switch the target AP MLD, to reflect the data transmitted after the previous context transfer.
We propose that the non-AP MLD sends a Leaving Indication frame to the current AP MLD to
  Indicate its leaving
  trigger the delta context transfer, so that the delta context transferring and the non-AP MLD’s switching can be executed in parallel.
After receiving the forwarded DL/UL data and the delta context, the target AP MLD sets up the transmit queue, the Transmit Buffer Control, the Receive Reordering Buffer control.
  the data transmission can be continued after a switch delay or an indication from the non-AP MLD, without any loss.

## Slide 8: Halt from roaming
It’s possible that the non-AP MLD moves back and the current AP MLD’s signal is better before it decides to fully switch to the target AP MLD.
  We proposed to set a deadline to send the Leaving Indication frame. If the non-AP MLD does not send the frame before the deadline,
  The roaming procedure is halted.
  The setup links to the target AP MLD are teared down automatically.
  DS mapping change back to the current AP MLD.
  The target AP MLD forwards the received data to the current AP MLD.

## Slide 9: UHR Roaming

## Slide 10: Summary
In this contribution, we analyze the further requirements based on the passed motions on seamless roaming.
  Association to both AP MLDs
  Default TID-To-Link mapping
We propose to use Reassociation Request/Response to the target AP MLD as the request/response exchange that initiates notification of the DS mapping.
  Starts the data forwarding and context transferring right after that.
The STA(s) affiliated with the non-AP MLD that can be reached shall be indicated to the current AP MLD and target AP MLD respectively.
It’s proposed the non-AP MLD sends a Leaving Indication frame to the current AP MLD to
  Indicate its leaving
  Trigger the current AP MLD to transfer the delta context to the target AP MLD, so that the delta context transferring and the non-AP MLD’s switching can be executed in parallel.
A deadline is configured to the Leaving Indication frame.

## Slide 11: SP 1:
Do you agree to use the Reassociation Request/Response exchange with the target AP MLD to initiate notification of the DS mapping change from the current AP MLD to the target AP MLD in the seamless roaming procedure?

## Slide 12: SP 2:
Do you agree to use default TID-To-Link Mapping during the seamless roaming procedure?

## Slide 13: SP 3:
Do you agree that the STA(s) affiliated with the non-AP MLD that can be reached shall be indicated to the current AP MLD and target AP MLD respectively in the seamless roaming procedure?
  The indication is delivered in FT Request/Response and Reassociation Request/Response.

## Slide 14: SP 4:
Do you agree that in the seamless roaming procedure the non-AP MLD sends a Leaving Indication frame to the current AP MLD before a deadline for the following purposes?
  To indicate the leaving of the non-AP MLD
  To trigger the delta context transfer to the target AP MLD

## Slide 15: Reference
[1] 11-24-0171-06-00bn-tgbn-motions-list-part-1, Alfred Asterjadhi
[2] 11-24-0830-00-00bn-improve-roaming-between-mlds-follow-up, Po-Kai Huang
[3] 11-24-0349-01-00bn-enhanced-fast-bss-transition, Guogang Huang
[4] 11-24-0679-01-00bn-thoughts-on-functionality-and-security-architecture-for-uhr-seamless-roaming, Thomas Derham