## Slide 1: Discussion on DCM of DRU
Date: 2024-09-10
Authors:
Name | Affiliations | Address | Phone | email
Mengshi Hu | Huawei |  |  | humengshi@huawei.com
Ross Jian Yu |  |  |  | 
Ming Gan |  |  |  | 

## Slide 2: DRU and Its Power Gain
11bn supports the distributed tone RU (DRU) for TB PPDU transmissions, where the DRU is an RU consisting of subcarriers spreading across a certain bandwidth [1].
  Compared to the regular RU (RRU), the transmit power of a DRU transmitted by a STA can be boosted because of the lowered subcarrier density under the PSD constraint -1 dBm/MHz.
The following table shows the transmit power in the RRU case and the DRU case with different distribution bandwidths (DBWs).
RU Size | RRU | DRU (M below indicates the number of tones in each 13 subcarriers (1 MHz)) |  |  | 
 |  | DBW = 20 MHz | DBW = 40 MHz | DBW = 80 MHz | DBW = 160 MHz
26 | 2.08 | 10.14 (M=2) | 13.15 (M=1) | 13.15 (M=1) | 13.15 (M=1)
52 | 5.09 | 11.39 (M=3) | 13.15 (M=2) | 16.16 (M=1) | 16.16 (M=1)
106 | 8.18 | 11.47 (M=6) | 14.48 (M=3) | 16.24 (M=2) | 19.25 (M=1)
242 | 11.77 | N/A | 14.39 (M=7) | 16.82 (M=4) | 19.83 (M=2)
484 | 14.78 | N/A | N/A | 17.40 (M=7) | 19.83 (M=4)
996 | 17.91 | N/A | N/A | N/A | 20.53 (M=7)
Table 1 Maximum Transmit Power of RU (dBm)

## Slide 3: DCM
Dual carrier modulation (DCM) has been introduced in HE and EHT to enable a more robust transmission of an RU or MRU.
For RU or MRU sizes smaller than or equal to 996 tones, the DCM signal contains an original part and the corresponding duplicated part.
For RU or MRU sizes larger than 996 tones, DCM is performed on the segment parser output for each 80 MHz frequency subblock.
Fig. 1 DCM in the case of RU or MRU sizes ≤ 996
Fig. 2 DCM in the case of RU or MRU sizes ＞ 996 (e.g. 160 MHz)
NOTE 1: is the original part, and is the duplicated part.
NOTE 2: The subscripts and indicate the lower and upper parts, respectively.

## Slide 4: DCM in DRU
Regarding the RRU case, DCM could provide 3 dB gain because of the duplication. However, things become different in the DRU case:
Due to the PSD limit in the DRU case, a large size DRU may lose power boosting gain compared to those smaller size DRUs within the same DBW.
For example, in the case of DBW = 20 MHz, the number of subcarriers of a 52-tone DRU is 3/MHz, and the number of subcarriers of a 106-tone DRU is 6/MHz. This indicates that each subcarrier of a 106-tone DRU loses 3 dB gain compared to the subcarrier of a 52-tone DRU.
Therefore, if DCM is applied to the above 106-tone DRU, the performance is not enhanced (3 dB gain and 3 dB loss), and more subcarriers are occupied, compared to using the above 52-tone DRU.
RU Size | RRU | DRU (DBW = 20 MHz)
52 | 5.09 dBm | 11.39 (M=3, 3 subcarriers per 1 MHz)
106 | 8.18 dBm | 11.47 (M=6, 6 subcarriers per 1 MHz)
Table 2 Maximum Transmit Power of RU

## Slide 5: DCM Crossing Two DBWs
From the above example, it can be noticed that in the case of DRU, the conventional DCM may not be as useful as in the RRU case, because of the additional loss of power boosting gain.
To enable an robust transmission, DCM crossing two DBWs is suggested, where the size of these two DBWs are the same, and the same relative subcarrier indices are used.
An example is shown below in the existing DBW case (DBW 20 + 20 + 40 within an 80 MHz):
Since the DCM crossing two DBWs will not affected by the power boosting gain, the 3 dB combining gain can be totally achieved.
Benefit: The performance in these two 20 MHz DBWs could be further enhanced.
DBW20
DBW20
DBW40
Select a DRU ()
A duplication ()
Fig. 3 DCM Crossing Two DBWs in the case of DBW 20 + 20

## Slide 6: Some Other Examples
If DBW 80 + 80 + 80 + 80 is allowed, then the following DCM crossing two DBWs can be defined:
If DBW 160 + 160 is allowed, then the following DCM crossing two DBWs can be defined:
DBW80
DBW80
A duplication ()
…
DBW160
DBW160
A duplication ()
Select a DRU ()
Select a DRU ()
Fig. 4 DCM Crossing Two DBWs in the case of DBW 80 + 80
Fig. 5 DCM Crossing Two DBWs in the case of DBW 160 + 160

## Slide 7: Benefits (1/2)
According to the previous discussion, the following DCM mode crossing two DBW is suggested:
The two DBWs are close to each other, and have the same size.
The selected DRUs in the two DBWs have the same relative subcarrier indices. One is the original part, and the other is the duplicated part.
The benefits on allowing the above configuration is obvious:
May further enhance the performance of the following DRUs (see the red color) in the case of DBW 20 + 20, 80 + 80, 160 + 160, etc.
NRU | DRU |  |  | 
 | DBW = 20 MHz | DBW = 40 MHz | DBW = 80 MHz | DBW = 160 MHz
26 | 8.06 | 11.07 | 11.07 | 11.07
52 | 6.3 | 8.06 | 11.07 | 11.07
106 | 3.29 | 6.3 | 8.06 | 11.07
242 | N/A | 2.62 | 5.05 | 8.06
484 | N/A | N/A | 2.62 | 5.05
996 | N/A | N/A | N/A | 2.62
Table 3 Power Gain Compared to RRU Case (dB)

## Slide 8: Benefits (2/2)
After the DCM crossing two DBWs, the following performance could be achieved (see the blue color, combining gain):
It is essential to enhance the performance of existing large size DRUs because their power gain cannot reach or be close to 6 dB (the power gap between the AP and STA).
NRU | DRU |  |  | 
 | DBW = 20 MHz | DBW = 40 MHz | DBW = 80 MHz | DBW = 160 MHz
26 | 8.06 | 11.07 | 11.07 | 11.07
52 | 6.3 | 8.06 | 11.07 | 11.07
106 | 3.29 + 3 | 6.3 | 8.06 | 11.07
242 | N/A | 2.62 + 3 | 5.05 + 3 | 8.06
484 | N/A | N/A | 2.62 + 3 | 5.05 + 3
996 | N/A | N/A | N/A | 2.62 + 3
Table 4 Gain Compared to RRU Case (dB)
Note that after the DCM implementation, the needed subcarriers are doubled. However, this will not affect the existing DBW structure:
The duplicated part still followings the same tone plan within its DBW.
DRU allocation will be not affected because of using the same relative indices.

## Slide 9: Summary
DCM crossing two DBWs (instead of using the conventional one within one DBW) was proposed.
The performance of DRUs under the existing DBW structures could be further improved (see the blue color).
The complexity is acceptable.
NRU | DRU |  |  | 
 | DBW = 20 MHz | DBW = 40 MHz | DBW = 80 MHz | DBW = 160 MHz
26 | 8.06 | 11.07 | 11.07 | 11.07
52 | 6.3 | 8.06 | 11.07 | 11.07
106 | 3.29 + 3 | 6.3 | 8.06 | 11.07
242 | N/A | 2.62 + 3 | 5.05 + 3 | 8.06
484 | N/A | N/A | 2.62 + 3 | 5.05 + 3
996 | N/A | N/A | N/A | 2.62 + 3
Table Gain Compared to RRU Case (dB)

## Slide 10
Do you agree to include the following into the 11bn SFD?
  DCM crossing two DBWs are allowed for the DRU transmission.
    Y
    N
    A
Straw Poll #1

## Slide 11
[1] Alfred Asterjadhi, TGbn Motions List - Part 1, 802.11 DCN 2024/0171r6
[2] Mengshi Hu, et al. Discussion on Distribution Bandwidth of DRU, 802.11 DCN 2024/801r1
References

## Slide 12
Example 1:
Example 2:
Appendix: Some Use Cases
DBW20
DBW20
DBW40
(P20)
STA A: 106-tone DRU 1 (A 20 MHz only STA, 3.29 dB)
STA B: 106-tone DRU 2 (May further use the DCM crossing two DBWs to enhance its performance, 6.29 dB)
STA C: 242-tone DRU 3 (2.62 dB)
STA D: 242-tone DRU 4 (2.62 dB)
DBW80
DBW80
…
STA A: 484-tone DRU 1 (2.62 dB)
STA B: 484-tone DRU 2 (May further use the DCM crossing two DBWs to enhance its performance, 5.62 dB)
Benefit: If the bottle neck is the performance instead of the available subcarriers, the proposed method could further achieve 3 dB gain, especially good for those large size DRUs affected by the low power boosting gain.