## Slide 1: R-TWT Sharing
Date: 2024-8-29
Authors:

## Slide 2: Introduction
As defined in 11be, Restricted Target Wake Time (R-TWT) provides enhanced medium protection and resource reservation for latency sensitive traffic delivery within a BSS
Several contributions, e.g., [1-7], have considered various aspects of coordinating R-TWT between multiple APs
In this contribution, we consider extending the existing R-TWT operation to enable sharing of R-TWT SPs with a neighbour (OBSS) AP

## Slide 3: Recap on R-TWT (11be)
Advertisement & protection
  AP (scheduling AP) advertises an R-TWT in its Beacon frame
  STAs in the BSS protect the start time of the R-TWT
Membership
  A STA (requesting STA) may request to join the R-TWT
  The AP negotiates and/or accepts the STA’s request
Operation
  AP contends at the start of the SP and obtains a TXOP to send to or trigger data from the STA
Termination
  The STA may terminate the membership by sending a TWT Teardown frame to the AP
AP
STA
Beacon
TWT resp
TWT req
Trigger
LL data
R-TWT SP
Advertise
Join
Accept
Operation

## Slide 4: Traffic during a neighbour AP’s R-TWT SP
An AP may expect traffic (e.g., periodic, LL, DL/UL) during a neighbour AP’s R-TWT SP
Option 1 – based on existing R-TWT operation
  The AP (AP2) schedules its own R-TWT SP at a different time from the neighbour AP (AP1) to avoid conflict
AP 1
STA 1
Trigger
LL data
R-TWT SP 1
AP 2
STA 2
Trigger
LL data
R-TWT SP 2
Beacon
TWT resp
TWT req
Expect periodic LL data
Observations:
Suitable if the delay is acceptable
Additional delays may occur during AP2’s contention
SP may be scheduled later if there are more SPs
Beacon

## Slide 5: Sharing of R-TWT SP
Option 2 – based on extending R-TWT operation
  The AP (AP2) requests the neighbour AP to share the R-TWT SP
  The neighbour AP (AP1) allocates time (e.g., C-TDMA) for the AP during its R-TWT SP
AP 1
STA 1
R-TWT SP 1
AP 2
STA 2
TXOP allocation
Beacon
TWT resp
TWT req
Expect periodic LL data
Observations:
Suitable if time to send is within existing R-TWT SP
Leverage AP1’s channel access (single contention)
Coexists well in dense environments
Notes:
AP2’s request reuses TWT req/resp protocol
TXOP allocation may be, e.g., an MU-RTS TXS
AP2 respects R-TWT SP1 start time protection
AP2 may schedule overlapping R-TWT SP
  But does not compete for SP1’s start time
AP1 may send MU-RTS/CTS to block hidden nodes
Beacon
(Optional) R-TWT SP 2 for protection from intra BSS STAs
Shared to AP2
MU-RTS
CTS
CTS
Frame exchange between AP 1 and STA 1
Frame exchange between AP 2 and STA 2

## Slide 6: Summary
We have considered allowing an AP to share its R-TWT SP with a neighbour AP as an extension of the existing R-TWT operation
This may be an option an AP can use to avoid delays for periodic LL DL/UL traffic

## Slide 7: Straw Poll 1
Do you support allowing an AP to request a neighbour AP to share its R-TWT SP?
  Y
  N
  A

## Slide 8: Straw Poll 2
Do you support allowing an AP to become a member of the R-TWT of a neighbour AP to be shared a portion of the R-TWT SP (e.g., C-TDMA)?
  Y
  N
  A

## Slide 9: References
[1] Yingqiao Quan (Spreadtrum), "Discussion on coordination of TWT", 24/1154r0, Jul, 2024
[2] Muhammad Kumail Haider (Meta), "R-TWT Multi-AP Coordination - Follow up", 24/407r0, Apr, 2024
[3] Liuming Lu (OPPO), "Coordinated R-TWT for Multi-AP scenarios - Follow up", 23/1952r3, Feb, 2024
[4] Jeongki Kim (Ofinno), "Enhanced R-TWT for UHR", 23/2084r1, Feb, 2024
[5] Laurent Cariou (Intel), "r-TWT for multi-AP follow up", 23/2022r1, Jan, 2024
[6] Rubayet Shafin (Samsung Research America), "Further considerations on coordinated TWT", 23/1932r3, Jan, 2024
[7] SunHee Baek (LG Electronics), "R-TWT Coordination in Multi-BSS", 23/1916r1, Jan, 2024