## Slide 1: Extension of TXOP-level IDC to Multi-Link Operation
Date: 2024-09-06
Authors:

## Slide 2: Introduction
The accommodation of other radio access technologies together has discussed under the term “In-Device Coexistence (IDC)”[1]-[10]
  At certain times or frequencies, it may not be possible for different radio access technologies to operate simultaneously
    2.4 GHz band: Bluetooth / BLE / P2P
    5 & 6 GHz bands: P2P, UWB, 3GPP radio (such as LAA / NR-U)
During the July F2F meeting, the motion
  To define a mechanism for a non-AP STA to report unavailability at TxOP level and define or reuse/update existing mechanism for a non-AP STA to report long term (periodic) unavailability
has been approved

## Slide 3: Backgrounds
Involving an unavailability into the TXOP operation[11]-[12]
  Peer STA (such as an AP) initiates a TXOP by sending an ICF
    ICF may either be a BSRP trigger frame or a MU-BAR trigger frame, both serving as solicitations for multi-station BA as per the ICR.
    The TXOP initiator sets the Duration field in the ICF MAC header to indicate the desired length of the TXOP in microseconds
    ICF includes the AIDs of STAs which is requested an ICR transmission
    The peer STA transmits a DL (MU) PPDU or requests an UL TB PPDU to ensure non-overlap with the STA's unavailable time and duration specified in the ICR
  Upon receiving an IDC, a STA sends an ICR containing the time and duration of its unavailability that coincides with or succeeds the TXOP

## Slide 4: Example of TXOP-Level IDC
IDC STA1
IDC
STA2
AP
(160 MHz BSS)
DL PPDU to STA1
(160 MHz, NSS = 2)
AP’s TXOP
SIFS
ICF
SIFS
ICR
SIFS
ICR
ICR
SIFS
Basic TF
SIFS
TB PPDU to AP
(80 MHz, NSS = 1)
SIFS
BA
SIFS
IDC operation (half bandwidth, NSS = 1)
Basic TF
SIFS
TB PPDU to AP
(160 MHz, NSS = 2)
SIFS
BA
Partial unavailability
Full unavailability
AP
STA1
STA2
DL MU PPDU
(160 MHz, NSS = 2)
SIFS
SIFS
ICR
M-BAICR
SIFS
IDC operation (fully unavailable)
AP can trigger TB PPDU from STA1 during a time period overlapping with the IDC operation reported by (M-)BA, taking into account the reduced capabilities
STAs performing IDC can inform the AP about their unavailability duration (or resulting capability reduction) within the AP's TXOP through (M-)BA

## Slide 5: Extension of TXOP-level IDC to Multi-Link Operation
Next-generation applications such as XR and AR require time-sensitive communication capabilities
  The delay bounds and tolerances are quite tight
Mobile phones are equipped with a wide range of connectivity features
  Location services can be accessed through Wi-Fi and Bluetooth technologies
  It is anticipated that Bluetooth operating at 5 GHz frequencies will be deployed to enable high data rates
When multiple heterogeneous connectivities occur simultaneously in the same frequency band, timely delivery of time-sensitive traffic becomes crucial
  Considering the given scenario, it is necessary to explore multi-link operations

## Slide 6: Extension of TXOP-level IDC to Multi-Link Operation
To enable this extension, ‘IDC Feedback Info’ field should incorporate IDC Capabilities for each link
  Radio Mode subfield determines whether the device operates in transmit or receive mode during the unavailable period
  Channel or bandwidth subfield specifies the subchannel accessible during the unavailable period
  Number of Spatial Stream subfield indicates the maximum number of spatial streams that can be utilized during the unavailable duration
  Service Specific Identifier subfield enables identification of the heterogenous technology type (such as BT, BLE, 5G, UWB, etc.) or P2P link to be utilized during the corresponding unavailable period
  Traffic information subfield encompasses details such as TID, AC, TSID, and other relevant parameters available during the corresponding IDC period.
  Preferred Link subfield symbolizes alternative links, potentially indicating a single link ID or encompassing a list of link IDs

## Slide 7: An Example of TXOP-Level IDC with Multi-Link Operation
AP MLD Link 1
ICF
SIFS
DL MU PPDU
SIFS
non-AP IDC MLD Link 2
non-AP IDC MLD
Link 1
Data Exchange between AP and STAs (other than non-AP IDC MLD)
ICR
M-BA
SIFS
IDC operation (fully unavailable on Link 1)
Basic TF
TB PPDU to AP
BA
AP MLD Link 2
SIFS
SIFS
Data Exchange between AP and non-AP IDC MLD
Preferred Link = 2
Frame Exchange between AP and non-AP IDC MLD
Basic TF
SIFS
TXOP (Link 1)
Notes: ICF / ICR 바꾸기

## Slide 8: Summary
TXOP-level IDC with multi-link operation
  Involves a STA responding a TXOP while needing to notify other STAs about its upcoming unavailability
  To accomplish this, the STA sends an ICF containing the desired TXOP duration and the AIDs of the STAs affected by the unavailability
  After receiving the ICF, the peer STA responds with an ICR acknowledging the unavailability and possibly offering alternative links
  This facilitates efficient coordination among STAs and maintains uninterrupted communication despite periods of unavailability

## Slide 9: References
[1] 11-23/1934r0 In-Device Interference Mitigation Follow Up (Liwen Chu, NXP)
[2] 11-23/1964r1 In-Device Coexistence (Alfred Asterjadhi, Qaulcomm)
[3] 11-23/2002r2 In-device Coexistence and P2P – follow-up (Laurent Cariou, Intel)
[4] 11-24/0094r0 Probe-Before-Talk and Unsolicited Unavailability Announcement for Co-ex Management (Qi Wang, Apple Inc.)
[5] 11-24/0420r2 Enabling Flexible Coexistence Operation (Guogang Huang, Huawei)
[6] 11-24/0543r1 Coexistence Protocols for UHR – Follow up (Shrief Helwa, Qualcomm)
[7] 11-24/0806r0 Multi-link In-device Coexistence Management (Juseong Moon, KNUT)
[8] 11-24/0834r0 Some Details on In-Device Coexistence (Insun Jang, LGE)
[9] 11-24/0856r0 Further Discussions on In-Device Coexistence (Jeongki Kim, Ofinno)
[10] 11-24/1108r1 Periodic IDC signaling for UHR Mobile AP (Hongwon Lee, LGE)
[11] 11-24/1226r0 Initial control frames and initial control response design (Laurent Cariou, Intel)
[12] 11-24/1247r0 ICF and ICR Design For Coex (Abdel Karim Ajami, Apple)

## Slide 10: Straw Poll 1
Do you agree to allow a TXOP responder to indicate preferred links during the unavailability interval in the ICR sent back to the TXOP initiator?
  Which ICR frame to use is TBD