## Slide 1: Credibility Criterion for TXOP Preemption
Date: 2024-09-04
Authors:

## Slide 2: Introduction
Latency reduction is one key objective as stated in UHR proposed PAR [1]
Several contributions [2]-[19] have made progress to support low latency medium access by constructing and furnishing the preemption mechanism
Among various branches, TXOP level preemption is a necessary branch towards achieving latency reduction
In this proposal, we focus on the TXOP level preemption, introducing a credibility criterion to assist the fair classification among streams and honest behavior between STAs to further promote the preemption feature

## Slide 3: Re-cap [19]: Preemptor VS Preemptee
Focusing on in BSS preemption
Preemptor:
  A STA who acquires the preempted transmission duration by initiating preemption
    The STA can be either AP or non-AP
  For traffic of AC2 that takes precedence over the current traffic of AC1, such as higher-priority traffic over lower-priority traffic
Preemptee:
  A non-AP STA who grants or accepts preemption by suspending the current traffic transmission or reception of AC1
    In the top view of traffic delivery, AP helps STAs forward traffic (either DL or UL), but does not generate traffic, only traffic intended for non-AP STA can be preempted
    The non-AP STA is either TXOP holder or TXOP responder
Exceptional scenario: Preempt DL/UL TXOP to transmit UL/DL higher-priority traffic
  Preemptor: EDCAF(AC2)
  Preemptee: EDCAF(AC1)

## Slide 4: Problem Statement
What is “low latency” stream [16]
  Static LL stream definition: any traffic in AC_VO ? or may be some with new UP/TID/AC?
  Dynamic LL definition: buffered frames of a stream for which certain “delivery delay” timer is expiring?
How to achieve approximate fairness between streams?
  Considering static LL definition, which potentially may cause “preemption request bloating” problem in highly loaded network scenario
  Considering dynamic LL definition, which potentially may let any stream to be classified as latency sensitive or delay sensitive stream
Besides, how to avoid possible misapplication among STAs?
  Considering the preemptor STAs may aggressively or frequently preempt other STA’s “legal” TXOP for its own benefits, which would cause bad user experience for the preemptee STA

## Slide 5: General Solution
Propose to introduce a credibility criterion to assist the fair classification among streams and honest behavior between STAs
  Each STA supporting preemption has a credibility parameter that reflects the quality/capability of its preemption behavior, in terms of how much of other STAs’ TXOP it has “borrowed” (by being preemptor) and how much it has managed to be “returned” (by being preemptee and “lend” TXOP to other STAs)
    credibility is a local parameter calculated at the potential preemptee side
  With the help of credibility parameter, the potential preemptee chooses whether to grant preemption
Potential effect: In order to establish positive credibility, STAs that borrowed/preempted TXOP would return it in another preemption occurrence, formulating virtuous circle
Benefit 1: Achieve approximate fairness between streams
  Considering static LL, limit the “preemption request” bloating, especially in highly loaded network scenario
  Considering dynamic LL, implicitly restrict LL classification at each STA’s (potential preemptor’s) local side
Benefit 2: Avoid possible misapplication among STAs
  Limit the situation where preemptor STAs aggressively or frequently preempt other STA’s “legal” TXOP for its own benefits, further limit bad user experience for the preemptee STA

## Slide 6: Preemption Response Decision Making
Potential preemptee sends preemption response, accept or reject preemption request
Given a “credibility threshold”
  If preemptor’s credibility is below such “credibility threshold”, then the potential preemptee may choose to reject its preemption request
  In case multiple preemptors initiate preemption request, the potential preemptee can determine how to respond according to their relative credibility
Preemption response decision may be made by considering credibility criterion together with the essential parameters in preemption request, such as
  AC or TID:
    To indicate (static) LL stream classification
  Delay information
    To indicate (dynamic) LL stream classification
  Request preemption start time
    Scheduled preemption
  Request preemption duration
    Airtime to be preempted/shared

## Slide 7: Credibility Criterion Calculation Method
Preemption duration can provide information regarding STA’s credibility
Credibility calculation during a given time window, sliding window or discrete window
  Method 1: Credibility of STA1 (at STA2) reflects the total returned duration minus the total borrowed duration to/from STA2
  Method 2: Credibility of STA1 (at STA2) reflects the total returned duration divided by the total borrowed duration to/from STA2
  At first time of preemption occurrence, such information may not be sufficient in reflecting credibility
    For a new joiner, additional design is needed (see follow-up discussion)
Preemption Occurrence | Preemptor | Preemptee | Preemption Duration | Credibility of STA1 (Method 1) | Credibility of STA2 (Method 1) | Credibility of STA1 (Method 2) | Credibility of STA2 (Method 2)
First time | STA1 | STA2 | t1 | -t1 | t1 | 0 | inf
Second time | STA1 | STA2 | t2 | -t1-t2 | t1+t2 | 0 | inf
Third time | STA2 | STA1 | t3 | -t1-t2+t3 | t1+t2-t3 | t3/(t1+t2) | (t1+t2)/t3
Example

## Slide 8: Include Rejection Reason in Preemption Response
Reason for Request Rejection | Meaning
REQUEST_DENIED_TRUST_ISSUE | Credibility criterion is not satisfied
REQUEST_DENIED_TX_CONTINUE | Continue own transmission due to sudden arrival of LL data
REQUEST_DENIED_CAPABILITIES_MISMATCH | Capability mismatch. For example, preemptor does not support credibility criterion calculation
SHARING_DENIED_RESOURCE_OVERLOAD | Request duration exceeds that can be offered
REQUEST_DENIED_IN_BSS | Release TXOP for contention based access
REQUEST_DENIED_MAX_STAS | Has reached the supported maximum number of preemption granted STAs
REQUEST_DENIED_MAX_AMOUNT | Has reached the supported maximum amount of sharing resources
By including rejection reason in preemption response, can
  Motivate preemptor to improve its credibility
  Limit the preemption frequency

## Slide 9: Determine Preemption Duration
Signaling to indicate the requested preemption duration/ actually used duration/ remaining duration
  Like TXOP return if actually used duration is smaller than requested duration, e.g. unicast CF-End
Event based to determine preemption ends
  Preemptee senses channel idle for certain time (e.g. PIFS time)
  Preemptee continues transmission w/o backoff

## Slide 10: Case 1: Preemptor is AP
Potential preemptee is a non-AP TXOP holder (STA1)
AP preempts UL TXOP to send DL LL data, either to some third STA (STA2) or STA1
  If to STA2: the preemption duration is counted into the credibility calculation
    either between {Preemptor AP, Preemptee STA1}
    or {Third STA STA2, Preemptee STA1}
  If to STA1: the preemption duration is not counted into the credibility calculation, since STA1 is involved in the preemption transmission

## Slide 11: Case 2: Preemptor is Non-AP
Preemptor is a non-AP third STA (STA2)
STA2 sends preemption request to AP
If AP is not TXOP holder, it may:
  Option1: forward the request to TXOP holder (STA1), STA1 makes the decision
  Option2: make the decision on behalf of STA1
  The preemption duration is counted
    either between {Preemptor STA2, Preemptee STA1}
    or {AP, Preemptee STA1}
If AP is TXOP holder
  The preemption duration may be counted between {Preemptor STA2, Preemptee STA1}

## Slide 12: Summary
In this contribution, we introduced a general credibility criterion for a preemption supporting STA, which reflects the quality/capability of its historical/future preemption behavior
  By being preemptor, how much of other STAs’ TXOP duration it has “borrowed”
  By being preemptee and “lend” TXOP to other STAs, how much duration it has managed to be “returned”
Benefit: To assist the fair classification among streams and honest behavior between STAs to further promote the preemption feature
  Benefit 1: Achieve approximate fairness between streams
  Benefit 2: Avoid possible misapplication among STAs
Notes: In this proposal, we focus on the TXOP level preemption, introducing a credibility criterion to assist the fair classification among streams and honest behavior between STAs to further promote the preemption feature

## Slide 13: Follow-up Discussion
For a new joiner, considering no credibility information about its preemption behavior may be available at the potential preemptee, additional design is needed
For a group of STAs, each STA’s local credibility information about other STAs’ preemption behavior can be distributed among the group for the group’s information
Whether such credibility criterion is STA-level or MLD-level can be further discussed

## Slide 14: Straw Poll 1
Do you agree in 11bn to introduce a certain credibility criterion reflecting participating STAs’ preemption behavior to help achieve approximate fairness between streams and avoid possible misapplication among STAs?
NOTE – The certain criterion is TBD

## Slide 15: References
11-23/480r3, UHR Proposed PAR
11-23-0018-01-0uhr-low-latency-support-in-uhr
11-23-0092-00-0uhr-preemption
11-23-1886-03-00bn-preemption-techniques-to-meet-low-latency-ll-targets
11-23-2076-03-00bn-multiple-channel-access-in-preemption-sequence
11-24-0091-01-00bn-enhanced-scheduling-method-for-low-latency-traffic-follow-up
11-24-0103-01-00bn-txop-level-preemption-for-low-latency-application-in-802-11bn
11-24-0131-00-00bn-signaling-of-preemption
11-24-0168-00-00bn-txop-preemption-in-11bn
11-24-0247-00-00bn-considerations-on-ll-preemption
11-24-0390-00-00bn-a-uniform-procedure-for-preemption
11-24-0391-00-00bn-legacy-sta-and-obss-issues-for-preemption
11-24-0416-00-00bn-target-sta-prioritization-in-edca-based-preemption-mechanisms-during-a-dl-txop
11-24-0431-01-00bn-signal-for-preemption-request
11-24-0442-03-00bn-latency-reduction-for-immediate-real-time-application-traffic-transmission
11-24-0470-00-00bn-rethinking-preemption
11-24-0804-00-00bn-the-transmission-of-preemption-request-frame
11-24-0852-01-00bn-timely-transmission-of-low-latency-traffic-with-reduced-preemption-occurance
11-24-1074-00-00bn-preemption-txop