## Slide 1: Proposal for DRU Tone Plan
Date: 2024-09-08
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Insik Jung |  |  |  | insik0618.jung@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Chenchen Liu | Huawei Technologies Co., Ltd | Huawei Base, Bantian, Shenzhen |  | liuchenchen1@huawei.com
Ross Jian Yu |  |  |  | ross.yujian@huawei.com
Ming Gan |  |  |  | ming.gan@huawei.com

## Slide 2: Overview
In this contribution, we propose DRU tone plans for 20 / 80 MHz

## Slide 3: 20 MHz DRU Tone Plan (1/2)
20 MHz DRU tone plans were discussed in [1,2]
  Tone plan in [1]
  Tone plan in [2]
    52 and 106 DRUs also have mirror symmetric property
  Detailed tone plans are shown in Appendix
 | PAPR | Power Boosting Gain | Channel Smoothing Complexity | Tone range | Mirror Symmetry
[1] “A” | Almost same | Both achieve the maximum gain | Not simple (different dist. patterns for 52 / 106 DRUs) | Within 242 RRU Boundary | No
[2] “B” |  |  | Simple thanks to mirror symmetry (different dist. patterns for 52 / 106 DRUs) |  | Yes
26-tone DRU i=1:9 | DRU1 [-120:9:-12, 6:9:114] | DRU2 [-116:9:-8, 10:9:118] | DRU3 [-118:9:-10, 8:9:116] | DRU4 [-114:9:-6, 12:9:120] | DRU5 [-112:9:-4, 5:9:113]
 | DRU6 [-119:9:-11, 7:9:115] | DRU7 [-115:9:-7, 11:9:119] | DRU8 [-117:9:-9, 9:9:117] | DRU9 [-113:9:-5, 4:9:112] | 
26-tone DRU i=1:9 | DRU1 [-120:9:-12, 6:9:114] | DRU2 [-115:9:-7, 11:9:119] | DRU3 [-118:9:-10, 8:9:116] | DRU4 [-113:9:-5, 4:9:112] | DRU5 [-117:9:-9, 9:9:117]
 | DRU6 [-112:9:-4, 5:9:113] | DRU7 [-116:9:-8, 10:9:118] | DRU8 [-119:9:-11, 7:9:115] | DRU9 [-114:9:-6, 12:9:120] | 

## Slide 4: 20 MHz DRU Tone Plan (2/2)
20 MHz DRU tone plans were discussed in [1,2] (cont.)
  “B” is implementation-friendly thanks to the mirror symmetric property
    Most of the previous Wi-Fi versions have mirror symmetric tone plans and if we make the DRU tone plan symmetric, we can use a similar approach for the implementation used in the previous Wi-Fi
    For PHY processing, we can only have information for some of the DRUs and we can use that information for their symmetric pair DRUs, e.g., channel smoothing for “B” can be simply performed even though there are different distribution patterns for the same size DRU
    In addition, if we design a new LTF sequence for DRU, we can design sequences specific for some of the DRUs and apply them to their symmetric pair DRUs
Hence, we propose “B” as a 20 MHz DRU tone plan in UHR

## Slide 5: 80 MHz DRU Tone Plan
80 MHz DRU tone plans were discussed in [1,3]
  Detailed tone plans are shown in Appendix
    Two tone plans have the same 242 / 484 DRUs while 52 / 106 DRUs are different
  In terms of the PAPR and channel smoothing, “D” is a better choice
We propose “D” as a 80 MHz DRU tone plan in UHR
 | PAPR | Power Boosting Gain | Channel Smoothing Complexity | False Alarm Performance for Packet Detection
[1] “C” | Relatively higher for small DRUs | Both achieve the maximum gain | Simple (consistent dist. Pattern) | No false PD issue
[3] “D” | Low (similar to RRU) |  | Simpler (consistent dist. pattern and simpler pattern for small DRUs) | 

## Slide 6: Summary
We have considered various factors to determine a better tone plan for 20 / 80 MHz
Finally, we have proposed DRU tone plans for 20 / 80 MHz

## Slide 7: Straw Poll #1
Do you agree to add the following text to the TGbn SFD?
  Data and pilot subcarrier indices for DRUs in a 20 MHz UHR PPDU are defined in the following table
Y/N/A: //
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in a 20 MHz UHR PPDU |  |  |  |  | 
DRU type | DRU index and subcarrier range |  |  |  | 
26-tone DRU i=1:9 | DRU1 [-120:9:-12, 6:9:114] | DRU2 [-115:9:-7, 11:9:119] | DRU3 [-118:9:-10, 8:9:116] | DRU4 [-113:9:-5, 4:9:112] | DRU5 [-117:9:-9, 9:9:117]
 | DRU6 [-112:9:-4, 5:9:113] | DRU7 [-116:9:-8, 10:9:118] | DRU8 [-119:9:-11, 7:9:115] | DRU9 [-114:9:-6, 12:9:120] | 
52-tone DRU i=1:4 | DRU1 26-tone [DRU1, DRU2] |  | DRU2 26-tone [DRU3, DRU4] |  | 
 | DRU3 26-tone [DRU6, DRU7] |  | DRU4 26-tone [DRU8, DRU9] |  | 
106-tone DRU i=1:2 | DRU1 26-tone [DRU1~4], [-3, 2] |  | DRU2 26-tone [DRU6~9], [-2, 3] |  | 

## Slide 8: Straw Poll #2
Do you agree to add the following text to the TGbn SFD?
  Data and pilot subcarrier indices for DRUs in a 80 MHz UHR PPDU are defined in the following tables
52-tone DRU i=1:16 | DRU1 [-495:56:-271, -479:56:-255, -455:56:-287, -239:56:-71, -215:56:-47, -199:56:-31, 17:56:241, 33:56:257, 57:56:225, 273:56:441, 297:56:465, 313:56:481] | DRU2 [-487:56:-263, -471:56:-247, -447:56:-279, -231:56:-63, -207:56:-39, -191:56:-23, 25:56:249, 41:56:265, 65:56:233, 281:56:449, 305:56:473, 321:56:489] | DRU3 [-491:56:-267, -475:56:-251, -451:56:-283, -235:56:-67, -211:56:-43, -195:56:-27, 21:56:245, 37:56:261, 61:56:229, 277:56:445, 301:56:469, 317:56:485] | DRU4 [-483:56:-259, -467:56:-243, -443:56:-275, -227:56:-59, -203:56:-35, -187:56:-19, 29:56:253, 45:56:269, 69:56:237, 285:56:453, 309:56:477, 325:56:493]
 | DRU5 [-489:56:-265, -473:56:-249, -449:56:-281, -233:56:-65, -209:56:-41, -193:56:-25, 23:56:247, 39:56:263, 63:56:231, 279:56:447, 303:56:471, 319:56:487] | DRU6 [-481:56:-257, -465:56:-241, -441:56:-273, -225:56:-57, -201:56:-33, -185:56:-17, 31:56:255, 47:56:271, 71:56:239, 287:56:455, 311:56:479, 327:56:495] | DRU7 [-493:56:-269, -477:56:-253, -453:56:-285, -237:56:-69, -213:56:-45, -197:56:-29, 19:56:243, 35:56:259, 59:56:227, 275:56:443, 299:56:467, 315:56:483] | DRU8 [-485:56:-261, -469:56:-245, -445:56:-277, -229:56:-61, -205:56:-37, -189:56:-21, 27:56:251, 43:56:267, 67:56:235, 283:56:451, 307:56:475, 323:56:491]
 | DRU9 [-494:56:-270, -478:56:-254, -454:56:-286, -238:56:-70, -214:56:-46, -198:56:-30, 18:56:242, 34:56:258, 58:56:226, 274:56:442, 298:56:466, 314:56:482] | DRU10 [-486:56:-262, -470:56:-246, -446:56:-278, -230:56:-62, -206:56:-38, -190:56:-22, 26:56:250, 42:56:266, 66:56:234, 282:56:450, 306:56:474, 322:56:490] | DRU11 [-490:56:-266, -474:56:-250, -450:56:-282, -234:56:-66, -210:56:-42, -194:56:-26, 22:56:246, 38:56:262, 62:56:230, 278:56:446, 302:56:470, 318:56:486] | DRU12 [-482:56:-258, -466:56:-242, -442:56:-274, -226:56:-58, -202:56:-34, -186:56:-18, 30:56:254, 46:56:270, 70:56:238, 286:56:454, 310:56:478, 326:56:494]
 | DRU13 [-488:56:-264, -472:56:-248, -448:56:-280, -232:56:-64, -208:56:-40, -192:56:-24, 24:56:248, 40:56:264, 64:56:232, 280:56:448, 304:56:472, 320:56:488] | DRU14 [-480:56:-256, -464:56:-240, -440:56:-272, -224:56:-56, -200:56:-32, -184:56:-16, 32:56:256, 48:56:272, 72:56:240, 288:56:456, 312:56:480, 328:56:496] | DRU15 [-492:56:-268, -476:56:-252, -452:56:-284, -236:56:-68, -212:56:-44, -196:56:-28, 20:56:244, 36:56:260, 60:56:228, 276:56:444, 300:56:468, 316:56:484] | DRU16 [-484:56:-260, -468:56:-244, -444:56:-276, -228:56:-60, -204:56:-36, -188:56:-20, 28:56:252, 44:56:268, 68:56:236, 284:56:452, 308:56:476, 324:56:492]
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in a 80 MHz UHR TB PPDU | 
DRU type | DRU index and subcarrier range

## Slide 9: Straw Poll #2
Y/N/A: //
106-tone DRU i=1:8 | DRU1 [52-tone DRU1, 52-tone DRU2, -463, 457] | DRU2 [52-tone DRU3, 52-tone DRU4, -459, 461] | DRU3 [52-tone DRU5, 52-tone DRU6, -457, 463] | DRU4 [52-tone DRU7, 52-tone DRU8, -461, 459]
 | DRU5 [52-tone DRU9, 52-tone DRU10, -462, 458] | DRU6 [52-tone DRU11, 52-tone DRU12, -458, 462] | DRU7 [52-tone DRU13, 52-tone DRU14, -456, 464] | DRU8 [52-tone DRU15, 52-tone DRU16, -460, 460]
242-tone DRU i=1:4 | DRU1 [-499:4:-19, 17:4:497] |  | DRU2 [-497:4:-17, 19:4:499] | 
 | DRU3 [-498:4:-18, 18:4:498] |  | DRU4 [-496:4:-16, 20:4:500] | 
484-tone DRU i=1:2 | DRU1 [-499:2:-17, 17:2:499] |  | DRU2 [-498:2:-16, 18:2:500] | 
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in a 80 MHz UHR TB PPDU | 
DRU type | DRU index and subcarrier range

## Slide 10: References
[1] 11-24-0468-02-00bn-dru-tone-plan-for-11bn
[2] 11-24-1096-00-00bn-mirror-symmetric-20-mhz-dru-tone-plan-within-242-rru-boundary
[3] 11-24-1465-01-00bn-updated-proposal-for-80mhz-dru-tone-plan

## Slide 11: Appendix (1/5)
20 MHz DRU tone plan in [1]
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in a 20 MHz UHR PPDU |  |  |  |  | 
DRU type | DRU index and subcarrier range |  |  |  | 
26-tone DRU i=1:9 | DRU1 [-120:9:-12, 6:9:114] | DRU2 [-116:9:-8, 10:9:118] | DRU3 [-118:9:-10, 8:9:116] | DRU4 [-114:9:-6, 12:9:120] | DRU5 [-112:9:-4, 5:9:113]
 | DRU6 [-119:9:-11, 7:9:115] | DRU7 [-115:9:-7, 11:9:119] | DRU8 [-117:9:-9, 9:9:117] | DRU9 [-113:9:-5, 4:9:112] | 
52-tone DRU i=1:4 | DRU1 26-tone [DRU1, DRU2] |  | DRU2 26-tone [DRU3, DRU4] |  | 
 | DRU3 26-tone [DRU6, DRU7] |  | DRU4 26-tone [DRU8, DRU9] |  | 
106-tone DRU i=1:2 | DRU1 26-tone [DRU1~4], [-3, 3] |  | DRU2 26-tone [DRU6~9], [-2, 2] |  | 

## Slide 12: Appendix (2/5)
20 MHz DRU tone plan in [2]
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in a 20 MHz UHR PPDU |  |  |  |  | 
DRU type | DRU index and subcarrier range |  |  |  | 
26-tone DRU i=1:9 | DRU1 [-120:9:-12, 6:9:114] | DRU2 [-115:9:-7, 11:9:119] | DRU3 [-118:9:-10, 8:9:116] | DRU4 [-113:9:-5, 4:9:112] | DRU5 [-117:9:-9, 9:9:117]
 | DRU6 [-112:9:-4, 5:9:113] | DRU7 [-116:9:-8, 10:9:118] | DRU8 [-119:9:-11, 7:9:115] | DRU9 [-114:9:-6, 12:9:120] | 
52-tone DRU i=1:4 | DRU1 26-tone [DRU1, DRU2] |  | DRU2 26-tone [DRU3, DRU4] |  | 
 | DRU3 26-tone [DRU6, DRU7] |  | DRU4 26-tone [DRU8, DRU9] |  | 
106-tone DRU i=1:2 | DRU1 26-tone [DRU1~4], [-3, 2] |  | DRU2 26-tone [DRU6~9], [-2, 3] |  | 

## Slide 13: Appendix (3/5)
80 MHz tone plan in [1]
52-tone DRU i=1:16 | DRU1 [-483:36:-51, 17:36:449],[-467:36:-35, 33:36:465] | DRU2 [-475:36:-43, 25:36:457],[-459:36:-27, 41:36:473] | DRU3 [-479:36:-47, 21:36:453],[-463:36:-31, 37:36:469] | DRU4 [-471:36:-39, 29:36:461],[-455:36:-23, 45:36:477]
 | DRU5 [-477:36:-45, 23:36:455],[-461:36:-29, 39:36:471] | DRU6 [-469:36:-37, 31:36:463],[-453:36:-21, 47:36:479] | DRU7 [-481:36:-49, 19:36:451],[-465:36:-33, 35:36:467] | DRU8 [-473:36:-41, 27:36:459],[-457:36:-25, 43:36:475]
 | DRU9 [-482:36:-50, 18:36:450],[-466:36:-34, 34:36:466] | DRU10 [-474:36:-42, 26:36:458],[-458:36:-26, 42:36:474] | DRU11 [-478:36:-46, 22:36:454],[-462:36:-30, 38:36:470] | DRU12 [-470:36:-38, 30:36:462],[-454:36:-22, 46:36:478]
 | DRU13 [-476:36:-44, 24:36:456],[-460:36:-28, 40:36:472] | DRU14 [-468:36:-36, 32:36:464],[-452:36:-20,48:36:480] | DRU15 [-480:36:-48, 20:36:452],[-464:36:-32, 36:36:468] | DRU16 [-472:36:-40, 28:36:460],[-456:36:-24, 44:36:476]
106-tone DRU i=1:8 | DRU1 52-tone [DRU1~2], [-495, 485] | DRU2 52-tone [DRU3~4],[-491, 489] | DRU3 52-tone [DRU5~6],[-489, 491] | DRU4 52-tone [DRU7~8],[-493, 487]
 | DRU5 52-tone [DRU9~10],[-494, 486] | DRU6 52-tone [DRU11~12],[-490,490] | DRU7 52-tone [DRU13~14],[-488,492] | DRU8 52-tone [DRU15~16],[-492,488]
242-tone DRU i=1:4 | DRU1 [-499:4:-19, 17:4:497] |  | DRU2 [-497:4:-17, 19:4:499] | 
 | DRU3 [-498:4:-18, 18:4:498] |  | DRU4 [-496:4:-16, 20:4:500] | 
484-tone DRU i=1:2 | DRU1 [-499:2:-17, 17:2:499] |  | DRU2 [-498:2:-16, 18:2:500] | 
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in a 80 MHz UHR TB PPDU | 
DRU type | DRU index and subcarrier range

## Slide 14: Appendix (4/5)
80 MHz tone plan in [3]
52-tone DRU i=1:16 | DRU1 [-495:56:-271, -479:56:-255, -455:56:-287, -239:56:-71, -215:56:-47, -199:56:-31, 17:56:241, 33:56:257, 57:56:225, 273:56:441, 297:56:465, 313:56:481] | DRU2 [-487:56:-263, -471:56:-247, -447:56:-279, -231:56:-63, -207:56:-39, -191:56:-23, 25:56:249, 41:56:265, 65:56:233, 281:56:449, 305:56:473, 321:56:489] | DRU3 [-491:56:-267, -475:56:-251, -451:56:-283, -235:56:-67, -211:56:-43, -195:56:-27, 21:56:245, 37:56:261, 61:56:229, 277:56:445, 301:56:469, 317:56:485] | DRU4 [-483:56:-259, -467:56:-243, -443:56:-275, -227:56:-59, -203:56:-35, -187:56:-19, 29:56:253, 45:56:269, 69:56:237, 285:56:453, 309:56:477, 325:56:493]
 | DRU5 [-489:56:-265, -473:56:-249, -449:56:-281, -233:56:-65, -209:56:-41, -193:56:-25, 23:56:247, 39:56:263, 63:56:231, 279:56:447, 303:56:471, 319:56:487] | DRU6 [-481:56:-257, -465:56:-241, -441:56:-273, -225:56:-57, -201:56:-33, -185:56:-17, 31:56:255, 47:56:271, 71:56:239, 287:56:455, 311:56:479, 327:56:495] | DRU7 [-493:56:-269, -477:56:-253, -453:56:-285, -237:56:-69, -213:56:-45, -197:56:-29, 19:56:243, 35:56:259, 59:56:227, 275:56:443, 299:56:467, 315:56:483] | DRU8 [-485:56:-261, -469:56:-245, -445:56:-277, -229:56:-61, -205:56:-37, -189:56:-21, 27:56:251, 43:56:267, 67:56:235, 283:56:451, 307:56:475, 323:56:491]
 | DRU9 [-494:56:-270, -478:56:-254, -454:56:-286, -238:56:-70, -214:56:-46, -198:56:-30, 18:56:242, 34:56:258, 58:56:226, 274:56:442, 298:56:466, 314:56:482] | DRU10 [-486:56:-262, -470:56:-246, -446:56:-278, -230:56:-62, -206:56:-38, -190:56:-22, 26:56:250, 42:56:266, 66:56:234, 282:56:450, 306:56:474, 322:56:490] | DRU11 [-490:56:-266, -474:56:-250, -450:56:-282, -234:56:-66, -210:56:-42, -194:56:-26, 22:56:246, 38:56:262, 62:56:230, 278:56:446, 302:56:470, 318:56:486] | DRU12 [-482:56:-258, -466:56:-242, -442:56:-274, -226:56:-58, -202:56:-34, -186:56:-18, 30:56:254, 46:56:270, 70:56:238, 286:56:454, 310:56:478, 326:56:494]
 | DRU13 [-488:56:-264, -472:56:-248, -448:56:-280, -232:56:-64, -208:56:-40, -192:56:-24, 24:56:248, 40:56:264, 64:56:232, 280:56:448, 304:56:472, 320:56:488] | DRU14 [-480:56:-256, -464:56:-240, -440:56:-272, -224:56:-56, -200:56:-32, -184:56:-16, 32:56:256, 48:56:272, 72:56:240, 288:56:456, 312:56:480, 328:56:496] | DRU15 [-492:56:-268, -476:56:-252, -452:56:-284, -236:56:-68, -212:56:-44, -196:56:-28, 20:56:244, 36:56:260, 60:56:228, 276:56:444, 300:56:468, 316:56:484] | DRU16 [-484:56:-260, -468:56:-244, -444:56:-276, -228:56:-60, -204:56:-36, -188:56:-20, 28:56:252, 44:56:268, 68:56:236, 284:56:452, 308:56:476, 324:56:492]
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in a 80 MHz UHR TB PPDU | 
DRU type | DRU index and subcarrier range

## Slide 15: Appendix (5/5)
80 MHz tone plan in [3] (cont.)
106-tone DRU i=1:8 | DRU1 [52-tone DRU1, 52-tone DRU2, -463, 457] | DRU2 [52-tone DRU3, 52-tone DRU4, -459, 461] | DRU3 [52-tone DRU5, 52-tone DRU6, -457, 463] | DRU4 [52-tone DRU7, 52-tone DRU8, -461, 459]
 | DRU5 [52-tone DRU9, 52-tone DRU10, -462, 458] | DRU6 [52-tone DRU11, 52-tone DRU12, -458, 462] | DRU7 [52-tone DRU13, 52-tone DRU14, -456, 464] | DRU8 [52-tone DRU15, 52-tone DRU16, -460, 460]
242-tone DRU i=1:4 | DRU1 [-499:4:-19, 17:4:497] |  | DRU2 [-497:4:-17, 19:4:499] | 
 | DRU3 [-498:4:-18, 18:4:498] |  | DRU4 [-496:4:-16, 20:4:500] | 
484-tone DRU i=1:2 | DRU1 [-499:2:-17, 17:2:499] |  | DRU2 [-498:2:-16, 18:2:500] | 
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in a 80 MHz UHR TB PPDU | 
DRU type | DRU index and subcarrier range