## Slide 1: Seamless roaming follow up

## Slide 2: Background
The following text has already been included into TGbn SFD:
As part of the seamless roaming procedure, during roaming,
  after the request/response exchange that initiates notification of the DS mapping change from the current AP MLD to the target AP MLD,
    The current AP MLD may deliver buffered DL data frames for a TBD period of time.
    The non-AP MLD may retrieve buffered DL data frames from the current AP MLD
    The non-AP MLD may send UL data to target AP MLD.
    It is assumed that the target AP MLD is able to deliver data frames to non-AP MLD after the DS mapping change
  The current AP MLD may forward DL data to the target AP MLD.
    When and how to initiate the forwarding of DL data is TBD
[Motion #27, [1] and [3, 7, 8, 42-48]]
TGbn defines that when a non-AP MLD is in the process of roaming from the current AP MLD to a target AP MLD, the context related to the non-AP MLD is transferred to the target AP MLD such that it preserves the data exchange context for the non-AP MLD or the context can be renegotiated with the target AP MLD.
  Details on what context can be transferred and what context can be renegotiated are TBD.
  How to transfer the context is TBD.
[Motion #26, [1] and [7,8,42-47]]

## Slide 3: Motivation
Obviously, it’s allowed to have different implementations based on the passed motion text.
  The context may be transferred or renegotiated.
    for the same context? or for the different context?
  DL buffered data frame may be delivered via current AP MLD or may be forwarding.
In this contribution, we would like to discuss some common procedures for various implementations.

## Slide 4: The buffered DL data frames transfer or drain out？
The non-AP MLD(STA) shall query the functionality of the buffered DL data transfer between two AP MLDs (APs)
  Known from reference [2], the buffered DL data frame transfer will increase the implementation complexity in some scenarios, and thus such function may not always being supported.
  It will be good for the STA to understand the capability of both the current and target APs via a query procedure before sending roaming request.

## Slide 5: The buffered DL data frames transfer or drain out？(Cont.)
Assuming the APs support the functionality of the buffered DL data transfer, the current AP or/and STA may set some additional conditions of receiving the buffered DL data frames.
  RSSI. The ratio of successfully transmission may drop linearly in lower RSSI scenarios, and cause a high delay or a long service interruption issue, also it relies on the performance of transmitter and receiver. It’s good if we allow both the AP or STA set a certain RSSI threshold.
  Explicitly signaling. The STA may indicate whether to exchange the DL/UL traffic with the current AP or not during roaming procedure.
  Other conditions.

## Slide 6: The context transfer or renegotiated？
Similarly, the STA shall query the APs’ capability of context transfer.
  Because APs may have the different capabilities on the optional features, like r-TWT,etc.
Based on the APs’ capability, STA may make the further decision the exactly requirement in the roaming request frame.
  Some parameters may be transferred.
  Some parameters may be renegotiated .
The AP may provide the status of each transferred parameter, and provides the corresponding response for each renegotiated parameter.
  The status code to show the transfer action is successful or failure.
  The response for each renegotiated parameter.

## Slide 7: The recap of RIC(Resource Information Container)
RIC in the baseline is used for parameter renegotiation with the target APs in FT case.
  Only 3 Resource types（TSPEC,BA,Vendor Specific） are defined in Table 13-3.
  Further extension for seamless roaming can be done in the RIC.

## Slide 8: The proposed extension on RIC for seamless roaming
To mitigate the overhead issue, the roaming request frame may include the (extended) RIC with the following aspects:
  Allow STA to include the transferred parameters
  Allow the STA to include the renegotiated parameters
  Allow the STA to indicate the DL/UL traffic exchange during roaming.
The roaming response frame may include the (extended) RIC with the following aspects:
  the status code for each transferred parameter
  the response for each renegotiated parameter
The transferred or the renegotiated parameters may include the follows:
  BA,(r)-TWT,TTLM,SCS, MSCS,IDC,QoS Characteristic, etc.
  Note: To identify the parameters which can be transferred , renegotiated or either is the next step.

## Slide 9: Summary
We propose to have some common procedures for various implementations on seamless roaming scheme.
  The STA should query the roaming capability of APs before making the roaming decision
  The STA may indicate to whether to exchange the UL/DL traffic or not during roaming via some internally threshold/conditions.
  The STA/AP may exchange the requirement of transferred context and/or the renegotiated context via the extended RIC.

## Slide 10
THANK YOU 

## Slide 11: Reference
24/209r4 Specification Framework for TGbn
24/655r0 Thoughts on SMD Roaming and FT Roaming
24/0679r0 thoughts-on-functionality-and-security-architecture-for-uhr-seamless-roaming.pptx
24/0349r3 enhanced-fast-bss-transition.pptx

## Slide 12: SP1
Do you agree that the non-AP MLD may query the roaming capability of the target AP MLD via a TBD frame, and receives the corresponding response though the current AP MLD or the target AP MLD before the request/response exchange that initiates notification of the DS mapping change from the current AP MLD to the target AP MLD.
Note: roaming capability may include the capability of the context renegotiation or transfer, and the capability of the DL buffered data transfer,etc.
Note: the details of the context is TBD.

## Slide 13: SP2
Do you agree that the non-AP MLD may indicate whether to receive to DL buffered data frame from the current AP MLD via a TBD signaling

## Slide 14: SP2’
Do you agree that the non-AP MLD may indicate whether to exchange the DL/UL traffic with the current AP MLD during roaming procedure via a TBD signaling

## Slide 15: SP3
Do you agree the non-AP MLD may request to transfer and/or renegotiate contexts with the target AP MLD via the RIC (or an extended RIC) in a TBD frame?