## Slide 1: Performance evaluation of ELR transmission
Date: 2024-09-09
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | Ensung.park@lge.com
Insik Jung |  |  |  | insik0618.jung@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Sanggook Kim |  | 10680 Treena St San Diego, CA 92131 |  | sanggook.kim@lge.com
September, 2024

## Slide 2: Introduction
In [1], to achieve the link budget gain(i.e. 6dB), we considered two methods for the ELR transmission in UHR.
In this contribution, we investigated the performance of each option for ELR transmission by considering the various conditions, and propose a suitable ELR transmission method.

## Slide 3: Recap.
ELR PPDU format
  We assumed the following PPDU format for ELR transmission described in [1].
    In the ELR preamble field, for the ELR-STF field and ELR-LTF field, we assumed the reusing of the EHT-STF sequence and 4x EHT-LTF sequence for 20MHz, respectively.
    For the data transmission, we used the defined RU size in EHT such as 52-tone RU and 106-tone RU.
Legacy Preamble
ELR Preamble
ELR Data

## Slide 4: Recap.
Two options for ELR transmission
  By considering the link budget margin, we considered the following options
    Option 1 – The repetition of 52-tone RU with MCS0
    Option 2 – The repetition of 106-tone RU with MCS 15
52 tone RU1
52 tone RU2
52 tone RU3
52 tone RU4
106 tone RU1 with MCS 15
106 tone RU2 with MCS15
Repeated RU
Repeated RU

## Slide 5: Performance evaluation (1/5)
Simulation parameters.
  5GHz Band
  20MHz bandwidth
  PPDU : Non-HT and ELR PPDU
  120 data bits for short packets such as ACK/CTS, 1000 data bits for normal packet.
  SISO
  MCS0 with BCC
  Channel B NLoS and D NLoS
  3 dB power boosting on L-STF, L-LTF, ELR-STF, and ELR-LTF
  Real Channel estimation with/without impairment such as CFO and TO
  We assumed the ELR PPDU was successfully detected through the received L-STF field.

## Slide 6: Performance evaluation (2/5)
120bits for Short packet, w/o impairment
  When impairment is not applied, the performance is similar regardless of options for ELR transmission.
  In this case, the ELR transmission can achieve about 5~6.5 dB gains than non-HT transmission in terms of performance.

## Slide 7: Performance evaluation (3/5)
120bits for Short packet, w/ impairment
  ELR transmission can achieve about the 5~6 dB gain than non-HT transmission.
  In both channels, the repetition using the 52-tone RU has a better performance than the repetition using the 106-tone RU with MCS15.
    106-tone RU has proportionally less pilot tones than 52-tones RU which may affect on the performance in environment with impairments

## Slide 8: Performance evaluation (4/5)
1000bits for normal packet, w/o impairment
  The performance of both options is similar when impairments are not considered.
  By using each option, we can get about 5.5~7dB gains.

## Slide 9: Performance evaluation (5/5)
1000bits for normal packet, w/ impairment
  It shows similar trends with the case of short packet size.
    Option 1 had performed better than Option 2.
    By using Option 1, we can obtain about 6dB gains than non-HT transmission.

## Slide 10: Summary
We evaluated the performance of each option for ELR transmission.
  In the various simulation environments, the performance of Option 1 was better than that of Option 2.
  And, by using Option 1, we can achieve the required link budget margin smoothly.
    Simple repetition in Option 1 may be beneficial for implementation.
We propose transmitting the data field by using the 52-tone RU repetition in 20MHz for ELR transmission.

## Slide 11: Straw poll 1
Do you agree to include the following text in the 11bn SFD?
  The BW of ELR PPDU is 20MHz and one Spatial stream is used for ELR transmission.

## Slide 12: Straw poll 2
Do you agree to include the following text in the 11bn SFD?
  In the ELR transmission, a repeating of 52-tone RRU is used in 20MHz.
    The same data is repeated in four 52-tone RRUs in 20 MHz.
    The subcarrier allocation of 52-tone RRU equals the 52-tone RU defined in 11be.

## Slide 13: Reference
[1] 11-24-1184-00-00bn-Considerations on ELR transmission