## Slide 1: Open Issues on DRU
Date: 2024-09-xx
Authors:
Name | Affiliations | Address | Phone | Email
Lin Yang | Qualcomm |  |  | 
Bin Tian |  |  |  | 
Youhan Kim |  |  |  | 
Qifan Chen |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
It has been almost a year since the discussion on DRU started
We have shared our thoughts on high level design directions on DRU [1,2], STF design consideration for DRU [3], and pilot tone design for DRU [4, 5]. Some of the SPs on these topics were deferred to give people more time to decide
It is time to converge and make some progress on DRU design
In this presentation we will refresh our thoughts on these topics and run some deferred SPs that are critical to move the project forward

## Slide 3: Recap: DRU Distribution BW and RU Sizes [1,2]
For 20/40/80MHz PPDU BW, it is reasonable for all DRUs to spread to PPDU BW
For PPDU BW>80MHz, still recommend to limit DRU distribution BW to 80MHz to balance gain vs complexity
  Leave distribution BW > 80MHz to future generation
Prefer BW dependent DRU size support to maximize BW and power efficiency
  Due to marginal gain, recommend not to support MRU to reduce DRU tone plan design /implementation/testing complexity
  20MHz: RU26, RU52, RU106
  40MHz: RU26, RU52, RU106, RU242
  80MHz: RU52, RU106, RU242, RU484

## Slide 4: Recap: Supporting BW Puncture [1,2]
Puncture brings another complexity to DRU design, need to balance the complexity/flexibility/gain
No puncture needs to be supported for 20/40MHz PPDU
  For 20MHz PPDUs, the distributing BW is 20MHz only
  For 40MHz PPDUs, the distributing BW is 40MHz only
For 80MHz and above, DRU and puncturing decision can be done per 80MHz segment
  If puncture occurs in 80MHz subblock, can leverage tone plan design for 20MHz and 40MHz distribution BW
    E.g., 20MHz punctured in 80MHz, one or multiple RUs spread over 20 MHz, another one or group of RUs spread over remaining 40MHz
    To avoid the need of new tone plan for 60MHz

## Slide 5: Recap: Mixture of DRU and RRU [1,2]
For 20/40/80MHz PPDU, mixture of DRU + RRU is not preferred
  More complicated in scheduling, tone plan, signaling and AP receive processing
  DRU can spread over entire PPDU BW to max Tx power
For 160/320MHz PPDU, hybrid mode can be supported with limited flexibility to reduce scheduling and signaling complexity
  Propose per 80MHz decision: each 80MHz segment can use either DRU or RRU but no mixture

## Slide 6: Recap: Global CSD with UHR-STF for DRU [3]
Global CSD was proposed in [3] to mitigate unintentional beamforming issue caused by multiple DRUs over same distribution BW transmitting the same UHR-STF
  Motion passed
Similar to per ss global CSD in UL MUMIMO , we can define global CSD index for each DRU assignment
  For a DRU assignment in a given distribution BW, it is assigned with a global CSD start index i
  If Nss for this DRU is larger than 1, then it will use CSD[mod(i: i+Nss-1, 8)] for each ss
  Re-use the existing 8 CSD table in the spec

## Slide 7: Recap: How to Choose the Pilot Locations? [4, 5]
Across the distribution BW
  Uniform pilot tone index spacing with maximal possible separation
    Ensure enough separation of pilots for any combination of DRU
    Maximal uniform separation for pilots is 11 tones for all 20/40/80MHz distribution
      No pilots around DC tones or edge tones of each DRU
Within each DRU
  Pilots’ separation is critical for small DRU to ensure diversity
    Especially for dRU26 which only has 2 pilots across the distribution BW for phase tracking
  Pilot tone separation pattern is important for large DRUs
    Large DRU has less power boosting gain but can potentially harvest more gain from channel smoothing
    Fixed pilot pattern may simplify smoothing filter design

## Slide 8: Recap: Pilots for 20MHz DRU [5]
Hierarchical uniform pilot structure of distance of 11
  [-111 -100 -89 -78 -67 -56 -45 -34 -23 15 26 37 48 59 70 81 92 103]
Fixed pilot tone separation patterns for all DRUs in 20MHz
Pilot indices for DRU transmission over 20MHz | 
dRU size | KdRxx_i
dRU26, i = 1:9 | {-111 15}, {-89 37}, {-100 26}, {-78 48}, {-67 59}, {-56 70}, {-34 92}, {-45 81}, {-23 103}
dRU52, i = 1:4 | {-111 -89 15 37}, {-100 -78 26 48}, {-56 -34 70 92}, {-45 -23 81 103}
dRU106, i = 1:2 | {-111 -78 15 48}, {-56 -23 70 103}

## Slide 9: Recap: Pilots for 40MHz DRU [5]
Hierarchical uniform pilot structure of distance of 11
  [-224 -213 -202 -191 -180 -169 -158 -147 -136 -125 -114 -103 -92 -81 -70 -59 -48 -37 28 39 50 61 72 83 94 105 116 127 138 149 160 171 182 193 204 215]
Fixed pilot tone separation patterns for all DRUs in 40MHz
Pilot indices for DRU transmission over 40MHz | 
dRU size | KdRxx_i
dRU26, i = 1:18 | {-224 28}, {-125 127}, {-202 50}, {-103 149}, {-81 171}, {-114 138}, {-213 39}, {-92 160}, {-191 61}, {-169 83}, {-70 182}, {-147 105}, {-48 204}, {-180 72}, {-59 193}, {-158 94}, {-37 215}, {-136 116}
dRU52, i = 1:8 | {-224 -125 28 127}, {-202 -103 50 149}, {-213 -114 39 138}, {-191 -92 61 160}, {-169 -70 83 182}, {-147 -48 105 204}, {-158 -59 94 193}, {-136 -37 116 215}
dRU106, i = 1:4 | {-224 -103 28 149}, {-213 -92 39 160}, {-169 -48 83 204}, {-158 -37 94 215}
dRU242, i = 1:2 | {-224 -213 -103 -92 28 39 149 160}, {-169 -158 -48 -37 83 94 204 215}

## Slide 10: Recap: Pilots for 80MHz DRU [5]
Hierarchical uniform pilot structure of distance of 11
  [-447 -436 -425 -414 -403 -392 -381 -370 -359 -348 -337 -326 -315 -304 -293 -282 -271 -260 -249 -238 -227 -216 -205 -194 -183 -172 -161 -150 -139 -128 -117 -106 -95 -84 -73 -62 53 64 75 86 97 108 119 130 141 152 163 174 185 196 207 218 229 240 251 262 273 284 295 306 317 328 339 350 361 372 383 394 405 416 427 438]
Fixed pilot tone separation patterns for DRU242 and DRU484 in 80MHz
  E.g., uniform pilot distribution for DRU242
Pilot indices for DRU transmission over 80MHz | 
dRU size | KdRxx_i
dRU52, i = 1:16 | {-447 -359 53 141}, {-403 -315 97 185}, {-227 -139 273 361}, {-183 -95 317 405}, {-425 -117 75 383}, {-381 -73 119 427}, {-337 -249 163 251}, {-293 -205 207 295}, {-194 -106 306 394}, {-150 -62 350 438}, {-370 -282 130 218}, {-326 -238 174 262}, {-260 -172 240 328}, {-216 -128 284 372}, {-392 -84 108 416}, {-436 -348 64 152}
dRU106, i = 1:8 | {-403 -315 97 185}, {-227 -139 273 361}, {-381 -117 119 383}, {-293 -205 207 295}, {-150 -62 350 438}, {-326 -238 174 262}, {-260 -172 240 328}, {-348 -84 152 416}
dRU242, i = 1:4 | {-403 -315 -227 -139 97 185 273 361}, {-381 -293 -205 -117 119 207 295 383}, {-326 -238 -150 -62 174 262 350 438}, {-348 -260 -172 -84 152 240 328 416}
dRU484, i = 1:2 | {-403 -381 -315 -293 -227 -205 -139 -117 97 119 185 207 273 295 361 383}, {-348 -326 -260 -238 -172 -150 -84 -62 152 174 240 262 328 350 416 438}

## Slide 11: Some Misc. Items
No UL MU MIMO with DRU: lack of gain and additional complexity
4x-LTF only with DRU: large tone spacing of DRU
Single stream pilots:
  RRU uses SSP for data in all 11ax/11be PPDUs
  SSP in LTF is used for non-MU MIMO cases with RRU
    Except 1x LTF
  Since DRU uses 4x LTF and does not support MU-MIMO, propose to still use SSP for dRU transmission in both LTF and data portion
LTF for RRU in hybrid mode
  In mixed RRU and DRU transmission, the RRU LTF follows the exact same rule as if there is no DRU; The DRU LTF sequence depends on the distribution BW
Nss: DRU supports up to 2ss only in UL TB PPDU
  Higher Nss may not benefit from the DRU gain
  For implementation simplicity

## Slide 12: References
[1] 23/1988, High-Level-Thoughts-on-DRU-Design
[2] 24/0500, Follow-Up-on-High-Level-Thoughts-on-DRU-Design
[3] 24/0752, STF-design-consideration-for-dRU
[4] 24/0501, Pilot-design-considerations-for-dRU
[5] 24/1230, pilot-tone-design-in-dRU-transmission

## Slide 13: Straw Poll #1 (defer)
Do you agree to add the following text to the TGbn SFD?
  11bn supports DRU transmission with distribution BWs of 20MHz, 40MHz and 80MHz

## Slide 14: Straw Poll #2
Do you agree to add the following text to the TGbn SFD?
  In a punctured 80MHz subblock, 11bn only supports the distribution BWs of 20MHz and 40MHz with DRU transmission

## Slide 15: Straw Poll #3
Do you agree to add the following text to the TGbn SFD?
  11bn supports the following BW dependent DRU size support to maximize BW and power efficiency
    No MRU in distributed transmission
    20MHz: RU26, RU52, RU106
    40MHz: RU26, RU52, RU106, RU242
    80MHz: RU52, RU106, RU242, RU484

## Slide 16: Straw Poll #4
Do you agree to add the following text to the TGbn SFD?
  11bn supports per 80MHz DRU/RRU switch if PPDU BW >80MHz and no hybrid DRU and RRU mode for up to 80MHz
    DRU (distributed tone RU)
    RRU (regular RU)

## Slide 17: Straw Poll #5
Do you agree to add the following text to the TGbn SFD?
In DRU transmission, global CSD provides CSD start index i for each DRU. If Nss for this DRU is larger than 1, then it will use CSD[mod(i: i+Nss-1, 8)] for each ss

## Slide 18: Straw Poll #6 (combine with other SPs)
Do you agree to add the following text to the TGbn SFD?
Hierarchical uniform pilot structure of distance of 11 will be used for distribution BW of 20/40/80MHz

## Slide 19: Straw Poll #7
Do you agree to add the following text to the TGbn SFD?
The following pilot index table from hierarchical uniform pilot structure of distance of 11 will be used for distributed transmission over 20MHz
Pilot indices for DRU transmission over 20MHz | 
dRU size | KdRxx_i
dRU26, i = 1:9 | {-111 15}, {-89 37}, {-100 26}, {-78 48}, {-67 59}, {-56 70}, {-34 92}, {-45 81}, {-23 103}
dRU52, i = 1:4 | {-111 -89 15 37}, {-100 -78 26 48}, {-56 -34 70 92}, {-45 -23 81 103}
dRU106, i = 1:2 | {-111 -78 15 48}, {-56 -23 70 103}

## Slide 20: Straw Poll #8
Do you agree to add the following text to the TGbn SFD?
The following pilot index table from hierarchical uniform pilot structure of distance of 11 will be used for distributed transmission over 40MHz
Pilot indices for DRU transmission over 40MHz | 
dRU size | KdRxx_i
dRU26, i = 1:18 | {-224 28}, {-125 127}, {-202 50}, {-103 149}, {-81 171}, {-114 138}, {-213 39}, {-92 160}, {-191 61}, {-169 83}, {-70 182}, {-147 105}, {-48 204}, {-180 72}, {-59 193}, {-158 94}, {-37 215}, {-136 116}
dRU52, i = 1:8 | {-224 -125 28 127}, {-202 -103 50 149}, {-213 -114 39 138}, {-191 -92 61 160}, {-169 -70 83 182}, {-147 -48 105 204}, {-158 -59 94 193}, {-136 -37 116 215}
dRU106, i = 1:4 | {-224 -103 28 149}, {-213 -92 39 160}, {-169 -48 83 204}, {-158 -37 94 215}
dRU242, i = 1:2 | {-224 -213 -103 -92 28 39 149 160}, {-169 -158 -48 -37 83 94 204 215}

## Slide 21: Straw Poll #9
Do you agree to add the following text to the TGbn SFD?
The following pilot index table from hierarchical uniform pilot structure of distance of 11 will be used for distributed transmission over 80MHz
Pilot indices for DRU transmission over 80MHz | 
dRU size | KdRxx_i
dRU52, i = 1:16 | {-447 -359 53 141}, {-403 -315 97 185}, {-227 -139 273 361}, {-183 -95 317 405}, {-425 -117 75 383}, {-381 -73 119 427}, {-337 -249 163 251}, {-293 -205 207 295}, {-194 -106 306 394}, {-150 -62 350 438}, {-370 -282 130 218}, {-326 -238 174 262}, {-260 -172 240 328}, {-216 -128 284 372}, {-392 -84 108 416}, {-436 -348 64 152}
dRU106, i = 1:8 | {-403 -315 97 185}, {-227 -139 273 361}, {-381 -117 119 383}, {-293 -205 207 295}, {-150 -62 350 438}, {-326 -238 174 262}, {-260 -172 240 328}, {-348 -84 152 416}
dRU242, i = 1:4 | {-403 -315 -227 -139 97 185 273 361}, {-381 -293 -205 -117 119 207 295 383}, {-326 -238 -150 -62 174 262 350 438}, {-348 -260 -172 -84 152 240 328 416}
dRU484, i = 1:2 | {-403 -381 -315 -293 -227 -205 -139 -117 97 119 185 207 273 295 361 383}, {-348 -326 -260 -238 -172 -150 -84 -62 152 174 240 262 328 350 416 438}

## Slide 22: Straw Poll #10 (passed)
Do you agree to add the following text to the TGbn SFD?
DRU only supports up to 2ss

## Slide 23: Straw Poll #11 (?)
Do you agree to add the following text to the TGbn SFD?
DRU only uses 4x LTF

## Slide 24: Straw Poll #12 (passed)
Do you agree to add the following text to the TGbn SFD?
UL MU-MIMO is not applicable to DRU

## Slide 25: Straw Poll #13
Do you agree to add the following text to the TGbn SFD?
    In mixed RRU and DRU transmission the RRU LTF follows the exact same rule as if there is no DRU. The DRU LTF sequence depends on the distribution BW

## Slide 26: Straw Poll #14
Do you agree to add the following text to the TGbn SFD?
    DRU transmission uses single stream pilots in both LTF and data portion