## Slide 1: Sounding Schemes for Coordinated Beamforming
Date: 2024-09-09
Authors:
Name | Affiliations | Address | Phone | email
Sameer Vermani | Qualcomm Technologies Inc. |  |  | svverman@qti.qualcomm.com
Alice Chen |  |  |  | 
Bin Tian |  |  |  | 
Manideep Dunna |  |  |  | 
Youhan Kim |  |  |  | 
Meriam Rezk |  |  |  | 
Alice Chen |  |  |  | 
Deniz Rende |  |  |  | 
Ahmed Elsherif |  |  |  | 
George Cherian |  |  |  | 

## Slide 2: Introduction
A motion passed in last TGbn session to include multi-AP Coordinated Beamforming (COBF) in UHR
In these slides, we propose sounding sequences for COBF
Outline
  Define some terminology
  Limitation on number of APs
  Propose two types of sounding sequences
    Sequential NDP based sounding
    Joint NDP based sounding
  Performance benefits of joint sounding
  Conclusions

## Slide 3: Terminology: Full-rank Nulling
AP1 and AP2 have 4 Tx antennas each
STA1 and STA2 have 2 Rx antennas each
Scenario 1: AP1 and AP2 form nulls to both the eigen modes of STA2 and STA1 respectively
  We call this case as the full-nulling scenario, where all eigen modes to the OBSS STA are being nulled to
AP1
AP2
BSS1
STA1 (2Rx)
BSS2
STA2 (2Rx)

## Slide 4: Terminology: Partial-rank Nulling
AP1 and AP2 have 4 Tx antennas each
STA1 and STA2 have 2 Rx antennas each
Scenario 2: AP1 and AP2 form nulls to only one of the eigen modes of STA2 and STA1 respectively
  We call this case as the partial-rank nulling scenario, where only a subset of the eigen modes to the OBSS STA are being nulled to
AP1
AP2
STA1
STA2
BSS1
BSS2

## Slide 5: Number of APs in a COBF transmission
We suggest restricting COBF transmissions to two APs
  Protocol and STA side complexity reasons
Note that one AP can still perform COBF with different APs at different times, but only with one other AP in each transmission
One AP can perform setup of COBF with multiple APs as well to maximize COBF opportunities

## Slide 6: Sequence Flavor 1: Sequential NDP based sounding
Design assumptions
  Would like to avoid NDPA to address OBSS STAs
    Power-save concerns (reading of all OBSS packets is a heavy burden on the STA)
    No need to exchange the per-STA stream allocation at the sounding stage
  From STA view: uses legacy sounding procedures as canonical components as-is
Below we show the case of 1 STA per BSS with some key attributes
  NDPA only addresses the in-BSS STAs
  Sounding happens for one BSS’s STAs at a time
NDPA
AP1
AP2
NDP
STA1
associated
with AP1
STA2
associated
with AP2
CSI
BFRP
BF
RP
NDPA
NDP
CSI
NDPA
BFRP
NDP
CSI
NDPA
NDP
CSI
BFRP
BSS 1 STAs being sounded
BSS 2 STAs being sounded
  Note: Additional
  MAC related
  frames may be needed

## Slide 7: Pros and cons: Sequential Sounding flavor
Pros
  Uses existing sounding protocol components from the point of view of the STA
  4ss-sounding-capable STAs can also participate in CoBF sounding involving two 4Tx APs
Con
  Does not work well with partial-rank nulling scenarios
Explanation of partial rank-nulling issue with sequential sounding
  Partial-rank null being formed to the OBSS STA implies an eigen mode with high interference at the STA
    This eigenmode may have a high projection on the in-BSS signal’s spatial signature leading to loss of in-BSS signal strength to avoid high interference

## Slide 8: Sequence Flavor 2: Joint NDP based sounding
Design assumptions
  Would like to avoid NDPA to address OBSS STAs
    Power-save concerns (reading of all OBSS packets is a heavy burden on the STA)
    No need to exchange the per-STA stream allocation at the sounding stage
  From STA view: uses legacy sounding procedures as canonical components as-is
Below we show the case of 1 STA per BSS with some key attributes
  NDPA only addresses the in-BSS STAs
  Sounding happens for one BSS’s STAs at a time
  Joint NDP based feedback will be based on large V-based feedback where the eigen-vectors span the antennas across both APs
  Note: Additional
  MAC related
  frames may be needed
NDPA
NDP
AP1
AP2
NDP
STA1 associated
with AP1
STA2 associated
with AP2
BFRP
BFRP
NDPA
NDP
NDP
Large V based feedback
Large V based feedback
BSS 1 STAs being sounded
BSS 2 STAs being sounded

## Slide 9: Pros and cons: Joint Sounding flavor
Pros
  Uses existing sounding protocol components from the point of view of the STA
  Works well with partial nulling case as global CSI knowledge can be utilized with a common U for both in-BSS and OBSS components of the channel
Con
  Does not work for 4ss-sounding-capable STAs and needs 8ss-sounding-capable STAs for the case of two 4Tx APs

## Slide 10: Need for partial-rank nulling case
Traffic/latency constraints may necessitate a partial nulling scenario as we might be transmitting 1ss to 2Rx STAs
Full nulling takes up more dimensions at the AP thereby making reducing opportunities for CoBF usage in field
  E.g., with a 4Tx AP, we cannot do full-nulling to two 2Rx STAs in the OBSS and transmit to in-BSS STA at the same time
Additionally, we run simulations to show why it is necessary to support partial nulling cases (through joint sounding)
  Compared the following for two 4Tx APs, and 2Rx STAs
    [2,2] ss allocation with full-nulling using sequential sounding
    [1,1,1,1] ss allocation with partial nulling using joint sounding
  Results on next slide

## Slide 11: Performance benefits of partial-nulling
Configuration
  Two 4 Tx APs
  STAs with 2 Rx each
  -30 dBc channel aging
  40MHz MU-MIMO D-NLOS channels
  We plot 10th percentile of the network throughput (sum at the two APs)
Observation
  For the same total number of streams, partial nulling can have a huge performance benefit

## Slide 12: Conclusion
We showed detailed designs for the two possible sounding sequences for COBF in UHR
  Sequential NDP based sounding
  Joint NDP based sounding
Both the sounding sequences have pros and cons
  Sequential sounding works well with lower sounding-capability STAs but does not work well for partial-rank nulling case
  Joint sounding works well for partial-rank nulling case but needs higher capability STAs
Showed the importance of supporting partial-rank nulling scenario
Suggest supporting both kinds of sounding sequences in UHR

## Slide 13: CFO Issues
New section in r1 document : Relevant to COBF Sounding

## Slide 14: Joint Sounding protocol needs CFO Pre-correction of NDP frames
Sounding happens one BSS at a time
  Below shows the 2 AP, 1STA per AP case
Results on next slide
NDPA
NDP
Sharing AP1
Shared AP2
NDP
STA1 associated
with AP1
STA2 associated
with AP2
BFRP
BFRP
NDPA
NDP
NDP
Large V based feedback
Large V based feedback
Needs precorrection to bring
frequency close to AP1
This frame is transmitted at
the same pre-correction as previous NDP

## Slide 15: Impact of 350 Hz CFO during joint NDP
Below we show the Rx sensitivity loss for MCS9 and MCS11 at 10% PER
Conclusion: 350 Hz can be tolerated, for MCS9 with 10 dB isolation and for MCS11 with 15 dB isolation
Isolation (dB) | MCS9 | MCS11
5 | 4 dB | >10% Err Floor
10 | 0 dB | 5 dB
15 | 0 dB | 0.5 dB
20 | 0 dB | 0 dB

## Slide 16: Sequential Sounding CFO Issues
Sounding happens one BSS at a time (shown by BRCM[1])
  Below shows the 2 AP, 1STA per AP case
  Phase 1 sounds STA1 in BSS1 and phase 2 sounds STA2 in BSS2
If the two APs just transmit NDPs at their frequency, the feedback tones at the two APs may differ by up-to 40ppm
During actual transmission stage, we will have to make shared AP synchronize to sharing AP for the joint LTF phase
Ran sims to evaluate performance impact of precoding tones being different than transmission tones
NDPA
Sharing
AP1
Shared
AP2
NDP
STA1
associated
with AP1
STA2
associated
with AP2
CSI
BFRP
BF
RP
NDPA
NDP
CSI
NDPA
BFRP
NDP
CSI
NDPA
NDP
CSI
BFRP
Phase 1
Phase 2

## Slide 17: Quantifying the impact of CFO in Sequential Sounding
2AP, 1 STA per AP, 3ss total, 4Tx per AP, full nulling case, no isolation
Impact of one AP’s precoding happening on tones which are certain number of tones apart from the transmission tones
  About 20% loss in throughput from 3-tone/234 kHz (~40 ppm) offset
Need to do some pre-correction during sequential sounding
  Isolation helps but we cannot design a system which works only for >10 dB isolation

## Slide 18: Possible solution for the sequential sounding CFO Issues
All NDP frames are synced to sharing AP (transmitter of the first NDPA)
  First yellow NDP needs to perform pre-correction to sync to the green NDPA before it
  Second yellow NDP needs to use the same pre-correction as the one during first yellow NDP
    Shared AP needs to remember the correction from the phase 1, to use it during the second phase when it is the transmitter of the NDP
NDPA
Sharing
AP1
Shared
AP2
NDP
STA1
associated
with AP1
STA2
associated
with AP2
CSI
BFRP
BF
RP
NDPA
NDP
CSI
NDPA
BFRP
NDP
CSI
NDPA
NDP
CSI
BFRP
Phase 1
Phase 2
CFO
Precorrection
CFO
Precorrection

## Slide 19: SP1
Do you support limiting the coordinated beamforming (COBF) transmission phase in 802.11bn to 2 APs only?

## Slide 20: SP2
Do you agree to include both sequential NDP based and joint NDP based sounding options for COBF in UHR?

## Slide 21: SP3
Do you agree with the sequential NDP based sounding protocol shown below for COBF?
  Sounding happens one BSS at a time
  NDPA only addresses the in-BSS STAs
  MAC related additional frames are TBD
NDPA
AP1
AP2
NDP
STA1
associated
with AP1
STA2
associated
with AP2
CSI
BFRP
BF
RP
NDPA
NDP
CSI
NDPA
BFRP
NDP
CSI
NDPA
NDP
CSI
BFRP

## Slide 22: SP4
Do you agree that for joint NDP based sounding, one AP will frequency synchronize to the other for both of its NDP transmissions?
  For both the NDPs, the AP doing the correction brings its frequency within in a certain TBD range of the reference AP

## Slide 23: SP5
Do you agree with the joint NDP based sounding protocol shown below for COBF?
  Sounding happens one BSS at a time
  NDPA only addresses the in-BSS STAs
  MAC related additional frames are TBD
  Joint NDP based feedback will be based on large V-based feedback where the eigen-vectors span the antennas across both APs
NDPA
NDP
AP1
AP2
NDP
STA1 associated
with AP1
STA2 associated
with AP2
BFRP
BFRP
NDPA
NDP
NDP
Large V based feedback
Large V based feedback

## Slide 24: SP6
Do you agree that for sequential NDP based sounding, one AP will frequency synchronize to the other for both of its NDP transmissions?
  For both its NDPs, the AP doing the correction brings its frequency within in a certain TBD range of the reference AP

## Slide 25: SP7
Do you support that in the UHR sounding process for COBF, for the joint sounding case as well as for the sequential sounding case, the NDP shall always carry the BSS color of the AP which transmitted the NDPA ?