## Slide 1: DSO follow up
Date: 2024-09-07
Authors:

## Slide 2: Recap
Many Wi-Fi clients do not support the full bandwidth option supported by the AP
  While APs may support up to 320 MHz, client may support only 80 MHz, or 160 MHz
When the AP has traffic for multiple STAs, if at least one client is wideband, Multi-User OFDMA can be used to schedule Resource Units (RUs) to the wideband STA in S80 or S160
  If no such client exists, large portions of the operational bandwidth go underutilized, leading to poor spectral efficiency
  802.11bn must address such underutilization by allowing narrowband devices to use different portions of the operational bandwidth
P20
S20
S40
S80
subchannels
In-BSS Transmission to 40 MHz STA
In-BSS Transmission to 160 MHz STA
Unutilized resource
Time
Frequency
WIFI 7

## Slide 3: Recap
In-BSS Transmission to 80 MHz STA1
(DL)
In-BSS Transmission to 80 MHz STA2
(DL)
Time
Frequency
Ack
(UL)
Ack
(UL)
STA1 parked on P20
Communicate with STAs to indicate the start of DSO frame exchange
AP and STAs exchange frames on the designated subchannels in an OFDMA PPDU. More than one SIFS-separated PPDUs may be exchanged
After STA2 sends the ACK, it waits on S80 for an additional timeout interval of aSIFSTime + aSlotTime + aRxPhyStartDelay
When no frame is addressed to STA2 during the timeout interval, it initiates switch back to P20
DSO Switch Back Delay
At the end of the DSO transition delay, STA2 has parked its radio back on P20
P20
BSS bandwidth
BSRP Trigger frame
non-HT dup PPDU
(DL)
BSR
STA2
(UL)
BSR
STA1
(UL)
PADDING
DSO allows the AP to allocate resources to a non-AP STA dynamically (i.e., on a per-TXOP basis) outside the non-AP STA’s operating bandwidth
Thus, it improves utilization of AP’s BSS bandwidth in the presence of narrowband STAs

## Slide 4: Operations during DSO
The AP initiates the DSO frame exchange using an initial Control frame
When the non-AP STA receives this initial Control frame, it performs the following operations:
  It transitions to the DSO sub-band that is indicated in the initial Control frame, and
  It transmits a response in the DSO sub-band a SIFS after the end of the initial Control frame, and
  Becomes ready to transmit/receive frames in the DSO sub-band a SIFS after the end of the response frame.
Thereafter, the non-AP STA and AP can perform frame exchanges on the DSO sub-band

## Slide 5: Switching across Primary & DSO sub-bands
A DSO non-AP STA incurs delays (i.e., DSO switching delay) when it switches to the DSO subband upon receiving an ICF from its associated AP asking it to switch to the DSO subband
Similarly, the DSO non-AP STA incurs delays (i.e., DSO Switch Back delay) when it switches to the primary subband at the end of the DSO frame exchange sequence
TGbn should allow the non-AP STA to signal the DSO Switching delay and DSO Switch Back delay to the associated AP when it enables DSO
The AP must provide padding in the initial Control frame sufficient for the non-AP STA to switch to the DSO sub-band
The initial Control frame can include an intermediate FCS to facilitate the STA’s transition to the DSO sub-band

## Slide 6: Error Sequence
It is possible that the non-AP STA(s) that are assigned resources in the primary sub-band does not respond to the ICF
If the AP continues its transmission only on the DSO sub-band, it loses medium synchronization on the primary sub-band, specifically on primary 20
  Moreover, legacy STAs may try to reach the AP on primary 20 and the AP will be unable to receive such frames
We propose that if the allocated STA on the primary20 channel does not respond, the AP does one of the following:
  Terminates the frame exchange with all STAs, or
  Ensures that the primary20 channel is occupied in the subsequent frames exchanges (as shown in the adjoining figure)

## Slide 7: Conclusions
In this presentation, we next level details on Dynamic Subband Operation:
  Operations during DSO frame exchanges
  Signaling considerations
  How to handle error sequence during DSO frame exchange

## Slide 8: Straw Polls
Do you support that in the DSO ICF, the AP indicates to a DSO STA to switch to a DSO sub-band
  Upon reception of the DSO ICF, the DSO STA shall
    transition to the DSO sub-band,
    transmit the response in the DSO sub-band a SIFS after the end of the DSO ICF
    And receive frames or be triggered to transmit frames, subject to its spatial stream capabilities and operation mode, in the DSO sub-band (derived from the DSO ICF), a SIFS after the end of the response frame
    Note: how the STA performs CS check before responding to DSO ICF is TBD

## Slide 9: Straw Polls
Do you agree that if no non-AP STA that is assigned resources in the primary 20 MHz responds to the initial Control frame and there is at least one response on other channels, the AP shall do one of the following:
  Terminate the frame exchange sequence with all non-AP STAs, or
  Continue the frame exchange sequence by ensuring that the primary 20 MHz is occupied
  Whether there are other options is TBD