## Slide 1: Thought on PAP Transmission in Joint Transmission
Date: 2024-09-13
Authors:

## Slide 2: Introduction
Joint Transmission (JT) is a way to increase the user throughput by cooperating multiple APs ([1-10]).
It is realized by collaborating an Initiating AP (IAP) that is associating with the STA with one or more Participating AP (PAP) that are not associating with the STA. It means PAP needs to transmit DATA to the target STA in OBSS.
This contribution shows a possible way for the DATA transmission from the IAP to the STA via the PAP.

## Slide 3: Recap: Joint Transmission
Joint Transmission (JT) is a way to increase the user throughput, especially in less-scattering (LOS) environment, by transmitting different user data from multiple APs simultaneously to a single STA .
JT is realized by collaborating an IAP associating with the STA with one or more PAPs that are not associating with the STA.
AP1
(IAP)
AP2
(PAP)
STA
DATA 1
DATA 2
DATA 2
Simultaneous transmission
from multiple APs
Associated
BSS
OBSS
Through in-band or backhaul

## Slide 4: Recap: Joint Transmission(cont.)
The basic process of JT can consist of four phases (Negotiation for JT, DATA delivery to PAP, JT, BlockAck).[10]
This presentation focuses on the phases of after the Negotiation for JT.
AP1
(IAP)
AP2
(PAP)
STA
Time
Time
Time
Negotiation for JT
BlockAck for JT
DATA2
form IAP to PAP
JT:
DATA1 from IAP
DATA2 from PAP
Through in-band or backhaul.

## Slide 5: Regular Transmission and Joint Transmission
BSS
DATA2
DATA1
AP1
(IAP)
STA
DATA1
DATA2
BA
AP2
(PAP)
DATA2
(1)
(2)
(2)
(3)
Regular transmission (i.e., not using JT) follows two steps: (1) AP1 transmits DATA1 and DATA2, and (2) the STA returns BA to AP1.
JT follows three steps: (1) AP1 (IAP) distributes DATA2 to AP2 (PAP), (2) AP1 transmits DATA1 and AP2 transmits DATA2 simultaneously, and (3) the STA returns BA to AP1.
Regular transmission
Joint Transmission
AP1
STA
BA
(1)
(2)
BSS

## Slide 6: Transmission from PAP to OBSS STA
The PAP is required to transmit DATA to the target (OBSS) STA.
  Dual association can be possible, but it might make the system complex.
    Management of sequence number and scoreboard may be complex.
    Packet handling may also become complex.
    AP1 and AP2 may use different security settings.
How can the PAP transmit DATA from the IAP to the STA without doing dual association?

## Slide 7: PAP DATA transmission using encapsulation
A possible way is to generate the MPDU for DATA2 in AP1.
  (1) AP1 generates MPDU for DATA2 (MPDU2) as if AP1 had directly transmitted it to the STA.
  (2) AP1 generates and transmits PPDU for Relay (PPDUfR) that encapsulates MPDU2 to AP2.
  (3) AP2 extracts the encapsulated MPDU2 from the received PPDUfR, and reframes it into PPDU2 to transmit toward the STA.
  (4) The STA receives the encapsulated MPDU2 as if it were transmitted from AP1.
AP1
(IAP)
STA
AP2(PAP)
MPDU1
MPDU2
PPDUfR
MPDU2
MPDU1
MPDU2
PPDU2
MPDU2
PPDU1
MPDU1
DATA2
(1)
DATA1
(2)
MPDU2
(3)
Reframe
(4)
Extract

## Slide 8: Benefits of PAP DATA transmission using encapsulation
This PAP DATA transmission using encapsulation would realize JT more easily than doing dual association in terms of the points as follows:
  The IAP is responsible for both DATA1 and DATA2. Therefore, management of sequence number and scoreboard can be done as in the regular transmission.
  Since the IAP receives all data from the Distributed System, packet handling is easy.
  The IAP generates MPDU for DATA2. Therefore, the PAP does not need to care the difference of security setting between the IAP and PAP.

## Slide 9: Summary
This contribution shows a possible way for the DATA transmission from the PAP to the (OBSS) STA in JT.
  The IAP generates the MPDU for the DATA transmitted from the PAP to the STA, as if the IAP had directly transmitted it to the STA.
It has several benefits as follows:
  Management of sequence number and scoreboard can be done as in the regular transmission.
  Since the IAP receives all data from the Distributed System, packet handling is easy.
  The PAP does not need to care the difference of security setting between the IAP and the PAP.

## Slide 10: References
[1] “Multi-AP Joint Transmission Simulations with Impairments”, IEEE 802.11-23/1843r0
[2] “Multi-AP Simulations: framework and Joint Transmission results”, IEEE 802.11-23/1176r1
[3] “Joint Transmission for UHR – Additional Results”, IEEE 802.11-23/0243r0
[4] “System Level Simulation of Co-BF and Joint Tx”, IEEE 802.11-22/1821r1
[5] “Joint Transmission for 11be”,IEEE 802.11-20/0071r1
[6] “Consideration on Joint Transmission”, IEEE 802.11-19x/1595r0
[7] “Multi-AP for reliability with Coherent and Non-coherent transmissions”, IEEE 802.11-23/2009r0
[8] “Joint Transmission for UHR – A Refresher and New Results”, IEEE 802.11-22/2188r0
[9] “Some thoughts on relay improvement”, IEEE802.11-23/2217r1
[10] “Consideration on Joint Transmission” , IEEE 802.11-24/0444r2