## Slide 1: Thoughts on DRU Availability for Regulatory Compliance
Date: 2024-09-08
Authors:

## Slide 2: Abstract
DRU is one of the most important features in 11bn because it greatly improves rate vs range performance.
There are many submission regarding DRU and some of features have already been approved to include the SFD [1].
On the other hand, some submissions [2][3] have raised concern about regulatory compliance with DRU, and thus TGbn should be careful about availability of DRU.
This submission discusses on DRU availability compliant with Japanese regulation as a case study.
Some restrictions for DRU patterns should be needed and propose a solution.

## Slide 3: Case Study: Japanese Regulation for 5/6 GHz bands
The regulatory rules for Japanese 5/6 GHz bands (i.e. 5150-5350MHz, 5470-5730 MHz, 5925-6425 MHz) are based on the rules for 5.2 GHz band (i.e. 5150-5250 MHz) which was opened in the year of 2000.
The rules for the 5.2 GHz band are generally dedicated for IEEE 802.11a and ETSI HIPERLAN/2, which are high-speed wireless local access systems. The following rules are typical examples.
  The number of subcarriers per 1 MHz is equal to or more than one in OFDM transmissions.
  The center frequencies and channel bandwidth sets (20/40/80/160/80+80/320 MHz) are identical to the baseline of IEEE 802.11.
  In 40 MHz or wider bandwidth transmission, the available modulation scheme is OFDM only.
  Energy based carrier sense mechanisms (similar to CCA-ED) is a mandatory function.

## Slide 4: Case Study: Japanese Regulation for 5/6 GHz bands (Cont’d)
The aim of these rules is to exclude low-rate systems such as frequency hopping and narrowband systems, for fully utilizing the potential of the broadband wireless access.
Therefore, such narrowband systems cannot obtain type approvals of Japan.
Those rules makes the Japanese 5/6 GHz bands clean (no narrowband interference), and thus it is beneficial for the WLAN system from the users’ perspective and should be preserved in the future.

## Slide 5: Case Study: Problem Statement
DRU mechanisms allocate subcarriers sparser than those in RRU.
It makes the occupied bandwidth of DRU larger than that of RRU.
Some patterns of DRU do not satisfy with the Japanese regulatory rules “The number of subcarriers per 1 MHz is equal to or more than one in OFDM transmissions.”
n_sc | sum of n_sc | Bw [MHz] | 40MHz | 80MHz |  | 
 |  | 20 | 40 | 80 | 160 | 320
26 | 26 | OK | NG | NG | NG | NG
52 | 52 | OK | OK | NG | NG | NG
52+26 | 78 | OK | OK | NG | NG | NG
106 | 106 | OK | OK | OK | NG | NG
106+26 | 132 | OK | OK | OK | NG | NG
242 | 242 | Invalid** | OK | OK | OK | NG
484 | 484 | - | Invalid** | OK | OK | OK
* When n_sc is “484+242” or more, any valid bandwidth satisfy with the rule.
** There is no room for applying the subcarrier allocation by DRU manner.
n_sc: DRU pattern
Bw: bandwidth of DRU
When (sum of n_sc)/Bw < 1, the subcarrier density is too sparse and labelled as “NG”.

## Slide 6: Discussions
This case study shows just an example but 11bn should prepare for additional restrictions of DRU usage for compliance with regulatory rules in various regulatory domains (including Japan).
Even when some of DRU variation cannot be used, we can still have some power boost effect, and thus to maximize the availability of DRU makes greatly sense.
DRU is used for UL OFDMA transmissions and each STA uses a DRU pattern that is signaled by a trigger frame.
If an AP knows the DRU patterns with NG in advance, it simply avoids to use them, and thus the problem is completely resolved.
An STA never select the DRUs with NG as far as a trigger frame does not set them; therefore, there is no need to add a rule for restrictions at STA side.

## Slide 7: Possible Solution
One of the possible solutions is to define the OK/NG table for DRU (as described on the previous slide) in each regulatory domain in Annex D and to define the restriction rules on the normative texts of DRU operation section.
Many WLAN products are based on globally common platform, and they are applied some customization for compliance with each regulatory domain.
If the 11bn amendment is designed assuming DRU restriction in advance, implementors can prepare and 11bn products will easily implement it, which will lead to cost reduction in terms of local customization (e.g., the cost for obtaining type approval).

## Slide 8: Conclusions
It is crucial to follow regulatory rules when DRU is used.
In addition, maximizing the availability of DRU is also important.
As a case study, we have reviewed the relation between DRU patters and Japanese regulatory rules, which showed some patterns of DRUs do not match with Japanese regulatory rules.
The availability of DRU depends on the regulatory rules.
To resolve this, 11bn should define to restrict DRU patterns according to the regulatory domain.
It can be done by restricting the DRU variations in AP side only.
It has the merit for cost reduction in terms of local customization.

## Slide 9: Straw Poll
Do you agree that the 11bn should define a mechanism to restrict DRU patterns for maximizing the availability as far as compliant with the regulatory rule in each regulatory domain?
Y-N-A:

## Slide 10: References
[1] Ross Jian Yu, “Specification Framework for TGbn,” 11-24/0209r4.
[2] Brian Hart, “Discussion on Distributed RUs (DRUs),” 11-24/0332r0.
[3] Yusuke Asai, et. al., “Thoughts on DRU Availability,” 11-24/0882r2, May 2024.
[4] The rules for radio equipment (in Japanese)
https://laws.e-gov.go.jp/law/325M50080000018