## Slide 1: AMP DL PPDU Design Considerations
Date: 2024-09-09
Authors:

## Slide 2: Introduction
Multiple AMP applications and requirements on the AMP communication definition are discussed [1~5]
  Efforts to harmonize AMP PPDU design for different use cases
Some initial thoughts on waveform and modulation for close-range mono-static backscattering [8, 9].
In this presentation, we share some of our view on the unified AMP PPDU definition for 2.4GHz

## Slide 3: AMP use cases and communication in 2.4GHz
Use cases | DL (2.4GHz) | UL (2.4GHz)
Mono-static Backscattering | Wakeup/control frame Backscattering Excitation (Energizer) frame | -
Bi-static Backscattering | Wakeup/control frame Backscattering Excitation (Energizer) frame from either AP or WPT device | -
Active Transmission with Legacy WiFi | Wakeup/control frame | Data frame (Legacy WiFi PPDU, no new PPDU)
Active Transmission with narrow BW | Wakeup/control frame | Data frame (Narrow BW PPDU)

## Slide 4: AMP DL PPDU
Amplitude modulation (e.g. OOK) is an effective modulation scheme enabling low-power Rx
If OOK is agreed to the modulation scheme for DL, AMP DL PPDU can be unified:
  WiFi preamble: support coex with legacy WiFi
    Either OFDM preamble or 11b/DSSS preamble
  Excitation symbols: provides carrier for energizing or backscattering
    Symbol signal bandwidth can be the same or smaller than preamble
    Active Tx Tag needs narrow BW carrier symbol, Rx filter BW.
    Backscatter Tag works for any symbol BW within the band
      Note: May not need to standardize the excitation symbol definition
WiFi-preamble | Excitation symbol | Excitation symbol | Excitation symbol | Excitation symbol | Excitation symbol | Excitation symbol | Excitation symbol | …

## Slide 5: Multi-segment PPDU
Excitation segment: Segments without modulation
  serve as either energizer or backscattering carrier
Data segment: Segments modulated with OOK
  serve as DL data transmission for wakeup or control
An AMP DL PPDU may consists of
  Data segment only: wakeup or control frame
  Energizer segment only: energizer/backscattering carrier
  Multiple mixed segments: control + backscattering / energizing
    The duration of all segments in the PPDU is indicated in WiFi preamble
WiFi-preamble | Excitation segment | Data segment (OOK Modulated) | Excitation segment | Data segment (OOK Modulated) | Excitation segment | Data segment (OOK Modulated) | …

## Slide 6: Data segment
Unified format: AMP SYNC + (SIG) + Data
  SYNC can be unified between backscatter and active Tx Tags
  SIG possibly needed to support different use cases with unified format
Modulation: OOK with waveform/bit encoding
  E.g. Manchester coding, differential Manchester coding, PIE, FM0, etc.
Data rate: to support different tag use cases
  One low rate of at most 250Kbps
  One high rate of at least 1Mbps
SYNC | (SIG) | Data

## Slide 7: Discussion: unified with UL Tx?
Backscattering: OOK is preferred
  Can share similar format of Data segment definition
  may skip SIG if not needed
Active NB transmission
  If OOK is defined as the modulation, may also reuse the format of Data segment definition
  The transmission will be polled by the AP, with legacy WiFi preamble included in the DL AMP PPDU carrying poll frame
SYNC | (SIG) | Data
WiFi preamble | SYNC | (SIG) | Poll frame

## Slide 8: Summary
Unified multi-segment AMP DL PPDU format that supports all use cases
  legacy WiFi preamble + excitation symbols
  Data segments, excitation segments
  Unified OOK modulation
May further unify with backscattering and UL NB Tx using OOK

## Slide 9: References
[1] 11-24/1345 High-Level Requirements for Downlink PHY in 2.4 GHz
[2] 11-24/1199, PHY Design for AMP
[3] 11-24/1496, PPDUs in AMP
[4] 11-24/1214, Carrier PPDU Discussion for Long-range Backscatter Operation
[5] 11-24/861, AMP DL PPDU consideration
[6] 11-24/900, Wireless Power Transfer and Frequency Regulation
[7] 11-23/2038, Close Range AMP Backscattering in 2.4GHz
[8] 11-24/1236, AMP-backscattering-waveform-and-modulation
[9] 11-24/1237, AMP-Tag-requirements-for-Mono-static-Backscattering

## Slide 10: SP
Do you agree that 11bp defines one unified DL AMP PPDU format that consists of
a legacy WiFi preamble and excitation symbols
  Legacy WiFi preamble definition TBD
  Excitation symbol definition TBD
Excitation symbols can consists of multiple Data segments and/or Excitation segments
Note:
  Data segment is the segment modulated with data bits
  Excitation segment is the segment without modulation

## Slide 11: Appendix

## Slide 12: UHF RFID Reading Sequence: Example [3]
Reader sends CW waveform for entire read sequence
Reader to modulate control info. on CW to Tag.
Tag to backscatter and modulate info. on CW back to Reader

## Slide 13: AMP DL PPDU: Structure
WiFi reader sends DL PPDU with all ON energy.
DL PPDU with the following functions:
  Wake up portion:
    Energy to wake up an AMP tag to prepare for backscattering, ~1ms
  Read control exchange:
    Ping the AMP tag with request signal, and control info
    e.g. acknowledge the request, identify the tag ID, exchange security key, etc.
  Backscattering data read:
    Energize the AMP tag to send backscattered data
    Acknowledge the data
Control Frame
Data backscattering
WiFi reader
Tag
Control Response
Control Frame
AMP DL PPDU
Control Frame
Wakeup portion
Read control Exchange
Backscattering data read

## Slide 14: DL TXOP: PPDUs
Energizer PPDU:
  Energize the tag for wakeup and/or backscattered transmission
Control-only PPDU:
  Send control signals to the tag without feedback
Control+Energizer PPDU:
  Send control signals and energize tag to send immediate feedback
WiFi-preamble | Energizer symbols
WiFi-preamble | AMP SYNC | Control payload
WiFi-preamble | AMP SYNC | Control payload | Energizer symbols