## Slide 1: Follow up on capability report and ID allocation for AMP STA
Date: 2024-09-04
Authors:

## Slide 2: Introduction
As stated in the 802.11bp PAR[1], 11bp amendment defines mechanisms for the coexistence of an AMP STA and deployed STAs in the same frequency.
There are couple of contributions [2] - [4] discussed the different PHY capabilities of AMP STAs.
In [5], we discussed the necessity of AMP capability reporting and methods of ID allocation for AMP STAs with storage capacity.
In this contribution, we will discuss the following:
  Details of the capability reporting for AMP STA
  Conditions and benefits of ID allocation
  Details of the ID allocation for AMP STA
September 2024

## Slide 3: Capability Report vs. Association
For AMP STAs which are unable to initiate transmission through EDCA, the AMP STA capability collection should be initiated by the reader. AMP STAs which can obtain transmission opportunities on their own can follow the existing association way.
For the .11 association, in general
  AP and STAs exchange capabilities
  AP assigns AID to STA
  Association is always initiated by the non-AP STA, not the AP
For the AMP STA capability report,
  AMP Non-AP STAs perform capability reporting, and AP capability exchange is not necessary
  The allocation of identifiers is not necessary
  Capability collection is initiated by the AMP AP / reader
    AP sends a control frame or a management frame to indicate the protection window for capability reporting to AMP STA
September 2024

## Slide 4: AMP capabilities to report
For the AMP STA，the capability to report to AMP AP or readers may include
  WPT capability
    WPT negotiation supported
    Capabilities as an energizer
    Energizing frequency band, energy capacity, power level…
  PHY capability
    Supported MCS
    Supported channel width
    Supported Nss
    Supported data rate…
  Power saving capability
    PS mode supported
    TWT supported …
  RAW supported
  Memory capability
  Positioning or sensing related capabilities…
AMP capability element
For the capability element or fields, there are two design options
  design a new AMP capability element，or
  Add AMP related capability fields to the Extended Capabilities element
Reserved bits in the Extended Capabilities element
September 2024

## Slide 5: AMP STA identification
An AMP STA declares that it is an AMP STA by transmitting the AMP capabilities element or fields
the capability reporting can be used for AMP STA identification, which allows the reader to learn about the AMP STA’s existence and capabilities
Within an identification protection window, multiple capability collections of AMP STA can be conducted, taking trigger frames as an example here
  AP or reader can decide the number of times to trigger capability reporting within the protection window, and can also terminate the protection window in advance when no response is received from AMP STA after multiple triggers
Periodic identification can be scheduled based on broadcast TWT or r-TWT, etc
September 2024

## Slide 6: ID allocation for AMP STA
Conditions for ID allocation to AMP STA
  AMP STA can store assigned ID(s), i.e. with memory capability
  AMP STA has a MAC address
  other conditions could be further discussed
The assigned ID can be used for device grouping and access restrictions, which is beneficial for
  Achieving unicast and multicast of DL control frames
  Achieving more accurate allocation of UL transmission resources and reduce conflicts
  Improving the reliability of AMP IoT
There are two options for the assigned ID
  Considering the legacy .11 AID or .11ah paged AID
  Considering identifiers and group identifiers specific to AMP STA
September 2024

## Slide 7: AP as reader-ID allocation method a & b
When AMP AP acts as a reader, there are two options for further ID allocation based on the identification of AMP STAs
AMP AP or reader can immediately assign an ID to AMP non-AP STA upon receiving its response (method a),
or it can assign IDs upon receiving multiple responses (method b).
AMP STAs that receive ACK or ID should not respond to subsequent Trigger frames.
Energy-sensitive devices can switch to PS mode within the remaining protection window
Reduce the collision probability of subsequent response frames sent by other AMP STAs
If there are multiple readers, there are two options for the assigned ID
Independent ID: To avoid ID conflicts, AMP STA stores the ID and its source information( such as the reader‘s MAC address or BSS ID). When the reader changes, it can obtain a new ID from a new reader
Global ID: when the reader changes, AMP STA will indicate the existing ID through a response frame, while AMP AP and AMP STA can negotiate whether existing IDs need to be modified
September 2024
Method a
Method b
Notes: 11ah AID：page、block、sub-block。。。。。

## Slide 8: non-AP STA as reader-ID allocation method c
September 2024
A non-AP STA acts as a reader, similar to a relay node.
Capability collection can be initiated by the reader or AP.
After receiving multiple responses, the reader can forward the information of AMP STA to AP for ID allocation.
Due to the unified allocation of IDs by AMP AP, even if multiple readers exist, there will be no ID conflicts.
Referring to .11 association procedure, there is also a limit to the number of IDs allocated by readers or AMP APs.
AMP AP should be able to update and reassign IDs
AMP STA should be able to determine whether the assigned ID is still valid
Notes: Considering the implementation of relay, both AP and non-AP STA can serve as readers

## Slide 9: ID update
September 2024
Due to some AMP STAs being unable to actively send association requests, we have designed a trigger based identification method in our contribution. Similarly, referring to the disassociation procedure, AMP STA may not be able to actively send disassociation request frame and may directly leave the transmission area of the current reader.
For AMP AP or reader:
The ID assigned to AMP STA can be lifetime or short-term valid
The identification and polling of AMP STA should be periodic
If the AMP AP unicast control frames to a AMP STA multiple times based on the assigned ID but does not receive a response, the AMP AP will reclaim and reassign this ID
For AMP non-AP STA:
When the ID becomes invalid or be reassigned, the AMP STA should respond to the identification initiated by the AMP AP again to reacquire the ID
Notes: Considering the implementation of relay, both AP and non-AP STA can serve as readers

## Slide 10: Summary
In [5], we discussed the necessity and methods of capability report and ID allocation for AMP STAs
In this contribution, we further discussed which capability information may need to be reported and how the capability collection procedure can be used as one of the identification methods for AMP STAs
In addition, based on potential benefits, we also discussed the details of ID allocation, including solutions to the multi reader problem and preliminary ideas for the ID update
September 2024

## Slide 11: SP1
Do you agree to add the following text to TGbp SFD?
AMP STAs shall report capability information to an AMP AP or reader
Note: The detailed capability information is TBD.
Y/N/A
September 2024

## Slide 12: SP2
Do you agree to add the following text to TGbp SFD?
An AMP AP or Reader can allocate IDs to AMP STAs based on their reported capabilities.
Note: Conditions for ID allocation are TBD.
Y/N/A
September 2024

## Slide 13: References
[1] 11-24-0575-01-0amp-p802-11bp-par
[2] 11-24-0849-00-00bp-harmonization-of-waveform
[3] 11-24-0867-00-00bp-thoughts-and-questions-on-amp-phy
[4] 11-24-0853-00-00bp-design-target-and-device-capabilities-for-amp-iot
[5] 11-24-1194-00-00bp-capability-report-for-AMP-STA
September 2024