## Slide 1: NPCA (Secondary Channel Usage) Follow Up
Date: 2024-09-08
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: NPCA Primary Channel Location
Each 80MHz channel covered by a BSS operating channel can’t have more than one backoff 20MHz channel (a backoff 20MHz channel is either the NPCA backoff 20MHz channel or the primary channel)
  NPCA is not allowed in a BSS with <80MHz operating channel
  Whether 80MHz BSS allows NPCA operation is TBD
In a BSS with N 20MHz channels, one non-primary backoff 20MHz channel (the backoff 20MHz channel that is not primary 20MHz channel) is defined, and the NPCA backoff channel is on non-primary (secondary) (N/2)*20 MHz channel.
  In a 160MHz BSS, NPCA primary channel is in secondary 80MHz channel.
  In a 320MHz BSS, NPCA primary channel is in secondary 160MHz channel.

## Slide 3: RU Index (1)
Observation:
  When an AP solicits TB PPDU from STAs after NPCA primary channel’s backoff, the BW of the soliciting Trigger frame may cover both primary channel and NPCA primary channel.
  The RU index for the same 20MHz channels may be different when the different channel being treat as primary channel for RU index coding.
    The STAs don’t do the NPCA channel switch since the OBSS activity is missing and the STAs do the NPCA channel switch have the different view of the backoff channel.

## Slide 4: RU Index (2)
Primary channel
NPCA
Primary channel
320MHz BSS
RU index coding per NPCA primary channel:
PS160 = 0
B0 of RU Allocation = 0
RU index coding per primary channel:
PS160 = 1
B0 of RU Allocation = 1
Low frequency
High frequency
Valid channel
for TB PPDU
40MHz OBSS PPDU
Primary channel
NPCA
Primary channel
160MHz BSS
Valid channel
for TB PPDU
RU index coding per NPCA primary channel:
B0 of RU Allocation = 0
RU index coding per primary channel:
B0 of RU Allocation = 1
Low frequency
High frequency
40MHz OBSS PPDU

## Slide 5: RU Index (3)
Solution:
  The Trigger frame indicates whether the NPCA Primary channel is used as the reference for RU index coding.

## Slide 6: RU Index (4)
Primary channel
NPCA
Primary channel
320MHz BSS
Valid channel
for TB PPDU
B0 of RU Allocation = 0
Low frequency
High frequency
Primary channel
NPCA
Primary channel
320MHz BSS
PS160 = 0
B0 of RU Allocation = 0
Low frequency
High frequency
Valid channel
for TB PPDU
160MHz OBSS PPDU
40MHz OBSS PPDU
Primary channel
NPCA
Primary channel
160MHz BSS
Valid channel
for TB PPDU
B0 of RU Allocation = 0
Low frequency
High frequency
40MHz OBSS PPDU

## Slide 7: Summary
This presentation discusses the following of the NPCA:
  The condition to allow NPCA primary channel in a BSS and the location of the NPCA primary channel.
  The RU index coding of TB PPDU when switching to NPCA primary channel.

## Slide 8: SP 1
Do you agree that an AP shall not allow the use of NPCA within its BSS if the BSS operating bandwidth is less than or equal to TBD MHz, where TBD = 40 MHz or 80 MHz?

## Slide 9: SP 2
Do you agree to the following?
  An AP shall place the NPCA Primary channel within the Secondary 80 MHz in a 160 MHz BSS.
  An AP shall place the NPCA Primary channel within the Secondary 160 MHz in a 320 MHz BSS.

## Slide 10: Backup Slide

## Slide 11: Initiating Frame on NPCA Primary Channel
Observation:
  The TXOP holder in NPCA primary channel needs to decide whether its peer device(s) is/are available or not.
To simplify the implementation and inter-op test, some restriction should be applied to the initiating frame
  Option 1:
    MU-RTS
    BSRP Trigger
    RTS
  Option 2:
    MU-RTS
    BSRP Trigger
  Option 3:
    Any control frame
  Option 4:
    Any frame.
  Prefer option 2.