## Slide 1: DSO Follow Up
Date: 2024-09-08
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Soliciting Control Frame and STA’s Parking Channel
Each STA that supports DSO (DSO STA) announces the padding time for STA’s switch from primary channel to the parking channel.
BSRP as the initiating frame is used to solicit DSO STA’s channel switch.
  The BSRP Trigger needs to satisfy the padding requirement of the solicited DSO STA(s).
  It is TBD whether MU-RTS can be used as the initiating frame.
The RU (RU) being allocated to a STA in the initiating frame that triggers the STA’s dynamic channel switch decides the STA’s DSO sub-band (parking secondary channels).
  Whether there is other indication is TBD.

## Slide 3: Channel Puncture (1)
11be’s channel puncture:
  Without Trigger frame soliciting the responding frame, a PPDU needs to follow BSS operating channel restricted by the unpunctured channel bitmap if exists for the secondary channels be used.
  With Trigger frame soliciting responding frame, a PPDU can puncture any secondary channel being allowed by the BSS operating channel.
  The primary channel can’t be punctured.
  A STA may not be able to execute frequency domain combination.

## Slide 4: Channel Puncture (2)
Under dynamic channel puncture, any secondary channel that a DSO switch to can be punctured.
  The AP and STAs switch DSO channel need to have same view that an unpunctured 20MHz secondary channel on DSO channel is used to start the DL PPDU reception/decoding.
DSO channel puncture option:
  The dynamic channel puncture is allowed within a TXOP with STÁs switching to DSO channel.
  In a TXOP, a secondary channel covered by the DSO channel that is not punctured by the Trigger frame soliciting DSO STA’s channel switch can’t be punctured in the future frame exchanges of the TXOP.
20MHz channels being not punctured in TB PPDU where DSO STAs do the channel switch
80 + 40 MHz channel can’t be punctured in the future frame exchanges of the TXOP

## Slide 5: Summary
This presentation discusses the following of DSO operation
  The method to indicating a STA’s parking DSO sub-band in soliciting BARP Trigger frame.
  The channel puncture operation.

## Slide 6: SP 1
Do you agree that to allocate resources to a DSO STA in a DSO sub-band, the AP shall initiate the frame exchange sequence with a DSO initial Control frame (ICF)?
  The BSRP Trigger frame shall be a DSO ICF
    Whether MU-RTS TF is a DSO ICF or not is TBD
  the DSO sub-band is indicated with the RU allocation field and whether we have additional signaling indicating that it is DSO TxOP or not is TBD