## Slide 1: Sounding Procedure for Relay Operation
Date: 2024-09-24
Authors:

## Slide 2: Abstract
In this contribution, we discuss some methods of sounding procedure for relay operation.

## Slide 3: Background
To improve QoS (e.g., reliability and throughput) in terms of Rate vs Range (RvR) requirement of UHR, relay operation has been discussed in IEEE 802.11 TGbn.
In order to provide the improvement of the QoS, channel information between a relay STA and a non-AP STA should be measured and estimated by channel sounding.
DL sounding for the Relay link is discussed in [1-3]. For example, AP may transmit a trigger frame used to initiate the sounding between relay and destination STA.

## Slide 4: Separate Sounding Procedures for Relay Operation
Channel sounding may include a first sounding phase for channel between a source AP STA and a relay STA and a second sounding phase for channel between the relay STA and a destination non-AP STA.
Each of the first and second sounding phases may include a separate sounding procedure, which increases overhead when channel sounding is performed more frequently.
Example
A relay STA (STA2) may be a mobile STA. First CSI between AP STA and relay STA and second CSI between relay STA and non-AP STA may change rapidly due to movement of relay STA.
Each sounding phase requires an NDPA, an NDP, and a feedback frame.
Additionally, there is a need a trigger frame to initiate the second sounding phase.

## Slide 5: Proposed Sounding Procedure for Relay Operation - Solution 1
A relay STA (e.g., STA2) may receive from a source AP STA (e.g., STA1) a control frame 1 (e.g., NDPA1).
The NDPA1 indicates a NDP1 to be transmitted (SIFS after NDPA1) by the STA1 for estimation, by the STA2, of a source-relay channel.
The NDPA1 further requests that the STA2 transmit to a destination non-AP STA (e.g., STA3) a control frame 2 (e.g., NDPA2) after receiving the NDP1.
The NDPA2 indicates a NDP2 to be transmitted (SIFS after NDPA2) by the STA2 to the STA3 for estimation, by the STA3, of a relay-destination channel.
As a result, the overhead can be reduced by eliminating the trigger frame used for the second sounding phase.

## Slide 6: Proposed Sounding Procedure for Relay Operation - Solution 2
Based on Solutions 1, the NDPA1 frame further solicits from STA2 a feedback 2 frame which includes a BF/CSI report based on estimation of NDP1 at STA2 and a BF/CSI report based on estimation of NDP2 at STA3.
As a result, the overhead can be further reduced.

## Slide 7: Summary
In this contribution, we shared some thoughts of sounding procedure for relay operation.

## Slide 8: References
23/1138, Features to consider for efficient relay operation, Dongguk Lim (LG Electronics)
23/1838, Follow up on the relay transmission, Dongguk Lim (LG Electronics)
23/1840, Relay for 11bn, Dongguk Lim (LG Electronics)
24/1038, Channel sounding for UHR relay, Pei Zhou (TCL)
24/0887, Consideration on relay operation for 11bn, Liuming Lu (OPPO)
24/0386, Lower MAC relay follow-up, Kiseon Ryu (NXP)
24/0385, Discussion on 11bn relay operation (Sony)
24/0074, Relay operation follow-up, Guogang Huang (Huawei)
23/1969, Consideration on UHR relay Architecture, Kosuke Aio (Sony)
23/1948, TXOP sharing based UL relaying, Serhat Erkucuk (Ofinno)
24/1565, Further considerations on data unit delivery using relaying, Serhat Erkucuk (Ofinno)
24/1572, Enhancements on relaying for UHR, Tuncer Baykas (Ofinno)