## Slide 1: Coordinated Sounding for CoBF
Date: 2024-09-09
Authors:
Name | Affiliations | Address | Phone | Email
You-Wei Chen | Mediatek | 2840 Junction Ave. San Jose, CA, 95134 |  | You-Wei.Chen@mediatek.com
Jianhan Liu |  |  |  | 
Huai-Yan Feng |  |  |  | 
Gary Anwyl |  |  |  | 
Kaiying Lu |  |  |  | 
Thomas Pare |  |  |  | 

## Slide 2: Introduction
In July IEEE meeting, the motion [1] passed to define CoBF in TGbn.
Sounding sequences for CoBF was discussed in [2-4].
In this presentation, we would like to discuss our view of sounding sequences and their overhead.

## Slide 3: Sequential Sounding
NDPA addresses to its own BSS non-AP STAs and the shared AP.
AP1 and AP2 transmit sounding NDP separately (similar to MU sounding in 11be). A duplicated sounding sequence needs to perform by AP2.
Since 11bn will still define a single AP sounding sequence, the sequential sounding is considered as a straightforward extension.
non-AP STA2
AP1
non-AP STA1
AP2
NDPA
BFRP
BFR
NDP
NDPA
BFRP
BFR
NDP
x2

## Slide 4: Joint Sounding
NDPA addresses to its own BSS non-AP STAs and the shared AP.
AP1 and AP2 transmit sounding NDP jointly. In this case, global CSI information can be solicited within two sounding sequences.
non-AP STA2
AP1
non-AP STA1
AP2
NDPA
NDP
BFRP
BFR
NDP
NDPA
NDP
BFRP
BFR
NDP

## Slide 5: Coordinated Sounding Sequence
There are some similarities for both sounding sequences, and from the STA point of view, the sounding sequences are transparent. Thus, they can be uniformed as one coordinated sounding scheme.
  AP1 and AP2 sound non-AP STAs in a ‘per-BSS’ based.
  Shared AP follows the instructions in NDPA to perform NDP transmission.
non-AP STA2
AP1
non-AP STA1
AP2
NDPA
NDP
BFRP
BFR
NDP

## Slide 6: NDP – Global Index LTFs
    Global index LTFs concept was discussed in [4].
    Sharing and Shared APs send LTFs regarding to the total sounding NSS.
Shared AP
Sharing AP
Y antenna
X antenna
NDP:
U-SIG
UHR-SIG
UHR-STF
UHR-LTF
UHR-LTF
…
0
X+Y-1
UHR-LTF
1
L-preamble
UHR-LTF
X-1
UHR-LTF
X
…
Only shared AP sounds
Sharing and shared AP transmit joint NDP

## Slide 7: Sequential vs Joint Sounding: BFR airtime
Assumion: 2AP (4TX antennas), 4STA (2RX antennas), BW80.
Joint sounding requires a bigger V. when the V matrix size increase from 4x2 to 8x2, then the number of angles (Na) value increases from 10 to 26.
 | Sequential Sounding | Joint Sounding
Preamble Airtime (us) | 104 us (4x LTF + 3.2 GI) | 104 us
Payload Airtime (us) | 384 us (4x2 matrix) (1SS, MCS3) | 932 us (8x2 matrix) (1SS, MCS3)
BFR Airtime (us) (Preamble + Payload) | 488 us | 1036 us

## Slide 8: Sequential vs Joint Sounding Overhead
Assumion: 2AP (4TX antennas), 4STA (2RX antennas), BW80.
Overhead difference of sequential and joint sounding per coordinated sounding interval is negligible. (<1%)
Note: sounding period is implementation dependent.
 | Sequential Sounding | Joint Sounding
Number of sounding sequences (NDPA->NDP->BFRP-> BFR) | 4 | 2
NDPA airtime | 32 us | 32 us (may increase, since 2x STA info field in NDPA) (I check from your table, there is a 4us increase; however, I think we do not need to show that in this table)
NDP airtime | 71 us (4 LTF) | 103 us (71+32us) (8 LTF)
BFRP airtime | 53 us | 
BFR airtime | 488 us (4x2 matrix) (1SS, MCS3) | 1036 us (8x2 matrix) (1SS, MCS3)
Total Airtime (NDPA + SIFS + NDP + SIFS + BFRP + SIFS + BFR) | = (32+16+71+16+53+16+488) * 4 = 692 * 4 = 2768 us | =(32+16+103+16+53+16+1036)*2 =1272 * 2 =2544 us
Diff | Each CoBF sounding interval: 224us (2768 - 2544) If sounding period = [100/50/25] ms, overhead diff per coordinated sounding interval = about [0.22/0.45/0.89] % | -

## Slide 9: Comparison of Joint and Sequential Sounding
In 11ax/be, the mandatory support for STA is 4 LTFs.
Sequential sounding provides significant gain over TDMA when conducting the full rank nulling for STA [5,6] .
Joint sounding provide additional gain when conducting the partial rank nulling for STA [6,7] .
  Complexity at STA-side:
    Support 8x2 feedback
    Support inteference cancellation algorithm
Enable coordinated sounding (both sequential and joint) can support a wide spectrum of STA category.

## Slide 10: Summary
We compare the overhead for coordinated sounding sequences.
  Difference between sequential and joint sounding sequences is negligible. (<1%)
For a relative low complexity STA (support 4x2 feedback only), a CoBF gain over TDMA can be achieved via full rank nulling.
We suggest to enable a coordinated sounding, includes both sequential and joint sounding for CoBF.

## Slide 11: Straw Poll #1
Do you agree that 802.11bn shall provide a coordinated sounding scheme for CoBF?
  coordinated sounding includes both sequential and joint sounding.

## Slide 12: References
[1] “TGbn Motions List - Part 1”, 24/0171r13
[2] “Coordinated Spatial Nulling (C-SN) Concept”, 24/0011r0.
[3] “Obtaining OBSS AP Channel Information for Multi-AP operation”, 23/0854r0
[4] “Joint Sounding for Multi-AP Systems”, 19/1593r3
[5] “Multi-AP Collaborative BF in IEEE 802.11”, 19/0772r1
[6] “Performance of C-BF and C-SR”, 22/0776r1
[7] “Coordinated BF Goodput Discussion”, 24/1211r1