## Slide 1: Non-Primary Channel Access (NPCA) Follow-Up
Date: 2024-09-05
Authors:

## Slide 2: Recap: NPCA operation [1]
Motion text for NPCA in TGbn SFD [1]
  [Motion #11, [1] and [21-30]]: TGbn defines a mode of operation that enables a STA to access the secondary channel while the primary channel is known to be busy due to OBSS traffic or other TBD conditions.
    The mode of operation shall not assume that the STA is capable to detect or decode a frame and obtain NAV information of the secondary channel concurrently with the primary channel.
    A BSS shall only have a single NPCA primary channel (name TBD) on which the STA contends while the primary channel of the BSS is known to be busy due to OBSS traffic or other TBD conditions.

## Slide 3: Recap: NPCA operation [2]
In [2], we proposed a method for more NPCA opportunities
  NPCA STA can switch to NPCA channel without the OBSS NAV, in which case STA may obtain the OBSS NAV on NPCA channel from another STA and then operate on NPCA channel during the OBSS NAV.

## Slide 4: Recap: NPCA operation [2-4]
Examples of NPCA switching time in NPCA operation
  For non-HT PPDU frame carrying control frame (e.g., RTS, Trigger frame, etc.): STA can switch to NPCA channel after receiving the PPDU (the control frame)
  For HE+ PPDU with valid TXOP: STA can switch to NPCA channel after receiving a SIG field (e.g., HE-SIG A, U-SIG , etc.) in the preamble of the PPDU
  For VHT(/HT) PPDU or HE+ PPDU with invalid TXOP: STA can switch to NPCA channel after trying to receive 1st MPDU or can switch to NPCA channel after receiving a SIG field
    If both switch to NPCA channel after a SIG field, they can use PPDU duration for frame exchanges on NPCA channel
    Otherwise, they may get OBSS NAV and operate on NPCA channel during the OBSS NAV
It’s desirable for AP and non-AP STA to switch to NPCA channel at the same time to avoid unnecessary control frame transmission
In this contribution, we discuss more details for NPCA switching time according to PPDU types

## Slide 5: Switching time for VHT+ PPDU (1)
For VHT PPDU or HE+ PPDU with invalid TXOP, (Option 1) STA explicitly indicates when it switches to NPCA PCH (e.g., either after SIG or 1st MPDU) before NPCA operation
STA can switch to NPCA channel under defined switching conditions (e.g., threshold)

## Slide 6: Switching time for VHT+ PPDU (2)
(Option 2) If the length of 1st MPDU is too long or the MPDU delimiter error occurs, STA can switch after the MPDU delimiter.
*DEL: MPDU delimiter

## Slide 7: Switching time for HT PPDU
For HT PPDU, STA can switch to NPCA PCH after detecting 1st MPDU.

## Slide 8: Switching time for non-HT PPDU
For non-HT PPDU with a large management frame, AP and non-AP STA can switch to NPCA channel after detecting OBSS frame in MAC header
This can also be applied to other PPDU types (e.g., HT PPDU, VHT PPDU, etc.)

## Slide 9: Conclusion
We proposed several methods for NPCA switching according to various PPDU types
  To have more TX opportunities for NPCA channel, STA can switch to NPCA channel for OBSS non-HT PPDU including a large MMPDU, OBSS HT PPDU, OBSS VHT PPDU, and OBSS HE+ PPDU with invalid TXOP as well as non-HT PPDU including a control frame and HE+ PPDU with valid TXOP

## Slide 10: References
[1] 24/0209r5, Specification Framework for TGbn
[2] 24/0829r0, Further Considerations on Non-Primary Channel Access
[3] 24/1115, Channel Switching Rules for NPCA
[4] 24/0803, The switching time in NPCA

## Slide 11: Straw Poll 1
Do you agree the following text?
  NPCA capable STA may switch to NPCA channel when it detects one of the following PPDUs
    VHT PPDU
    HT PPDU
    Non-HT PPDU including an MMPDU