## Slide 1: Signal Field and LDPC Rate Matching for Enhanced Long-Range
Date: 2024-Sep-9
Authors:

## Slide 2: Introduction
Enhanced long-range (ELR) was being discussed in [1-3] to address the uplink/downlink range imbalance
Designs on ELR PPDU format, U-SIG design for ELR PPDU, ELR-SIG, ELR-Mark sequence and ELR data transmission were proposed [4-13]
In this presentation, designs on ELR-SIG and LDPC rate matching were proposed
Design assumptions:
  ELR uses SU mode over 20MHz for simplicity
  ELR device may not be able to receive U-SIG due to weak SNR
September 2024

## Slide 3: Recap of U-SIG and EHT-SIG for EHT SU PPDU
U-SIG1 | B0-B2 | B3-B5 | B6 | B7-B12 | B13-B19 | B20-B24 | B25
 | PHY version | PPDU BW | UL/DL | BSS color | TXOP | Disregard | Validate
U-SIG2 | B0-B1 | B2 | B3-B7 | B8 | B9-B10 | B11-B15 | B16-B19 | B20-B25
 | PPDU Type | Validate | Punctured Channel Information | Validate | EHT-SIG MCS | Number of EHT-SIG Symbols | CRC | Tail
EHT-SIG (EHT SU) | Common Info(non-OFDMA) |  |  |  |  |  |  |  |  |  |  |  | 
 | B0-B3 | B4-B5 | B4-B5 | B6-B8 | B6-B8 | B9 | B9 | B10-B11 | B10-B11 | B12 | B12 | B13-B16 | B17-B19
 | Spatial Reuse | GI+LTF Size | GI+LTF Size | Number of EHT-LTF Symbols | Number of EHT-LTF Symbols | LDPC Extra Symbol Segment | LDPC Extra Symbol Segment | Pre-FEC padding Factor | Pre-FEC padding Factor | PE Disambiguity | PE Disambiguity | Disregard | Number of non-OFDMA Users
 | User field |  |  |  |  |  |  |  |  |  |  | CRC | Tail
 | B20-B30 |  | B31-B34 |  | B35 |  | B36-B39 | B40 |  | B41 |  | B42-B45 | B46-B51
 | STA-ID |  | MCS |  | Reserved |  | NSS | BF |  | Coding |  | CRC | Tail
September 2024
Subset of fields may be included in ELR-SIG

## Slide 4: U-SIG Fields Needed in ELR-SIG
September 2024
U-SIG1 | B0-B2 | B3-B5 | B6 | B7-B12 | B13-B19 | B20-B24 | B25
 | PHY version | PPDU BW | UL/DL | BSS color | TXOP | Disregard | Validate
Note for ELR-SIG | ELR Version (1-bit) for future proof | No need. 20 MHz only. | Better to keep UL/DL | Better to keep BSS color and be carried earlier such as in ELR-MARK for earlier drop [5,9] | Better to keep TXOP if there is space |  | 
U-SIG2 | B0-B1 | B2 | B3-B7 | B8 | B9-B10 | B11-B15 | B16-B19 | B20-B25
 | PPDU Type | Validate | Punctured Channel Information | Validate | EHT-SIG MCS | Number of EHT-SIG Symbols | CRC | Tail
Note for ELR-SIG | No need. SU only |  | No need. 20 MHz only |  | No need. Only one MCS | No need. Only one length | Needed | Needed

## Slide 5: EHT-SIG Fields Needed in ELR-SIG
September 2024
EHT-SIG (EHT SU) Part 1 | Common Info(non-OFDMA) |  |  |  |  |  |  | 
 | B0-B3 | B4-B5 | B6-B8 | B9 | B10-B11 | B12 | B13-B16 | B17-B19
 | Spatial Reuse | GI+LTF Size | Number of UHR-LTF Symbols | LDPC Extra Symbol Segment | Pre-FEC padding Factor | PE Disambiguity | Disregard | Number of non-OFDMA Users
Note for ELR-SIG | No need. No SR | No need. Only one combination | No need. Only one number | ? | ? | No need. Only one GI+LTF & PE combination |  | No need. Only one user
EHT-SIG (EHT SU) Part 2 | User field |  |  |  |  |  | CRC | Tail
 | B20-B30 | B31-B34 | B35 | B36-B39 | B40 | B41 | B42-B45 | B46-B51
 | STA-ID | MCS | Reserved | NSS | BF | Coding | CRC | Tail
Note for ELR-SIG | Better to keep STA-ID | Need to keep MCS |  | No need. Single stream only | No need. No beamforming | Needed. Support BCC and LDPC | Needed | Needed

## Slide 6: Legacy LDPC Rate Matching Approaches
Pros and Cons of legacy approaches:
802.11ac approach can be used for ELR
  OFDM symbol is not divided into symbol segments, which provide negligible gains for ELR with small NDBPS.
  Pre-FEC padding is padded to the end of OFDM symbol. LDPC extra OFDM symbol instead of LDPC extra OFDM symbol segment is indicated.
The number of OFDM symbols within one TXOP can be indicated using 9 bits in ELR-SIG.
September 2024
Approach | Pros | Cons
802.11n | No pre-FEC MAC padding | More bits are needed to indicate PSDU length
802.11ac | Simple pre-FEC MAC padding, no indication of a factor is needed | 
802.11ax/be | Reduce pre-FEC MAC padding with 2-bit a factor indication | 2-bit a factor indication

## Slide 7: Summary of ELR-SIG Fields
Contents | Number of Bits | Note
Version Number | 1 | For next Gen. ELR
UL/DL | 1 | Power saving for ELR STA
Length | 9 | Number of OFDM data symbols
MCS | 1 | Two MCSs
Coding | 1 | BCC/legacy LDPC, no 2x LDPC
STA-ID | 11 | Power saving for non-targeted ELR receiver
LDPC extra OFDM symbol | 1 | Reuse 802.11ac LDPC rate matching to minimize change
TXOP | 7 | can be skipped if there is no space
CRC | 4 | 4-bit in each ELR-SIG symbol
Tail | 6 | 6-bit in each ELR-SIG symbol
September 2024

## Slide 8: Proposed Design for ELR-SIG
RRU52 with 4x duplication in 20MHz in [4, 11] is a simple solution for ELR Data transmission
It can be reused for ELR-SIG transmission with BPSK for simplicity
Two OFDM symbols are individually BCC/CRC encoded for early receiver configuration and low false-alarm rate
ELR-SIG-1 | B0 | B1 | B2 | B3 | B4-B12 | B13 | B14-B17 | B18-B23
 | ELR-version | UL/DL | MCS (two MCSs[1]) | Coding (BCC/legacy LDPC) | Length (number of OFDM symbols) | LDPC extra symbol | CRC | Tail
ELR-SIG-2 | B0-B10 |  |  |  | B11-B13 |  | B14-B17 | B18-B23
 | STA-ID |  |  |  | Reserved |  | CRC | Tail
September 2024

## Slide 9: Summary
This contribution proposed designs for ELR-SIG and ELR LDPC rate matching
September 2024

## Slide 10: References
https://mentor.ieee.org/802.11/dcn/24/11-24-0873-00-00bn-design-targets-and-considerations-for-enhanced-long-range.pptx
https://mentor.ieee.org/802.11/dcn/24/11-24-0875-01-00bn-uhr-enhanced-long-range-support.pptx
https://mentor.ieee.org/802.11/dcn/24/11-24-1232-00-00bn-thoughts-on-extended-long-range-transmission.pptx
https://mentor.ieee.org/802.11/dcn/24/11-24-1184-00-00bn-considerations-on-elr-transmission.pptx
https://mentor.ieee.org/802.11/dcn/24/11-24-1410-00-00bn-legacy-preamble-for-elr-ppdu.pptx
https://mentor.ieee.org/802.11/dcn/24/11-24-1454-00-00bn-discussion-on-configuration-indication-of-elr-ppdu.pptx
https://mentor.ieee.org/802.11/dcn/24/11-24-1485-00-00bn-considerations-for-elr-ppdu-format.pptx
https://mentor.ieee.org/802.11/dcn/24/11-24-1455-00-00bn-discussion-on-tb-elr-ppdu.pptx
https://mentor.ieee.org/802.11/dcn/24/11-24-1478-00-00bn-elr-ppdu-design.pptx
https://mentor.ieee.org/802.11/dcn/24/11-24-1592-00-00bn-usig-fields-in-an-elr-ppdu.pptx
https://mentor.ieee.org/802.11/dcn/24/11-24-1488-00-00bn-elr-ppdu-transmission-design.pptx
https://mentor.ieee.org/802.11/dcn/24/11-24-1571-00-00bn-extended-long-range-elr-mark-symbol-design.pptx
https://mentor.ieee.org/802.11/dcn/24/11-24-1573-00-00bn-an-elr-ppdu-follow-up.pptx
September 2024

## Slide 11: SP1
Do you support to reuse the existing 802.11ac LDPC rate matching with 1-bit LDPC extra OFDM symbol indication for ELR LDPC rate matching
September 2024

## Slide 12: SP2
Do you support the following two-symbol design for ELR-SIG?
ELR-SIG-1 | B0 | B1 | B2 | B3 | B4-B12 | B13 | B14-B17 | B18-B23
 | ELR-version (0 for UHR ELR PPDU) | UL/DL | MCS | Coding | Length (number of OFDM data symbols -1) | LDPC extra OFDM symbol | CRC | Tail
ELR-SIG-2 | B0-B10 |  |  |  | B11-B13 |  | B14-B17 | B18-B23
 | STA-ID |  |  |  | Reserved (Disregard) |  | CRC | Tail
September 2024