## Slide 1: Thoughts on Seamless Roaming and NPCA
Date: 2025-01-6
Authors:
Name | Affiliation | Address | Phone | Email
Ning Gao | OPPO |  |  | gaoning1@oppo.com
Chaoming Luo |  |  |  | 
Liuming Lu |  |  |  | 
Liangxiao Xin |  |  |  | 
Dong Wei |  |  |  | 
Yapu li |  |  |  | 

## Slide 2: Introduction
Seamless Roaming enables context transfer and/or data transfer between current AP MLD and target AP MLD so as to make the roaming procedure faster.
NPCA enables a STA to access the NPCA primary channel while the BSS primary channel is known to be busy due to OBSS traffic or other conditions.
In this contribution, we would like to discuss a different view of channel problem when take the seamless roaming and NPCA into consideration at the same time.

## Slide 3: Scenario and Problem
Assume an NPCA-enabled seamless roaming scenario, after the roaming preparation phase,
  the non-AP MLD will monitor the RSSI with the target AP MLD. [1, 2]
  the non-AP MLD will send a Roaming Request frame to the target AP MLD when appropriate. [1, 2]
Since roaming usually occurs at the edge of a BSS, the non-AP MLD and the target AP MLD may suffer a more severe different view of channel problem,
the non-AP MLD is on BSS P-CH while the target AP MLD is on NPCA P-CH.
the non-AP MLD is on NPCA P-CH while the target AP MLD is on BSS P-CH.
As a result,
  the non-AP MLD may miss some opportunities to monitor the RSSI with the target AP MLD.
  the non-AP MLD may not be able to send the Roaming Request frame to the target AP MLD in time.
Finally, a delayed Roaming Request frame will reduce the seamless roaming performance.

## Slide 4: Proposed Solution
Proposed: Target AP MLD informs non-AP MLD of its NPCA Status and Expiration Time information through the current AP MLD
  The NPCA Status may include BSS/NPCA P-CH, Dwell Time, and Max BW.
  The Expiration Time may be a TSF timestamp.
  If the received Expiration Time has not expired, the non-AP MLD may switch to the NPCA P-CH if the target AP MLD is still on it. Then, monitor the RSSI and/or send a Roaming Request frame to the target AP MLD if needed.
  This approach can make the NPCA-enabled seamless roaming procedure more effective.

## Slide 5: Summary
A different view of channel problem is discussed in an NPCA-enabled seamless roaming scenario.
Since roaming usually occurs at the edge of a BSS, the non-AP MLD and the target AP MLD may suffer a more severe different view of channel problem.
Due to this problem, the non-AP MLD may miss some opportunities to monitor the RSSI with the target AP MLD and may be unable to send the Roaming Request frame to the target AP MLD in time.
To solve this problem, a solution that transmits the NPCA status of the target AP MLD and the expiration time to the non-AP MLD through the current AP MLD is proposed.
This approach can make the NPCA-enabled seamless roaming procedure more effective.
Further discussion on this problem may be needed.

## Slide 6: Reference
[1] 11-24-0349-03-00bn-enhanced-fast-bss-transition, Guogang Huang
[2] 11-24-1812-00-00bn-seamless-roaming-through-a-target-ap-follow-up, Binita Gupta

## Slide 7: SP 1
Do you agree that the different view of channel problem (shown in slide 3) should be considered when NPCA is enabled in seamless roaming procedure?
  Yes/No/Abstain