## Slide 1: Coordinated TDMA analysis for time-sensitive traffic - Follow Up
Date: 10-14-2024

## Slide 2: Goals
Performance evaluation of C-TDMA under congested scenarios, including OBSS/ESS and repeater deployments, focusing on time-sensitive services
Establishment of realistic simulation frameworks including modeling of high-level transport protocols
Discuss and evaluate different C-TDMA strategies to calculate the shared TXOP length

## Slide 3: Introduction and Motivation
802.11bn targets the improvement of packet delivery by reducing the transmission latency and enhancing network reliability [1]
Applications and use cases with QoS-related requirements (e.g., bounded latency and reliability) have been growing in recent times [2]
In [3], C-TDMA simulation results were presented for some specific network scenarios, covering OBSS and Repeater/Mesh scenarios.
In this follow-up contribution we want to cover additional scenarios where the traffic load for different BSSs is not balanced, creating new network conditions and analyzing the performance under different strategies for deciding which fraction of the gaining TXOP is shared.
The objective of this contribution is to identify aspects to be taken into account for making decisions about how and with whom to cooperate.

## Slide 4: C-TDMA: Recap
BSS1 TXOP
Time
BSS2 TXOP
Time
AP BSS1
AP BSS2
TXS RTS TF
CTS
Shared TXOP
BSS2 TXOP
BSS1 TXOP
TXS RTS TF
CTS
Shared TXOP
Coordinated TDMA allows cooperation of two APs, by sharing the gained TXOP between them
Both BSSs take advantage of the gained time, reducing the waiting time to access the channel, and hence the latency of the different traffic flows, especially for those that have higher priority access category
Other AP BSSs
TXOP
TXOP
Time

## Slide 5: C-TDMA: Latency Reduction
C-TDMA does not change the time used per BSS, it redistributes the assigned time to the coordinated APs, getting an improvement in latency, by reducing the access time for the shared AP
BSS1 TXOP
Time
Time
AP BSS1
AP BSS2
TXOP
BSS2 TXOP
BSS1 TXOP
TXOP
BSS1 Inter Access Interval
Time
Uncoordinated
Other AP and non-AP STAs
Heavily Congested
BSS1 TXOP
Time
BSS2 TXOP
Time
AP BSS1
AP BSS2
TXS RTS TF
CTS
Shared TXOP
BSS2 TXOP
BSS1 TXOP
TXS RTS TF
CTS
Shared TXOP
Other AP and non-AP STAs
TXOP
Time
TXOP
BSS1 TXOP
BSS2 TXOP
TXS RTS TF
CTS
Shared TXOP
BSS1 Inter Access Interval
BSS1 Inter Access Interval
C-TDMA
Heavily Congested

## Slide 6: Simulation Setup
We identify two scenarios where the C-TDMA mechanism can be deployed
  OBSS scenario: coordination between one pair of independent neighboring BSSs sharing the same channel
  Repeater (ESS) scenario: coordination between two in-home AP devices from the same network (ESS), and sharing the same channel.

## Slide 7: OBSS Simulation Setup
Three OBSS scenarios are proposed, under two different conditions
Scenario 1: Balanced OBSS
  Four BSSs sharing the same channel, having balanced traffic load and number of associated STAs between the BSSs
  Coordination is enabled between BSS1 and BSS2, while BSS3/4 remain as uncoordinated OBSS
Scenario 2: Unbalanced OBSS
  Two BSSs sharing the same channel, having unbalanced traffic load and number of associated STAs between the two BSSs
  Similar network traffic generation and priority classification in both BSSs: Both APs generate TXOPs on commonly assigned ACs, creating opportunities on both sides, having an effective cooperation
Scenario 3: Unbalanced OBSS and unequal priority assignment
  Three BSSs sharing the same channel
  Coordination is possible between BSS1 and BSS2, while BSS3 remains as an OBSS
  Unbalanced traffic load and number of associated STAs between BSS1 and BSS2
  Different network traffic generation and priority assignment in each BSS: Both APs do not generate TXOPs on commonly assigned ACs, creating fewer cooperation opportunities
Data frames PHY/MAC link configuration for associated STAs
  SU 80 MHz/1SS/MCS:11 for creating overloading situation
OBSS STAs are in [PD,ED] range
  BSS STAs are in ED range

## Slide 8: Repeater Simulation Setup
ESS is composed of a Gateway (GW) and Repeater (R) devices, connected through a wireless backhaul
The Repeater is composed of a non-AP STA and AP devices, internally bridged and using the same radio
The Repeater has 5 associated STAs, creating an unbalanced situation between GW and R
OBSS STAs are in [PD, ED] range, and BSS STAs are in ED range
  Gateway and Repeater are in ED range
Two possible coordination scenarios: uncoordinated and GW/R coordinated (both do C-TDMA)
PHY/MAC configuration for Data frames
  SU 80 MHz/1SS/MCS:11 for creating overloading situation
GW
R
802.11 Backhaul

## Slide 9: Traffic Generation (OBSS Case): Scenario 1
From four BSSs [3], two BSSs that may be coordinated (C-TDMA)
Each BSS has the following data services:
  STA1 Service: Video conference (DL/UL 3 Mbps, 250B length) [UDP, VI_AC]
  STA2 Service: Video streaming 4K UHD H264 (DL 32 Mbps, 1500B length) [closed-loop TCP, VI_AC]
  STA3 Service: Gaming (DL/UL 140kbps, Periodicity 7 ms, 110B length) [UDP, VO_AC]
  STA4 Service: Cloud file sync (DL/UL 10 Mbps, 1500B length) [closed-loop TCP, BE_AC]
  STA5 Service: Camera (UL 2 Mbps, 1450B length) [UDP, VI_AC]

## Slide 10: Traffic Generation (OBSS Case): Scenario 2
Two BSSs that may be coordinated (C-TDMA)
Unbalanced traffic and associated STAs, with respect to each BSS
BSS1 data services (9 associated STAs):
  2x Video conference (DL/UL 3 Mbps, 250B length) [UDP, VI_AC]
  2x Video streaming 4K UHD H264 (DL 64 Mbps, 1500B length) [closed-loop TCP, VI_AC]
  2x Gaming (DL/UL 140kbps, Periodicity 7 ms, 110B length) [UDP, VO_AC]
  2x Cloud file sync (DL/UL 10 Mbps, 1500B length) [closed-loop TCP, BE_AC]
  1x Camera (UL 2 Mbps, 1450B length) [UDP, VI_AC]
BSS2 data services (5 associated STAs):
  1x Video conference (DL/UL 3 Mbps, 250B length) [UDP, VI_AC]
  1x Video streaming 4K UHD H264 (DL 64 Mbps, 1500B length) [closed-loop TCP, VI_AC]
  1x Gaming (DL/UL 140kbps, Periodicity 7 ms, 110B length) [UDP, VO_AC]
  1x Cloud file sync (DL/UL 10 Mbps, 1500B length) [closed-loop TCP, BE_AC]
  1x Camera (UL 2 Mbps, 1450B length) [UDP, VI_AC]

## Slide 11: Traffic Generation (OBSS Case): Scenario 3
BSS1 and BSS2 that may be coordinated (C-TDMA), and a third OBSS (BSS3)
BSS1 data services (7 associated STAs):
  2x Video conference (DL/UL 3 Mbps, 250B length) [UDP, VI_AC]
  2x Video streaming 4K UHD H264 (DL 64 Mbps, 1500B length) [closed-loop TCP, VI_AC]
  1x Gaming (DL/UL 140kbps, Periodicity 7 ms, 110B length) [UDP, VO_AC]
  1x Cloud file sync (DL/UL 10 Mbps, 1500B length) [closed-loop TCP, BE_AC]
  1x Camera (UL 2 Mbps, 1450B length) [UDP, VI_AC]
BSS2 data services (3 associated STAs):
  1x Gaming (DL/UL 140kbps, Periodicity 7 ms, 110B length) [UDP, VO_AC]
  1x Cloud file sync (DL/UL 10 Mbps, 1500B length) [closed-loop TCP, BE_AC]
  1x Camera (UL 2 Mbps, 1450B length) [UDP, VI_AC]
BSS3 data services (5 associated STAs):
  1x Video conference (DL/UL 3 Mbps, 250B length) [UDP, VI_AC]
  1x Video streaming 4K UHD H264 (DL 64 Mbps, 1500B length) [closed-loop TCP, VI_AC]
  1x Gaming (DL/UL 140kbps, Periodicity 7 ms, 110B length) [UDP, VO_AC]
  1x Cloud file sync (DL/UL 10 Mbps, 1500B length) [closed-loop TCP, BE_AC]
  1x Camera (UL 2 Mbps, 1450B length) [UDP, VI_AC]

## Slide 12: Traffic Generation (Repeater Case)
Gateway associated STAs:
  STA Repeater: Backhaul link including all the traffic transferred to the Repeater
Repeater associated STAs:
  STA1 Service: Video conference (DL/UL 3 Mbps, 250B length) [UDP, VI_AC]
  STA2 Service: Video streaming 4K UHD H264 (DL 64 Mbps) [closed-loop TCP, VI_AC]
  STA3 Service: Video streaming 4K UHD H264 (DL 64 Mbps) [closed-loop TCP, VI_AC]
  STA4 Service: Gaming (DL/UL 140kbps, Periodicity 7 ms, 110B length) [UDP, VO_AC]
  STA5 Service: Camera (UL 2 Mbps, 1450B length) [UDP, VI_AC]
Backhaul link: STA1-5 services
All the STAs generate UL traffic (using TB and EDCA mechanisms)

## Slide 13: C-TDMA Strategies (1/2)
We distinguish four different approaches to decide the shared TXOP length
Strategy 1 (S1): Share the remaining TXOP length, after the sharing AP local buffers are empty (for the gained and higher ACs)
  TXOP ends after the shared AP finishes, which may send a CF-End frame for early termination
Strategy 2 (S2): Soft time threshold set from higher layers (managed networks)
  The sharing AP may start sharing the TXOP before the time threshold if it has no more data, for the gained and higher ACs, in its BSS (Case A)
  The sharing AP may delay sharing the TXOP if there is an ongoing data exchange that exceeds the time threshold (Case B)
  It defines a flexible maximum time length that the sharing AP can use for transferring data, established by an external arbiter, while the rest will be used by the shared AP
  TXOP ends after the shared AP finishes, which may send a CF-End frame for early termination
BSS1 TXOP
(Sharing)
BSS2 TXOP (Shared)
Time
AP BSS1
AP BSS2
TXOP
C-TDMA
BSS1
No Data
Time
Threshold
BSS2 TXOP
(Sharing)
BSS1 TXOP (Shared)
TXOP
Time
Threshold
Last exchange finished
S2: Case A
S2: Case B
BSS2
No Data
BSS1
No Data
Note: control frame exchange removed for figure simplification

## Slide 14: C-TDMA Strategies (2/2)
Strategy 3 (S3): Dynamically calculated time threshold based on the buffer status knowledge
  Based on the current knowledge of the buffer’s status for the gained AC, each AP calculates the needed TXOP length
  The sharing AP sends its calculation in the ICF, and the shared AP includes its calculation in the ICR
  The sharing AP prioritizes its own needs when the sum of both calculations exceeds the TXOP limit
  Once the pre-negotiation concludes, strategy 2 rules are followed
Strategy 4 (S4): Dynamically calculated time threshold based on the buffer status knowledge and traffic prediction
  In addition to the estimation from Strategy 3, the APs estimate additional time based on the prediction of future incoming data frames along the TXOP (out of the scope of this standard), having a more accurate calculation.
  Based on the previous calculation, strategy 3 rules are followed
In summary, S1 is intended to work in standalone mode, while S2-S4 require pre-negotiation or management from higher layers. Each strategy should be selected depending on the nature of the network

## Slide 15: OBSS Scenario 1 - Balanced OBSS (1/2)
Overall slight reduction of the network tail latency for all the strategies (except for S1), as BSS3 and BSS4 remain uncoordinated.
Gaming service shows similar performance for any of the C-TDMA strategies, mainly since it sends short-duration data frames, having no problems for sharing time from a gained TXOP.

## Slide 16: OBSS Scenario 1 - Balanced OBSS (2/2)
Video conference and video streaming show similar behavior, except for S1, same performance is reported by the other strategies, mainly to due the fact that both networks are balanced and share similar traffic.
For this setup, managed threshold and dynamic threshold calculation converge to same result, being equivalent strategies under this balanced situation.

## Slide 17: OBSS Scenario 2 - Unbalanced OBSS (1/2)
Overall reduction of the network tail latency for all the strategies, except for S1, which has a minor impact on the performance.
Gaming service shows similar performance for any of the C-TDMA strategies, mainly since it sends short-duration data frames, having no problems sharing time from a gained TXOP.

## Slide 18: OBSS Scenario 2 - Unbalanced OBSS (2/2)
Video conference and video streaming show similar behavior, depending on the strategy it may have a different impact.
Both S2 strategies have the opposite result. In the case of balanced S2, it gives more resources to BSS2, while for the unbalanced S2 it is the contrary.
Strategy S3/S4 adapts dynamically, giving an intermediate improvement, balancing the performance gain.

## Slide 19: OBSS Scenario 3 - Unequal Priority (1/2)
The overall network latency performance is decreased, as a consequence of having large unbalanced traffic between BSS1 and BSS2, and at the same time both networks do not share the same priority AC for the main services, not allowing effective cooperation.
For gaming, both networks generate VO AC traffic and it may take advantage from lower priority opportunities. As BSS2 generates fewer VI opportunities to share, there is no advantage for BSS1. On the other side, BSS2 takes advantage of BSS1 network.

## Slide 20: OBSS Scenario 3 - Unequal Priority (2/2)
For video streaming and video conference, BSS2 has no VI AC traffic, therefore there is no effective cooperation between the APs, and resulting in a performance degradation.
In the case of having cooperation between BSS1 and BSS3, instead of BSS2, the results would be different, similar to the ones found in OBSS Scenario 1.

## Slide 21: Summary (OBSS)
For OBSS scenarios, the C-TDMA coordination is effective only in the case that both APs generate an equal number of channel gain opportunities in the same or equivalent ACs (priority), otherwise it may deteriorate the performance of both networks.
Only for balanced OBSS we get similar performance results for managed and dynamic C-TDMA threshold setup, while dynamic calculation seems to be more adequate in OBSS scenarios, considering its uncorrelated nature.

## Slide 22: Repeater/Mesh Simulation Results
Five different coordination setups
  No coordination between GW and Repeater (baseline)
  C-TDMA Strategy 1 (S1)
  C-TDMA Strategy 2 (S2)
    Having a sharing threshold of 50/50: 50% of TXOP length for the GW, and 50% length for the Repeater
    Having a sharing threshold of 40/60: 40% of TXOP length for the GW, and 60% length for the Repeater
  C-TDMA Strategy 3 (S3)
  C-TDMA Strategy 4 (S4)
C-TDMA based on S2/S3/S4 improves the network latency tail by 69% to 136%, where S1 has a minor impact on the performance.
C-TDMA S4 based on dynamic TXOP calculation gets the best performance, obtaining a similar result for the unbalanced tunning of S2 (40/60).

## Slide 23: Repeater/Mesh – Gaming/Video Conference Results
C-TDMA based on unbalanced S2 and S3/S4 improves the gaming and video conference latency tail, where S1 has a low impact on the performance improvement, and balanced S2 is less effective due to the network topology characteristics.

## Slide 24: Repeater/Mesh – Video Streaming Results
Regardless of video streaming throughput, the best performance is obtained for unbalanced S2 and S4.
The performance difference between balanced S2 and S4 is due to the nature of the unbalanced network topology, where S4 adjusts the needs dynamically.
Even in the unbalanced network situation, C-TDMA S2 still performs well, as both BSSs are correlated.

## Slide 25: Summary (Repeater/Mesh)
As expected, and considering the simulation results shown in [3], C-TDMA may improve the high-priority latency performance in repeater/mesh topologies.
In repetear/mesh scenarios, the correlated backhaul traffic flow helps to guarantee cooperation between the APs, unlike in the OBSS scenario.
Both C-TDMA strategies, based on managed setup or dynamic calculation, we get similar performance for the case where the C-TDMA threshold is set from higher layers (managed) and the case where the threshold is dynamically calculated and negotiated between the APs.

## Slide 26: Conclusion
We have shown performance results for C-TDMA under different topologies, traffic situations, and sharing TXOP calculation strategies.
The network topology and traffic setup are important parameters that define the suitability of cooperation between the APs. A wrong choice can deteriorate the performance of the networks.
The C-TDMA coordination is effective only in the case that both APs generate an equal number of channel gain opportunities in equivalent ACs.
Consequently, C-TDMA mechanism could be enabled per AC, instead of using for all the network traffic, especially for those high-priority services, being used in both networks.

## Slide 27: References
[1] IEEE 802.11-23/0028r6, UHR PAR discussion
[2] Inaki Val and et al. (MaxLinear), “High Criticality Use Cases and Requirements”, 23/1522r0
[3] Inaki Val and et al. (MaxLinear), “Coordinated TDMA analysis for time-sensitive traffic under congested scenarios”, 24/1375r0