## Slide 1: DRU Tone Plan for 20 MHz Distribution Bandwidth
Date: 2024-10-28
Authors:

## Slide 2: Abstract
In this contribution, we discuss several recommendations on DRU tone allocation
  We propose a tone allocation plan for 20 MHz based on the contribution in [1]

## Slide 3: DRU Tone Plan Recommendations
Recommendation 1: DRU tones should be shifted versions of each other to ensure they perform similarly in fading channel
  For example, 26-tone DRU 9 and 26-tone DRU 5 will perform differently as the corresponding tones are not shifted versions of other 26-tone DRUs for the tone plan in [1]
  Tone plans in [1] for 40 MHz and 80 MHz do not have this issue
Recommendation 2: DRU tone plan should avoid distortions by providing more DC tones given the available subcarriers in UHR LTF
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in a 20 MHz UHR PPDU [1] |  |  |  |  | 
DRU type | DRU index and subcarrier range |  |  |  | 
26-tone DRU i=1:9 | DRU1 [-120:9:-12, 6:9:114] | DRU2 [-116:9:-8, 10:9:118] | DRU3 [-118:9:-10, 8:9:116] | DRU4 [-114:9:-6, 12:9:120] | DRU5 [-112:9:-4, 5:9:113]
 | DRU6 [-119:9:-11, 7:9:115] | DRU7 [-115:9:-7, 11:9:119] | DRU8 [-117:9:-9, 9:9:117] | DRU9 [-113:9:-5, 4:9:112] | 
52-tone DRU i=1:4 | DRU1 26-tone [DRU1, DRU2] |  | DRU2 26-tone [DRU3, DRU4] |  | 
 | DRU3 26-tone [DRU6, DRU7] |  | DRU4 26-tone [DRU8, DRU9] |  | 
106-tone DRU i=1:2 | DRU1 26-tone [DRU1~4], [-3, 3] |  | DRU2 26-tone [DRU6~9], [-2, 2] |  | 
DRU2 = DRU1 + 4
DRU3 = DRU1 + 2
DRU4 = DRU1 + 6
DRU6 = DRU1 + 1
DRU7 = DRU1 + 5
DRU8 = DRU1 + 3
DRU5?
DRU9?
Mahmoud Kamel, InterDigital

## Slide 4: DRU Tone Plan Constraints
Recommendation 3: Pilot indices should be spread across the BW to exploit frequency diversity
  For instance, 106-tone DRU 2 can span from indices -119 to 112 whereas the pilot indices are from -56 to 103 for the plan in [1]
Pilot indices for DRU transmission over 20MHz | 
DRU size | KdRxx_i
DRU26, i = 1:9 | { -111 15 }, { -89 37 }, { -100 26 }, { -78 48 }, { -67 59 }, { -56 70 }, { -34 92 }, { -45 81 }, { -23 103 }
DRU52, i = 1:4 | { -111 -89 15 37 }, { -100 -78 26 48 }, { -56 -34 70 92 }, { -45 -23 81 103 }
DRU106, i = 1:2 | { -111 -78 15 48 }, { -56 -23 70 103 }
Mahmoud Kamel, InterDigital

## Slide 5: Proposed 20 MHz DRU Tone Plan
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in a 20 MHz UHR PPDU (Proposed) |  |  |  |  | 
DRU type | DRU index and subcarrier range |  |  |  | 
26-tone DRU i=1:9 | DRU1 [-121:9:-13, 5:9:113] | DRU2 [-117:9:-9, 9:9:117] | DRU3 [-119:9:-11, 7:9:115] | DRU4 [-115:9:-7, 11:9:119] | DRU5 [-113:9:-5, 13:9:121]
 | DRU6 [-120:9:-12, 6:9:114] | DRU7 [-116:9:-8, 10:9:118] | DRU8 [-118:9:-10, 8:9:116] | DRU9 [-114:9:-6, 12:9:120] | 
52-tone DRU i=1:4 | DRU1 26-tone [DRU1, DRU2] |  | DRU2 26-tone [DRU3, DRU4] |  | 
 | DRU3 26-tone [DRU6, DRU7] |  | DRU4 26-tone [DRU8, DRU9] |  | 
106-tone DRU i=1:2 | DRU1 26-tone [DRU1~4], [-4, 3] |  | DRU2 26-tone [DRU6~9], [-3, 4] |  | 
With the proposed tone plan in this contribution,
  The DRU1-DRU9 are shifted versions of each other
  Two more DC tones are available for 106-DRU as this tone plan ranges from -121 to -3 and 3 to 121, instead of -120 to -2 and 2 to 120 in [1]
Pilot indices are TBD
Mahmoud Kamel, InterDigital

## Slide 6: SP 1
Do you agree that DRU tone indices should be shifted versions of each other to ensure they perform similarly in fading channel?

## Slide 7: References
[1] 11/24-0468r2 DRU Tone Plan for 11bn, Mediatek
Mahmoud Kamel, InterDigital