## Slide 1: Downlink Data Rates for Bi-static Backscattering
Date: 2024-11-11
Authors:
Name | Affiliations | Address | Phone | Email
Bin Qian | Huawei | Shenzhen, China |  | qianbin14@huawei.com
Lei Huang |  | Singapore |  | 
Panpan Li |  | Singapore |  | 
David, Xun Yang |  | Singapore |  | 
Nov. 2024
Notes: September 2012

## Slide 2: Introduction
Downlink data rates have been previously discussed in the integrated energizer deployment [1]
Bi-static backscattering communication in 2.4 GHz has been agreed as an important use case in AMP [2]
This contribution aims to define suitable downlink data rates for bi-static backscattering in 2.4 GHz
Nov. 2024

## Slide 3: Recap: Bi-static Backscattering
In a bi-static backscatter topology, a separate Carrier Source provides the input carrier signal, while the AMP AP receives the backscattered signal
  Half duplex operation at the AP side
  Approximate coverage of ~10 meters
Nov. 2024

## Slide 4: Bi-static Backscatter Tag Requirements
AMP mono-static backscattering tag requirements were proposed in [3]
It is preferred that the bi-static and mono-static backscattering tag can share the similar basic requirements
  Standardization across technology: Shared requirements enable unified protocols and simplified compliance for both mono-static and bi-static tags
  Cost efficiency: Streamlined development reduces design costs, supporting widespread deployment
  Interoperability: Consistent requirements improve cross-device compatibility and network integration without specialized equipment
  Scalability and flexibility in applications: Shared requirements broaden application range and simplify upgrades, making deployments more scalable and flexible
The backscattering tag could support optional enhanced requirements, e.g., reflection amplifier, larger energy storage
Nov. 2024

## Slide 5: Link Budget Analysis
Link budget between AMP AP and AMP Tag [4]
With a lower DL link budget (ETSI & China), lower data rates may be necessary to maintain reliability, especially under noisy or distant conditions
Nov. 2024
DL: AMP AP to AMP Tag |  | 
Antenna gain of AMP Tag (dBi) | 0 | 
Minimum receiving power for AMP Tag (dBm) | -45 | 
Bandwidth & Frequency | 4 MHz @ 2.4 GHz | 
EIRP of AP (dBm) | 27 (FCC) | 16 (ETSI & China)
DL Link Budget (dB) | 72 | 61
UL: AMP Tag to AMP Reader | 
Receiver sensitivity of AP (dBm) | -95
Minimum incident power of AMP Tag (dBm) | -20
Backscattering loss at AMP Tag (dB) | 5
Frequency | 2.4 GHz
UL Link Budget (dB) | 70

## Slide 6: Downlink Data Rate Considerations
Recommended DL rates
  250 kbps: For applications needing efficient communication
  125 kbps: A balanced rate, suitable for medium-range applications
  62.5 kbps: Optimized for long-range and low-power operations
Rationale summary
  Alignment with RFID: Comparable requirements make similar DL rates effective
    Typical RFID DL rates (40 – 160 kbps) are suitable for low-power AMP tags
  Link budget suitability: Recommended DL rates fit within regional link budget constraints
    Maximum UL data rate can reach 500 kbps to 1 Mbps
  WUR compatibility: Supports consistency with 802.11ba
    Extending 125 kbps from current WUR rates is straightforward
Nov. 2024

## Slide 7: Summary
Aligning bi-static and mono-static tags supports standardization, cost-efficiency, interoperability, and scalability
DL data rate recommendations
  250 kbps, 125 kbps, and 62.5 kbps to address various application needs from high throughput to long-range
Nov. 2024

## Slide 8: References
[1] 11-24-1345-02-00bp-high-level-requirements-for-downlink-phy-in-2-4-ghz
[2] 11-24-1322-04-00bp-tgbp-motion-dock
[3] 11-24-1237-00-00bp-amp-tag-sta-requirements-for-close-range-backscattering
[4] 11-24-1215-00-00bp-feasibility-study-on-long-range-backscatter-operation
Nov. 2024

## Slide 9: SP 1
Do you support the following text:
  11bp defines a data rate of 62.5 kbps for DL transmission
  Yes:
  No:
  Abstain:
Nov. 2024

## Slide 10: SP 2
Do you support the following text:
  11bp defines a data rate of 125 kbps for DL transmission
  Yes:
  No:
  Abstain:
Nov. 2024

## Slide 11: SP 3
Do you support the following text:
  11bp defines a data rate of 250 kbps for DL transmission
  Yes:
  No:
  Abstain:
Nov. 2024