## Slide 1: Downlink Data Rates for Bi-static Backscattering
Date: 2024-11-11
Authors:
Name | Affiliations | Address | Phone | Email
Bin Qian | Huawei | Shenzhen, China |  | qianbin14@huawei.com
Lei Huang |  | Singapore |  | 
Panpan Li |  | Singapore |  | 
David, Xun Yang |  | Singapore |  | 
Nov. 2024
Notes: September 2012

## Slide 2: Introduction
Downlink data rates have been previously discussed in the integrated energizer deployment [1]
Bi-static backscattering communication in 2.4 GHz has been agreed as an important use case in AMP [2]
This contribution aims to define suitable downlink data rates for bi-static backscattering in 2.4 GHz
Nov. 2024

## Slide 3: Recap: Bi-static Backscattering
In a bi-static backscatter topology, a separate Carrier Source provides the input carrier signal, while the AMP AP receives the backscattered signal
  AP operates in half duplex mode
  Coverage typically extends to several meters
Nov. 2024

## Slide 4: Bi-static Backscatter Tag Requirements
Requirements for AMP mono-static backscattering tags were proposed in [3]
It is preferred that the bi-static and mono-static backscattering tag can share the similar basic requirements
  Standardization: Shared requirements enable unified protocols and simplified compliance for both mono-static and bi-static tags
  Cost efficiency: Standardized designs reduce development costs, supporting widespread deployment
  Interoperability: Consistent requirements improve cross-device compatibility and network integration without specialized equipment
  Scalability and flexibility in applications: Shared requirements broaden application range and simplify upgrades, making deployments more scalable and flexible
The backscattering tag could support optional enhanced requirements, e.g., mixer, reflection amplifier, larger energy storage
Nov. 2024

## Slide 5: Noise Analysis
DL link budget analysis between AMP AP and AMP Tag [4]
In practice, the backscatter tags typically lack baseband filters, capturing all noise and interference within the 80 MHz bandwidth in the 2.4 GHz band
Thermal noise power in 2.4 GHz band is about -95 dBm, providing sufficient SNR for higher data rates, such as 250 kbps
Nov. 2024
DL: AMP AP to AMP Tag |  | 
Antenna gain of AMP Tag (dBi) | 0 | 
Minimum receiving power for AMP Tag (dBm) | -45 | 
Bandwidth & Frequency | 4 MHz | 
Frequency | 2.4 GHz | 
EIRP of AP (dBm) | 27 (FCC) | 16 (ETSI & China)
DL Link Budget (dB) | 72 | 61

## Slide 6: Interference Analysis (1/2)
In mono-static use case, the AP-tag distance is typically 10-20 cm, ensuring a stronger signal than interference. However, in bi-static configurations, distances can extend to several meters (e.g., 5 meters), where the signal strength can be comparable to interference
In 11n Channel Model D, SNR for WUR HDR at 10% PER is ~2 dB, while for WUR LDR, it’s ~-1.5 dB, a 3.5 dB difference [5].
This 3.5 dB difference enables the AP-tag distance to extend 1-2 meters beyond the the interference source
Given severe interference in the 2.4 GHz band, interference has to be accounted for in downlink data rate selection.
Nov. 2024
Distance (m) | 0.1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Path loss (dB) | 23 | 43 | 49 | 52 | 55 | 57 | 58.6 | 59.9 | 61.1 | 62.1

## Slide 7: Interference Analysis (2/2)
Example: Indoor environment
  Assume a tag is positioned at the center of a 15m  15m indoor area, with an interference source randomly placed within the area
  Assume the threshold SIR for 250 kbps (10% PER) is 2 dB, and the threshold SIR for 62.5 kbps is -1.5 dB
  Probabilities are calculated for downlink SIR falling below threshold in this indoor environment
  Using 62.5 kbps can significantly reduce the probability of severe interference, enabling more reliable communication in environments with higher interference levels
Nov. 2024
AP-Tag distance (m) | 250 kbps | 62.5 kbps
4 | 0.35 | 0.16
5 | 0.55 | 0.24
6 | 0.68 | 0.35

## Slide 8: Interference with Legacy Wi-Fi
Using 62.5 kbps improves reliability in challenging environments, which reduces the likelihood of packet errors
Reduced errors lead to fewer re-transmissions compared to 250 kbps
For each downlink data transmission, there will be one or more Excitation fields, each lasting about 1.5 ms
Lower data rates like 62.5 kbps can reduce overall airtime usage and long-term interference with legacy Wi-Fi
Nov. 2024

## Slide 9: Downlink Data Rate Considerations
Recommended DL rates
  250 kbps: For applications needing efficient communication with minimal interference
  125 kbps: A balanced rate, suitable for medium-range applications
  62.5 kbps: Optimized for long-range, and resilient to interference
Rationale summary
  Noise and interference: Recommended DL rates fit various scenarios from efficient communication to long-range (potentially strong interference)
  WUR compatibility: Compatible with 802.11ba
    Extending 125 kbps from current WUR rates is straightforward
  RFID Alignment: Comparable requirements make similar DL rates effective
    Typical RFID DL rates (40 – 160 kbps) are suitable for low-power AMP tags
Nov. 2024

## Slide 10: Summary
Aligning bi-static and mono-static tags supports standardization, cost-efficiency, interoperability, and scalability
DL data rate recommendations
  250 kbps, 125 kbps, and 62.5 kbps to address various application needs from high throughput to long-range, interference-resilient communication
Nov. 2024

## Slide 11: References
[1] 11-24-1345-02-00bp-high-level-requirements-for-downlink-phy-in-2-4-ghz
[2] 11-24-1322-04-00bp-tgbp-motion-dock
[3] 11-24-1237-00-00bp-amp-tag-sta-requirements-for-close-range-backscattering
[4] 11-24-1215-00-00bp-feasibility-study-on-long-range-backscatter-operation
[5] Steve Shellhammer, Alfred Asterjadhi, Yanjun Sun, “IEEE 802.11ba: Ultra-low power wave-up radio standard”
[6] EPC Radio-Frequency Identity Generation-2 UHF RFID Standard, Release 3.0, Ratified, Jan 2024
Nov. 2024

## Slide 12: SP 1
Do you support the following text:
  11bp defines a data rate of 62.5 kbps for DL transmission
  Yes:
  No:
  Abstain:
Nov. 2024

## Slide 13: SP 2
Do you support the following text:
  11bp defines a data rate of 125 kbps for DL transmission
  Yes:
  No:
  Abstain:
Nov. 2024

## Slide 14: SP 3
Do you support the following text:
  11bp defines a data rate of 250 kbps for DL transmission
  Yes:
  No:
  Abstain:
Nov. 2024