## Slide 1: TXOP sharing in contention style
Date: 2025-04-14
Authors:
Name | Affiliation | Address | Phone | Email
Junbin Chen | TP-Link Systems Inc. |  |  | chenjunbin@tp-link.com.hk
Yunpeng Yang |  |  |  | yangyunpeng@tp-link.com.hk
Renfang Zhou |  |  |  | zhourenfang@tp-link.com.hk
Yaoshen Cui |  |  |  | cuiyaoshen@tp-link.com.hk
Haozheng Li |  |  |  | lihaozheng@tp-link.com.hk
Qingwei Fu |  |  |  | fuqingwei@tp-link.com.hk
Shuyu Shi |  |  |  | shishuyu@tp-link.com.hk
Yu Zhu |  |  |  | zhuyu@tp-link.com.hk

## Slide 2: Abstract
In TGbn D0.2 [1-2] we have define the Co-TDMA to enables an AP to share a time portion of an obtained TXOP with one or more other APs to transmit one or more PPDUs.
  The procedure contains a polling phase, a TXOP allocation phase and a possible TXOP return phase [1-5].
Basically, the TXOP allocation is scheduled by the sharing AP based on the information collected during the polling phase.
  However, sometimes the polled AP may not be able to report it in time during the polling phase.
  E.g., due to aperiodic IDC issues occur in the polled AP [6]; or, the event-based low latency (EBLL) traffic [7-9] just arrives after the polling phase.
  Besides, the EBLL traffic may come to the sharing AP during the TXOP allocated to shared AP.
In this presentation, we’d like to discuss about the Co-TDMA for handling the issues above.

## Slide 3: The Co-TDMA in TGbn
There still remains several issues in the Co-TDMA of previous contributions:
If the LL traffic of sharing AP arrives during the TXOP allocation phase, it waits until TXOP return.
The sharing AP needs to collect the information of the pending LL traffic of multiple shared APs and determines which shared AP to be the TXOP Sharing (TXS) responder based on such information.
  However, the information collection can be quite difficult for the event-based Low Latency (EBLL) traffic.
MU-RTS TXS
CTS
Data transmission
LL traffic arrives and suffers delay
TXOP return
Data transmission
Sharing AP
Shared AP
MU-RTS TXS
CTS
Data transmission
Sharing AP1
Shared AP2
TXOP return
MU-RTS TXS
CTS
Data transmission
TXOP return
Shared AP3
Shared AP4
BSRP
BSR
BSR
BSR
LL traffic arrives
LL traffic arrives
EBLL traffic arrives and suffers delay

## Slide 4: Proposal 1: TXS with puncturing mode
We propose to define a mode that:
  The sharing AP can share a subset of its bandwidth to the shared AP(s), and operate with the remaining bandwidth in the puncturing mode during the allocated duration.
  In such mode, the sharing AP is still available to deliver any possible LL traffic arrived during the allocated TXS duration in puncturing mode.
  Further, the sharing AP may announce multiple bandwidth units (BWUs) for multiple shared APs.
    The granularity of BWU can be 20MHz for simplicity.
MU-RTS TXS
CTS
Data transmission on BWU1
BWU1 shared to AP2
Data transmission in puncturing mode
Sharing AP1
Shared AP2
Data transmission
LL traffic arrives and can be delivered
CTS
Data transmission on BWU2
Shared AP3
BWU2 shared to AP3

## Slide 5: Proposal 2: allow contention in TXS duration (1/2)
Considering the fact that the EBLL traffic arrives randomly, we suggest to allow some shared APs to contend some RA-BWUs for their EBLL traffic
  The contention can be P-EDCA-based or UORA-based, TBD.
  The number of shared APs allowed to participated in the contention can be limited by conditions (e.g., the delay bound limit) announced by sharing AP.
  The same RA-BWU can be utilized by more than one shared APs if there is more allocated TXS duration left.
MU-RTS TXS
CTS
Data transmission on BWU1
RA-BWU2
BWU1 for AP2
Sharing AP1
Shared AP2
Data transmission
Win RA-BWU2
Shared AP3
Data transmission in puncturing mode
Win RA-BWU2
Shared AP4

## Slide 6: Proposal 2: allow contention in TXS duration (2/2)
Considering the fact that the EBLL traffic arrives randomly, we suggest to allow some shared APs to contend some RA-BWUs for their EBLL traffic
  Also, the sharing AP may assign a contention-free period in RA-BWU for a specific shared AP, during which the specific shared AP can use the RA-BWU without contention.
MU-RTS TXS
CTS
Data transmission on BWU1
RA-BWU2, (AP3 contention-free)
BWU1 for AP2
Sharing AP1
Shared AP2
Data transmission
RA-BWU2
Shared AP3
Data transmission in puncturing mode
Win RA-BWU2
Shared AP4
Contention-free

## Slide 7: The priority of shared APs
The shared AP which are assigned a specific BWU with a CFP is of the highest priority during the contention.
The sharing AP can announce some constraints (e.g. the delay bound requirement) in the MRTT frame.
  For example, only the shared APs whose delay bound of the pending LL data is lower than the announced requirement can participate in the contention.
  An exemplary of the MRTT frame can be defined as follow.
The contention for RA-BWU can be performed in a similar way as EDCA, or in the UORA contention style.
  In P-EDCA style, the shared APs shall initiate a TXS back-off counter based on the delay bound of pending LL data.
  In UORA style, the shared AP shall invoke the OBO contention procedure and transmit a RTS to protect its following transmission.
MAC Header
Common info
User info list
Padding
FCS
APID
BWU index
BWU size
Allocation duration
Contention-free period
Delay requirement

## Slide 8: Summary
The polled AP might not be able to report its requirements in time during the polling phase
  The polled AP might suffers aperiodic IDC issues.
  The arrival of event-based low-latency (EBLL) traffic is unpredictable to the sharing AP.
  The sharing AP has to query the buffer status of multiple shared APs over and over again.
  The EB-LL traffic of sharing AP may also arrive during the TXS procedure and suffer significant delay.
In this presentation, we proposed a special TXS mode for EBLL traffic/aperiodic IDC:
  The sharing AP has no need to query the information such as buffer status from shared APs.
  The sharing AP can reserve some sub-channels which are announced for TXOP sharing.
  The sharing AP continues its data transmission on the remaining parts of its bandwidth.
  The reserved sub-channels are assigned to or contended by multiple shared APs with LL traffic.
  The priority of multiple shared APs can be distinguished by the contention procedure.

## Slide 9: References
[1] P802.11bn D0.2
[2] 25/0521 PDT-MAC-Co-TDMA-CR-CC50-Part-1, Sanket Kalamkar (Qualcomm Technologies Inc.)
[3] 23/1871 M-AP Coordinated Transmission framework,
[4] 24/0512 Considerations for Coordinated TDMA,
[5] 24/0411 TXOP Return in C-TDMA, Geonhwan Kim (LG Electronics)
[6] 24/1504 Considerations on Aperiodic In-device Coexistence, Hyeonjun Sung (WILUS Inc.)
[7] 24/0811 Overlapped indication for aperiodic low latency traffic, Daniel Verenzuela (Sony Group Corporation)
[8] 24/0091 Enhanced Scheduling Method for Low Latency Traffic Follow up, Serhat Erkucuk (Ofinno)
[9] 23/1229 Preemption for Low Latency Application (follow up), Juan Fang (Intel)