## Slide 1: Discussion on DRU Indication Follow-up
Date: 2024-11-10
Authors:
Name | Affiliations | Address | Phone | email
Mengshi Hu | Huawei |  |  | humengshi@huawei.com
Ross Jian Yu |  |  |  | 
Ming Gan |  |  |  | 

## Slide 2: Background
11bn supports the distributed tone RU (DRU) for a TB PPDU transmission, where the DRU means an RU consisting of subcarriers spreading across a certain bandwidth [1].
As discussed in [2], to know which DRU is allocated, the following information is needed:
  RRU Indication
  It is actually a DRU & The corresponding DBW (distribution bandwidth)
  In this contribution, we further discuss the details of DRU indication.
After knowing it is a DRU and its corresponding DBW, the indicated RRU is mapped to a specific DRU.
Figure 1 DRU Indication

## Slide 3: Indication of DBW
After knowing the corresponding RRU and DBW of a DRU, the accurate position of a DRU can be determined.
  The corresponding RRU could be indicated by the conventional method.
  To indicate whether it is a DRU and its corresponding DBW, two directions have been discussed [2-4]:
  Per-User Indication
  Common Indication
In the subsequent slides, we further discuss the performance of three options related to the above two directions .

## Slide 4: Per-User Indication of DRU: Opt. A
  To indicate the DRU, one simple and natural thought is to convey the DBW related information in the User Info field of each user.
  The following green block shows an example:
Figure 2 Per-User Indication of DBW

## Slide 5: Example of Per-User Indication: Opt. A
Regarding the details of the DBW related information, an example is further shown below:
  Each User Info field comprises 2 or 3 additional bits to indicate the DBW related information.
Note that it may be hard to get so many additional bits for the DBW related indication. Thus in [4], repurposing several bits in the User Info field for DRU indication is proposed, which is shown in the next slide (Opt. B).
Value | Meaning
000 | RRU
001 | DRU (20 MHz DBW)
010 | DRU (40 MHz DBW)
011 | DRU (80 MHz DBW)
100 | DRU (160 MHz DBW)
101 - 111 | Reserved
Table 1 DBW Related Information

## Slide 6: Per-User Indication of DRU: Opt. B
  To enable repurposing some bits in the User Info field for DBW indication, a 4-bit bitmap is proposed in [4] to show the DRU/RRU status of each 80 MHz.
  Three parts are needed for the DRU indication:
  RRU indication
  DRU/RRU Indication per 80 MHz
  DBW indication
  Because of the 4-bit bitmap, the DBW Indication could reuse some existing bits.
Figure 3 DRU/RRU Indication per 80 MHz
Value | Meaning (If the RRU indication and the 4-bit bitmap corresponds to a DRU) | Meaning (If the RRU indication and the 4-bit bitmap corresponds to a RRU)
00 | 20 MHz DBW | Other meanings (such as being part of the SS Allocation)
01 | 40 MHz DBW | 
10 | 80 MHz DBW | 
11 | Reserved | 
Table 2 DBW Indication in DRU Transmission

## Slide 7: Common Indication of DRU: Opt. C
Different from the per-user indication, the common indication can also be used to notify the DRU, saving the overhead in User Info fields:
  Since the DBW pattern in each 80 MHz is limited to only several types, a table with 80 MHz granularity could be used to indicate the DBW of RUs related to that 80 MHz.
  Opt. C shows the DBW patterns with a granularity of 80 MHz.
  Note 1: The common indication could be in the Common Info field or Special User Info fields.
  Note 2： DBW 60 MHz, DBW 160 MHz, DBW 20 + 20 MHz and DBW 40 MHz (for puncturing case 1001) can also be included in the indication.
Figure 4 An example of common Indication
Containing sixteen 20 MHz sub-channels (320 MHz)
Value | Meaning
00 | RRU
01 | DRU (DBW: Left 20 + Right 40)
10 | DRU (DBW: Left 40 + Right 20)
11 | DRU (DBW: min(PPDU BW, 80)
Table for each 80 MHz
The same table
The same table
The same table
20 + 20 + 40 (DBW)
40 + 20 + 20 (DBW)

## Slide 8: Available Bits for Opt. C
The DRU indication could be in the following places:
  Common Info field
  Special User Info field
  Additional Special User Info field used for DRU (No need to exist if there is no DRU)

## Slide 9: Comparison
The comparison of the previous three DRU indications is shown below: (Note: The RRU indication is not considered in the comparison because all the options need it):
  Opt. A: Per-User Indication (without Common Part)
  Opt. B: Per-User Indication + Common Part
  Opt. C: Common Indication
Options | Opt. A [2] | Opt. B [4] | Opt. C [2, 3]
Pros | Needs only one additional subfield | / | Needs only one additional subfield Knows the DRU pattern in advance
Cons | Needs additional bits in each User Info field | Needs two additional subfields Needs additional bits in each User Info field in the case of DRU Transmission (repurposing) | Needs additional bits in the common part
Minimum Overhead | 2*number of User Info fields | 4 bits + 2*number of the User Info fields corresponding to DRU transmissions | 8 bits
Note: For Opt. C, if the indication is put into a special DRU related User Info field, there is no overhead in the case of pure RRU transmission.
Suggest using this Opt. C

## Slide 10: Summary
In this contribution, we further share some thoughts on the DRU indication:
  Compared with Opt. B and Opt. A, Opt. C is relatively simple and saves the overhead in User Info fields.
  Suggest indicates the DRU in the common part (such as the Common Info field or Special User Info field).

## Slide 11
[1] Alfred Asterjadhi, TGbn Motions List - Part 1, 802.11 DCN 2024/171r6
[2] Mengshi Hu, et al., Distribution Bandwidth of DRU - Follow up, 802.11 DCN 2024/1130r1
[3] Eunsung Park, et al., Signaling for DRU in Trigger Frame, 802.11 DCN 2024/1471r1
[4] Shengquan Hu, et al., Signaling for DRU Transmission, 802.11 DCN 2024/1489r0
References