## Slide 1: Discussion on Frequency Domain UEQM
Date: 2024-11-10
Authors:
Name | Affiliations | Address | Phone | email
Mengshi Hu | Huawei |  |  | humengshi@huawei.com
Ross Jian Yu |  |  |  | 
Ming Gan |  |  |  | 

## Slide 2: Background
UEQM (Unequal Modulation) is a promising feature enabling different modulation orders in the resource allocated to a user. It could provide obvious gains when there exists a large SNR difference [1]. In general, there are mainly two kinds of UEQM [2]:
  Spatial domain UEQM (Different modulations are applied to different spatial streams)
  Frequency domain UEQM (Different modulations are applied to different subcarriers)
The spatial domain UEQM has been adopted in UHR, while the frequency domain UEQM is still under discussion.
  Define unequal modulation over different spatial streams (Motion 23)
  In this contribution, the performance of the frequency domain UEQM is further discussed.
  This is a follow-up contribution of Reference [3].

## Slide 3: Frequency Domain UEQM
  Regarding the frequency domain UEQM, some related simulation results and benefits are mentioned in [2].
  Take advantage of the channel selective gains.
  Good for the interference case where some of the subcarriers suffer from a relatively strong interference.
Fig. 1 A use case of frequency UEQM

## Slide 4: Simulation Configuration
  To find the benefits using frequency domain UEQM, the following simulation configurations are used.
Item | Configuration
PPDU BW | 40 MHz
Channel Mode & Estimation | Channel D & Realistic & Smoothing
RU | 484-tone RU with 468 data subcarriers
Frequency Domain UEQM | The left 234 subcarriers correspond to Modulation A; The right 234 subcarriers correspond to Modulation B; One PSDU & Same Coding Rate
Length | 1200 Bytes
Data Encoding | LDPC (Joint Coding)
Transmission | Single User & One Spatial Stream
Interference | Add additional interference to the right half of the 484-tone RU
Fig. 2 A 484-tone RU with frequency domain UEQM
Table. 1 Simulation Configuration

## Slide 5: Adding Interference
  To establish a environment that some of the subcarriers are affecting by a narrow band interference, we have the following modifications:
  Add a narrow band interference to the noise in the time domain. To clearly show the power difference in the following figures, the noise power is normalized to 1 (0 dB).
  The left half subcarriers of the RU are affected by the noise, while the right half subcarriers of the RU are affected both by the noise and interference.
Fig. 4 Examples of add interference (6 dB & 18 dB)

## Slide 6: Simulation Clarification
  To clearly show the performance of EQM and UEQM, the PER and Goodput are used to analyze it.
  The the following equation is used for the goodput calculation:
  The SNR values shown in the results later indicate the signal-to-noise ratio without considering the interference.
  The following cases of interference are simulated:
  6 dB interference compared to the noise
  12 dB interference compared to the noise

## Slide 7: Simulation Result A (6 dB interference)
  The following goodput result considers a 6 dB interference
  The three UEQM schemes shown by solid curves below all provide additional gains at some SNRs.
20% gain at this point

## Slide 8: Simulation Result B (12 dB interference)
  The following goodput result considers a 12 dB interference
  All the curves have a right shift of several decibels, compared to the case of 12 dB interference. In addition, the gains provided by the frequency domain UEQM become more obvious.
39% gain at this point

## Slide 9: Conclusion
In this contribution, the frequency domain UEQM was discussed.
  The performance of frequency domain UEQM was shown.
  Some different interference levels were investigated in the simulations.
  Simulation results showed that the frequency domain UEQM provides obvious gains if there exists obvious SINR gaps at different frequencies. For example, a 39% gain could be seen at the SNR of 20 dB in the case of a 12 dB interference added to the right part of the 484-tone RU.
  Suggest enabling frequency domain UEQM for the interference case.

## Slide 10
[2] 11-24-0438-00-00bn-ueqm-benefit-analysis
[1] 11-24-0433-00-00bn-analysis-on-ueqm-and-ueq-mcs
[3] 11-24-1132-01-00bn-frequency-domain-ueqm
References

## Slide 11
Do you agree to include the following into the 11bn SFD?
  11bn defines frequency domain unequal modulation (UEQM).
    Different data subcarriers allocated to a user may correspond to different modulation orders.
    Y
    N
    A
Straw Poll #1