## Slide 1: ELR PPDU follow up
Date: 2024-11-10
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | Ensung.park@lge.com
Insik Jung |  |  |  | insik0618.jung@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Sanggook Kim |  | 10680 Treena St San Diego, CA 92131 |  | sanggook.kim@lge.com
November 2024

## Slide 2: Introduction
The various contributions[1-8] related to ELR have been discussed in the September meeting.
Although several features have been defined for the ELR PPDU by agreement, the details on the U-SIG and ELR-SIG and methods to reduce PAPR have not been determined.
In this contribution, we consider the design of each SIG field for ELR PPDU and the method to reduce the PAPR in ELR transmission.

## Slide 3: Recap.
Passed motions in the previous F2F meeting
  Motion 32
    ELR PPDU starts with a legacy preamble in the PPDU for the ELR transmission
      The legacy preamble contains the L-STF, L-LTF, L-SIG, RL-SIG, and U-SIG
  Motion 33
    In the U-SIG field of a UHR ELR PPDU, the PHY Version Identifier is set to 1. And the PPDU Type And Compression Mode is used to indicate ELR PPDU.
  Motion 36
    ELR-SIG is located right after ELR-LTF in ELR PPDU
      Note that ELR-LTF is the short name of UHR-LTF for ELR PPDU

## Slide 4: U-SIG field for ELR PPDU(1/2)
As defined in 11be, U-SIG field contained the version-independent fields and the version-dependent fields.
To keep the consistency of U-SIG design regardless of PHY version or PPDU type of 11bn, it is desirable to retain the version-independent fields defined in the U-SIG field.
  So, the U-SIG1 of the ELR PPDU is composed of same subfields in U-SIG1, as defined in 11be.
    U-SIG1 of ELR PPDU
 | Bit | Subfield | Number of bits
U-SIG-1 | B0-B2 | PHY Version identifier | 3
 | B3-B5 | Bandwidth | 3
 | B6 | UL/DL | 1
 | B7-B12 | BSS color | 6
 | B13-B19 | TXOP | 7
 | B20-B24 | Disregard | 5
 | B25 | Validate | 1
PHY version Identifier is set to 1 based on motion 33.
BW may be fixed with 20MHz. So, it is set to 0.

## Slide 5: U-SIG field for ELR PPDU(2/2)
Unlike U-SIG1, U-SIG2 which contains version-dependent fields can be reconfigurable for ELR PPDU format.
  To indicate the ELR PPDU format to 11bn STA, PPDU Type and Compression Mode field is set to 3 for ELR PPDU[1].
    Since reserved value is used for ELR PPDU, the size of this field is not changed.
  The other bits except PPDU Type and Compression Mode, CRC, and Tail in U-SIG2 may be defined as validate bits for ELR PPDU.
    For example, validate bits in U-SIG2(i.e., B2~B15) are set to all 1s.
      We are open for using some of bits from Validate subfield as other beneficial purpose in case that RSSI of the PPDU is enough
  By using the PPDU Type and Compression Mode field and validate bits, STAs (11bn non-ELR STA or legacy) can stop the processing and defer for the duration of PPDU.
    By doing this, we can easily reuse the receiver process defined 11be without adding of new fields in the U-SIG2.
  U-SIG2 of ELR PPDU
 | Bit | Subfield | Number of bits
U-SIG-2 | B0-B1 | PPDU type & Compression Mode | 2
 | B2-B15 | Validate | 14
CRC & Tail | B16-B19 | CRC | 4
 | B20-B25 | Tail | 6

## Slide 6: ELR-SIG field for ELR PPDU (1/4)
As proposed in [2], the RRU 52 with 4x repetition can be reused for ELR-SIG field.
  For the simple implementation, this field is transmitted with MCS0 only.
  One ELR-SIG symbol carries the 24bits information.
Additionally, this is a reachable signal field to 11bn STAs located in an extended range so, it may include some common information as blow.
  PHY Version Identifier: indication of the version of the ELR PPDU, set to equal value with it in U-SIG field
  UL/DL: for STA power saving
  Length information : either TXOP or the number of OFDMA symbols may be considered.
    If the TXOP is used, we can inherit the procedure of 11be/ax. For simple implementation, some related fields( e.g., Pre-FEC Padding Factor, PE Disambiguity) can be fixed and omitted.
    If the number of OFDMA symbols is used, as described in [7], we can use the procedure of 11ac.
  LDPC Extra Symbol/ Segment : depending on which length information is used, it can be determined.

## Slide 7: ELR-SIG field for ELR PPDU (2/4)
Also, since ELR PPDU is used for SU transmission, this field may be simplified based on the EHT-SIG field for EHT SU transmission.
  Some parameters can be fixed or not used in ELR transmission and those subfields can be omitted in the ELR-SIG.
    Spatial Reuse : not used
    GI+LTF Size : fixed with a specific size
    Number of LTF Symbols : fixed with one symbol
    NSS : fixed with one spatial stream
    Beamformed : not used

## Slide 8: ELR-SIG field for ELR PPDU (3/4)
To improve the reliability of the ELR-SIG field, we can consider the separated encoding of the ELR-SIG field per symbol.
  As in [7], for encoding per one OFDM symbol, each symbol of ELR-SIG includes the CRC and Tail.
  ELR-SIG performance
    As shown below, when we use the individual symbol encoding for ELR-SIG, the aggregated PER(for assuring correct information from both symbols) is better than the PER of the two symbol encoding.

## Slide 9: ELR-SIG field for ELR PPDU (4/4)
  By considering previous slides, we can design the ELR-SIG field as follows
    ELR-SIG consists of two OFDM symbols.
    Each ELR-SIG symbol includes the CRC and Tail.
    The MCS and Coding fields is located in the ELR-SIG symbol 1for the early receiver configuration.
ELR-SIG symbol 1 |  | ELR-SIG symbol 2 | 
Subfields | Number of bits | Subfields | Number of bits
PHY Version Identifier | 3 | STA-ID | 11
UL/DL | 1 | Reserved | 3
TXOP | 7 | CRC | 4
LDPC extra symbol segment | 1 | Tail | 6
MCS | 1 |  | 
Coding | 1 |  | 
CRC | 4 |  | 
Tail | 6 |  | 

## Slide 10: PAPR reduction (1/3)
In [1], we proposed the transmitting of the ELR-SIG field and data field by using RRU52 with 4 repetitions.
With a simple frequency repetition, we achieved the required margin but RRU52 with 4 repetitions has higher PAPR.
For efficient PAPR reduction, we can consider applying the proper coefficients that consist of various combinations of elements (1,-1,i,-i).
  As a coefficient for ELR, we evaluate the performance of two coefficients i.e., length 4 based on 52 carriers and length 8 based on 26 carriers.

## Slide 11: PAPR reduction (2/3)
A length 4 coefficient based on 52 carriers.
  It is simple in terms of implementation but, the PAPR by applying those coefficients is not good compared with the PAPR of RRU 242.
    In the results, we showed some sets of coefficient sequences that provide the best PAPR performance out of the whole coefficient set(i.e., 4^4).
Note: the details of coefficient sequence is described in Appendix 2

## Slide 12: PAPR reduction (3/3)
A length 8 coefficient based on 26 carriers.
  By applying the coefficient of length 8, we got the better PAPR performance than that of coefficient of length 4.
    PAPR of some coefficient is better than PAPR of RRU 242
    In the results, we applied the same method as the previous results and we observed that these sets with the best PAPR consist of only coefficients of 1 and -1.
  Since we achieve enough PAPR performance compatible with RRU 242, we will not apply less unit size than 8 coefficient for reducing implementation complexity.
Note: the sequence of Order 247 is same sequence that was proposed in [5]
the details of coefficient sequence is described in Appendix 3

## Slide 13: Summary
For efficient transmission, we considered some points for the SIG configuration of ELR PPDU and evaluated the coefficient to reduce the PAPR of ELR transmission.
  To maintain consistency with UHR PPDU, U-SIG includes the same version-independent field with UHR PPDU.
    The version-independent fields are same as those defined in U-SIG of EHT.
  To indicate the ELR-PPDU and it’s version, PPDU Type and Compression Mode and PHY version identifier are included in the U-SIG and the ELR-SIG respectively.
    PPDU Type and Compression Mode and PHY version identifier are set to 3 and 1 respectively.
  To reduce the PAPR of ELR transmission, the coefficient can be applied to ELR SIG and Data fields.
    This coefficient is a length 8 sequence composed of (1 and -1) and a coefficient value is applied per 26 carriers.

## Slide 14: Straw poll 1
Do you agree to add the following text to the 11bn SFD?
  The PPDU type & Compression Mode field included in the U-SIG of the ELR PPDU is set to 3 for indication of ELR transmission.

## Slide 15: Straw poll 2
Do you agree to add the following text to the 11bn SFD?
  The ELR-SIG in a ELR PPDU composes of two OFDM symbols.
    Each symbol is encoded independently.

## Slide 16: Straw poll 3
Do you agree to add the following text to the 11bn SFD?
  The ELR-SIG in the ELR PPDU includes the PHY version identifier.
    It is set to equal value of U-SIG field.

## Slide 17: Straw poll 4
Do you agree to add the following text to the 11bn SFD?
  The ELR-SIG includes the TXOP to indicate the length of the ELR PPDU.

## Slide 18: Straw poll 5
Do you agree to add the following text to the 11bn SFD?
  The coefficient is applied to ELR-SIG field and ELR-data field for PAPR reduction.
    It is applied per 26 carriers and is composed of 1 and -1
    The length of the coefficient is 8.

## Slide 19: Reference
[1] 11-24-1485-00-00bn-Considerations for ELR PPDU format
[2] 11-24-1486-00-00bn-Performance evaluation of ELR transmission
[3]11-24-1410-00-00bn-legacy-preamble-for-elr-ppdu
[4] 11-24-1478-00-00bn-elr-ppdu-design
[5] 11-24-1488-00-00bn-elr-ppdu-transmission-design
[6] 11-24-1573-00-00bn-an-elr-ppdu-follow-up
[7] 11-24-1590-00-00bn-extended-long-range-signaling
[8] 11-24-1592-00-00bn-usig-fields-in-an-elr-ppdu

## Slide 20: Appendix 1
Processing of the USIG field in 11be.

## Slide 21: Appendix 2
Coefficient sequence for length 4
Order | Sequence | Order | Sequence
2 | 1 1 1 -1 | 82 | -1 -1 1 -1
5 | 1 1 -1 1 | 85 | -1 -1 -1 1
17 | 1 -1 1 1 | 99 | -1 1i 1 1i
22 | 1 -1 -1 -1 | 116 | -1 - 1i 1 -1i
56 | 1 - 1i -1 1i | 235 | -1i 1i 1i 1i
65 | -1 1 1 1 | 240 | -1i 1i -1i -1i
70 | -1 1 -1 -1 | 252 | -1i -1i 1i - 1i

## Slide 22: Appendix 3
Coefficient of length 8 & PAPR
Order | Sequence | Mean/Median PAPR(BPSK) | Mean/Median PAPR(QPSK)
10 | -1 -1 -1 -1 1 -1 -1 1 | 7.8557/7.6740 | 8.2072/ 8.1342
59 | -1 -1 1 1 1 -1 1 -1 | 7.8479/7.6529 | 8.2091/ 8.1342
93 | -1 1 -1 1 1 1 -1 -1 | 7.8530/7.6733 | 8.2061/ 8.1342
112 | -1 1 1 -1 1 1 1 1 | 7.8575/7.6741 | 8.2102/ 8.1342
145 | 1 -1 -1 1 -1 -1 -1 -1 | 7.8446/7.6691 | 8.2017/ 8.1341
164 | 1 -1 1 -1 -1 -1 1 1 | 7.8627/7.6760 | 8.2021/8.1263
198 | 1 1 -1 -1 -1 1 -1 1 | 7.8623/7.6791 | 8.1994/8.1307
247[5] | 1 1 1 1 -1 1 1 -1 | 7.8504/7.6686 | 8.2039/ 8.1342