## Slide 1: Pilot Value Design for ELR PPDU
Date: 2024-11-10
Authors:
Name | Affiliations | Address | Phone | Email
Bo Gong | Huawei |  |  | gongbo8@huawei.com
Jian Yu (Ross) |  |  |  | ross.yujian@huawei.com
Ming Gan |  |  |  | ming.gan@huawei.com

## Slide 2: Background
Nov 2024
In ref [1], ELR PPDU has been proposed.
L-SIG
RL-SIG
ELR-Data
L-LTF
L-STF
ELR-mark2
ELR-mark1
ELR-STF
ELR-LTF
ELR-SIG
U-SIG1
U-SIG2
In ref [2], for ELR-SIG/ELR-Data field, RRU52 with 4x DUP was proposed for lower data rate and longer range.
52
52
52
52
13
13
DUP
DUP
DUP
RRU52 4x DUP
RRU52 based encoding/mod
RU1
RU2
RU3
RU4
In this proposal, the pilot value design for ELR-SIG/ELR-Data field is discussed.

## Slide 3: Two Options for Pilot Value Design
Opt-1: Each of the four 52-tone RRUs keeps its initial pilot values and pilot mapping rule as 11ax/be.
    Pn={ψn mod 4, ψ(n+1) mod 4, ψ(n+2) mod 4, ψ(n+3) mod 4}, n denotes the symbol index.
    ψ0= 1, ψ1= 1, ψ2= 1, ψ3= -1
Opt-2: The four 52-tone RRUs with 16 pilots reuse the initial pilot values and pilot mapping rule of 484/996-tone RRU in 11ax/be.
    ψ0= 1, ψ1= 1, ψ2= 1, ψ3= -1, ψ4= -1, ψ5= 1, ψ6= 1, ψ7= 1
    Pn={ψn mod 8, ψ(n+1) mod 8, ψ(n+2) mod 8, ψ(n+3) mod 8, ψ(n+4) mod 8, ψ(n+5) mod 8, ψ(n+6) mod 8 , ψ(n+7) mod 8 ,ψ(n+8) mod 8, ψ(n+9) mod 8, ψ(n+10) mod 8, ψ(n+11) mod 8, ψ(n+12) mod 8, ψ(n+13) mod 8, ψ(n+14) mod 8 , ψ(n+15) mod 8}
Nov 2024

## Slide 4: References
[1] 24/11-24-1478-00-00bn-elr-ppdu-design.pptx
[2] 11-24-1488-00-00bn-elr-ppdu-transmission-design.pptx
Nov 2024