## Slide 1: Signaling for UHR PPDU follow up
Date: 2024-11-08
Authors:
Name | Affiliations | Address | Phone | email
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com
Oded Redlich |  |  |  | 
Ming Gan |  |  |  | 
Shimi Shilo |  |  |  | 
Genadiy Tsodik |  |  |  | 

## Slide 2: Introduction
In [1], we show our thoughts on the potential signaling for non-TB case.
The following decisions have been made in Sep meeting:
  [Motion #34] Introduce new MCSs which are applicable to single spatial stream transmissions, as well as to equal modulation and unequal modulation cases in multiple spatial stream transmissions.
  [Motion #42] Add the following modulation and code rate combinations as the new MCSs for 11bn:
    Modulations of {QPSK, 16QAM, 256QAM} with code rate R=2/3
    Modulation of 16QAM with code rate R=5/6
  [Motion #52,43,39] UEQM patterns for Nss=2,3,4 are limited to:
  [Motion #40] For a (non-ELR) UHR MU PPDU, there exists a 1-bit EQM/UEQM indication in a User field for non-MU-MIMO in the UHR-SIG field.
We further update the proposed signaling based on the passed motions.
1st ss | 2nd SS
M | M-1
M | M-2
1st ss | 2nd SS | 3rd SS
M | M | M-1
M | M | M-2
M | M-1 | M-2
1st ss | 2nd SS | 3rd SS | 4th SS
M | M | M | M-1
M | M | M | M-2
M | M | M-1 | M-2
M | M-1 | M-1 | M-2

## Slide 3: UHR-SIG signaling - EQM
For non-MU-MIMO User field, let’s first see the EQM case.
  The EQM case is first shown as follows. B19 is used as a EQM/UEQM flag as an example.
  Regarding longer LDPC codeword, besides potential signaling, an alternative way could be following 11ax and 11be style, and defines equations to choose codeword length.
11 | 5 | 3 | 1 | 1 | 1 | 
STA ID | MCS | NSS | EQM/UEQM | Beamformed | Coding | …
B0 B10 | B11 B15 | B16 B18 | B19 | B20 | B21 | 

## Slide 4: UHR-SIG signaling - UEQM
For non-MU-MIMO User field, for UEQM signaling, there could be several options:
  Opt 1: First indicate EQM/UEQM, indicate MCS, indicate NSS, and indicate UEQM patterns per NSS using a table.
    Max 4SS to reduce the pattern variations. May group larger NSS if needed.
    LDPC only, TxBFed is assumed for UEQM： bits in EQM case are repurposed to indicate UEQM pattern variations.
  For NSS=2, 3, or 4, the UEQM patterns are as shown in slide 2.
  EQM/UEQM position shall be the same for EQM and UEQM case.
11 | 5 | 2 | 1 or 2 | 1 | 2 | 
STA ID | MCS | NSS | Reserved | EQM/UEQM | UEQM patterns | …

## Slide 5: Summary
In this contribution, we talk about the User field signaling for non-TB, non-ELR case.
An EQM/UEQM flag is introduced to contain different information for EQM and UEQM case.
A MCS field and UEQM patterns field are proposed to simplify the parsing.
  Similar as EQM case
  Compared with joint QAM combinations in 11n
Signaling regarding longer LDPC CW will be further discussed.

## Slide 6: Motion 1
Move to include the following into the 11bn SFD?
  For a (non-ELR) UHR MU PPDU, when EQM/UEQM indicates UEQM in a User field for non-MU-MIMO, there exists a MCS field, a NSS field and a 2 bit field indicating UEQM patterns.
  Y
  N
  A
  SP result: 64Y, 10N, 12A.

## Slide 7: SP 1
Move to include the following into the 11bn SFD?
  The UEQM patterns indication for NSS=2, 3 and 4 are as follows:
  Note: reserved entries will be further categorized as Validate or Disregard, following principles in 11be
  Y
  N
  A
Index | 1st ss | 2nd SS
0 | M | M-1
1 | M | M-2
2-3 | Reserved | 
Index | 1st ss | 2nd SS | 3rd SS
0 | M | M | M-1
1 | M | M | M-2
2 | M | M-1 | M-2
3 | Reserved |  | 
Index | 1st ss | 2nd SS | 3rd SS | 4th SS
0 | M | M | M | M-1
1 | M | M | M | M-2
2 | M | M | M-1 | M-2
3 | M | M-1 | M-1 | M-2
NSS=2
NSS=3
NSS=4

## Slide 8: Reference
11-24-1411-01-00bn-signaling-for-uhr-ppdu, Ross Jian Yu (Huawei)

## Slide 9: Appendix

## Slide 10: UHR-SIG signaling - UEQM
NSS and UEQM pattern variations could be also merged:
  Opt 2: First indicate EQM/UEQM, indicate base MCS, then indicate NSS and UEQM patterns at the same time.
NSS and UEQM patterns Index | NSS | UEQM patterns |  |  | 
 |  | 1st Stream | 2nd Stream | 3rd Stream | 4th Stream
0000 | 2SS | M | M-1 |  | 
0001 |  | M | M-2 |  | 
0010 | 3SS | M | M | M-1 | 
0011 |  | M | M | M-2 | 
0100 |  | M | M-1 | M-2 | 
0101 | 4SS | M | M | M | M-1
0110 |  | M | M | M | M-2
0111 |  | M | M | M-1 | M-2
1000 |  | M | M-1 | M-1 | M-2
1001-1111 | Reserved |  |  |  | 
11 | 4 or 5 | 4 | 1 | 1 or 2
STA ID | MCS | NSS and UEQM patterns | EQM/UEQM | Reserved

## Slide 11: SP 2
Move to include the following into the 11bn SFD?
  For a (non-ELR) UHR MU PPDU, when EQM/UEQM indicates UEQM in a User field for non-MU-MIMO, there exists a MCS field and a NSS and UEQM pattern field, where the NSS and UEQM pattern field indicates both the number of spatial streams and the UEQM patterns.
  Y
  N
  A

## Slide 12: SP 3
Move to include the following into the 11bn SFD?
  The NSS and UEQM pattern field indication is as follows:
  Note: reserved entries will be further categorized as Validate or Disregard, following principles in 11be
  Y
  N
  A
Input | Output |  |  |  | 
NSS and UEQM patterns Index | NSS | UEQM patterns |  |  | 
 |  | 1st Stream | 2nd Stream | 3rd Stream | 4th Stream
0000 | 2SS | M | M-1 |  | 
0001 |  | M | M-2 |  | 
0010 | 3SS | M | M | M-1 | 
0011 |  | M | M | M-2 | 
0100 |  | M | M-1 | M-2 | 
0101 | 4SS | M | M | M | M-1
0110 |  | M | M | M | M-2
0111 |  | M | M | M-1 | M-2
1000 |  | M | M-1 | M-1 | M-2
1001-1111 | Reserved |  |  |  |