## Slide 1: In-device-coexistence use cases follow-up
Date: 2025-2-20
Authors:
Name | Affiliation | Address | Phone | Email
Hongwon Lee | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | hongwon.lee@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Geonhwan Kim |  |  |  | geonhwan.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Sunhee Baek |  |  |  | sunhee.baek@lge.com
Yelin Yoon |  |  |  | yl.yoon@lge.com
Dongju Cha |  |  |  | dongju.cha@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Sanggook Kim |  | 10680 Treena St, San Diego CA 92131 , USA |  | sanggook.kim@lge.com

## Slide 2: Introduction
The Motion related to defining a mechanism for an AP to announce unavailability, which is related to periodic in-device-coexistence(IDC), was passed in the November F2F meeting
The Motion related to reusing the mechanism for Scheduled AP Power Save mode was passed in the November F2F meeting
The mechanism for AP Power Save mode can also be applied to AP Periodic Unavailability Operation due to in-device coexistence
We should further examine use cases to determine if there are any issues when the mechanism operates in Scheduled AP Power Save Mode(PSM) and/or AP Periodic Unavailability Operation(PUO)
  We refer to AP Periodic Unavailability Operation as AP PUO for convenience in this contribution. This term can be further discussed within this group to determine a more appropriate one if necessary

## Slide 3: Scheduled AP PSM mechanism
The current rules for TWT scheduling APs, aligned with Motion 161, are defined in subclause 26.8.3.2 (Rules for TWT Scheduling APs), and the unavailability outside of broadcast TWT SPs can currently be applied optionally
26.8.3.2 Rules for TWT scheduling AP
……
(#4010)If a TWT scheduling AP has advertised a TWT element that carries one or more Broadcast TWT Parameter Set fields with a Broadcast TWT ID subfield equal to 0 and a Responder PM Mode subfield equal to 1, then:
— If the NDP Paging Indicator/Unavailability Mode subfield is set to 0, the AP may be unavailable outside of these broadcast TWT SPs, except within any other TWT SP that is setup with the AP or advertised by the AP.
— If the NDP Paging Indicator/Unavailability Mode subfield is set to 1, the AP may be unavailable outside of these broadcast TWT SPs, even if that time falls within any other TWT SP that is setup with the AP or advertised by the AP.
…….
The TWT scheduling AP shall include a unique value in the Broadcast TWT ID subfield for each Broadcast TWT to allow identification of each Broadcast TWT, unless the TWT Setup Command field is Alternate TWT or the Broadcast TWT ID subfield is zero.
NOTE 6—The broadcast TWT element contains two Broadcast TWT Parameter Set fields with the same Broadcast TWT ID subfield value if the TWT Setup Command field indicates Alternate TWT in one of the Broadcast TWT Parameter Set fields. The broadcast TWT element might contain multiple Broadcast TWT Parameter Set fields with the Broadcast TWT ID subfield equal to 0.
In order to apply this mechanism for Scheduled AP PSM and AP PUO, we need so slightly change these rules

## Slide 4: Considerations for Scheduled AP PSM and AP PUO
The rules discussed in the previous slide are optional in the baseline
  For UHR STAs, these rules shall apply in cases where an AP operates in Scheduled AP PSM and/or AP PUO
  Additionally, if an UHR AP operates with multiple Broadcast TWT for Scheduled AP PSM and/or AP PUO, the overlapped periods outside the broadcast TWT SPs should not be unavailable anymore
  To guarantee unavailable in the overlapped periods, the NDP Paging Indicator/Unavailability Mode subfield shall be set to 1(stating “may” in the baseline)

## Slide 5: Consideration for the unavailability mode subfield
Case 1: The outside of Broadcast TWT SPs that do not overlap(either fully or partially) with any other TWT SP by the AP
  Unavailability mode set to either 0 or 1 are allowable
Case 2: The outside of Broadcast TWT SPs that overlap(either fully or partially) with any other TWT SP by the AP
  Only unavailability mode set to 1 is allowable
The simple proposal to add rules for TWT Scheduling APs
  If a TWT scheduling UHR AP has advertised a TWT element that carries one or more Broadcast TWT Parameter Set fields with a Broadcast TWT ID subfield equal to 0 and a Responder PM Mode subfield equal to 1, for Scheduled AP PSM and/or AP PUO, then:
    The value of the NDP Paging Indicator/Unavailability Mode subfield, either 0 or 1, is permissible if the time outside of these Broadcast TWT SPs does not fall within any other TWT SP that is setup with the UHR AP or advertised by the UHR AP.
    The value of the NDP Paging Indicator/Unavailability Mode subfield shall be set to 1 if the time outside these Broadcast TWT SPs falls within any other TWT SP that is setup with the UHR AP or advertised by the UHR AP. In this case, the UHR AP shall be considered unavailable outside these Broadcast TWT SPs

## Slide 6: Conclusion
We discussed reusing the baseline mechanism for TWT scheduling APs to apply to Scheduled AP PSM and AP PUO
For efficient power consumption, avoidance of unnecessary medium access and unfavorable rate adaptation, the doze state during the overlapping periods shall be guaranteed
A simple rule can be added to achieve this
  The value of the NDP Paging Indicator/Unavailability Mode subfield shall be set to 1 if the time outside these Broadcast TWT SPs falls within any other TWT SP that is setup with the UHR AP or advertised by the UHR AP. In this case, the UHR AP shall be considered unavailable outside these Broadcast TWT SPs
Through this, the efficient operation of Scheduled AP PSM and/or AP PUO can be achieved

## Slide 7: Straw Poll 1
Do you agree to include the following into the 11bn SFD?
  The report for long term(periodic) unavailability due to in-device-coexistence on AP side is performed in UHR using Broadcast TWT with TWT ID=0 with Responder PM=1 as described in 26.8.3.2 (Rules for TWT scheduling AP)

## Slide 8: Straw Poll 2
Do you agree to include the following into the 11bn SFD?
  If a TWT scheduling UHR AP has advertised a TWT element that carries one or more Broadcast TWT Parameter Set fields with a Broadcast TWT ID subfield equal to 0 and a Responder PM Mode subfield equal to 1, for Scheduled AP PSM and/or AP PUO, then:
    The value of the NDP Paging Indicator/Unavailability Mode subfield, either 0 or 1, is permissible if the time outside of these Broadcast TWT SPs does not fall within any other TWT SP that is setup with the UHR AP or advertised by the UHR AP.
    The value of the NDP Paging Indicator/Unavailability Mode subfield shall be set to 1 if the time outside these Broadcast TWT SPs falls within any other TWT SP that is setup with the UHR AP or advertised by the UHR AP. In this case, the UHR AP shall be considered unavailable outside these Broadcast TWT SPs

## Slide 9: References
[1] 11-24/831r0, Periodic IDC use cases and considerations for signaling
[2] 11-24/1108r1, Periodic IDC signaling for UHR Mobile AP
[3] 11-24/1490r0, More Consideration of ICR/CRF for in-device-coexistence
[4] 11-23/1103r0, In-Device Interference Discussion
[5] 11-23/1934r0, In-Device Interference Mitigation Follow Up
[6] 11-23/2002r2, In-device coexistence and interference follow-up