## Slide 1: New LTF Sequences for DRU
Date: 2024-11-05
Authors:

## Slide 2: Abstract
In this contribution, we propose new LTF sequences for DRU corresponding to different distribution bandwidths. The new sequences are constructed from component sequences for the 26-tone DRUs. In this document, we share
  The PAPR performance results of the new LTF sequences for different DRU sizes and distribution bandwidths

## Slide 3: Main Proposal
LTF component sequences for 26-tone DRUs corresponding to each distribution bandwidth are found.
The LTF component sequences of length 26 each can be combined to form LTF sequences for larger DRU sizes.
Example: For DBW = 20 MHz, 7 LTF component sequences are found (LTF26DRU20_1 to LTF26DRU20_7).
  For 26DRU20, a subset of these component sequences are found to be optimal (in terms of PAPR).
  For 52DRU20, two sequences can be combined to construct an LTF sequence for 52-tone DRUs
  For 106DRU20, four sequences can be combined to construct an LTF sequence for 106-tone DRUs
    Two extra LTF values are also found for each 106DRU20
Similar concept applies to larger distribution bandwidths (e.g., 40/80 MHz)

## Slide 4: LTF Sequences for DBW = 20 MHz
The proposed component sequences for DBW = 20 MHz are listed below considering the tone plan in [1]
Sequence ID | LTF Sequence
LTF26DRU20_1 | -1,-1,-1,1,1,1,-1,-1,-1,1,-1,-1,-1,1,-1,1,1,1,-1,1,1,-1,1,1,-1,1
LTF26DRU20_2 | -1,-1,1,1,-1,-1,-1,1,1,-1,1,1,1,1,1,1,-1,-1,1,-1,1,1,1,-1,1,-1
LTF26DRU20_3 | 1,-1,1,-1,-1,1,-1,1,1,-1,1,1,1,-1,1,1,1,1,-1,1,-1,-1,-1,1,-1,-1
LTF26DRU20_4 | -1,-1,-1,1,-1,1,1,1,-1,-1,1,1,-1,-1,1,-1,1,-1,-1,1,-1,-1,-1,-1,-1,1
LTF26DRU20_5 | -1,1,-1,-1,1,1,-1,-1,-1,-1,1,-1,-1,1,1,1, -1,1,-1,1,1,-1,-1,-1,1, -1
LTF26DRU20_6 | -1,1,-1,1,1,1,1,-1,-1,-1,-1,-1,1,1,1,1,-1,-1,1,1,-1,1,-1,1,-1,1
LTF26DRU20_7 | -1,-1,1,1,1,-1,1,-1,-1,1,1,1,1,-1,-1,-1,-1,1,-1,-1,-1,-1,1,-1,1,-1

## Slide 5: Mapping of the LTF Sequence to DRUs for DBW = 20 MHz
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
26DRU20 | LTF26DRU20_1 | LTF26DRU20_1 | LTF26DRU201 | LTF26DRU20_1 | LTF26DRU20_2 | LTF26DRU20_1 | LTF26DRU20_1 | LTF26DRU20_1 | LTF26DRU20_2
52DRU20 | LTF52DRU20_1 |  | LTF52DRU20_1 |  |  | LTF52DRU20_1 |  | LTF52DRU20_2 | 
106DRU20 | LTF106DRU20_1 |  |  |  |  | LTF106DRU20_2 |  |  | 
LTF Sequence ID | Component LTF Sequences
LTF52DRU20_1 | {LTF26DRU20_1, LTF26DRU20_3}
LTF52DRU20_2 | {LTF26DRU20_1, LTF26DRU20_4}
LTF106DRU20_1 | {LTF26DRU20_1, LTF26DRU20_3, LTF26DRU20_5, LTF26DRU20_6}, {1,-1}
LTF106DRU20_2 | {LTF26DRU20_1, LTF26DRU20_3, LTF26DRU20_5, LTF26DRU20_7},{-1,-1}

## Slide 6: PAPR Performance for DBW = 20 MHz
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
26DRU20 | 1.89 | 1.89 | 1.89 | 1.89 | 2.37 | 1.89 | 1.89 | 1.89 | 2.37
52DRU20 | 3.77 |  | 3.77 |  |  | 3.77 |  | 3.91 | 
106DRU20 | 4.64 |  |  |  |  | 4.74 |  |  | 

## Slide 7: LTF Sequences for DBW = 40 MHz
The proposed component sequences for DBW = 40 MHz are listed below considering the tone plan in [1]
Sequence ID | LTF Sequence
LTF26DRU40_1 | -1,-1,-1,1,1,1,-1,-1,-1,1,-1,-1,-1,1,-1,1,1,1,-1,1,1,-1,1,1,-1,1
LTF26DRU40_2 | -1,-1,1,-1,1,-1,1,-1,-1,-1,-1,1,-1,-1,-1,-1,-1,1,-1,1,1,-1,1,-1,-1,-1
LTF26DRU40_3 | 1,-1,1,-1,1,1,1,1,1,-1,1,1,-1,-1,1,-1,1,-1,1,-1,1,1,-1,1,1,1
LTF26DRU40_4 | 1,1,-1,1,-1,-1,1,-1,-1,-1,-1,-1,-1,-1,1,1,-1,1,1,-1,-1,-1,1,-1,-1,1

## Slide 8: Mapping of LTF Sequences to DRUs for DBW = 40 MHz
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18
26 DRU40 | LTF26DRU40_1 | LTF26DRU40_1 | LTF26DRU40_1 | LTF26DRU40_1 | LTF26DRU40_1 | LTF26DRU40_1 | LTF26DRU40_1 | LTF26DRU40_1 | LTF26DRU40_1 | LTF26DRU40_1 | LTF26DRU40_1 | LTF26DRU40_1 | LTF26DRU40_1 | LTF26DRU40_1 | LTF26DRU40_1 | LTF26DRU40_1 | LTF26DRU40_1 | LTF26DRU40_1
52 DRU40 | LTF52DRU40_1 |  | LTF52DRU40_1 |  |  | LTF52DRU40_1 |  | LTF52DRU40_1 |  | LTF52DRU40_1 |  | LTF52DRU40_1 |  |  | LTF52DRU40_1 |  | LTF52DRU40_1 | 
106 DRU40 | LTF106DRU40_1 |  |  |  |  | LTF106DRU40_1 |  |  |  | LTF106DRU40_1 |  |  |  |  | LTF106DRU40_1 |  |  | 
LTF Sequence ID | Component LTF Sequences
LTF52DRU40_1 | {LTF26DRU_1, LTF26DRU_2}
LTF106DRU40_1 | {LTF26DRU_1, LTF26DRU_2, LTF26DRU_3, LTF26DRU_4}, {1,-1}

## Slide 9: PAPR Performance for DBW = 40 MHz
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18
26 DRU40 | 1.89 | 1.89 | 1.89 | 1.89 | 1.89 | 1.89 | 1.89 | 1.89 | 1.89 | 1.89 | 1.89 | 1.89 | 1.89 | 1.89 | 1.89 | 1.89 | 1.89 | 1.89
52 DRU40 | 3.06 |  | 3.06 |  |  | 3.06 |  | 3.06 |  | 3.06 |  | 3.06 |  |  | 3.06 |  | 3.06 | 
106 DRU40 | 4.63 |  |  |  |  | 4.63 |  |  |  | 4.63 |  |  |  |  | 4.63 |  |  | 

## Slide 10: LTF Sequences for DBW = 80 MHz
The proposed component sequences for DBW = 80 MHz are listed below considering the tone plan in [1]
Sequence ID | LTF Sequence
LTF26DRU80_1 | -1,-1,-1,1,-1,1,1,1,-1,1,-1,-1,1,-1,1,-1,-1,-1,-1,1,-1,-1,-1,-1,1,1
LTF26DRU80_2 | -1,-1,1,1,-1,-1,1,-1,1,-1,-1,-1,-1,-1,1,-1,1,1,1,-1,-1,1,1,-1,-1,1
LTF26DRU80_3 | 1,1,1,1,1,1,-1,1,1,1,-1,-1,1,-1,-1,-1,1,-1,1,1,1,-1,-1,-1,-1,-1
LTF26DRU80_4 | 1,-1,1,1,-1,1,-1,1,1,-1,1,-1,-1,1,1,-1,-1,-1,-1,1,1,-1,1,-1,1,-1

## Slide 11: Mapping of LTF Sequences to DRUs for DBW = 80 MHz
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
52 DRU80 | LTF52 DRU80_1 | LTF52 DRU80_1 | LTF52 DRU80_1 | LTF52 DRU80_1 | LTF52 DRU80_1 | LTF52 DRU80_1 | LTF52 DRU80_1 | LTF52 DRU80_1 | LTF52 DRU80_1 | LTF52 DRU80_1 | LTF52 DRU80_1 | LTF52 DRU80_1 | LTF52 DRU80_1 | LTF52 DRU80_1 | LTF52 DRU80_1 | LTF52 DRU80_1
106 DRU80 | LTF106DRU80_1 |  | LTF106DRU80_1 |  | LTF106DRU80_1 |  | LTF106DRU80_1 |  | LTF106DRU80_1 |  | LTF106DRU80_1 |  | LTF106DRU80_1 |  | LTF106DRU80_1 | 
LTF Sequence ID | Component LTF Sequences
LTF52DRU80_1 | {LTF26DRU80_1, LTF26DRU80_2}
LTF106DRU80_1 | {LTF26DRU80_1, LTF26DRU80_2, LTF26DRU80_3, LTF26DRU80_4}, {1,1}

## Slide 12: PAPR Performance for DBW = 80 MHz
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
52 DRU80 | 4.23 | 4.23 | 4.23 | 4.23 | 4.23 | 4.23 | 4.23 | 4.23 | 4.23 | 4.23 | 4.23 | 4.23 | 4.23 | 4.23 | 4.23 | 4.23
106 DRU80 | 4.87 |  | 4.87 |  | 4.87 |  | 4.87 |  | 4.87 |  | 4.87 |  | 4.87 |  | 4.87 | 

## Slide 13: Discussion on the New LTF Sequences
The new LTF component sequences are considering masked LTF
The PAPR performance is significantly better than that of the RRU and the proposed LTF sequence in [4]
The component sequences requires significantly less storage than the legacy LTF.
Simple mapping of the component sequences to the DRU is required.

## Slide 14: Conclusions and Way Forward
New LTF sequence for DRU is proposed for each corresponding distribution bandwidth and the PAPR performance is evaluated
The new sequence is constructed from component sequence of length 26 each
The mapping of the sequences to the DRUs is unique
  In almost all cases, one sequence is found to improve the PAPR performance for all DRUs of the same size.
  For example, in DBW = 40 MHz, one 26 long LTF sequence is found to minimize the PAPR for all 26DRU40 (PAPR = 1.89 dB)

## Slide 15: SP 1
Do you agree to add the following to 11bn SFD:
The LTF sequence to use for DBW = 20 MHz is
{-1,-1,-1,1,1,1,-1,-1,-1,1,-1,-1,-1,1,-1,1,1,1,-1,1,1,-1,1,1,-1,1,1,-1,1,-1,-1,1,-1,1,1,-1,1,1,1,-1,1,1,1,1,-1,1,-1,-1,-1,1,-1,-1,-1,1,-1,-1,1,1,-1,-1,-1,-1,1,-1,-1,1,1,1,-1,1,-1,1,1,-1,-1,-1,1,-1,-1,1,-1,1,1,1,1,-1,-1,-1,-1,-1,1,1,1,1,-1,-1,1,1,-1,1,-1,1,-1,1,1,-1,-1,-1,1,1,-1,-1,-1,1,1,-1,1,1,1,1,1,1,-1,-1,1,-1,1,1,1,-1,1,-1,-1,-1,-1,1,1,1,-1,-1,-1,1,-1,-1,-1,1,-1,1,1,1,-1,1,1,-1,1,1,-1,1,1,-1,1,-1,-1,1,-1,1,1,-1,1,1,1,-1,1,1,1,1,-1,1,-1,-1,-1,1,-1,-1,-1,1,-1,-1,1,1,-1,-1,-1,-1,1,-1,-1,1,1,1,-1,1,-1,1,1,-1,-1,-1,1,-1,-1,-1,1,1,1,-1,1,-1,-1,1,1,1,1,-1,-1,-1,-1,1,-1,-1,-1,-1,1,-1,1,-1,-1,-1}

## Slide 16: SP 2
Do you agree to add the following to 11bn SFD:
The LTF sequence to use for DBW = 40 MHz is
{-1,-1,-1,1,1,1,-1,-1,-1,1,-1,-1,-1,1,-1,1,1,1,-1,1,1,-1,1,1,-1,1,-1,-1,1,-1,1,-1,1,-1,-1,-1,-1,1,-1,-1,-1,-1,-1,1,-1,1,1,-1,1,-1,-1,-1,1,-1,1,-1,1,1,1,1,1,-1,1,1,-1,-1,1,-1,1,-1,1,-1,1,1,-1,1,1,1,1,1,-1,1,-1,-1,1,-1,-1,-1,-1,-1,-1,-1,1,1,-1,1,1,-1,-1,-1,1,-1,-1,1,1,-1}

## Slide 17: SP 3
Do you agree to add the following to 11bn SFD:
The LTF sequence to use for DBW = 80 MHz is
{-1,-1,-1,1,-1,1,1,1,-1,1,-1,-1,1,-1,1,-1,-1,-1,-1,1,-1,-1,-1,-1,1,1,-1,-1,1,1,-1,-1,1,-1,1,-1,-1,-1,-1,-1,1,-1,1,1,1,-1,-1,1,1,-1,-1,1,1,1,1,1,1,1,-1,1,1,1,-1,-1,1,-1,-1,-1,1,-1,1,1,1,-1,-1,-1,-1,-1,1,-1,1,1,-1,1,-1,1,1,-1,1,-1,-1,1,1,-1,-1,-1,-1,1,1,-1,1,-1,1,-1,1,1}

## Slide 18: References
[1] 11/24-0468r2 DRU Tone Plan for 11bn, Mediatek
[2] 11/24-0799r0 DRU Tone Plan from the perspective of PAPR, Huawei
[3] 11/24-1096r0 Mirror Symmetric 20 MHz DRU Tone Plan within 242 RRU Boundary, LGE
[4] 11/24-1567r0 LTF Design for DRU, Broadcom

## Slide 19: Appendix 1: Tone Plan [1] (1/3)
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in a 20 MHz UHR TB PPDU [1] |  |  |  |  | 
DRU Type | DRU index and subcarrier range |  |  |  | 
26DRU20 i = 1:9 | DRU1 [-120:9:-12, 6:9:114] | DRU2 [-116:9:-8, 10:9:118] | DRU3 [-118:9:-10, 8:9:116] | DRU4 [-114:9:-6, 12:9:120] | DRU5 [-112:9:-4, 5:9:113]
 | DRU6 [-119:9:-11, 7:9:115] | DRU7 [-115:9:-7, 11:9:119] | DRU8 [-117:9:-9, 9:9:117] | DRU9 [-113:9:-5, 4:9:112] | 
52DRU20 i = 1:4 | DRU1 26DRU20 [DRU1, DRU2] |  | DRU2 26DRU20 [DRU3, DRU4] |  | 
 | DRU3 26DRU20 [DRU6, DRU7] |  | DRU4 26DRU20 [DRU8, DRU9] |  | 
106DRU20 i = 1:2 | DRU1 26DRU20 [DRU1~4], [-3, 3] |  | DRU2 26DRU20 [DRU6~9], [-2, 2] |  | 

## Slide 20: Appendix 1: Tone Plan [1] (2/3)
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in a 40 MHz UHR TB PPDU [1] |  |  |  |  |  | 
DRU Type | DRU index and subcarrier range |  |  |  |  | 
26DRU40 i = 1:18 | DRU1 [-242:18:-26, 10:18:226] | DRU2 [-233:18:-17, 19:18:235] | DRU3 [-238:18:-22, 14:18:230] | DRU4 [-229:18:-13, 23:18:239] | DRU5 [-225:18:-9, 27:18:243] | DRU6 [-240:18:-24, 12:18:228]
 | DRU7 [-231:18:-15, 21:18:237] | DRU8 [-236:18:-20, 16:18:232] | DRU9 [-227:18:-11, 25:18:241] | DRU10 [-241:18:-25, 11:18:227] | DRU11 [-232:18:-16, 20:18:236] | DRU12 [-237:18:-21, 15:18:231]
 | DRU13 [-228:18:-12, 24:18:240] | DRU14 [-234:18:-18, 18:18:234] | DRU15 [-239:18:-23, 13:18:229] | DRU16 [-230:18:-14, 22:18:238] | DRU17 [-235:18:-19, 17:18:233] | DRU18 [-226:18:-10, 26:18:242]
52DRU40 i = 1:8 | DRU1 [-242:9:-17, 10:9:235] |  | DRU2 [-238:9:-13, 14:9:239] |  | DRU3 [-240:9:-15, 12:9:237] | 
 | DRU4 [-236:9:-11, 16:9:241] |  | DRU5 [-241:9:-16, 11:9:236] |  | DRU6 [-237:9:-12, 15:9:240] | 
 | DRU7 [-239:9:-14, 13:9:238] |  | DRU8 [-235:9:-10, 17:9:242] |  |  | 
106DRU40 i = 1:4 | DRU1 26DRU40 [DRU1~4], [-8,5] |  | DRU2 26DRU40 [DRU6~9], [-6,7] |  | DRU3 26DRU40 [DRU10~13], [-7,6] | 
 | DRU4 26DRU40 [DRU15~18], [-5,8] |  |  |  |  | 
242DRU40 i = 1:2 | DRU1 106DRU40 [DRU1~2], 26DRU40 DRU5, [-244,-4,3,9] |  | DRU2 106DRU40 [DRU3~4], 26DRU40 DRU14, [-243,-3,4,244] |  |  | 

## Slide 21: Appendix 1: Tone Plan [1] (3/3)
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in an 80 MHz UHR TB PPDU [1] |  |  |  | 
DRU Type | DRU index and subcarrier range |  |  | 
52DRU80 i = 1:16 | DRU1 [-483:36:-51, 17:36:449], [-467:36:-35, 33:36:465] | DRU2 [-475:36:-43, 25:36:457], [-459:36:-27, 41:36:473] | DRU3 [-479:36:-47, 21:36:453], [-463:36:-31, 37:36:469] | DRU4 [-471:36:-39, 29:36:461], [-455:36:-23, 45:36:477]
 | DRU5 [-477:36:-45, 23:36:455], [-461:36:-29, 39:36:471] | DRU6 [-469:36:-37, 31:36:463], [-453:36:-21, 47:36:479] | DRU7 [-481:36:-49, 19:36:451], [-465:36:-33, 35:36:467] | DRU8 [-473:36:-41, 27:36:459], [-457:36:-25, 43:36:475]
 | DRU9 [-482:36:-50, 18:36:450], [-466:36:-34, 34:36:466] | DRU10 [-474:36:-42, 26:36:458], [-458:36:-26, 42:36:474] | DRU11 [-478:36:-46, 22:36:454], [-462:36:-30, 38:36:470] | DRU12 [-470:36:-38, 30:36:462], [-454:36:-22, 46:36:478]
 | DRU13 [-476:36:-44, 24:36:456], [-460:36:-28, 40:36:472] | DRU14 [-468:36:-36, 32:36:464], [-452:36:-20,48:36:480] | DRU15 [-480:36:-48, 20:36:452], [-464:36:-32, 36:36:468] | DRU16 [-472:36:-40, 28:36:460], [-456:36:-24, 44:36:476]
106DRU80 i = 1:8 | DRU1 52DRU80 [DRU1~2], [-495, 485] | DRU2 52DRU80 [DRU3~4],[-491, 489] | DRU3 52DRU80 [DRU5~6],[-489, 491] | DRU4 52DRU80 [DRU7~8],[-493, 487]
 | DRU5 52DRU80 [DRU9~10],[-494, 486] | DRU6 52DRU80 [DRU11~12],[-490,490] | DRU7 52DRU80 [DRU13~14],[-488,492] | DRU8 52DRU80 [DRU15~16],[-492,488]
242DRU80 i = 1:4 | DRU1 [-499:4:-19, 17:4:497] |  | DRU2 [-497:4:-17, 19:4:499] | 
 | DRU3 [-498:4:-18, 18:4:498] |  | DRU4 [-496:4:-16, 20:4:500] | 
484DRU80 i = 1:2 | DRU1 [-499:2:-17, 17:2:499] |  | DRU2 [-498:2:-16, 18:2:500] |