## Slide 1: Data rates for AMP
Date: 2024-11-09
Authors:
Name | Affiliation | Address | Phone | Email
Weijie Xu | OPPO |  |  | xuweijie@oppo.com
Wang Ke |  |  |  | 
Shengjiang cui |  |  |  | 
Chuanfeng He |  |  |  | 
Yinan Qi |  |  |  | 
Jinyu Zhang |  |  |  | 
Zhisong Zuo |  |  |  | 
Doc.: IEEE 802.11-24/1801r1
Nov. 2024

## Slide 2: Abstract
In this submission, it firstly review the link budget for AMP, then the data rates for AMP are evaluated.
Based on the evaluations, we give our proposal on data rates for AMP.
Doc.: IEEE 802.11-24/1801r1

## Slide 3
Weijie Xu (OPPO)
Slide 3
Doc.: IEEE 802.11-24/1801r1
Nov. 2024
  The following shall be considered when defining data rates:
    Link budget (target coverage)
    Receiver type (receiving bandwidth, Noise Figure)
    Interference from other channels/legacy systems
    Device complexity
    Device power consumption
    System efficiency
    Consistent design among different devices
      Strive to support common data rate for different devices
    etc.
General consideration

## Slide 4
Link budget for DL
  Link budget for DL:
  For integrated case, the DL link budget is about 65dB.
    -45 dB is assumed as the receiver sensitivity (Envelope detector)[1].
  For non-integrated case, the DL link budget is about 90dB
    -70 dB is assumed as the receiver sensitivity (IF receiver)[1].
Weijie Xu (OPPO)
Slide 4
Doc.: IEEE 802.11-24/1801r1
Nov. 2024
 | WPT | DL (Integrated) | DL (Non-Integrated)
Frequency Band | 920MHz | 2.4GHz | 2.4GHz
EIRP of AP (dBm) | 36 | 20 | 20
Min. power for energy harvesting (dBm) | -20 | - | -
Receiver sensitivity | - | -45 (ED receiver) | -70 (IF receiver)
Link Budget | 56(=64.5 @2.4GHz) | 65 | 90

## Slide 5
Achievable SINR for DL(1)
  For ED (envelope detector) receiver, its receiving BW can be tens of MHz.
    Due to wide RF filter (covering the whole 2.4G band) and no BB filter
    The noise level measured in the receiving BW will be far below -45dB, assuming Noise Figure of 15.
      ~-80dBm (same NF as WUR and 80MHz Receiving BW)
    However, the interference from adjacent channels may be high and it may depend on the load of these channels and the deployment topologies
    So, the SINR can be very high(35dB) in some cases and relatively low(0dB or lower) in some other cases.
      Assume Same Tx power from
      AMP AP and interfering AP/STAs
Weijie Xu (OPPO)
Slide 5
Doc.: IEEE 802.11-24/1801r1
Nov. 2024
Receiving BW for ED receiver

## Slide 6
Achievable SINR for DL(2)
  For IF receiver, the SINR will mainly depend on the noise level. A high SNR can be available.
    It has RF filter and/or BB filter of 20MHz
    The noise level measured in the receiving BW will be far below -45dB, assuming Noise Figure of 15.
      ~-86dBm (same NF as WUR and 20MHz Receiving BW)
    So, the SINR can be high(16dB)
Weijie Xu (OPPO)
Slide 6
Doc.: IEEE 802.11-24/1801r1
Nov. 2024
Receiving BW for IF receiver

## Slide 7
Simulation assumptions for AMP DL
Weijie Xu (OPPO)
Slide 7
Doc.: IEEE 802.11-24/1801r1
Nov. 2024
  Link level simulations are performed for AMP DL data rate evaluations with the following simulation assumptions.
Parameters | Values
Date Rate | 250kpbs/1Mbps
Waveform | DSSS-OOK[2]
Channel model | Channel D
Chip duration | 2µs/0.5µs
Sampling rate at AMP device | 2MHz/8MHz
Coding | Manchester
Receiver type | ED receiver

## Slide 8
Simulation results for AMP DL date rate(1)
Weijie Xu (OPPO)
Slide 8
Doc.: IEEE 802.11-24/1801r1
Nov. 2024

## Slide 9
Simulation results for AMP DL date rate(2)
Weijie Xu (OPPO)
Slide 9
Doc.: IEEE 802.11-24/1801r1
Nov. 2024

## Slide 10
Observations
Weijie Xu (OPPO)
Slide 10
Doc.: IEEE 802.11-24/1801r1
Nov. 2024
  For 250kbps data rate@10% BLER, SINR of about -2dB and -3dB is needed respectively when the device sampling rate is 2MHz and 8MHz
    No obvious gain with high sampling rate for ED receiver
  For 1Mbps @10% BLER, SINR of ~13dB is required with sampling rate of 8MHz
    Complicated channel such as Channel D has negative impact on the OOK decoding with ED receiver (not possible to do channel equalization via channel estimation)
      OOK ON signal will spread into OOK OFF due to large delay spread
      For 1Mbps, the chip duration is 0.5µs and only 4 sampling within each chip

## Slide 11
Discussion and proposals
Weijie Xu (OPPO)
Slide 11
Doc.: IEEE 802.11-24/1801r1
Nov. 2024
  Maximum sampling of 2MHz can be supported for AMP device in close range case[3] and maximum sampling of 8MHz is feasible based on our evaluation.
  DL is mainly to convey control signaling and ~100 bits will be sufficient. The air time is about hundred of us @250kbps and short @1Mbps, which is acceptable from the perspective of system efficiency.
  The following data rates are proposed for AMP DL
    250kbps is the low data rate for AMP DL
    1Mbps is the high data rate for AMP DL

## Slide 12
Link budget for UL
Weijie Xu (OPPO)
Slide 12
Doc.: IEEE 802.11-24/1801r1
Nov. 2024
  For active device,
  For integrated case, the link budget for DL = ~65dB, X1=19dB and X2=29dB. m
  For non-integrated case, the link budget for DL = ~90dB (-70dB is assumed as the receiver sensitivity), X1 = -6dB and X2=4dB.
  For BC device, the link budget for DL = ~65dB (same as that for active device), X3=4dB.
Parameter | Active AMP(1) | Active AMP(2) | BC
TX Power(dBm) | -10 | 0 | -25
Thermal Noise Floor(dBm) (@20MHz) | -101 | -101 | -101
Noise Figure(dB) | 7 dB | 7 dB | 7 dB
Noise Power Level(dBm) | -94 | -94 | -94
Required SNR (dB) | X1 | X2 | X3
Receiver Sensitivity (dB) | -94+X1 | -94+X2 | -94+X3
Link Budget | 84-X1 | 94-X2 | 69-X3

## Slide 13
Simulation assumptions for AMP UL
Weijie Xu (OPPO)
Slide 13
Doc.: IEEE 802.11-24/1801r1
Nov. 2024
  Link level simulations are performed for AMP UL data rate evaluations with the following simulation assumptions.
Parameters | Values
Date Rate | 250kpbs/1Mbps/2Mbps/4Mbps
Waveform | OOK
Channel model | Channel B/Channel D
Chip duration | 2µs/0.5µs/0.25µs/0.125µs
Sampling rate at AMP AP | 20MHz
Coding | Manchester
Receiver type | Correlation detection

## Slide 14
Simulation results for AMP UL date rate (Channel B)
Weijie Xu (OPPO)
Slide 14
Doc.: IEEE 802.11-24/1801r1
Nov. 2024

## Slide 15
Simulation results for AMP UL date rate (Channel B)
Weijie Xu (OPPO)
Slide 15
Doc.: IEEE 802.11-24/1801r1
Nov. 2024

## Slide 16
Simulation results for AMP UL date rate (Channel D)
Weijie Xu (OPPO)
Slide 16
Doc.: IEEE 802.11-24/1801r1
Nov. 2024

## Slide 17
Simulation results for AMP UL date rate (Channel D)
Weijie Xu (OPPO)
Slide 17
Doc.: IEEE 802.11-24/1801r1
Nov. 2024

## Slide 18
Impact of channel on OOK decoding
Weijie Xu (OPPO)
Slide 18
Doc.: IEEE 802.11-24/1801r1
Nov. 2024
  Chanel delay spread will make it difficult and even impossible for OOK decoding, especially at high data rate.
    Take 1Mbps as example, 10 sampling for each Manchester chip(assuming 20MHz sampling rate), there may be several high power sampling of in Manchester OFF chip due to delay spread from Manchester ON chip
    OOK signal before experience of channel D
    OOK signal after experience of channel D

## Slide 19
Observations and proposal
Weijie Xu (OPPO)
Slide 19
Doc.: IEEE 802.11-24/1801r1
Nov. 2024
  Higher date rate can be achieved for AMP UL due to better receiver and high sampling rate at the AP.
    250kbps/1Mbps/2Mbps and 4Mbps are achievable data rates for AMP UL
  Date rate of higher than 4Mbps is not feasible due to:
    Impact from complicated channel (e.g. channel D)
    Maximum clock rate of 8MHz for the AMP device(i.e. active device)
      also considering Manchester coding
  It is proposed 250kbps/1Mbps/2Mbps and 4Mbps as AMP UL data rates.
      4Mbps is only for active AMP device

## Slide 20
Summary and proposals
  In this submission, determination of AMP DL link date rates and AMP UL link date rate is discussed, considering the following
    Link budget (receiver sensitivity, output power from AMP device), device capability(receiver type, clock capability etc.)
    Interference, impact from propagation channel etc.
  With intensive evaluation and comprehensive analysis, the following are proposed:
    250kbps is the low AMP DL data rate
    1Mbps is the high AMP DL data rate
      It is at least for active AMP device.
    250kbps/1Mbps/2Mbps and 4Mbps are AMP UL data rates.
      4Mbps is only for active AMP device
Weijie Xu (OPPO)
Slide 20
Doc.: IEEE 802.11-24/1801r1
Nov. 2024

## Slide 21
Straw Poll #1
Weijie Xu (OPPO)
Slide 21
Doc.: IEEE 802.11-24/1801r1
Nov. 2024
Do you agree with the following text:
  2 data rates are defined for AMP DL (from AMP AP to AMP STA).
        250kbps is the low AMP DL data rate
        1Mbps is the high AMP DL data rate
          It is at least for active AMP device.
Yes
No
Abstain

## Slide 22
Straw Poll #2
Weijie Xu (OPPO)
Slide 22
Doc.: IEEE 802.11-24/1801r1
Nov. 2024
Do you agree with the following text:
    250kbps/1Mbps/2Mbps and 4Mbps are AMP UL data rates.
      4Mbps is only for active AMP device
Yes
No
Abstain

## Slide 23
Straw Poll #2
Weijie Xu (OPPO)
Slide 23
Doc.: IEEE 802.11-24/1801r1
Nov. 2024
Do you agree with the following text:
    250kbps/1Mbps/2Mbps and 4Mbps are AMP UL data rates.
      4Mbps is only for active AMP device
Yes
No
Abstain

## Slide 24
Straw Poll #2
Weijie Xu (OPPO)
Slide 24
Doc.: IEEE 802.11-24/1801r1
Nov. 2024
Do you agree with the following text:
    250kbps/1Mbps/2Mbps and 4Mbps are AMP UL data rates.
      4Mbps is only for active AMP device
Yes
No
Abstain

## Slide 25: Reference
IEEE 802.11-24/0853r0, Design target and device capabilities for AMP IoT
IEEE 802.11-24/1802r0 OOK generation for AMP DL
IEEE IEEE 802.11-24/1237r0 AMP Tag Requirements for Close-range Mono-Static Backscattering
Doc.: IEEE 802.11-24/1801r1
Nov. 2024