## Slide 1: Providing Priority When Addressing IDC Issues
Nov 2024
Authors:
Name | Affiliation | Phone | email
Brian Hart | Cisco Systems |  | brianh@cisco.com
Malcolm Smith | Cisco Systems |  | 
Binita Gupta | Cisco Systems |  | 
Juan Carlos Zuniga | Cisco Systems |  | 
Stephen Orr | Cisco Systems |  | 
Jerome Henry | Cisco Systems |  | 

## Slide 2: Problem Statement: IDC happens, but Wi-Fi shouldn’t volunteer to become the “kick me” wireless technology[1]
Modern AP and client devices contain multiple radios with in-device coexistence (IDC) requirements
  TX PSD leakage/spurs affecting other operating channels:
    For performance, best addressed internally (e.g., RF ASIC design, RF filtering; with costs)
    Market pressure to externalize those costs via a protocol solution
  Overlapping operating channels
    Requires a protocol solution
Hence current SFD text: “11bn defines a mechanism for a non-AP STA to report unavailability at TXOP level and define or reuse/update existing mechanism for a non-AP STA to report long term (periodic) unavailability. [Motion #30, [1] and [66-82]]”
Meanwhile:
  Solving In-Device Coexistence (IDC) shouldn’t come exclusively or predominantly at any one wireless technology’s expense
  Just because a wireless technology is more polite and resilient doesn’t mean that the wireless technology should volunteer to be subordinated to less polite and/or more brittle technologies
  Rather, we should plant the flag, for now and the future, for a balanced proposal, based on traffic/service priority (~expiry imminence)

## Slide 3: Many Problem Subvariants according to IDC source, use case and implementation
Define “Serving link” (802.11) and “IDC link” (802.11 P2P / TDLS, Bluetooth, UWB, cellular etc)
Define “Serving device” (operates serving link only) and “IDC device” (operates 802.11 link + IDC link)
IDC characteristics can create different impacts and constraints:
  Same wireless resources: one or the other service can proceed but not both at the same time
    E.g., on-channel P2P, or same-channel TDLS
  Nearby wireless resources with unshared device resources: i.e., TX+TX or RX+RX possible but not TX+RX
    E.g., 802.11 and BT at 2.4 GHz (thru same antenna)
    RX+RX is low hanging fruit
    TX+TX quickly leads to “NSTR”-like coordination requirements (very hard between wireless technologies)
  Different wireless resources with shared device resources:
    E.g., off-channel 802.11 P2P / TDLS, or a shared 2.4 GHz transceiver with a different passband width, etc
    When communicating on the IDC link, no resources are available for the serving link and vice versa
    Corollary: IDC activity, once started, cannot be interrupted
IDC link may have:
  Predictable start times [+predictable duration], or
  Unpredictable start times, when TX/RX knowledge is only established a few milliseconds beforehand; also
  Also brittleness: if the start time is missed, no retries-in-time are supported  encourage modernization

## Slide 4: There is no magic bullet to address all these problems, so we need a tool kit of partial solutions …
When the serving activity has higher priority, and the IDC device’s policy supports it, feasible ways to override/ interrupt the unavailability time for IDC activity:
    Not possible (IDC has started, with A/BTX+TX/C)
    If the TXOP of the serving traffic has already started and IDC device does not need to respond (A/BTX+TX/C via IDC deferral; also while BRX+RX)
    If the TXOP of the serving traffic has already started; and the IDC device is able to respond (A/BTX+TX/C with IDC deferral; also BRX+RX then interrupted IDC)
    If the IDC device does not need to respond, for any priority of serving traffic (BRX+RX)
    For serving traffic of higher priority traffic, which may start at any time (BRX+RX then interrupted IDC)
Unavailability time for IDC activity, “AC_VI”
 SFD; 1
Serving device
IDC device
BA
 SFD; 1
Serving device
IDC device
BA
2: “AC_VO”
Serving device
IDC device
3: “AC_VO”
Serving device
IDC device
BA
4: “AC_BE”
Serving device
IDC device
4: “AC_BE”
Serving device
IDC device
Serving device
IDC device
5: “AC_VO”
BA

## Slide 5: … with protocol support
Problem Subvariant | I. Periodic | II. Aperiodic
Tasks for IDC Device |  | 
A. Same wireless resources | Send SCS( QC( ControlInfo(TID, UP), MediumTime) | EDCA contention according to AC // Priority-based LBT etc for non-802.11 systems
B. Nearby wireless resources + unshared device resources | Proposals towards: - P2P TWT // Missing priority information and negotiation | Proposals towards: - Send Initial control frame indicating start of upcoming unavailability [+ duration], and/or - Send Control response frame indicating start of upcoming unavailability [+ duration] // Both missing priority information
C. Different wireless resources with shared device resources |  | 
Tasks for Serving Device |  | 
A. Same wireless resources | After the SCS negotiation converges, issue regular TXS, according to priority | Proposals towards: - IDC session start+stop. During the session, non-IDC peer starts with an ICF+CRF Data(QoS Control(TID)) is available but is later – ICF is better. // Non-IDC Peer’s ICF is missing TXOP priority.
B. Nearby wireless resources + unshared device resources | // Current P2P TWT requirements are missing priority-based arbitration Otherwise, should honor accepted P2P TWT SPs | 
C. Different wireless resources with shared device resources |  | 

## Slide 6: Two New Parameters need to be Signaling
AC / UP / TID to indicate priority of the unavailability activity (e.g., 2-4 bits)
  Or priority needed to interrupt the unavailability activity
  Priority values can be mapped to a nominal expiry imminence time, for non-data services such as ranging
Interruptibility of IDC activity (e.g., 0-3 bits)
  Not possible (AC/UP/TID is reserved), or
  Interruptible when the TXOP of the serving, higher priority traffic has already started and IDC device does not need to respond, or
  Interruptible when the TXOP of the serving, higher priority traffic has already started. The IDC device is able to respond, or
  Interruptible when the recipient does not need to respond, for any priority of serving traffic starting at any time (AC/UP/TID is reserved), or
  Interruptible for serving, higher priority traffic starting at any time, or
  Interruptible for either 4 or 5.
  Max compression: no bits are allocated for interruptibility, then AC / UP / TID indicates priority needed to interrupt the unavailability activity at (say) “6”) but sending highest priority AC / UP / TID means “1”
i.e., 2 – 7 bits; less than 1 octet

## Slide 7: To round out the toolset, these parameters need multiple containers
ICF sent by IDC device
  Included alongside new time fields
CRF sent by IDC device
  Included alongside new time fields
ICF sent by serving device
  Depends on which frame is sent:
    If MU-RTS then Special User Info field++
    If BSRP then many choices (and TID is already available)
  // Also need a mgmt. frame exchange so Serving and IDC devices can negotiate the IDC session start + end
Channel Usage Request frame with a Channel Usage element with Usage Mode = 3 (for P2P TWT)
  Most naturally signaled via a new element
  Or possibly included via hacking the Channel Usage element
    e.g., allocate a range of Usage Modes
    e.g., assign a range of currently unassigned / unassignable values for the (operating class, channel number)
  // Other concerns related to this protocol will be addressed in a separate presentation

## Slide 8: Summary
Balanced and informed In-Device Coexistence has strategic value to 802.11
There are many IDC scenarios …
  Same wireless resources: one or the other service can proceed but not both at the same time
  Nearby wireless resources with unshared device resources
  Different wireless resources with shared device resources
… leading to different mitigations:
  Working around the IDC activity whenever higher priority, or
  Completing higher-priority serving TXOPs that started before the expected IDC activity
  During RX+RX, if higher-priority serving TXOPs need to TX for success (e.g., control response), then allow the IDC device to defer / cancel the lower priority IDC activity according to policy
The signaling requirements are very modest (< 1 octet)
  Priority of the IDC activity (or what priority it would take for it to defer or cancel the IDC activity)
  Under what circumstances the IDC activity can be performed in parallel / deferred / cancelled
The signaling requirements can be readily contained in the applicable control and mgmt. frames

## Slide 9: SP1
Do you support adding, to the SFD, the following text:
The 802.11bn amendment shall define signaling for IDC devices that signal unavailability for their serving link to further signal a) the priority of the unavailability activity and b) under what circumstances, if any, the IDC device is prepared to operate the serving link during the signaled unavailability.
Y / N/ A

## Slide 10: Backup

## Slide 11: References
[1] 23/573 “Balanced In-Device Coexistence”