## Slide 1: 5 bit MCS Table Design
Date: 2024-11-10
Authors:
Name | Affiliations | Address | Phone | email
Ron Porat | Broadcom |  |  | ron.porat@broadcom.com
Michael Wang | Broadcom |  |  | 

## Slide 2: Introduction
The group agreed to add 4 new MCS [1]. This naturally calls for a clean design using a 5 bit MCS table to accommodate the existing 16 MCS options and the new MCS.
In here we propose:
  The first 16 entries of the new table are identical to 11be as changing that order is highly unattractive across the industry
  The 4 new MCS are placed in locations that simplify implementation as unlike in previous amendments these new MCS fall in between existing MCS
As shown in the next slide we propose to define the location of the new MCS such that the (new MCS entry – 16) forms a monotonically increasing rate table easy to understand and use

## Slide 3: Proposed Locations of new MCS
New rates in blue: MCS[4] =1 (MSB) yields a rate right above the rate when MCS[4]=0 for the same MCS[3:0]
MCS (effectively) | MCS[4] | MCS[3:0] | Modulation | Code rate | bps/Hz
0 | 0 | 0 | BPSK | 1/2 | 0.5
1 | 0 | 1 | QPSK | 1/2 | 1
17 (17-161.5) | 1 | 1 | QPSK | 2/3 | 1.33
2 | 0 | 2 | QPSK | 3/4 | 1.5
3 | 0 | 3 | 16 | 1/2 | 2
19 (19-163.5) | 1 | 3 | 16 | 2/3 | 2.67
4 | 0 | 4 | 16 | 3/4 | 3
20 (20-164.5) | 1 | 4 | 16 | 5/6 | 3.33
5 | 0 | 5 | 64 | 2/3 | 4
6 | 0 | 6 | 64 | 3/4 | 4.5
7 | 0 | 7 | 64 | 5/6 | 5
23 (23-167.5) | 1 | 7 | 256 | 2/3 | 5.33
8 | 0 | 8 | 256 | 3/4 | 6
9 | 0 | 9 | 256 | 5/6 | 6.67
10 | 0 | 10 | 1K | 3/4 | 7.5
… |  |  |  |  | 

## Slide 4: Summary
We proposed a 5 bit MCS table design:
  The first 16 entries of the new table are identical to 11be
  Locations for the 4 new MCS

## Slide 5: References
[1] 11-24-1186-01-00bn-new-mcss-for-11bn-follow-up, Shengquan Hu (Mediatek)

## Slide 6: SP#1
Do you agree to add to the 11bn SFD?
A 5 bit MCS table is used to indicate all UHR MCSs.

## Slide 7: SP#2
Do you agree to add to the 11bn SFD?
The first 16 entries of the 5 bit MCS table (MCS0 to MCS15) are identical to 11be

## Slide 8: SP#3
Do you agree to add to the 11bn SFD?
In the 5bit MCS table
  MCS17 signals QPSK rate 2/3
  MCS19 signals 16QAM rate 2/3
  MCS20 signals 16QAM rate 5/6
  MCS23 signals 256QAM rate 2/3