## Slide 1: Considerations for AMP STA Access
Authors:
Date: 2024-xx-xx
Name | Affiliations | Address | Phone | email
Sanket Kalamkar | Qualcomm Technologies Inc. |  |  | sankal@qti.qualcomm.com
George Cherian |  |  |  | 
Manideep Dunna |  |  |  | 
Alfred Asterjadhi |  |  |  | 

## Slide 2: Introduction
Within 11bp, the group is discussing several use cases for AMP:
  Active UL transmissions
  Close-range backscatter
  Bistatic backscatter
A common thread between these use cases is that:
  AMP STAs may not be able to contend for the medium on their own
    E.g., due to energy constraints, NAV protection, etc.
This contribution provides a high-level view of MAC aspects to provide channel access to AMP STAs for different phases of its operation

## Slide 3: Different Phases
Discovery Phase
  Helps the AP to discover the presence of AMP clients
  A few thoughts discussed in the following slides
Association/Authentication Phase
  Expected to largely follow legacy procedures, with enhancements for AMP use cases
    In particular, we may need to improve access schemes for unassociated clients due to their very limited capabilities
Channel Access Phase
  Default is to have scheduled operation, wherein AP schedules the STAs
    Some additional thoughts in the following slides

## Slide 4: Discovery Phase
Before assisting AMP STAs with channel access, an AP may need to detect the presence of active AMP STAs in the neighborhood
  The mechanism needs to be simple and should not burden the STAs too much
Need to uniquely identify an AMP STA when multiple STAs are active
  Reduce the number of frame exchanges between AP and AMP STAs
  Reduce the chance of collisions between AMP STAs’ responses when AP seeks detection of active STAs
A simple MAC protocol needs to be used to achieve this goal
  Discussions needed for frame exchanges, MAC frame format

## Slide 5: Discovery Phase (Contd…)
The AP transmits an AMP (control) frame
  Some considerations needed depending on whether AP and energizer are the same device or not
    E.g., If the same, then the AMP frame can follow the energizing signal to increase the chance of STA receiving the frame
If an AMP STA is awake and receives this frame, it can report its presence to the AP
  This presence report can indicate whether the AMP STA is present or not
  Need to address potential collisions of presence reports from multiple AMP STAs

## Slide 6: Channel Access by AMP STAs
Propose to use a scheduled mode, where AP triggers a STA for UL transmission
  E.g., AP sends a Trigger frame to an associated AMP STA carrying a respective STA ID
AMP STA can respond with an UL packet
If the AP and energizer are collocated, the Trigger frame will follow the energizing signal carried in the same AMP PPDU
Consideration: how to efficiently provide UL access to multiple AMP STAs?
Same AMP PPDU if AP and energizer are collocated

## Slide 7: Summary
Some high-level considerations from MAC perspective to enable a simple access mechanism for AMP STAs
Potential phases to be considered:
  Discovery
  Association/Authentication
  Channel access