## Slide 1: UHR MU PPDU User Info Field Signaling
Date: 2024-11
Authors:

## Slide 2: Introduction
New PHY features are defined for UHR
  Unequal modulation
  New MCSs
  2x1944 LDPC code
Several contributions discuss about the UHR MU PPDU signaling the new features [1~5].
In this contribution, we proposes our preference of UHR-SIG design

## Slide 3: Recap: UHR MU PPDU
L-STF/LLTF/L-SIG/RL-SIG definition: no change
U-SIG: keep the encoding structure
  Version-independent fields (B1:B19): PHY version identifier  “1”
  Version-dependent fields
UHR-SIG: follow the same structure as EHT-SIG
  Common field: U-SIG over flow bits
  User specific field: changes needed to accommodate new features
L-SIG | RL-SIG
L-STF | LLTF
UHR-STF
UHR-LTF | UHR-Data
U-SIG
UHR-SIG

## Slide 4: New Features
UEQM: max four patterns per Nss
  Need 2-bits to indicate
New MCSs: four new MCS
  QPSK-2/3, 16QAM-2/3, 16QAM-5/6, 256QAM-2/3
  Expand current 4-bit to 5-bits
2x1944 code: 1-bit
Total Nss | 1st ss | 2nd ss | 3rd ss | 4th ss
2ss | M | M-1 |  | 
 | M | M-2 |  | 
3ss | M | M | M-1 | 
 | M | M | M-2 | 
 | M | M-1 | M-2 | 
4ss | M | M | M | M-1
 | M | M | M | M-2
 | M | M | M-1 | M-2
 | M | M-1 | M-1 | M-2

## Slide 5: User Field in UHR MU PPDU
Proposal: UHR user info field, expands 22-bits to 23-bits
Non-MUMIMO Allocation
  New MCS: expand to 5-bit MCS and shrink Nss to 3-bit (8 Nss)
  UEQM: 1-bit UEQM + 2-bit (BF and coding/Modulation pattern)
    Bit 19 set to 0 (EQM) : B20 (Beamforming) and B21 (Coding)
    Bit 19 set to 1 (UEQM): B20-B21 (Modulation pattern)
  One bit to indicate 2x1944 code
STA-ID B0-B10 | MCS B11-B15 | Nss B16-B18 | UEQM B19 | Beamforming B20 | Coding B21 | 2x1944 B22
STA-ID B0-B10 | MCS B11-B15 | UEQM B16 | Nss B17-B18 | Modulation pattern B20-B21 |  | 

## Slide 6: Non-MUMIMO Allocation (2)
Modulation pattern (B20-B21)
B20-B21 | Nss = 2 | Nss = 3 | Nss = 4
00 | [M, M-1] | [M, M, M-1] | [M, M, M, M-1]
01 | [M, M-2] | [M, M, M-2] | [M, M, M, M-2]
10 | Reserved | [M, M-1, M-2] | [M, M, M-1, M-2]
11 | Reserved | Reserved | [M, M-1, M-1, M-2]

## Slide 7: MUMIMO Allocation
  MUMIMO mode does not define unequal modulation
  Expand to 5-bit MCS subfield
  Reduce Spatial Configuration bits from 6 to 4, limit Nss,tot = 8
    same as HE-SIGB Spatial Configuration Table
  One bit to indicate 2x1944 code
STA-ID B0-B10 | MCS B11-B15 | Spatial configuration B16-B19 | Reserved B20 | Coding B21 | 2x1944 B22

## Slide 8: UHR SIG: Common field
U-SIG overflow bits for non-OFDMA transmission
  User info field increase to 23-bits
  SU transmission: good to keep UHR-SIG in two symbols for MCS0
    Total overflow bits: 20  19
UHR-SIG (U-SIG Overflow) | Spatial Reuse | 4
 | GI+LTF size | 2
 | Number of EHT-LTF symbols | 3
 | LDPC extra symbol segment | 1
 | Pre-FEC padding | 2
 | PE disambiguity | 1
 | Disregard | 43
 | Number of Non-OFDMA Users | 3
Total # of Overflow Bits |  | 19

## Slide 9: Summary
Propose UHR-SIG User info field design to indicate the new PHY features
  23-bits user info field design of non-MUMIMO and MUMIMO allocation
UHR-SIG U-SIG overflow bits for non-OFDMA transmission change to keep SU transmission to 2 symbols with MCS 0.

## Slide 10: Reference
[1] 11-24/1695, 11bn-signaling-design-for-extra-mcs-ueqm-2xldpc
[2] 11-24/1427, signaling-for-mcs-and-ueqm-in-11bn
[3] 11-24/1411, signaling-for-uhr-ppdu
[4] 11-24/1431, a-unified-signaling-scheme-for-eqm-and-ueqm
[5] 11-24-0876, uhr-ppdu-phy-version

## Slide 11: SP1
Do you agree that the “Disregard” bits reduce from 4 bits to 3 bits in UHR-SIG common field for a non-OFDMA transmission?
  Note: other bits definition unchanged

## Slide 12: SP2
Do you agree to define user info field for non-MUMIMO allocation in UHR MU PPDU as?
STA-ID B0-B10 | MCS B11-B15 | Nss B16-B18 | UEQM B19 | Beamforming B20 | Coding B21 | 2x1944 B22
STA-ID B0-B10 | MCS B11-B15 | UEQM B16 | Nss B17-B18 | Modulation pattern B20-B21 |  | 

## Slide 13: SP3
Do you agree to define user info field for MUMIMO allocation in UHR MU PPDU as?
STA-ID B0-B10 | MCS B11-B15 | Spatial configuration B16-B19 | Reserved B20 | Coding B21 | 2x1944 B22

## Slide 14: SP4
Do you support to include the following to the 11bn SFD?
The four new MCSs are defined for both BCC and LDPC for UHR
  The four new MCSs are QPSK-2/3, 16QAM-2/3, 16QAM-5/6, 256QAM-2/3